Bay Area Air Quality Management District

939 Ellis Street

San Francisco, CA  94109

(415) 771-6000

Darft

# Major Facility Review Permit

# Issued To:

# ConocoPhillips Company – San Francisco Refinery

# Facility #A0016

# Facility Address:

# 1380 San Pablo Avenue

# Rodeo, CA  94572

# Mailing Address:

# 1380 San Pablo Avenue

# Rodeo, CA  94572

Responsible Official 	                                            Facility Contact

J. Michael Kenney, General Manager	Valerie Uyeda, Environmental Specialist

510 245 4415		510 245 5249

Type of Facility:	Petroleum refinery	BAAQMD Engineering Division Contact:

Primary SIC:	2911	Julian Elliot

Product:	refined petroleum products

# ISSUED BY THE BAY AREA AIR QUALITY MANAGEMENT DISTRICT

Jack P. Broadbent, Executive Officer/Air Pollution Control Officer		Date

# TABLE OF CONTENTS

I.	STANDARD CONDITIONS	3

II.	EQUIPMENT	7

III.	GENERALLY APPLICABLE REQUIREMENTS	23

IV.	SOURCE-SPECIFIC APPLICABLE REQUIREMENTS	26

V.	PERMIT CONDITIONS	274

VI.	APPLICABLE LIMITS & COMPLIANCE MONITORING REQUIREMENTS	318

VII.	TEST METHODS	459

VIII.	SCHEDULE OF COMPLIANCE	274

IX.	PERMIT SHIELD	467

X.	GLOSSARY	470

XI.	APPLICABLE STATE IMPLEMENTATION PLAN	479

# STANDARD CONDITIONS

## Administrative Requirements

The permit holder shall comply with all applicable requirements in the following regulations:

BAAQMD Regulation 1 - General Provisions and Definitions

(as amended by the District Board on 5/2/01);

SIP Regulation 1 - General Provisions and Definitions

(as approved by EPA on 8/1/01);

BAAQMD Regulation 2, Rule 1 - Permits, General Requirements

(as amended by the District Board on 8/1/01);

SIP Regulation 2, Rule 1 - Permits, General Requirements

(as approved by EPA on 2/25/99);

BAAQMD Regulation 2, Rule 2 - Permits, New Source Review

(as amended by the District Board on 5/17/00);

SIP Regulation 2, Rule 2 - Permits, New Source Review and Prevention of Significant Deterioration

(as approved by EPA on 2/25/99);

BAAQMD Regulation 2, Rule 4 - Permits, Emissions Banking

(as amended by the District Board on 5/17/00);

SIP Regulation 2, Rule 4 - Permits, Emissions Banking

(as approved by EPA on 2/25/99); and

BAAQMD Regulation 2, Rule 6 - Permits, Major Facility Review

(as amended by the District Board on 5/2/01).

## Conditions to Implement Regulation 2, Rule 6, Major Facility Review

This Major Facility Review Permit was issued on December 1, 2003, and expires on November 30, 2008.  The permit holder shall submit a complete application for renewal of this Major Facility Review Permit no later than May 31, 2008 and no earlier than November 30, 2007.  If a complete application for renewal has not been submitted in accordance with this deadline, the facility may not operate after November 30, 2008.  (Regulation 2-6-307, 404.2, & 409.6; MOP Volume II, Part 3, §4.2)

The permit holder shall comply with all conditions of this permit.  The permit consists of this document and all appendices.  Any non-compliance with the terms and conditions of this permit will constitute a violation of the law and will be grounds for enforcement action; permit termination, revocation and re-issuance, or modification; or denial of a permit renewal application.  (Regulation 2-6-307; MOP Volume II, Part 3, §4.11)

In the event any enforcement action is brought as a result of a violation of any term or condition of this permit, the fact that it would have been necessary for the permittee to halt or reduce the permitted activity in order to maintain compliance with such term or condition shall not be a defense to such enforcement action. (MOP Volume II, Part 3, §4.11)

This permit may be modified, revoked, reopened and reissued, or terminated for cause.  (Regulation 2-6-307, 409.8, 415; MOP Volume II, Part 3, §4.11)

The filing of a request by the facility for a permit modification, revocation and re-issuance, or termination, or the filing of a notification of planned changes or anticipated non-compliance does not stay the applicability of any permit condition.  (Regulation 2-6-409.7; MOP Volume II, Part 3, §4.11)

This permit does not convey any property rights of any sort, or any exclusive privilege.  (Regulation 2-6-409.7; MOP Volume II, Part 3, §4.11)

The permit holder shall supply within 30 days any information that the District requests in writing to determine whether cause exists for modifying, revoking and reissuing, or terminating the permit or to determine compliance with the permit.  (Regulation 1-441, Regulation 2-6-409.4 & 501; MOP Volume II, Part 3, §4.11)

Any records required maintained pursuant to this permit, which the permittee considers to contain proprietary or trade secret information shall be prominently designated as such.  Copies of any such proprietary or trade secret information which are provided to the District shall be maintained by the District in a locked confidential file, provided, however, that requests from the public for the review of any such information shall be handled in accordance with the District's procedures set forth in Section 11 of the District’s Administrative Code.  (Regulation 2-6-419; MOP Volume II, Part 3, §4.11)

Proprietary or trade secret information provided to EPA will be subject to the requirements of 40 CFR Part 2, Subpart B - Public Information, Confidentiality of Business Information.  (40 CFR Part 2)

The emissions inventory submitted with the application for this Major Facility Review Permit is an estimate of actual emissions or the potential to emit for the time period stated and is included only as one means of determining applicable requirements for emission sources.  It does not establish, or constitute a basis for establishing, any new emission limitations.  (MOP Volume II, Part 3, §4.11)

The responsible official shall certify all documents submitted by the facility pursuant to the major facility review permit.  The certification shall state that based on information and belief formed after reasonable inquiry, the statements and information in the document are true, accurate, and complete.  The certifications shall be signed by a responsible official for the facility. (MOP Volume II, Part 3, §4.11)

## Requirement to Pay Fees

The permit holder shall pay annual fees in accordance with District Regulation 3, including Schedule P.  (Regulation 2-6-402 & 409.13, Regulation 3; MOP Volume II, Part 3, §4.12)

## Inspection and Entry

Access to Facility:  The permit holder shall provide reasonable access to the facility and equipment which is subject to this permit to the APCO and/or to his or her designee.  (Regulation 1-440, Regulation 2-6-409.3; MOP Volume II, Part 3, §4.14)

## Records

1.	The permit holder must provide any information, records, and reports requested or specified by the APCO.  (Regulation 1-441, Regulation 2-6-409.4)

2.	Notwithstanding the specific wording in any requirement, all records for federally enforceable requirements shall be maintained for at least five years from the date of creation of the record.  (Regulation 2-6-501, Regulation 3; MOP Volume II, Part 3, §4.7)

## Monitoring Reports

Reports of all required monitoring must be submitted to the District at least once every six months, except where an applicable requirement specifies more frequent reporting. The first reporting period for this permit shall be December 1, 2003, to May 31, 2004.  The second reporting period for this permit shall be June 1, 2004, to June 30, 2004.  Subsequent reports shall be for the following periods:  July 1st through December 31st and January 1st through June 30th.  All reports are due on the last day of the month after the end of the reporting period.  All instances of non-compliance shall be clearly identified in these reports.  The reports shall be certified by the responsible official as true, accurate, and complete.  In addition, all instances of non-compliance with the permit shall be reported in writing to the District’s Compliance and Enforcement Division within 10 calendar days of the discovery of the incident.  Within 30 calendar days of the discovery of any incident of non-compliance, the facility shall submit a written report including the probable cause of non-compliance and any corrective or preventative actions. The reports shall be sent to the following address:

Director of Compliance and Enforcement

Bay Area Air Quality Management District

939 Ellis Street

San Francisco, CA 94109

Attn:  Title V Reports

(Regulation 2-6-502, Regulation 3; MOP Volume II, Part 3, §4.7)

## Compliance Certification

Compliance certifications shall be submitted annually by the responsible official of this facility to the Bay Area Air Quality Management District and to the Environmental Protection Agency.  The first certification period shall be December 1, 2003, to November 30, 2004. The second certification period shall be December 1, 2004, to December 31, 2004.  Subsequent certification periods will be January 1st to December 31st.  All compliance certifications are due on the last day of the month after the end of the certification period.  The certification must list each applicable requirement, the compliance status, whether compliance was continuous or intermittent, the method used to determine compliance, and any other specific information required by the permit.  The permit holder may satisfy this requirement through submittal of District-generated Compliance Certification forms.  The certification should be directed to the District’s Compliance and Enforcement Division at the address above, and a copy of the certification shall be sent to the Environmental Protection Agency at the following address:

# Director of the Air Division

USEPA, Region IX

75 Haweighthorne Street

San Francisco, CA   94105

Attention:  Air-3

(MOP Volume II, Part 3, §4.5 and 4.15)

## Emergency Provisions

- The permit holder may seek relief from enforcement action in the event of a breakdown, as defined by Regulation 1-208 of the District's Rules and Regulations, by following the procedures contained in Regulations 1-431 and 1-432.  The District will thereafter determine whether breakdown relief will be granted in accordance with Regulation 1-433.  (MOP Volume II, Part 3, §4.8)

The permit holder may seek relief from enforcement action for a violation of any of the terms and conditions of this permit by applying to the District's Hearing Board for a variance pursuant to Health and Safety Code Section 42350.  The Hearing Board will determine after notice and hearing whether variance relief should be granted in accordance with the procedures and standards set forth in Health and Safety Code Section 42350 et seq.  (MOP Volume II, Part 3, §4.8)

The granting by the District of breakdown relief or the issuance by the Hearing Board of a variance will not provide relief from federal enforcement.  (MOP Volume II, Part 3, §4.8)

## Severability

In the event that any provision of this permit is invalidated by a court or tribunal of competent jurisdiction, or by the Administrator of the EPA, all remaining portions of the permit shall remain in full force and effect.  (Regulation 2-6-409.5; MOP Volume II, Part 3, §4.10)

J.	Miscellaneous Conditions

For grandfathered sources, the throughput limits as shown in Condition 20989 are based upon District records at the time of the MFR permit issuance.  The facility must report any exceedance of these limits following the procedures in Section I.F.  This reporting requirement is intended to facilitate a determination of whether a modification has occurred as defined in Regulation 2-1-234.3.  The throughput limits for grandfathered sources are for reporting purposes only.  Exceedance of this limit does not establish a presumption that a modification has occurred, nor does compliance with the limit establish a presumption that a modification has not occurred.

## Accidental Release

This facility is subject to 40 CFR Part 68, Chemical Accident Prevention Provisions.  The permit holder shall submit a risk management plan (RMP) by the date specified in §68.10.  The permit holder shall also certify compliance with the requirements of Part 68 as part of the annual compliance certification, as required by Regulation 2, Rule 6.  (40 CFR Part 68, Regulation 2, Rule 6)

# EQUIPMENT

| Table II A - Permitted Sources Each of the following sources has been issued a permit to operate pursuant to the requirements of BAAQMD Regulation 2, Permits. The capacities in this table are the maximum allowable capacities for each source, pursuant to Standard Condition I.J and Regulation 2-1-301. |
| --- |
| S-# | Description | Make or Type | Model | Capacity |
| 2 | U229, B-301 Heater (natural gas, refinery fuel gas) | Petro-Chem | process heater | 22 MM BTU/hr |
| 3 | U230, B-201 Heater (natural gas, refinery fuel gas, naphtha) | Petro-Chem | process heater | 62 MM BTU/hr |
| 4 | U231, B-101 Heater (natural gas, refinery fuel gas) | Braun | process heater | 96 MM BTU/hr |
| 5 | U231, B-102 Heater (natural gas, refinery fuel gas) | Braun | process heater | 104 MM BTU/hr |
| 7 | U231, B-103 Heater (natural gas, refinery fuel gas, naphtha) | Petro-Chem | process heater | 64 MM BTU/hr |
| 8 | U240, B-1 Boiler (natural gas, refinery fuel gas) | Combustion Engineering | process heater | 256 MM BTU/hr |
| 9 | U240, B-2 Boiler (natural gas, refinery fuel gas) | Born | process heater | 61 MM BTU/hr |
| 10 | U240, B-101 Heater (natural gas, refinery fuel gas) | Foster-Wheeler | process heater | 223 MM BTU/hr |
| 11 | U240, B-201 Heater (natural gas, refinery fuel gas) | Econo-Therm | process heater | 108 MM BTU/hr |
| 12 | U240, B-202 Heater (natural gas, refinery fuel gas) | Econo-Therm | process heater | 42 MM BTU/hr |
| 13 | U240, B-301 Heater (natural gas, refinery fuel gas) | Born | process heater | 194 MM BTU/hr |
| 14 | U240, B-401 Heater (natural gas, refinery fuel gas) | Selas | process heater | 556 MM BTU/hr |
| 15 | U244, B-501 Heater (natural gas, refinery fuel gas) | Alcorn | process heater | 239.75 MM BTU/hr total for S-15 through S-19 |
| 16 | U244, B-502 Heater (natural gas, refinery fuel gas) | Alcorn | process heater | 239.75 MM BTU/hr total for S-15 through S-19 |
| 17 | U244, B-503 Heater (natural gas, refinery fuel gas) | Alcorn | process heater | 239.75 MM BTU/hr total for S-15 through S-19 |
| 18 | U244, B-504 Heater (natural gas, refinery fuel gas) | Alcorn | process heater | 239.75 MM BTU/hr total for S-15 through S-19 |
| 19 | U244, B-505 Heater (natural gas, refinery fuel gas) | Alcorn | process heater | 239.75 MM BTU/hr total for S-15 through S-19 |
| 20 | U244, B-506 Heater (natural gas, refinery fuel gas) | Econo-Therm | process heater | 23 MM BTU/hr |
| 21 | U244, B-507 Heater (natural gas, refinery fuel gas) | Econo-Therm | process heater | 8.1 MM BTU/hr |
| 22 | U248, B-606 Heater (natural gas, refinery fuel gas) | Econo-Therm | process heater | 31 MM BTU/hr |
| 29 | U200, B-5 Heater (natural gas, refinery fuel gas) | Foster-Wheeler | process heater | 103 MM BTU/hr |
| 30 | U200, B-101 Heater (natural gas, refinery fuel gas) | Petro-Chem | process heater | 50 MM BTU/hr |
| 31 | U200, B-501 Heater (natural gas, refinery fuel gas) | Petro-Chem | process heater | 20 MM BTU/hr |
| 36 | U200, B-N001 Heater (natural gas, refinery fuel gas) | NA | process heater | 82.1 MM BTU/hr |
| 43 | U200, B-202 Heater (natural gas, refinery fuel gas) |  | process heater | 230 MM BTU/hr |
| 44 | U200, B-201 PCT Reboil Furnace (natural gas, refinery fuel gas) |  | process heater | 46 MM BTU/hr |
| 50 | Diesel Engine (turbine S-352 startup) | Allis-Chalmers | 6138, 435 hp | <100 hr/yr operation |
| 51 | Diesel Engine (turbine S-353 startup) | Allis-Chalmers | 6138, 435 hp | <100 hr/yr operation |
| 52 | Diesel Engine (turbine S-354 startup) | Allis-Chalmers | 6138, 435 hp | <100 hr/yr operation |
| 53 | SPP Emergency Generator G-27 | Cummins | 6B-5.9, 97 hp | <100 hr/yr operation (excluding emergency use) |
| 54 | Pump Station 3 CP-198 Emergency Engine | Waukesha Scania | F647DSUF, 258 hp | <100 hr/yr operation (excluding emergency use) |
| 55 | Pump Station 3 CP-199 Emergency Engine | Waukesha Scania | F647DSUF, 258 hp | <100 hr/yr operation (excluding emergency use) |
| 56 | Pump Station 4 G-201A Emergency Engine | Caterpillar | 3406, 370 hp | <100 hr/yr operation (excluding emergency use) |
| 57 | Pump Station 4 G-201B Emergency Engine | Caterpillar | 3406, 370 hp | <100 hr/yr operation (excluding emergency use) |
| 58 | Pump Station 4 G-422A Emergency Engine | Caterpillar | 3406, 370 hp | <100 hr/yr operation (excluding emergency use) |
| 59 | Pump Station 4 G-422B Emergency Engine | Caterpillar | 3406, 370 hp | <100 hr/yr operation (excluding emergency use) |
| 97 | Tank 100 | external floating roof | crude oil | 298 thousand bbl |
| 100 | Tank 103 | external floating roof | ship ballast | 47 thousand bbl |
| 101 | Storm Water Equalization Tank T-104 | external floating roof | stormwater | 5.5 million gal |
| 102 | Storm Water Equalization Tank T-105 | external floating roof | stormwater | 5.5 million gal |
| 106 | Storm Water Equalization Tank T-130 | external floating roof | stormwater | 10.6 million gal |
| 107 | Tank 150 | external floating roof | crude oil | 68 thousand bbl |
| 110 | Tank 155 | external floating roof | crude oil, gas oil, distillate oil | 4.2 million gal |
| 111 | Tank 156 | external floating roof | crude oil | 100 thousand bbl |
| 112 | Tank 157 | external floating roof | crude oil | 100 thousand bbl |
| 113 | Tank 158 | external floating roof | crude oil | 101 thousand bbl |
| 114 | Tank 159 | external floating roof | crude oil | 136 thousand bbl |
| 115 | Tank 160 | external floating roof | naphtha | 75 thousand bbl |
| 117 | Tank 162 | external floating roof | naphtha | 5300 gal |
| 118 | Tank 163 | fixed roof | lube oil | 5300 gal |
| 121 | Tank 166 | external floating roof | gasoline | 18500 gal |
| 122 | Tank 167 | external floating roof | naphtha | 3.1 million gal |
| 123 | Tank 168 | external floating roof | naphtha | 75 thousand bbl |
| 124 | Tank 169 | external floating roof | naphtha | 75 thousand bbl |
| 125 | Tank 170 | external floating roof | naphtha | 75 thousand bbl |
| 126 | Tank 172 | external floating roof with dome | naphtha, MTBE | 75 thousand bbl |
| 128 | Tank 174 | external floating roof | crude oil, naphtha | 76 thousand bbl |
| 129 | Tank 180 | external floating roof | naphtha | 76 thousand bbl |
| 133 | API Waste Oil Tank T-193 | external floating roof | waste oil | 22 thousand bbl |
| 134 | API Waste Oil Tank T-194 | external floating roof | waste oil | 22 thousand bbl |
| 139 | Tank 204 | fixed roof | distillate oil | 81 thousand bbl |
| 140 | Tank 205 | fixed roof | naphtha | 54 thousand bbl |
| 150 | Tank 241 | external floating roof | gasoline | 79 thousand bbl |
| 151 | Tank 242 | external floating roof | gasoline | 75 thousand bbl |
| 177 | Tank 287 | external floating roof | gasoline | 104 thousand bbl |
| 178 | Tank 288 | external floating roof | diesel | 104 thousand bbl |
| 182 | Tank 294 | fixed roof | naphtha | 40 thousand bbl |
| 183 | Tank 295 | external floating roof | naphtha | 13 thousand bbl |
| 184 | Tank 296 | external floating roof | naphtha | 70 thousand bbl |
| 186 | Tank 298 | external floating roof | naphtha | 47 thousand bbl |
| 193 | Tank 305 | fixed roof | dye | 2000 gal |
| 194 | Tank 306 | fixed roof | dye | 2000 gal |
| 195 | Water Treatment Sludge Tank T-501 | fixed-roof | sludge | 2500 bbl |
| 196 | Water Treatment Sludge Tank T-502 | fixed-roof | sludge | 2500 bbl |
| 216 | Tank 695 | external floating roof | naphtha | 2.0 million gal |
| 238 | Used Caustic Tank T-211 | fixed-roof | caustic waste | 10000 bbl |
| 239 | Stripped Foul Water Tank T-212 | fixed-roof | sour water | 10000 bbl |
| 254 | Tank 1001 | external floating roof | gasoline | 104 thousand bbl |
| 255 | Tank 1002 | external floating roof | gasoline | 104 thousand bbl |
| 256 | Tank 1003 | external floating roof | gasoline | 104 thousand bbl |
| 257 | Tank 1004 | external floating roof with dome | gasoline | 104 thousand bbl |
| 258 | Tank 1005 | external floating roof with dome | gasoline | 104 thousand bbl |
| 259 | Tank 1006 | external floating roof | gasoline | 104 thousand bbl |
| 261 | Tank 1010 | external floating roof | naphtha, distillate oil | 104 thousand bbl |
| 294 | Non-Retail Gasoline Dispensing Facility (GDF 7609 – 1 nozzle) | phase I / II vapor recovery | EW A4000 | 15000 gal underground tank |
| 296 | C-1 Flare | Callidus |  | 845 ton/hr gas handling capacity, 6.6 MM BTU/hr pilot |
| 300 | U200 Delayed Coker | delayed coker | NA | 81,000 bbl/day |
| 301 | Molten Sulfur Pit 234 | NA | NA | 245 long ton/day for S-301, 302 , 303 |
| 302 | Molten Sulfur Pit 236 | NA | NA | 245 long ton/day for S-301, 302 , 303 |
| 303 | Molten Sulfur Pit 238 | NA | NA | 245 long ton/day for S-301, 302 , 303 |
| 304 | U229 Mid-Barrel Unionfining (Light Naphtha Hydrotreater after modification in accordance with A/C 5814) | NA | NA | 12198 bbl/day |
| 305 | U230 Prefractionator/Naphtha Hydrotreater | NA | NA | 25300 bbl/day |
| 306 | U231 Platforming Unit | NA | NA | 21,000 bbl/day |
| 307 | U240 Unicracking Unit | NA | NA | 38,000 bbl/day |
| 308 | U244 Reforming Unit | NA | NA | 16087 bbl/day |
| 309 | U248 UNISAR Unit | NA | NA | 16740 bbl/day |
| 318 | U76 Gasoline/Mid Barrel Blending Unit | NA | NA | 80000 bbl/day gasoline 41200 bbl/day diesel |
| 319 | U215 Gasoline Fractionating Unit | NA | NA | 9,600 bbl/day |
| 322 | U40 Raw Materials Receiving | NA | NA | throughput limited at specific tanks, process units |
| 324 | U100_API Oil Wastewater Separator (with outlet channel cover) | NA | NA | 7,500 gpm during media filter backwash and 7,000 gpm during all other times |
| 334 | Tank 107 | external floating roof | crude oil | 180 thousand bbl |
| 336 | U231 B-104 Heater (natural gas, refinery fuel gas) | Foster-Wheeler | process heater | 111 MM BTU/hr |
| 337 | U231 B-105 Heater (natural gas, refinery fuel gas) | Foster-Wheeler | process heater | 34 MM BTU/hr |
| 338 | U233 Fuel Gas Center |  |  | 7.5 E 6 cubic feet/hr |
| 339 | U80 Refined Oil Shipping Unit | gasoline shipping |  | 294 thousand gal/hr |
| 340 | Tank 108 | external floating roof | crude oil | 200 thousand bbl |
| 341 | Tank 208 | external floating roof | gasoline | 103 thousand bbl |
| 342 | Tank 209 | external floating roof | gasoline | 103 thousand bbl |
| 343 | Tank 210 | external floating roof | gasoline | 103 thousand bbl |
| 350 | U267 Crude Distillation Unit | atmospheric/vacuum towers |  | 33000 bbl/day |
| 351 | U267 B-601/602 Tower Pre-heaters (natural gas, refinery fuel gas) |  |  | 101 MM BTU/hr |
| 352 | Combustion Turbine (natural gas, refinery fuel gas) | Westinghouse | 191 | 291MMBTU/hr continuously |
| 353 | Combustion Turbine (natural gas, refinery fuel gas) | Westinghouse | 191 | 291MMBTU/hr continuously |
| 354 | Combustion Turbine (natural gas, refinery fuel gas) | Westinghouse | 191 | 291MMBTU/hr continuously |
| 355 | Supplemental Firing Duct Burners (natural gas, refinery fuel gas) | Coen |  | 175 MM BTU/hr |
| 356 | Supplemental Firing Duct Burners (natural gas, refinery fuel gas) | Coen |  | 175 MM BTU/hr |
| 357 | Supplemental Firing Duct Burners (natural gas, refinery fuel gas) | Coen |  | 175 MM BTU/hr |
| 360 | Mid-Barrel Tank 223 | fixed roof | distillate oil | 110 thousand bbl |
| 370 | U228 Isomerization Unit |  |  | 460 bbl/hr |
| 371 | U228 B-520 (Adsorber Feed) Furnace (natural gas, refinery fuel gas) | Selas |  | 58 MM BTU/hr for S-371, 372 |
| 372 | U228 B-521 (Hydrogen Plant) Furnace (natural gas, refinery fuel gas) | Selas |  | 58 MM BTU/hr for S-371, 372 |
| 376 | Tool Room Cold Cleaner | Build-All | DM-32 | 29 gal |
| 377 | Machine Shop Cold Cleaner | Build-All | DM-32 | 29 gal |
| 378 | Auto Shop Cold Cleaner | Snap-On | DM-226 | 18 gal |
| 380 | Activated Carbon Silo (P-204) |  |  | 50,000 lb |
| 381 | Aeration Tank, Pact (F-201) | wastewater | 100 ft dia | 1.2 million gal |
| 382 | Aeration Tank, Pact (F-202) | wastewater | 100 ft dia | 1.2 million gal |
| 383 | Clarifier, F-203 | wastewater | 95 ft dia | 0.69 million gal |
| 384 | Clarifier (F-204) | wastewater | 95 ft dia | 0.69 million gal |
| 385 | Media Filter (F-207 A-H) | wastewater |  | 420 thousand gal/hr |
| 386 | PAC Regeneration Sludge Thickener (F-211) |  | 25 ft dia | 44000 gal |
| 387 | Wet Air Regeneration (P-202) | Zimpro |  | 15 gpm |
| 388 | Sludge Pretreatment (T276, F205) | 30 ft dia by 24 ft 12 ft dia by 24 ft |  | 17.5 ton/hr |
| 389 | Diatomaceous earth silo (F-214) |  |  | 40000 lb |
| 390 | F-106 Thickened Sludge Storage | 15 ft diameter open tank |  | 38,000 gal |
| 392 | Regenerated PAC Slurry Storage Tank F-266 | fixed roof |  | 42000 gal |
| 398 | MP-30 Flare | John Zink | Q5-48C | 845 ton/hr gas handling capacity, 3.1 MM BTU/hr pilot |
| 400 | Wet Weather Wastewater Sump (with vented cover) | 32 ft x 36 ft x 23 ft deep |  | 175 thousand gal |
| 401 | Dry Weather Wastewater Sump (with vented cover) | 33 ft x 25 ft x 26 ft deep |  | 150 thousand gal |
| 425 | Marine Loading Berth M1 | 2 permitted arms |  | 25000 bbl/day annual average for S-425, 426 |
| 426 | Marine Loading Berth M2 | 4 permitted arms |  | 25000 bbl/day annual average for S-425, 426 |
| 432 | U215 Deisobutanizer |  |  | 7600 bbl/day |
| 433 | MOSC Storage Tank | fixed roof |  | 30000 gal |
| 435 | Reformate Splitter |  |  | 18100 bbl/day |
| 436 | Deisopentanizer |  |  | 13400 bbl/day |
| 437 | Hydrogen Manufacturing Unit |  |  | 25 million scf/day |
| 438 | U110, H-1 (H2 Plant Reforming) Furnace (natural gas, refinery fuel gas, PSA offgas) | Claudius Peters | reforming furnace | 210 MM BTU/hr |
| 439 | Tank 109 | external floating roof | gasoline, others | 161 thousand bbl |
| 440 | Tank 110 (Alkylate) | external floating roof | alkylate | 161 thousand bbl |
| 442 | Tank 112 | external floating roof | gasoline, others | 161 thousand bbl |
| 444 | Tank 243 | external floating roof | gasoline, others | 113 thousand bbl |
| 445 | Tank 271 (Cracked Naphtha) | underground tank | naphtha | 189 thousand bbl |
| 446 | Tank 310 (Isopentane) | fixed roof | isopentane | 41 thousand bbl |
| 447 | Tank 311 (Isopentane) | fixed roof | isopentane | 41 thousand bbl |
| 448 | Tank 1007 (Blendstock Receiving) | internal floating roof | gasoline, others | 243 thousand bbl |
| 449 | Tank 285 (Cracked Naphtha) | fixed roof | naphtha | 189 thousand bbl |
| 450 | Groundwater Extraction Trenches |  | ground- water remediation | 3 gpm continuously |
| 451 | Tank 695 | external floating roof | naphtha, gasoline, others | 81 thousand bbl |
| 460 | U250 ULSD Hydrotreater | NA | NA | 35,000 bbl/day |
| 461 | U250, B-1 Heater (natural gas, refinery fuel gas) | NA | process heater | 50.2 MM BTU/hr |
| 462 | U215 Fuel Gas Caustic Treatment System | NA | NA | 4.2 million scf/day of fuel gas |
| 463 | U215 Butane Caustic Treatment System | NA | NA | 1,000 bbl/day of butane |
| 1001 | Sulfur Plant Unit 234 (including aux. burner) |  | Claus | 245 long ton/day for S-1001, 1002 and 1003 (271 long ton/day after execution of A/C 5814) |
| 1002 | Sulfur Plant Unit 236 (including aux. burner, water stripper) |  | Claus | 245 long ton/day for S-1001, 1002 and 1003 (271 long ton/day after execution of A/C 5814) |
| 1003 | Sulfur Plant Unit 238 (including aux. burner) |  | Claus | 245 long ton/day for S-1001, 1002 and 1003 (271 long ton/day after execution of A/C 5814) |
| 1007 | U100 Dissolved Air Flotation Unit (with fixed roof) |  |  | 7,500 gpm during media filter backwash and 7,000 gpm during all other times |
| 1008 | U100 Primary Stormwater Basin |  |  | 7000 gpm |
| 1009 | U100 Main Stormwater Basin |  |  | 7000 gpm |

| Table II B – Abatement Devices |
| --- |
| A-# | Description | Source(s) Controlled | Applicable Requirement | Operating Parameters | Limit or Efficiency |
| 1 | Sulfur Plant Tail-Gas Treatment Plant | S-1001 tailgas | BAAQMD 9-1-313.2 and SIP 9-1-313.2 | none | 95% of H2S in refinery fuel gas is removed and recovered on a refinery-wide basis |
| 1 | Sulfur Plant Tail-Gas Treatment Plant | S-1001 tailgas | BAAQMD 6-330 | none | 0.08 grain/dscf exhaust concentration of SO3 and H2SO4, expressed as 100% H2SO4 |
| 2 | Sulfur Plant Tail-Gas Treatment Plant | S-1002 tailgas | BAAQMD 9-1-313.2 and SIP 9-1-313.2 | none | 95% of H2S in refinery fuel gas is removed and recovered on a refinery-wide basis |
| 2 | Sulfur Plant Tail-Gas Treatment Plant | S-1002 tailgas | BAAQMD 6-330 | none | 0.08 grain/dscf exhaust concentration of SO3 and H2SO4, expressed as 100% H2SO4 |
| 3 | Sulfur Plant Tail-Gas Treatment Plant | S-1003 tailgas | BAAQMD 9-1-313.2 and SIP 9-1-313.2 | none | 95% of H2S in refinery fuel gas is removed and recovered on a refinery-wide basis |
| 3 | Sulfur Plant Tail-Gas Treatment Plant | S-1003 tailgas | BAAQMD 6-330 | none | 0.08 grain/dscf exhaust concentration of SO3 and H2SO4, expressed as 100% H2SO4 |
| 4 | SCR System | S-43 | BAAQMD Condition 1694 | NOx, O2 CEMs | 40 ppmv NOx at 3% O2 (over 8-hr period) except at startup and shutdown |
| 4 | SCR System | S-43 | BAAQMD Condition 1694 | none | 50 ppmv CO at 3% O2 (monthly average) except at startup and shutdown |
| 6 | SCR System | S-351 | BAAQMD Condition 1694 | NOx, O2 CEMs | 20 ppmv NOx at 3% O2 (over 3-hr period) except at startup and shutdown |
| 7 | Vapor Recovery System (3 electrically driven compressors) | Tanks S-139, S-140, S-182, S-388, S-433, S-445, S-446, S-447 | BAAQMD 7-301, 7-302, 7-303 | none | nuisance odors |
| 7 | Vapor Recovery System (3 electrically driven compressors) | S-139, S-140, S-182 | SIP 8-5-311.3 | None | 95% overall control of emissions |
| 7 | Vapor Recovery System (3 electrically driven compressors) | S-139, S-140, S-182 | BAAQMD 8-5-306 | None | 95% overall control of emissions |
| 7 | Vapor Recovery System (3 electrically driven compressors) | S-449 | BAAQMD Condition 11219 | None | vent emissions to the refinery fuel gas system |
| 7 | Vapor Recovery System (3 electrically driven compressors) | S-433 | BAAQMD Condition 7353 | None | vent emissions to the refinery fuel gas system |
| 7 | Vapor Recovery System (3 electrically driven compressors) | S-445 | BAAQMD Condition 12130 | None | vent emissions to the refinery fuel gas system |
| 7 | Vapor Recovery System (3 electrically driven compressors) | S-446 | BAAQMD Condition 12131 | None | vent emissions to the refinery fuel gas system |
| 7 | Vapor Recovery System (3 electrically driven compressors) | S-447 | BAAQMD Condition 12132 | None | vent emissions to the refinery fuel gas system |
| 7 | Vapor Recovery System (3 electrically driven compressors) | S-182 | BAAQMD Condition 13184 | None | vent emissions to the refinery fuel gas system |
| 8 | Stretford Evaporative Cooler | S-301 | BAAQMD 9-1-313.2 and SIP 9-1-313.2 | none | 95% of H2S in refinery fuel gas is removed and recovered on a refinery-wide basis |
| 8 | Stretford Evaporative Cooler |  | BAAQMD 6-330 | none | 0.08 grain/dscf exhaust concentration of SO3 and H2SO4, expressed as 100% H2SO4 |
| 9 | Stretford Evaporative Cooler | S-302 | BAAQMD 9-1-313.2 and SIP 9-1-313.2 | none | 95% of H2S in refinery fuel gas is removed and recovered on a refinery-wide basis |
| 9 | Stretford Evaporative Cooler |  | BAAQMD 6-330 | none | 0.08 grain/dscf exhaust concentration of SO3 and H2SO4, expressed as 100% H2SO4 |
| 10 | Stretford Evaporative Cooler | S-303 | BAAQMD 9-1-313.2 and SIP 9-1-313.2 | none | 95% of H2S in refinery fuel gas is removed and recovered on a refinery-wide basis |
| 10 | Stretford Evaporative Cooler |  | BAAQMD 6-330 | none | 0.08 grain/dscf exhaust concentration of SO3 and H2SO4, expressed as 100% H2SO4 |
| 13 | SCR System | S-352, S-355 | BAAQMD Condition 12122, Part 9a | NOx CEM | 66 lb/hr NOx (3 hr average), 167 ton/yr NOx at S-352-357; 528 lb/day NOx per turbine/duct burner set |
| 13 | SCR System | S-352, S-355 | BAAQMD Condition 12122, Part 7 and 10a | CO, O2 CEMs | 39 ppmv @ 15% O2 (30-day average) per turbine/duct burner set; 200 ton/yr CO at S-352-357 |
| 13 | SCR System | S-352 | BAAQMD 9-9-301 | NOx, CO, and O2 (or CO2) CEM | 9 ppmv NOx at 15% O2 |
| 14 | SCR System | S-353, S-356 | BAAQMD Condition 12122, Part 9a | NOx CEM | 66 lb/hr NOx (3 hr average), 167 ton/yr NOx at S-352-357; 528 lb/day NOx per turbine/duct burner set |
| 14 | SCR System | S-353, S-356 | BAAQMD Condition 12122, Part 7 and 10a | CO, O2 CEMs | 39 ppmv @ 15% O2 (30-day average) per turbine/duct burner set; 200 ton/yr CO at S-352-357 |
| 14 | SCR System | S-353 | BAAQMD 9-9-301 | NOx, CO, and O2 or CO2 CEM | 9 ppmv NOx at 15% O2 |
| 15 | SCR System | S-354, S-357 | BAAQMD Condition 12122, Part 9a | NOx CEM | 66 lb/hr NOx (3 hr average), 167 ton/yr NOx at S-352-357; 528 lb/day NOx per turbine/duct burner set |
| 15 | SCR System | S-354, S-357 | BAAQMD Condition 12122, Part 7 and 10a | CO, O2 CEMs | 39 ppmv @ 15% O2 (30-day average) per turbine/duct burner set; 200 ton/yr CO at S-352-357 |
| 15 | SCR System | S-354 | BAAQMD 9-9-301 | NOx, CO, and O2 (or CO2) CEM | 9 ppmv NOx at 15% O2 |
| 16 | SCR System | S-371 | BAAQMD Condition 1694, Part C2 | none | 20 ppmv NOx at 3% O2 (3-hr average) |
| 16 | SCR System | S-371 | BAAQMD Condition 1694, Part C3 | none | 50 ppmv CO at 3% O2 (3-hr average) |
| 17 | SCR System | S-372 | BAAQMD Condition 1694, Part C2 | none | 20 ppmv NOx at 3% O2 (3-hr average) |
| 17 | SCR System | S-372 | BAAQMD Condition 1694, Part C3 | none | 50 ppmv CO at 3% O2 (3-hr average) |
| 20 | Activated Carbon Silo Baghouse | S-380 | BAAQMD Regulations 6-301 6-305 6-310 6-311 BAAQMD Condition 18251 | differential pressure | normal range |
| 21 | Diatomaceous Earth Silo Baghouse | S-389 | BAAQMD Regulations 6-301 6-305 6-310 6-311 BAAQMD Condition 18251 | differential pressure | normal range |
| 36 | SCR System | S-36 | BAAQMD Condition 21097 | NOx, O2 CEM | 10 ppmv NOx at 3% O2 (3-hr average) |
| 46 | SCR System | S-438 | BAAQMD Condition 1694, Part E | NOx, O2 CEMs | 10 ppmv NOx at 3% O2 (3-hr average) |
| 46 | SCR System | S-438 | BAAQMD Condition 1694, Part E | none | 32 ppmv CO at 3% O2 (daily average) |
| 50 | Hydrogen Plant Vent Scrubber | S-307 | BAAQMD 8-2-301 | None | 15 lb/day POC from emission streams with more than 300 ppm total carbon |
| 113 | SCR System | S-13 | BAAQMD 9-10-301 | NOx, O2 CEM | 0.033 lb NOx/MMBTU refinery-wide limit |
| 420 | Marine Terminal Thermal Oxidizer | S-425 S-426 | BAAQMD 8-44-301 | None | 2 pounds POC per 1,000 bbl loaded OR at least 95% by weight reduction of POC emissions |
| 420 | Marine Terminal Thermal Oxidizer | S-425 S-426 | 40 CFR 60.104(a)(1) | None | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) |
| 461 | SCR System | S-461 | BAAQMD Condition 21096 | NOx, O2 CEM | 10 ppmv NOx at 3% O2 (3-hr average) |

| Table II C – Sources Exempt from Permit Requirements |
| --- |
| S-# | Description | Basis for Exemption |
| 69 | Propane Loading Rack | BAAQMD 2-1-123.3.1 |
| 70 | Butane Loading Rack | BAAQMD 2-1-123.3.1 |
| 71 | Wax & Lube Oil Loading Rack (Tank Cars) | BAAQMD 2-1-123.3.4, BAAQMD 2-1-123.3.6 |
| 72 | Wax Loading Rack (Trucks) | BAAQMD 2-1-123.3.6 |
| 73 | Lube Oil Loading Rack (Trucks) | BAAQMD 2-1-123.3.4 |
| 90 | Tank 67 | BAAQMD 2-1-123.3.2 |
| 91 | Tank 73 | BAAQMD 2-1-123.3.6 |
| 94 | Tank 78 | BAAQMD 2-1-123.3.10 |
| 98 | Tank 101 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123..3.3 |
| 99 | Tank 102 | BAAQMD 2-1-123.3.2 |
| 103 | Tank 106 | BAAQMD 2-1-123.3.2 |
| 105 | Tank 129 | BAAQMD 2-1-123.3.2 |
| 108 | Tank 153 | BAAQMD 2-1-123.3.2 |
| 109 | Tank 154 | BAAQMD 2-1-123.3.2 |
| 120 | Tank 165 | BAAQMD 2-1-123.3.4 |
| 127 | Tank 173 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.3 |
| 130 | Tank 188 | BAAQMD 2-1-123.3.6 |
| 131 | Tank 189 | BAAQMD 2-1-123.3.6 |
| 132 | Tank 191 | BAAQMD 2-1-123.3.4 |
| 135 | Tank 200 | BAAQMD 2-1-123.3.2 |
| 136 | Tank 201 | BAAQMD 2-1-123.3.2 |
| 137 | Tank 202 | BAAQMD 2-1-123.3.2 |
| 138 | Tank 203 | BAAQMD 2-1-123.3.3 |
| 141 | Tank 213 | BAAQMD 2-1-123.3.6 |
| 142 | Tank 214 | BAAQMD 2-1-123.3.6 |
| 143 | Tank 215 | BAAQMD 2-1-123.3.6 |
| 144 | Tank 216 | BAAQMD 2-1-123.3.6 |
| 145 | Tank 217 | BAAQMD 2-1-123.3.4 |
| 148 | Tank 231 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.9 |
| 149 | Tank 232 | BAAQMD 2-1-123.2, BAAQMD 2-1-123.3.9 |
| 157 | Tank 252 | BAAQMD 2-1-123.3.6 |
| 158 | Tank 258 | BAAQMD 2-1-123.3.2 |
| 162 | Tank 262 | BAAQMD 2-1-123.3.6 |
| 164 | Tank 264 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.3 |
| 165 | Tank 265 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.3 |
| 166 | Tank 266 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.3 |
| 167 | Tank 268 | BAAQMD 2-1-123.3.6 |
| 168 | Tank 269 | BAAQMD 2-1-123.3.2 |
| 169 | Tank 270 | BAAQMD 2-1-123.3.2 |
| 171 | Tank 273 | BAAQMD 2-1-123.3.6 |
| 172 | Tank 279 | BAAQMD 2-1-123.3.6 |
| 173 | Tank 280 | BAAQMD 2-1-123.3.2 |
| 174 | Tank 281 | BAAQMD 2-1-123.3.3 |
| 175 | Tank 284 | BAAQMD 2-1-123.3.2 |
| 179 | Tank 291 | BAAQMD 2-1-123.3.2 |
| 180 | Tank 292 | BAAQMD 2-1-123.3.2 |
| 187 | Tank 299 | BAAQMD 2-1-123.3.4 |
| 188 | Tank 300 | BAAQMD 2-1-123.3.1 |
| 189 | Tank 301 | BAAQMD 2-1-123.3.1 |
| 190 | Tank 302 | BAAQMD 2-1-123.3.1 |
| 191 | Tank 303 | BAAQMD 2-1-123.3.3 |
| 192 | Tank 304 | BAAQMD 2-1-123.3.3 |
| 202 | Tank 521 | BAAQMD 2-1-123.3.6 |
| 204 | Tank 528 | BAAQMD 2-1-123.3.2 |
| 205 | Tank 529 | BAAQMD 2-1-123.3.2 |
| 206 | Tank 530 | BAAQMD 2-1-123.3.4 |
| 207 | Tank 531 | BAAQMD 2-1-123.3.6 |
| 209 | Tank 674 | BAAQMD 2-1-123.3.2 |
| 224 | Tank 746 | BAAQMD 2-1-123.3.4 |
| 225 | Tank 747 | BAAQMD 2-1-123.3.4 |
| 226 | Tank 748 | BAAQMD 2-1-123.3.6 |
| 227 | Tank 749 | BAAQMD 2-1-123.3.6 |
| 228 | Tank 750 | BAAQMD 2-1-123.3.6 |
| 229 | Tank 751 | BAAQMD 2-1-123.3.6 |
| 230 | Tank 752 | BAAQMD 2-1-123.3.6 |
| 231 | Tank 753 | BAAQMD 2-1-123.3.4 |
| 236 | Tank 770 | BAAQMD 2-1-123.3.4 |
| 237 | Tank 771 | BAAQMD 2-1-123.3.4 |
| 240 | Tank 774 | BAAQMD 2-1-123.3.4 |
| 241 | Tank 775 | BAAQMD 2-1-123.3.4 |
| 253 | Tank 833 | BAAQMD 2-1-123.3.1 |
| 260 | Tank 1009 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.3 |
| 262 | Tank 1011 | BAAQMD 2-1-123.3.3 |
| 263 | Tank 1012 | BAAQMD 2-1-123.3.3 |
| 266 | Tank 1345 | BAAQMD 2-1-123.3.4 |
| 267 | Tank 1346 | BAAQMD 2-1-123.3.4 |
| 286 | Tank F3 | BAAQMD 2-1-123.3.3 |
| 287 | Tank F10 | BAAQMD 2-1-123.3.4 |
| 293 | Tank F805 | BAAQMD 2-1-123.3.3 |
| 427 | Marine Loading Berth B2 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.3 |
| 428 | Marine Loading Berth B3 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.3 |
| 429 | Marine Loading Berth B4 | BAAQMD 2-1-123.3.2, BAAQMD 2-1-123.3.3 |
| 500 | ULSD Cooling Tower | BAAQMD 2-1-128.4 |

# GENERALLY APPLICABLE REQUIREMENTS

The permit holder shall comply with all applicable requirements, including those specified in the BAAQMD and SIP Rules and Regulations and other federal requirements cited below.  These requirements apply in a general manner to the facility and/or to sources exempt from the requirement to obtain a District Permit to Operate.  The District has determined that these requirements will not be violated under normal, routine operations, and that no additional periodic monitoring or reporting to demonstrate compliance is warranted.  In cases where a requirement, in addition to being generally applicable, is also specifically applicable to one or more sources, the requirement and the source are also included in Section IV, Source-Specific Applicable Requirements, of this permit.

The dates in parenthesis in the Title column identify the versions of the regulations being cited and are, as applicable:

- BAAQMD regulation(s):  The date(s) of adoption or most recent amendment of the regulation by the District Board of Directors

- Any federal requirement, including a version of a District regulation that has been approved into the SIP:  The most recent date of EPA approval of any portion of the rule, encompassing all actions on the rule through that date

The full language of SIP requirements is on EPA Region 9’s website.  The address is included at the end of this permit.

NOTE:

There are differences between the current BAAQMD rules and the versions of the rules in the SIP. All sources must comply with both versions of the rule until US EPA has reviewed and approved the District’s revision of the regulation.

| Table III Generally Applicable Requirements |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) | N |
| SIP Regulation 1 | General Provisions and Definitions (6/28/99) | Y - note 1 |
| BAAQMD Regulation 2, Rule 1 | General Requirements (8/01/01) | N |
| SIP Regulation 2, Rule 1 | General Requirements (1/26/99) | Y - note 1 |
| BAAQMD Regulation 2, Rule 2 | New Source Review (5/17/00) | N |
| SIP Regulation 2, Rule 2 | New Source Review (1/26/99) | Y - note 1 |
| BAAQMD Regulation 2, Rule 4 | Emissions Banking (5/17/00) | N |
| SIP Regulation 2, Rule 4 | Emissions Banking (1/26/99) | Y - note 1 |
| BAAQMD Regulation 2, Rule 6 | Major Facility Review (5/2/01) | N |
| SIP Regulation 2, Rule 6 | Major Facility Review (6/23/95) | Y - note 1 |
| BAAQMD Regulation 2, Rule 9 | IERCs (4/7/99) | N |
| BAAQMD Regulation 3 | Fees (6/5/02) | N |
| SIP Regulation 3 | Fees (5/3/84) | Y - note 1 |
| BAAQMD Regulation 4 | Air Pollution Episode Plan (3/20/91) | N |
| SIP Regulation 4 | Air Pollution Episode Plan (8/06/90) | Y - note 1 |
| BAAQMD Regulation 5 | Open Burning (11/2/94) | N |
| SIP Regulation 5 | Open Burning (9/4/98) | Y - note 1 |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) | Y |
| BAAQMD Regulation 7 | Odorous Substances (3/17/82) | N |
| BAAQMD Regulation 8, Rule 1 | Organic Compounds - General Provisions (6/15/94) | Y |
| BAAQMD Regulation 8, Rule 2 | Organic Compounds – Miscellaneous Operations (06/15/94) | Y |
| BAAQMD Regulation 8, Rule 3 | Organic Compounds - Architectural Coatings (11/21/01) | Y |
| SIP Regulation 8, Rule 3 | Organic Compounds - Architectural Coatings (2/18/98) | Y - note 1 |
| SIP Regulation 8, Rule 10 | Organic Compounds – Pressure Vessel Depressurization (7/20/83) | Y |
| BAAQMD Regulation 8, Rule 40 | Organic Compounds – Aeration of Contaminated Soil and Removal of Underground Storage Tanks (12/15/99) | Y |
| BAAQMD Regulation 8, Rule 49 | Organic Compounds - Aerosol Paint Products (12/20/95) | N |
| SIP Regulation 8, Rule 49 | Organic Compounds - Aerosol Paint Products (3/22/95) | Y – note 1 |
| BAAQMD Regulation 8, Rule 51 | Organic Compounds - Adhesive and Sealant Products (7/17/02) | N |
| BAAQMD Regulation 8, Rule 51 | Organic Compounds - Adhesive and Sealant Products (2/26/02) | Y - note 1 |
| BAAQMD Regulation 11, Rule 10 | Hazardous Pollutants – Hexavalent Chromium Emissions from Cooling Towers (11/15/99) | Y |
| BAAQMD Regulation 12, Rule 4 | Miscellaneous Standards of Performance - Sandblasting (7/11/90) | N |
| SIP Regulation 12, Rule 4 | Miscellaneous Standards of Performance - Sandblasting (9/2/81) | Y - note 1 |
| Notification Requirement – Process Unit Startup and Shutdown | Notification Requirement – Process Unit Startup and Shutdown (Permit Section VI) | N |
| EPA Regulation 40 CFR 82 | Protection of Stratospheric Ozone (2/21/95) | Y |
| Subpart F, 40 CFR 82.156 | Leak Repair | Y |
| Subpart F, 40 CFR 82.161 | Certification of Technicians | Y |
| Subpart F, 40 CFR 82.166 | Records of Refrigerant | Y |
| Subpart H, 40 CFR 82.270(b) | Prohibitions, Halon | Y |
| Subpart M, 40 CFR 61 | Asbestos Demolition and Renovation | Y |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

# SOURCE-SPECIFIC APPLICABLE REQUIREMENTS

The permit holder shall comply with all applicable requirements, including those specified in the BAAQMD and SIP Rules and Regulations and other federal requirements cited below.  The requirements cited in the following tables apply in a specific manner to the indicated source(s).

The dates in parenthesis in the Title column identify the versions of the regulations being cited and are, as applicable:

1.	BAAQMD regulation(s):  The date(s) of adoption or most recent amendment of the regulation by the District Board

2.	Any federal requirement, including a version of a District regulation that has been approved into the SIP:  The most recent date of EPA approval of any portion of the rule, encompassing all actions on the rule through that date

The full text of each permit condition cited is included in Section VI, Permit Conditions, of this permit.  The full language of SIP requirements is on EPA Region 9’s website.  The address is included at the end of this permit.  All other text may be found in the regulations themselves.

| Table IV – All Sources Facility-Specific Generally Applicable Requirements |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/02/01) |  |  |
| 1-301 | Public Nuisance Prohibition | N |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-510 | Area Monitoring | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-523 | Parametric Monitoring and Recordkeeping Procedures | N |  |
| 1-530 | Area Monitoring Downtime | Y |  |
| 1-540 | Area Monitoring Date Examination | Y |  |
| 1-542 | Area Concentration Excesses | Y |  |
| 1-543 | Record Maintenance for Two Years | Y |  |
| SIP Regulation 1 | General Provisions and Definitions (6/28/99) |  |  |
| 1-523 | Parametric Monitoring and Recordkeeping Procedures | Y-note 1 |  |
| 1-544 | Monthly Summary | Y |  |
| BAAQMD Regulation 2, Rule 1 | General Requirements (8/1/01) |  |  |
| 2-1-429 | Federal Emissions Statement | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particle Weight Limitation | Y |  |
| 6-310.3 | Heat transfer operations | Y |  |
| 6-311 | Process Weight Rate Limits | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| District Regulation 8, Rule 2 | Organic Compounds, Miscellaneous Operations |  |  |
| 8-2-301 | Miscellaneous Operations: emissions shall not exceed 15 lb/day and 300 ppm total carbon on a dry basis | Y |  |
| BAAQMD Regulation 8, Rule 4 | General Solvent and Surface Coating Operations (05/15/96) |  |  |
| 8-4-302 | Solvent and Surface Coating Operations | N |  |
| 8-4-312 | Solvent Evaporative Loss Minimization | N |  |
| 8-4-501 | Recordkeeping Requirements | Y |  |
| SIP Regulation 8, Rule 4 | General Solvent and Surface Coating Operations (12/23/97) |  |  |
| 8-4-302 | Solvent and Surface Coating Operations | Y-note 1 |  |
| BAAQMD Regulation 8, Rule 5 | Storage of Organic Liquids (11/27/02) |  |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements, Approved Emission Control System | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-502 | Tank Cleaning Annual Source Test Requirements | Y |  |
| 8-5-603 | Determination of Emissions | Y |  |
| 8-5-603.2 | Tank degassing equipment | Y |  |
| BAAQMD Regulation 8, Rule 15 | Emulsified and Liquid Asphalts (09/16/87) |  |  |
| 8-15-305 | Prohibition of Manufacturer and Sale | Y |  |
| 8-15-501 | Manufacturing Records | Y |  |
| BAAQMD Regulation 8, Rule 40 | Aeration of Contaminated Soil and Removal of Underground Storage Tanks (12/15/01) |  |  |
| 8-40-116 | Exemption, Small Volume | Y |  |
| 8-40-205 | Contaminated Soil | Y |  |
| 8-40-306 | Contaminated Soil – Excavation and Removal | Y |  |
| 8-40-601 | Contaminated Soil Sampling | Y |  |
| 8-40-604 | Measurement of Organic Concentration | Y |  |
| BAAQMD Regulation 9, Rule 1 | Inorganic Gaseous Pollutants – Sulfur Dioxide (3/15/95) |  |  |
| 9-1-110 | Conditional Exemption, Area Monitoring | Y |  |
| 9-1-110.1 | comply with monitoring, records and reporting requirements of 1-1-510, 1-1-530, 1-1-540, 1-1-542, 1-1-543, 1-1-544 | Y |  |
| 9-1-110.2 | comply with 9-1-301 ground level SO2 concentration limits | Y |  |
| 9-1-301 | Limitations on Ground level Concentrations | Y |  |
| 9-1-302 | General Emission Limitation (applicable if monitoring required in 9-110 fails) | Y |  |
| 9-1-313 | Sulfur Removal Operations at Petroleum Refineries (processing more than 20,000 bbl/day of crude oil) | Y |  |
| 9-1-313.2 | Install a sulfur recovery plant | N |  |
| 9-1-501 | Area Monitoring Requirements (Regulations 1-510, 1-530, 1-540, 1-542, 1-543, 1-544) | Y |  |
| 9-1-502 | Emission Monitoring Requirements (Regulations 1-520, 1-522) | Y |  |
| 9-1-604 | Ground Level Monitoring | Y |  |
| SIP Regulation 9, Rule 1 | Inorganic Gaseous Pollutants – Sulfur Dioxide (6/8/99) [only provisions which are different than current BAAQMD regulation are listed] |  |  |
| 9-1-313.2 | Operation of a sulfur removal and recovery system that removes and recovers: 95% of H2S from refinery fuel gas, 95% of H2S and ammonia from process water streams | Y |  |
| BAAQMD Regulation 9, Rule 2 | Inorganic Gaseous Pollutants- Hydrogen Sulfide (10/6/99) |  |  |
| 9-2-301 | Limitations on Ground Level Concentrations | N |  |
| 9-2-501 | Area Monitoring Requirements (Regulations 1-510, 1-530, 1-540, 1-542, 1-543, 1-544) | N |  |
| 9-2-601 | Ground Level Monitoring | N |  |
| BAAQMD Regulation 11, Rule 2 | Asbestos Demolition, Renovation and Manufacturing (10/07/98) |  |  |
| 11-2-301 | Prohibited Operations | N |  |
| 11-2-302 | Visible Emissions | N |  |
| 11-2-303 | Demolition, Renovation, and Removal | N |  |
| 11-2-304 | Waste Disposal | N |  |
| 11-2-305 | Waste Disposal Sites | N |  |
| 11-2-501 | Temperature Records | N |  |
| 11-2-502 | Waste Shipment Records | N |  |
| 11-2-503 | Active Waste Disposal Records | N |  |
| 11-2-504 | Conversion Operations | N |  |
| NSPS 40 CFR 60 Subpart A | New Source Performance Standards – General Provisions (12/23/71) |  |  |
| 60.1 | Applicability | Y |  |
| 60.2 | Definitions | Y |  |
| 60.3 | Units and abbreviations | Y |  |
| 60.4 | Address | Y |  |
| 60.5 | Determination of construction or modification | Y |  |
| 60.6 | Review of plans | Y |  |
| 60.7 | Notification and record keeping | Y |  |
| 60.8 | Performance tests | Y |  |
| 60.9 | Availability of information | Y |  |
| 60.10 | State authority | Y |  |
| 60.11 | Compliance with standards and maintenance requirements | Y |  |
| 60.12 | Circumstances | Y |  |
| 60.13 | Monitoring requirements | Y |  |
| 60.14 | Modifications | Y |  |
| 60.15 | Reconstruction | Y |  |
| 60.16 | Priority list | Y |  |
| 60.17 | Incorporation by reference | Y |  |
| 60.18 | General control device requirements | Y |  |
| 60.19 | General notification and reporting requirements | Y |  |
| NESHAP 40 CFR 61 Subpart A | National Emission Standards for Hazardous Air Pollutants - General Provisions (3/16/95) |  |  |
| 61.1 | List of pollutants and applicability | Y |  |
| 61.2 | Definitions | Y |  |
| 61.3 | Units and abbreviations | Y |  |
| 61.4 | Address | Y |  |
| 61.5 | Prohibited activities | Y |  |
| 61.6 | Determination of construction or modification | Y |  |
| 61.7 | Application for approval of construction or modification | Y |  |
| 61.8 | Approval of construction or modification | Y |  |
| 61.9 | Notification of startup | Y |  |
| 61.10 | Source reporting and waiver request | Y |  |
| 61.11 | Waiver of compliance | Y |  |
| 61.12 | Compliance with standards and maintenance requirements | Y |  |
| 61.13 | Emission tests and waiver of emission tests | Y |  |
| 61.14 | Monitoring requirements | Y |  |
| 61.15 | Modifications | Y |  |
| 61.16 | Availability of information | Y |  |
| 61.17 | State Authority | Y |  |
| 61.18 | Incorporations by reference | Y |  |
| 61.19 | Circumvention | Y |  |
| NESHAP Part 61 Subpart FF; BAAQMD Regulation 11, Rule 12 | National Emission Standard for Benzene Waste Operations (3/7/90); BAAQMD National Emission Standard for Benzene Emissions from Benzene Transfer Operations and Benzene Waste Operations (4/19/89) |  |  |
| 61.340(a) | Applicability | Y |  |
| 61.340(c) | Applicability: Exempt Waste | Y |  |
| 61.342 | Standards: General | Y |  |
| 61.342(a) | exemption for facilities with less than 10 Mg/yr of benzene in waste from 61.342(b) and 61.342(c) | Y |  |
| 61.355 | Test methods, procedures and compliance provisions | Y |  |
| 61.355(b)(1) | quantification of annual waste quantity at sour water strippers (including ammonia stills at coke by-product plants) shall be made at the water effluent from the still | Y |  |
| 61.355(c)(1) (i)(A) | quantification of flow-weighted annual average benzene concentration (including ammonia stills at coke by-product plants) shall be made at the water effluent from the still | Y |  |
| 61.356 | Recordkeeping requirements | Y |  |
| 61.356(a) | recordkeeping and retention requirements | Y |  |
| 61.356(b) | waste stream records | Y |  |
| 61.357 | Reporting requirements | Y |  |
| 61.357(c) | reporting requirements for facilities with less than 10 Mg/yr total benzene in waste | Y |  |
| BAAQMD Regulation 11-12 | Incorporates by reference 40 CFR 61 Subpart FF | Y |  |
| NESHAP 40 CFR 63 Subpart A | National Emission Standards for Hazardous Air Pollutants for Source Categories | Y |  |
| 63.1 | Applicability | Y |  |
| 63.2 | Definitions | Y |  |
| 63.3 | Units and abbreviations | Y |  |
| 63.4 | Prohibited activities | Y |  |
| 63.5 | Construction and reconstruction | Y |  |
| 63.5(d) | Application for approval of construction or reconstruction | Y |  |
| 63.5(d)(1) | General Application Requirements | Y |  |
| 63.5(d)(2) | Application for approval of construction | Y |  |
| 63.5(d)(3) | Application for approval of reconstruction | Y |  |
| 63.5(d)(4) | Additional information | Y |  |
| 63.6 | Compliance with standards and maintenance | Y |  |
| 63.7 | Performance testing requirements | Y |  |
| 63.8 | Monitoring requirements | Y |  |
| 63.9 | Notification requirements | Y |  |
| 63.10 | Recordkeeping and reporting requirements | Y |  |
| 63.11 | Control device requirements | Y |  |
| 63.12 | State authority and delegation | Y |  |
| 63.13 | Addresses of State air pollution control agencies and EPA Regional Offices | Y |  |
| 63.14 | Incorporation by references | Y |  |
| 63.15 | Availability of Information & Confidentiality | Y |  |
| NESHAP 40 CFR 63 Subpart B | National Emission Standards for Hazardous Air Pollutants for Source Categories: General Provisions; and Requirements for Control Technology Determinations for Major Sources in Accordance with Clean Air Act Sections, Section 112(g) and 112(j); Final Rule |  |  |
| 63.52 | Approved process for new and existing affected sources. | Y |  |
| 63.52(a) | Sources subject to section 112(j) as of the section 112(j) deadline | Y |  |
| 63.52(a)(1) | Submit an application for Title V permit revision | Y |  |
| 63.52(e) | Permit application review | Y |  |
| 63.52(e)(1) | Submit a Part 2 MACT application meeting the requirements of 63.53(b) for Combustion Turbines | Y | 12/29/03 |
| 63.52(e)(1) | Submit a Part 2 MACT application meeting the requirements of 63.53(b) for Site Remediation | Y | 12/29/03 |
| 63.52(e)(1) | Submit a Part 2 MACT application meeting the requirements of 63.53(b) for Boilers and Process Heaters | Y | 6/27/04 |
| 63.52(e)(1) | Submit a Part 2 MACT application meeting the requirements of 63.53(b) for Reciprocating Internal Combustion Engines | Y | 6/27/04 |
| 63.52(h) | Enhanced monitoring | Y |  |
| 63.52(h)(i) | MACT emission limitations | Y |  |
| 63.52(h)(i)(1) | Compliance with all requirements applicable to affected sources, including compliance date for affected sources | Y |  |
| 63.53 | Application content for case-by-case MACT determination | Y |  |
| 63.53(a) | Part 1 MACT application | Y |  |
| 63.53(b) | Part 2 MACT application | Y |  |
| MACT 40 CFR 63 Subpart CC | National Emissions Standards for Hazardous Air Pollutants from Petroleum Refineries (8/18/95) |  |  |
| 63.640(a) | applies to petroleum refining process units and to related emission points | Y |  |
| 63.640(c)(3) | wastewater streams and treatment operations associated with petroleum refining process units meeting the criteria of section 63.640(a) | Y |  |
| 63.640(d)(1) | exclusion for stormwater from segregated stormwater sewers | Y |  |
| 63.640(f) | Applicability and Designation of Affected Sources | Y |  |
| 63.640(g) | Applicability and Designation of Affected Sources-Exempt processes | Y |  |
| 63.640(h) | Applicability and Designation of Affected Sources-Compliance dates | Y |  |
| 63.640(i) | Applicability and Designation of Affected Sources-New petroleum refining processes | Y |  |
| 63.640(j) | Applicability and Designation of Affected Sources-Changes to existing petroleum units | Y |  |
| 63.640(k) | Applicability and Designation of Affected Sources-Changes to existing petroleum units | Y |  |
| 63.640(l) | Applicability and Designation of Affected Sources-Additional requirements for new or changed sources | Y |  |
| 63.640(l)(3) | owner/operator of a petroleum refining wastewater stream shall comply with the recordkeeping and reporting requirements including the reports of (l)(3)(i) through (l)(3)(vii) of this section | Y |  |
| 63.642 | General Standards |  |  |
| 63.642(a) | apply for a Part 70 or Part 71 operating permit | Y |  |
| 63.642(c) | Table 6 of this subpart specifies the Subpart A provisions that apply. | Y |  |
| 63.642(d) | initial performance tests and compliance determinations shall be required only as specified in this subpart | Y |  |
| 63.642(e) | keep copies of all applicable reports and records for at least 5 years, except as otherwise specified in this subpart. | Y |  |
| 63.642(f) | all reports required by this subpart shall be sent to the Administrator | Y |  |
| 63.642(g) | existing source owners/operators shall control emissions of organic HAPs to the level represented by the equation in this paragraph | Y |  |
| 63.642(h) | new source owner/operators shall control emissions of organic HAPs to the level represented by the equation in paragraph (g) of this section. | Y |  |
| 63.642(i) | existing source owners/operators shall demonstrate compliance with (g) by following procedures in (k) for all emission points, or by following emission averaging compliance approach in (l) for specified emission points and the procedures in (k) for all other emission points within the source. | Y |  |
| 63.642(j) | new source owner/operators shall demonstrate compliance with (h) by following procedures in (k). they may not use emission averaging compliance approach | Y |  |
| 63.642(k) | existing source owners/operators may comply, and new sources owners/operators shall comply with the wastewater provisions in 63.647 and comply with 63.654 and is exempt from (g) | Y |  |
| 63.642(l) | emission averaging compliance approach | Y |  |
| 63.642(m) | States may restrict existing source owners/operators to only use the method in (k) to comply without allowance to use the emission averaging compliance approach | Y |  |
| 63.647 | Wastewater provisions | Y |  |
| 63.647(a) | Owners/operators of Group 1 wastewater streams shall comply with sections 61.340 to 61.355 of 40 CFR Part 61, Subpart FF for each stream that meets the definition of 63.641. | Y |  |
| 63.647(c) | Owners/operators required under Subpart FF of 40 CFR Part 61 to perform periodic measurement of benzene concentration in wastewater, or to monitor process or control device operating parameters shall operate consistently with the permitted concentration or operating parameter values. | Y |  |
| 63.648 | Equipment Leak Standards | Y |  |
| 63.648(a) | Existing source owners/operators subject to this subpart shall comply with the provisions of 40 CFR Part 60 Subpart VV and paragraph (b) of this section except as provided in paragraphs (a)(1), (a)(2), and (c) through (i) of this section. New source owners/operators shall comply with Subpart H of this part except as provided in paragraphs (c) through (i) of this section. | Y |  |
| 63.648(b) | Monitoring data generated before 8/18/95 to qualify for less frequent monitoring of valves and pumps as provided in 40 CFR Part 60 Subpart VV or Subpart H of this part and paragraph (c) of this section is governed by paragraphs (b)(1) and (b)(2) of this section. | Y |  |
| 63.648(c) | In lieu of complying with the existing source provisions of paragraph (a) an owner/operator may elect to comply with certain requirements of Subpart H of this part except as provided in paragraphs (c)(1) through (c)(10) and (e) through (i) of this section. | Y |  |
| 63.648(d) | Upon startup of new sources, the owner/operator shall comply with section 63.163(a)(1)(ii) of Subpart H of this part for light liquid pumps and 63.168(a)(1)(ii) of Subpart H for gas/vapor and light liquid valves. | Y |  |
| 63.648(e) | For reciprocating pumps in heavy liquid service and agitator in heavy liquid service and agitators in heavy liquid service, owners/operators are not required to comply with the requirements in section 63.169 of Subpart H of this part. | Y |  |
| 63.648(f) | Reciprocating pumps in light liquid service are exempt from section 63.163 and 60.482 if recasting the distance piece or reciprocating pump replacement is required. | Y |  |
| 63.648(h) | Owner/operators of sources subject to this subpart must maintain all records for a minimum of 5 years. | Y |  |
| 63.654 | Reporting and recordkeeping requirements | Y |  |
| 63.654(a) | Owner/operators subject to the wastewater provisions of 63.647 shall comply with the recordkeeping and reporting requirements in 61.356 and 61.357 of 40 CFR Part 61, Subpart FF, unless they comply with those specified in paragraph (o)(2)(ii) of 63.640. Recordkeeping and reporting for wastewater streams included in emission averages are specified in 63.653 and in paragraphs (f)(5) and (g)(8) of this section. | Y |  |
| 63.654(d) | Owner/operators subject to the equipment leaks standards in 63.648 shall comply with the recordkeeping and reporting provisions of paragraphs (d)(1) through (d)(6) of this section. | Y |  |
| BAAQMD Condition 20989, Part B | The owner/operator shall notify the District in writing by fax or email no less than three calendar days in advance of any scheduled startup or shutdown of any process unit and as soon as feasible for any unscheduled startup or shutdown of a process unit, but no later than 48 hours after the unscheduled startup/shutdown. [Basis: Regulation 2-1-403] | N |  |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.1 Source-specific Applicable Requirements S-2 – Unit 229, B-301 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.2 | Annual fuel firing limit at S-2, S-3, S-4, S-5, S-7 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.2 Source-specific Applicable Requirements S-3 – Unit 230, B-201 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-110.5 | Exemptions: Fired on non-gaseous fuel when natural gas is unavailable for use | N |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.2b | Visible emission monitoring for liquid-fired sources during tube cleaning [Basis: Regulation Regulation 2-6-409.2] | Y | 4/1/04 |
| Part A.2c | Visible emissions monitoring for liquid-fired sources [Basis: Regulation Regulation 2-6-409.2] | Y | 4/1/04 |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.2 | Annual fuel firing limit at S-2, S-3, S-4, S-5, S-7 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.3 Source-specific Applicable Requirements S-4 – Unit 231, B-101 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.2 | Annual fuel firing limit at S-2, S-3, S-4, S-5, S-7 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.4 Source-specific Applicable Requirements S-5 – Unit 231, B-102 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/021/5/94) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.2 | Annual fuel firing limit at S-2, S-3, S-4, S-5, S-7 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.5 Source-specific Applicable Requirements S-7 – Unit 231, B-103 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-110.5 | Exemptions: Fired on non-gaseous fuel when natural gas is unavailable for use | N |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.2b | Visible emission monitoring for liquid-fired sources during tube cleaning [Basis: Regulation Regulation 2-6-409.2] | Y | 4/1/04 |
| Part A.2c | Visible emissions monitoring for liquid-fired sources [Basis: Regulation Regulation 2-6-409.2] | Y | 4/1/04 |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.2 | Annual fuel firing limit at S-2, S-3, S-4, S-5, S-7 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.6 Source-specific Applicable Requirements S-8 – Unit 240, B-1 Boiler |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-520 | Continuous Emission Monitoring | Y |  |
| 1-520.1 | NOx, O2 monitors for steam generators with capacity of 250 MM BTU/hr or more | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures |  |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-304 | Tube Cleaning | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2 or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.1 | Annual fuel firing limit at S-8, S-9, S-10, S-11, S-12, S-13, S-14 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.7 Source-specific Applicable Requirements S-9 – Unit 240, B-2 Boiler |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.1 | Annual fuel firing limit at S-8, S-9, S-10, S-11, S-12, S-13, S-14 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.8 Source-specific Applicable Requirements S-10 – Unit 240, B-101 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures |  |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-304 | Tube Cleaning | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2 or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.1 | Annual fuel firing limit at S-8, S-9, S-10, S-11, S-12, S-13, S-14 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.9 Source-specific Applicable Requirements S-11 – Unit 240, B-201 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.1 | Annual fuel firing limit at S-8, S-9, S-10, S-11, S-12, S-13, S-14 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.10 Source-specific Applicable Requirements S-12 – Unit 240, B-202 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.1 | Annual fuel firing limit at S-8, S-9, S-10, S-11, S-12, S-13, S-14 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.11 Source-specific Applicable Requirements S-13 – Unit 240, B-301 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-304 | Tube Cleaning | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2 or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.1 | Annual fuel firing limit at S-8, S-9, S-10, S-11, S-12, S-13, S-14 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.12 Source-specific Applicable Requirements S-14 – Unit 240, B-401 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-304 | Tube Cleaning | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2 or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part F.1 | Annual fuel firing limit at S-8, S-9, S-10, S-11, S-12, S-13, S-14 [Basis: Cumulative Increase] | Y |  |
| Part F.3 | Monthly fuel firing records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.13 Source-specific Applicable Requirements S-15 – Unit 244, B-501 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limit for S-15 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.14 Source-specific Applicable Requirements S-16 – Unit 244, B-502 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-16 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.15 Source-specific Applicable Requirements S-17 – Unit 244, B-503 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-17 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.16 Source-specific Applicable Requirements S-18 – Unit 244, B-504 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-18 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.17 Source-specific Applicable Requirements S-19 – Unit 244, B-505 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-19 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.18 Source-specific Applicable Requirements S-20 – Unit 244, B-506 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-20 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.19 Source-specific Applicable Requirements S-21 – Unit 244, B-507 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-111 | Limited Exemption: Small Units: Between 1 and 10 MMBTU/hr and capable of firing fuel other than natural gas or LPG | Y |  |
| 9-10-217 | Definition: Small Unit: Between 1 and 10 MMBTU/hr and capable of firing fuel other than natural gas or LPG | Y |  |
| 9-10-306 | Small Unit Requirments | Y |  |
| 9-10-306.2 | Small Unit Requirments: Tune-up at least every 12 months, or within two weeks of start-up if not operated in the last 12 months | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.2 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-605 | Tune-up Procedures | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-21 [Basis: 2-1-234.3] | Y |  |

| Table IV – A.20 Source-specific Applicable Requirements S-22 – Unit 248, B-606 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-22 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.21 Source-specific Applicable Requirements S-29 – Unit 200, B-5 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-29 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.22 Source-specific Applicable Requirements S-30 – Unit 200, B-101 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-30 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.23 Source-specific Applicable Requirements S-31 – Unit 200, B-501 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-31 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.24 Source-specific Applicable Requirements S-36 – Unit 200, B-N001 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  | startup date |
| 1-520 | Continuous Emission Monitoring | Y | startup date |
| 1-520.8 | Monitors pursuant to Regulation 2-1-403 | Y | startup date |
| 1-521 | Monitoring May Be Required | Y | startup date |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N | startup date |
| 1-522.4 | reporting of inoperative CEMs | Y | startup date |
| 1-522.5 | CEM calibration requirements | Y | startup date |
| 1-522.6 | CEM accuracy requirements | Y | startup date |
| 1-522.7 | emission limit exceedance reporting requirements | N | startup date |
| 1-522.8 | monitoring data submittal requirements | Y | startup date |
| 1-522.9 | recordkeeping requirements | Y | startup date |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y | startup date |
| 1-602 | Area and Continuous Monitoring Requirements | N | startup date |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  | startup date |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 | startup date |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 | startup date |
| BAAQMD Regulation 2, Rule 1 | Regulation 2, Rule 1 - Permits, General Requirements (5/2/01; SIP approved 1/26/99 {adopted 11/01/89}) |  | startup date |
| 2-1-403 | Permit conditions requiring measurement of emissions | N | startup date |
| 2-1-501 | Monitors shall comply with Volume V of the Manual of Procedures | Y | startup date |
| SIP Regulation 2, Rule 1 | PROVISIONS NO LONGER IN CURRENT RULE Permits, General Requirements (1/26/99 {adopted 11/01/89}) |  | startup date |
| 2-1-403 | Permit conditions requiring measurement of emissions | Y – note 1 | startup date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  | startup date |
| 6-301 | Ringelmann #1 Limitation | Y | startup date |
| 6-305 | Visible Particles | Y | startup date |
| 6-310.3 | Particulate Weight Limitation | Y | startup date |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N | startup date |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  | startup date |
| 60.100 | Applicability | Y | startup date |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y | startup date |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y | startup date |
| 60.105 | Monitoring of Emissions and Operations | Y | startup date |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y | startup date |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y | startup date |
| 60.106(a) | Test methods and procedures | Y | startup date |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y | startup date |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y | startup date |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  | startup date |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y | startup date |
| BAAQMD Condition 21097 |  |  | startup date |
| Part 1 | Fuel restrictions [Basis: BACT, Cumulative Increase] | Y | startup date |
| Part 2 | Heat ratings, annual firing limits [Basis: Cumulative Increase] | Y | startup date |
| Part 3a | Abatement requirement [Basis: BACT, Cumulative Increase] | Y | startup date |
| Part 3b | Emission rate limits [Basis: BACT, Cumulative Increase, Toxic Management] | Y, except for ammonia limit (Toxic Management) | startup date |
| Part 4 | Continuous fuel monitor requirement [Basis: Cumulative Increase] | Y | startup date |
| Part 5a | NOx, O2 CEM requirement [Basis: BACT, Cumulative Increase] | Y | startup date |
| Part 5b | Annual CO source test requirement [Basis: BACT, Cumulative Increase] | Y | startup date |
| Part 6 | Fuel gas TRS concentration limit [Basis: BACT, Cumulative Increase, SO2 bubble] | Y | startup date |
| Part 7a | TRS testing requirement [Basis: BACT, Cumulative Increase, SO2 Bubble] | Y | startup date |
| Part 7b | TRS records requirement [Basis: BACT, Cumulative Increase, SO2 Bubble] | Y | startup date |
| Part 8 | Initial source test requirement [Basis: BACT, Cumulative Increase, Toxic Management] | Y, except for ammonia limit (Toxic Management) | 90 days after startup |
| Part 9 | Initial source test procedures TRS reporting requirements [Basis: BACT, Cumulative Increase, Toxic Management] | Y, except for ammonia limit (Toxic Management) | 90 days after startup |
| BAAQMD Condition 21099 |  |  |  |
| Part 1 | Light hydrocarbon control valve requirements [Basis: BACT] | Y | startup date |
| Part 2 | Light hydrocarbon flange/connector requirements [Basis: BACT] | Y | startup date |
| Part 3 | Centrifugal compressor requirements [Basis: BACT] | Y | startup date |
| Part 4 | Light hydrocarbon centrifugal pump requirements [Basis: BACT] | Y | startup date |
| Part 5 | Monitoring and repair program requirement [Basis: BACT] | Y | startup date |
| Part 6 | ULSD project component count report requirement [Basis: BACT, Cumulative Increase, Toxic Management Policy] | Y | startup date |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.25 Source-specific Applicable Requirements S-43 – Unit 200, B-202 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-520 | Continuous Emission Monitoring | Y |  |
| 1-520.8 | Monitors pursuant to Regulation 2-1-403 | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 2, Rule 1 | Regulation 2, Rule 1 - Permits, General Requirements (5/2/01; SIP approved 1/26/99 {adopted 11/01/89}) |  |  |
| 2-1-403 | Permit conditions requiring measurement of emissions | N |  |
| 2-1-501 | Monitors shall comply with Volume V of the Manual of Procedures | Y |  |
| SIP Regulation 2, Rule 1 | PROVISIONS NO LONGER IN CURRENT RULE Permits, General Requirements (1/26/99 {adopted 11/01/89}) |  |  |
| 2-1-403 | Permit conditions requiring measurement of emissions | Y – note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-304 | Tube Cleaning | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  |  |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part D.1 | S-43 abatement requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part D.2 | S-43, S-44 NOx emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part D.3 | S-43, S-44 CO emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part D.4 | S-43, S-44 NOx, O2 CEM requirement [Basis: BACT, Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-43 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.26 Source-specific Applicable Requirements S-44 – Unit 200, B-201 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-520 | Continuous Emission Monitoring | Y |  |
| 1-520.8 | Monitors pursuant to Regulation 2-1-403 | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 2, Rule 1 | Regulation 2, Rule 1 - Permits, General Requirements (5/2/01; SIP approved 1/26/99 {adopted 11/01/89}) |  |  |
| 2-1-403 | Permit conditions requiring measurement of emissions | N |  |
| 2-1-501 | Monitors shall comply with Volume V of the Manual of Procedures | Y |  |
| SIP Regulation 2, Rule 1 | PROVISIONS NO LONGER IN CURRENT RULE Permits, General Requirements (1/26/99 {adopted 11/01/89}) |  |  |
| 2-1-403 | Permit conditions requiring measurement of emissions | Y – note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  |  |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part D.2 | S-43, S-44 NOx emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part D.3 | S-43, S-44 CO emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part D.4 | S-43, S-44 NOx, O2 CEM requirement [Basis: BACT, Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-44 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.27 Source-specific Applicable Requirements S-50, S-51, S-52 – Turbine Startup Engines |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-303.1 | Ringelmann #2 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 9, Rule 1 | Inorganic Gaseous Pollutants, Sulfur Dioxide Emissions Limitations (3/15/95) |  |  |
| 9-1-304 | Fuel Burning (Liquid and Solid fuels) | Y |  |
| BAAQMD Regulation 9, Rule 8 | Nitrogen Oxides And Carbon Monoxide From Stationary Internal Combustion Engines (8/1/01) |  |  |
| 9-8-111.1 | Exemptions: Engines rated at or below 1000 brake horsepower which operate less than 200 hours in any 12-consecutive month period are only subject to recordkeeping | Y |  |
| 9-8-502 | Recordkeeping | Y |  |
| BAAQMD Condition 19488 |  |  |  |
| Part 1 | 100 hr/yr operating limit per engine [Basis: Cumulative increase] | Y |  |
| Part 2 | Operating hour records [Basis: Regulation 9-8-502] | Y |  |

| Table IV – A.28 Source-specific Applicable Requirements S-53, S-54, S-55, S-56, S-57, S-58, S-59 – Emergency Diesel Engines |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-303.1 | Ringelmann #2 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 9, Rule 1 | Inorganic Gaseous Pollutants, Sulfur Dioxide Emissions Limitations (3/15/95) |  |  |
| 9-1-304 | Fuel Burning (Liquid and Solid fuels) | Y |  |
| BAAQMD Regulation 9, Rule 8 | Nitrogen Oxides And Carbon Monoxide From Stationary Internal Combustion Engines (8/1/01) |  |  |
| 9-8-330 | Emergency Standby Engines, Hours of Operation | N |  |
| 9-8-530 | Emergency standby engines, monitoring and recordkeeping | N |  |
| BAAQMD Condition 19488 |  |  |  |
| Part 3 | 100 hr/yr operating limit per engine (non-emergency) [Basis: Regulation 9-8-330] | Y |  |
| Part 6 | Monitoring [Basis: Regulation 9-8-530] | Y |  |
| Part 7 | Operating hour records [Basis: Regulation 9-8-530] | Y |  |

| Table IV – A.29 Source-specific Applicable Requirements S-336 – Unit 231, B-104 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01)] |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-336 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.30 Source-specific Applicable Requirements S-337 – Unit 231, B-105 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01)] |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-337 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 3 | "NOx Box" requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 4 | "NOx Box" development procedure [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 5 | "NOx Box" parameters [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6a | Allowed "NOx Box" deviations [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 6b | "NOx Box" deviation reporting requirement [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 7 | NOx, CO, O2 source test requirement for sources without NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

| Table IV – A.31 Source-specific Applicable Requirements S-351 – Unit 267, B-601/602 Heaters |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-520 | Continuous Emission Monitoring | Y |  |
| 1-520.8 | Monitors pursuant to Regulation 2-1-403 | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 2, Rule 1 | Regulation 2, Rule 1 - Permits, General Requirements (5/2/01; SIP approved 1/26/99 {adopted 11/01/89}) |  |  |
| 2-1-403 | Permit conditions requiring measurement of emissions | N |  |
| 2-1-501 | Monitors shall comply with Volume V of the Manual of Procedures | Y |  |
| SIP Regulation 2, Rule 1 | PROVISIONS NO LONGER IN CURRENT RULE Permits, General Requirements (1/26/99 {adopted 11/01/89}) |  |  |
| 2-1-403 | Permit conditions requiring measurement of emissions | Y – note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  |  |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part B.1 | S-351 abatement requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part B.2 | S-351 NOx emission limit [Basis: BACT, Cumulative Increase] | Y |  |
| Part B.3 | S-351 NOx, O2 CEM requirement [Basis: BACT, Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-351 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.32 Source-specific Applicable Requirements S-371 – Unit 228, B-520 Furnace |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  |  |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part C.1 | S-371, S-372 abatement requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part C.2 | S-371, S-372 NOx emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part C.3 | S-371, S-372 CO emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-371 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.33 Source-specific Applicable Requirements S-372 – Unit 228, B-521 Furnace |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-301 | Emission Limit for Facility, NOx: 0.033 lb NOx/MMBTU | N |  |
| 9-10-301.1 | ...Start-up/Shutdown Contribution | N |  |
| 9-10-301.2 | ...Out-of-Service Units Contribution | N |  |
| 9-10-301.3 | ...Test-firing on Non-gaseous fuel Contribution | N |  |
| 9-10-303 | Federal Facility-wide NOx emission rate limit | Y |  |
| 9-10-305 | CO emission limit | N |  |
| 9-10-502 | Monitoring | Y |  |
| 9-10-502.1 | CEMS for NOx, CO, and O2, or equivalent monitoring | N |  |
| 9-10-502.2 | Fuel flowmeters | Y |  |
| 9-10-504 | Recordkeeping | N |  |
| 9-10-504.1 | Records | N |  |
| 9-10-505 | Reporting | N |  |
| 9-10-601 | Determination of NOx | N |  |
| 9-10-602 | Determination of CO and Stack Gas O2 | N |  |
| 9-10-603 | Compliance Determination | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  |  |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part C.1 | S-371, S-372 abatement requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part C.2 | S-371, S-372 NOx emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part C.3 | S-371, S-372 CO emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-372 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 21235 |  |  |  |
| Part 1 | Sources subject to Regulation 9-10–301 and 305 [Basis: Regulation 9-10-301, 305] | N | 6/1/04 |
| Part 2 | O2 CEM requirement [Basis: Regulation 9-10-502] | N | 9/1/04 |
| Part 8 | CO source test requirement for sources with NOx CEMs [Basis: Regulation 9-10-502] | N | 6/1/04 |
| Part 9 | CO, O2 CEM requirement [Basis: Regulation 9-10-502, 1-522] | N | 6/1/04 |
| Part 10 | Recordkeeping requirement [Basis: Regulation 9-10-504] | N | 6/1/04 |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.34 Source-specific Applicable Requirements S-438 – Unit 110, H-1 Furnace |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-304 | Tube Cleaning | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  |  |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y |  |
| BAAQMD Condition 1694 |  |  |  |
| Part A.1 | Heat ratings, firing limits [Basis: Regulation 2-1-234.3] | N |  |
| Part A.2a | Fuel restrictions [Basis: Regulation 2, Rule 1] | Y |  |
| Part A.3a | TRS testing requirement [Basis: SO2 Bubble] | Y |  |
| Part A.3b | TRS reporting requirements [Basis: SO2 Bubble] | Y |  |
| Part A.4 | SO2 emission limit [Basis: SO2 Bubble] | Y |  |
| Part A.5 | Records [Basis: Regulation 2, Rule 1; SO2 Bubble; Regulation 2-6-409.2] | Y |  |
| Part E.1 | S-438 abatement requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part E.2 | S-438 annual firing limit [Basis: Cumulative Increase] | Y |  |
| Part E.3 | S-438 PSA offgas fuel TRS limit [Basis: BACT, Cumulative Increase] | Y |  |
| Part E.4 | S-438 NOx and CO emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part E.5 | S-438 fuel gas TRS limit [Basis: BACT, Cumulative Increase] | Y |  |
| Part E.6 | S-438 Records [Basis: Recordkeeping] | Y |  |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – A.35 Source-specific Applicable Requirements S-461 – Unit 250, B-1 Heater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  | startup date |
| 1-520 | Continuous Emission Monitoring | Y | startup date |
| 1-520.8 | Monitors pursuant to Regulation 2-1-403 | Y | startup date |
| 1-521 | Monitoring May Be Required | Y | startup date |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N | startup date |
| 1-522.4 | reporting of inoperative CEMs | Y | startup date |
| 1-522.5 | CEM calibration requirements | Y | startup date |
| 1-522.6 | CEM accuracy requirements | Y | startup date |
| 1-522.7 | emission limit exceedance reporting requirements | N | startup date |
| 1-522.8 | monitoring data submittal requirements | Y | startup date |
| 1-522.9 | recordkeeping requirements | Y | startup date |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y | startup date |
| 1-602 | Area and Continuous Monitoring Requirements | N | startup date |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  | startup date |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 | startup date |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 | startup date |
| BAAQMD Regulation 2, Rule 1 | Regulation 2, Rule 1 - Permits, General Requirements (5/2/01; SIP approved 1/26/99 {adopted 11/01/89}) |  | startup date |
| 2-1-403 | Permit conditions requiring measurement of emissions | N | startup date |
| 2-1-501 | Monitors shall comply with Volume V of the Manual of Procedures | Y | startup date |
| SIP Regulation 2, Rule 1 | PROVISIONS NO LONGER IN CURRENT RULE Permits, General Requirements (1/26/99 {adopted 11/01/89}) |  | startup date |
| 2-1-403 | Permit conditions requiring measurement of emissions | Y – note 1 | startup date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  | startup date |
| 6-301 | Ringelmann #1 Limitation | Y | startup date |
| 6-305 | Visible Particles | Y | startup date |
| 6-310.3 | Particulate Weight Limitation | Y | startup date |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N | startup date |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  | startup date |
| 60.100 | Applicability | Y | startup date |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y | startup date |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y | startup date |
| 60.105 | Monitoring of Emissions and Operations | Y | startup date |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y | startup date |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y | startup date |
| 60.106(a) | Test methods and procedures | Y | startup date |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y | startup date |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y | startup date |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  | startup date |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y | startup date |
| BAAQMD Condition 21096 |  |  | startup date |
| Part 1 | Fuel restrictions [Basis: BACT, Cumulative Increase] | Y | startup date |
| Part 2 | Heat ratings, annual firing limits [Basis: Cumulative Increase] | Y | startup date |
| Part 3a | Abatement requirement [Basis: BACT, Cumulative Increase] | Y | startup date |
| Part 3b | Emission rate limits [Basis: BACT, Cumulative Increase, Toxic Management] | Y, except for ammonia limit (Toxic Management) | startup date |
| Part 4 | Continuous fuel monitor requirement [Basis: Cumulative Increase] | Y | startup date |
| Part 5a | NOx, O2 CEM requirement [Basis: BACT, Cumulative Increase] | Y | startup date |
| Part 5b | Annual CO source test requirement [Basis: BACT, Cumulative Increase] | Y | startup date |
| Part 6 | Fuel gas TRS concentration limit [Basis: BACT, Cumulative Increase, SO2 bubble] | Y | startup date |
| Part 7a | TRS testing requirement [Basis: BACT, Cumulative Increase, SO2 Bubble] | Y | startup date |
| Part 7b | TRS records requirement [Basis: BACT, Cumulative Increase, SO2 Bubble] | Y | startup date |
| Part 8 | Initial source test requirement [Basis: BACT, Cumulative Increase, Toxic Management] | Y, except for ammonia limit (Toxic Management) | 90 days after startup |
| Part 9 | Initial source test procedures TRS reporting requirements [Basis: BACT, Cumulative Increase, Toxic Management] | Y, except for ammonia limit (Toxic Management) | 90 days after startup |
| BAAQMD Condition 21099 |  |  |  |
| Part 1 | Light hydrocarbon control valve requirements [Basis: BACT] | Y | startup date |
| Part 2 | Light hydrocarbon flange/connector requirements [Basis: BACT] | Y | startup date |
| Part 3 | Centrifugal compressor requirements [Basis: BACT] | Y | startup date |
| Part 4 | Light hydrocarbon centrifugal pump requirements [Basis: BACT] | Y | startup date |
| Part 5 | Monitoring and repair program requirement [Basis: BACT] | Y | startup date |
| Part 6 | ULSD project component count report requirement [Basis: BACT, Cumulative Increase, Toxic Management Policy] | Y | startup date |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – B Source-specific Applicable Requirements S-400 Wet Weather Wastewater Sump S-401 Dry Weather Wastewater Sump |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| NSPS 40 CFR 60 Subpart QQQ | Standards of Performance for VOC Emissions from Petroleum Refinery Wastewater Systems |  |  |
| 60.690(a)(1) | Applicability: Subpart QQQ applies to affected facilities constructed, modified, or reconstructed after May 4, 1987 | Y |  |
| 60.690(a)(2) | Wastewater sumps are considered part of an individual drain system which is a separate affected facility | Y |  |
| 60.692-1(a) | The provisions of Subpart QQQ apply except during periods of startup, shutdown, or malfunction | Y |  |
| 60.692-1(b) | Determine compliance through review of records and reports, performance test results, and inspections | Y |  |
| 60.692-2 (c)(1) | Wastewater sumps in the wastewater process sewer line shall not be open to the atmosphere and shall be covered or enclosed in a manner with no visible gaps or cracks in joints, seals. | Y |  |
| 60.692-2 (c)(2) | The portion of each unburied wastewater sump in the wastewater process sewer line shall be visually inspected semiannually for indication of cracks, gaps, or other problems that could result in VOC emissions | Y |  |
| 60.692-2 (c)(3) | Whenever cracks, gaps, or other problems are detected, repairs shall be made as soon as practicable, but not later than 15 calendar days after identification, except as provided in 60.692-6. | Y |  |
| 60.692-6(a) | Delay of repairs are allowed if the repair is technically impossible without a complete or partial refinery or process unit shutdown. | Y |  |
| 60.692-6(b) | Delayed repairs shall be completed before the end of the next refinery or process unit shutdown. | Y |  |
| 60.697(a) | Each owner or operator shall comply with the recordkeeping provisions of Subpart QQQ. | Y |  |
| 60.697(b)(3) | Record the location, date, and corrective action for inspections required by 60.692-2(c) when a problem is identified that could result in VOC emissions. | Y |  |
| 60.697(e)(1) | If an emission npoint cannot be repaired or corrected without a process unit shutdown, record the expected date of a successful repair. | Y |  |
| 60.697(e)(2) | The reason for the delay as specified in 60.692-6 shall be recorded if an emission point or equipment problem is not repaired or corrected in the specified amount of time. | Y |  |
| 60.697(e)(3) | The signature of the owner or operator whose decision it was that repair could not be effected without refinery or process shutdown shall be recorded. | Y |  |
| 60.697(e)(4) | The date of successful repair or corrective action shall be recorded. | Y |  |
| 60.697(f)(1) | A copy of the design specifications for all equipment used to comply with the provisions of this subpart shall be kept for the life of the source in a readily accessible location. | Y |  |
| 60.697(f)(2) | Detailed information pertaining to the design specifications shall be kept. | Y |  |
| 60.698(b)(1) | Submit semiannually to the Administrator a certification that all of the required inspections have been carried out in accordance with Subpart QQQ standards. | Y |  |
| 60.698(c) | Submit semiannually to the Administrator a report that summarizes all inspections when cracks, gaps, or other problems that could result in VOC emissions are identified, including information about the repairs or corrective actions taken | Y |  |
| BAAQMD Condition 1440 |  |  |  |
| Part 4b | No detectable VOC from equipment [Basis: Cumulative Increase] | Y |  |
| Part 5 | Semiannual VOC monitoring and records [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-400, S-401 [Basis: 2-1-234.3] | Y |  |

| Table IV - C Source-specific Applicable Requirements S-324 API Oil/Wastewater Separator |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 8 | Wastewater (Oil-Water) Separator (6/15/94) | N |  |
| 8-8-113 | Exemption, secondary wastewater treatment processes and storm water sewer systems | Y |  |
| 8-8-114 | Exemption, bypassed oil-water separator or air flotation influent | Y |  |
| 8-8-302 | Wastewater separators rated capacity larger than or equal to 18.9 liters per seconds (300 gal/min), must be equipped with one of the following: | Y |  |
| 8-8-302.1 | a solid, vapor-tight, full contact fixed cover which totally encloses the separator tank, chamber, or basin liquid contents, with all cover openings closed and sealed, except when the opening is being used for inspection, maintenance, or wastewater sampling. | Y |  |
| 8-8-306 | Wastewater separator effluent channels rated capacity larger than or equal to 25.2 liters per second (400 gal/min) must be equipped with one of the following: | Y |  |
| 8-8-306.1 | a solid, gasketed, fixed cover total enclosing the oil-water separator effluent channel liquid contents, with all cover openings closed, except when being used for inspection, maintenance, or wastewater sampling. | Y |  |
| 8-8-501 | Maintain records when wastewater bypasses the API Separator or the Air Floatation Unit | Y |  |
| 8-8-503 | Maintain records for semiannual gap inspections, closure requirements, and repairs for oil-water separator effluent channel fixed roof seals, access doors, and other openings. | Y |  |
| NSPS 40 CFR 60 Subpart QQQ | Standards of Performance for VOC Emissions from Petroleum Refinery Wastewater Systems | N |  |
| 60.690(a)(1) | Applicability: Subpart QQQ applies to affected facilities constructed, modified, or reconstructed after May 4, 1987 | Y |  |
| 60.690(a)(3) | An oil-water separator is a separate affected facility | Y |  |
| 60.692-1(a) | The provisions of Subpart QQQ apply except during periods of startup, shutdown, or malfunction | Y |  |
| 60.692-1(b) | Determine compliance through review of records and reports, performance test results, and inspections | Y |  |
| 60.692-3 | Standards: Oil-water separators. | Y |  |
| 60.692-3 (a) | Each oil-water separator tank, slop oil tank, storage vessel, or other auxiliary equipment shall be equipped and operated with a fixed roof which meets the following specifications: | Y |  |
| 60.692-3 (a)(1) | The fixed roof shall completely cover the separator tank, slop oil tank, storage vessel or other auxiliary equipment. | Y |  |
| 60.692-3 (a)(2) | The vapor space under a fixed roof shall not be purged unless the vapor is directed to a control device. | Y |  |
| 60.692-3 (a)(3) | Roof access doors or openings shall be gasketed, latched, and kept closed during operation, except during inspection and maintenance. | Y |  |
| 60.692-3 (a)(4) | Roof seals, access doors, and other openings shall be checked by visual inspection initially and semiannually thereafter. | Y |  |
| 60.692-3 (a)(5) | When a broken seal or gasket or other problem is identified repairs shall be attempted as soon as practicable, but no later than 15 days later. | Y |  |
| 60.692-3 (e) | Slop oil from an oil-water separator and oily wastewater from slop oil handling equipment shall be collected, stored, transported, recycled, reused, or disposed of in an enclosed system. | Y |  |
| 60.692-6(a) | Delay of repairs are allowed if the repair is technically impossible without a complete or partial refinery or process unit shutdown. | Y |  |
| 60.692-6(b) | Delayed repairs shall be completed before the end of the next refinery or process unit shutdown. | Y |  |
| 60.697(a) | Each owner or operator shall comply with the recordkeeping provisions of Subpart QQQ. | Y |  |
| 60.697(c) | Record the location, date, and corrective action for inspections required by 60.692-3(a) when a problem is identified that could result in VOC emissions. | Y |  |
| 60.697(e)(1) | If an emission point cannot be repaired or corrected without a process unit shutdown, record the expected date of a successful repair. | Y |  |
| 60.697(e)(2) | The reason for the delay as specified in 60.692-6 shall be recorded if an emission point or equipment problem is not repaired or corrected in the specified amount of time. | Y |  |
| 60.697(e)(3) | The signature of the owner or operator whose decision it was that repair could not be effected without refinery or process shutdown shall be recorded. | Y |  |
| 60.697(e)(4) | The date of successful repair or corrective action shall be recorded. | Y |  |
| 60.697(f)(1) | A copy of the design specifications for all equipment used to comply with the provisions of this subpart shall be kept for the life of the source in a readily accessible location. | Y |  |
| 60.697(f)(2) | Detailed information pertaining to the design specifications shall be kept. | Y |  |
| 60.698(b)(1) | Submit semiannually to the Administrator a certification that all of the required inspection have been carried out in accordance with Subpart QQQ standards. | Y |  |
| 60.698(c) | Submit semiannually to the Administrator a report that summarizes all inspections when cracks, gaps, or other problems that could result in VOC emissions are identified, including information about the repairs or corrective actions taken | Y |  |
| BAAQMD Condition 1440 |  |  |  |
| Part 1 | No vapor space in separator [Basis: Cumulative Increase] | Y |  |
| Part 4a | No detectable VOC from doors, hatches, covers or other openings [Basis: Cumulative Increase] | Y |  |
| Part 5 | Semiannual VOC monitoring and records [Basis: Cumulative Increase] | Y |  |
| Part 6 | Maximum wastewater throughput [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limit for source S-324 [Basis: 2-1-234.3] | Y |  |

| Table IV – D Source-specific Applicable Requirements S-1007 Dissolved Air Flotation Unit |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 8 | Wastewater (Oil-Water) Separator | N |  |
| 8-8-307 | Air Flotation Unit: any air flotation unit and/or pre-air flotation unit flocculation sump, basin, chamber or tank with a maximum allowable capacity greater than 400 gals/min unless is equipped with one of the following: | Y |  |
| 8-8-307.1 | a solid, gasketed, fixed cover totally enclosing the vessel liquid contents, with all cover openings closed, except for inspection, maintenance, or wastewater sampling. The cover may include an atmospheric vent or a pressure/vacuum valve. Also includes gap inspection frequency and limits. | Y |  |
| 8-8-503 | Maintain records for semiannual gap inspections, closure requirements, and repairs for oil-water separator effluent channel fixed roof seals, access doors, and other openings. | Y |  |
| BAAQMD Condition 1440 |  |  |  |
| Part 4b | No detectable VOC from equipment [Basis: Cumulative Increase] | Y |  |
| Part 5 | Semiannual VOC monitoring and records [Basis: Cumulative Increase] | Y |  |
| Part 6 | Maximum wastewater throughput [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limit for S-1007 [Basis: 2-1-234.3] | Y |  |

| Table IV - E Source-specific Applicable Requirements – Wastewater Ponds/Biotreaters/Surface Impoundments S-381 Aeration Tank F-201 S-382 Aeration Tank F-202 S-383 Clarifier F-203 S-384 Clarifier F-204 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Condition 1440 |  |  |  |
| Part 4c | No detectable VOC from equipment [Basis: Cumulative Increase] | Y |  |
| Part 5 | Semiannual VOC monitoring and records [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-381, S-382, S-383, S-384 [Basis: 2-1-234.3] | Y |  |

| Table IV - F Source-specific Applicable Requirements – Wastewater Ponds/Biotreaters/Surface Impoundments S-1008 Primary Stormwater Basin S-1009 Main Stormwater Basin |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 8 | Wastewater (Oil-Water) Separator (6/15/94) | N |  |
| 8-8-114 | Exemption, bypassed oil-water separator or air flotation influent | Y |  |
| 8-8-501 | API Separator or Air Flotation Bypassed Wastewater Records: record requirements for water which bypasses normal treatment and is diverted to S-1008, S-1009 | Y |  |
| BAAQMD Condition 1440 |  |  |  |
| Part 2 | Minimize diversion of wastewater to S-1008, S-1009 [Basis: Cumulative Increase] | Y |  |
| Part 3 | Records of wastewater diversions to S-1008, S-1009 [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-1008, S-1009 [Basis: 2-1-234.3] | Y |  |

| Table IV – G Source-specific Applicable Requirements – Miscellaneous Wastewater Sources Subject to Condition 1440 S-385 – Wastewater Effluent Media Filter F-207 S-386 – PAC Regeneration Sludge Thickener F-211 S-387 – Wet Air Regeneration System P-202 S-390 – Thickened Sludge Storage F-106 S-392 – Regenerated PAC Slurry Storage F-266 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Condition 1440 |  |  |  |
| Part 4c | No detectable VOC from equipment [Basis: Cumulative Increase] | Y |  |
| Part 5 | Semiannual VOC monitoring and records [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-385, S-386, S-387, S-390, S-392 [Basis: 2-1-234.3] | Y |  |

| Table IV - H Source-specific Applicable Requirements Wastewater Junction Boxes |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 8 | Wastewater (Oil-Water) Separator (6/15/94) | N |  |
| 8-8-308 | Junction Box: equipped with either a solid, gasketed, fixed cover totally enclosing the junction box or a solid manhole cover. May include openings in the covers and vent pipes if the total open area of the junction box does not exceed 12.6 square inches and all vent pipes are at least 3 feet in length. | Y |  |
| NSPS 40 CFR 60 Subpart QQQ | Standards of Performance for VOC Emissions from Petroleum Refinery Wastewater Systems [APPLIES ONLY TO J-BOXES DOWNSTREAM OF S-400, S-401 SUMPS] | N |  |
| 60.690(a)(1) | Applicability: Subpart QQQ applies to affected facilities constructed, modified, or reconstructed after May 4, 1987 | Y |  |
| 60.690(a)(2) | Wastewater junction boxes are considered part of an individual drain system which is a separate affected facility | Y |  |
| 60.692-1(a) | The provisions of Subpart QQQ apply except during periods of startup, shutdown, or malfunction | Y |  |
| 60.692-1(b) | Determine compliance through review of records and reports, performance test results, and inspections | Y |  |
| 60.692-2 (b)(1) | Junction boxes shall be equipped with a cover and may have an open vent pipe which is at least 3 feet in length and does not exceed 4 inches in diameter. | Y |  |
| 60.692-2 (b)(2) | Junction box covers shall have a tight seal around the edge and shall be kept in place at all times, except during inspection and maintenance. | Y |  |
| 60.692-2 (b)(3) | Junction box shall be visually inspected semiannually to ensure that the cover is in place and to ensure that the cover has a tight seal around the edge. | Y |  |
| 60.692-2 (b)(4) | If a broken seal or gap is identified, first effort at repair shall be ade as soon as practicable, but not later than 15 calendar days after the broken seal or gap is identified, except as provided in 60.692-6. | Y |  |
| 60.692-2 (e) | Refinery wastewater routed through new process drains and a new first common downstream junction box, shall not be routed through a downstream catch basin. | Y |  |
| 60.692-6(a) | Delay of repairs are allowed if the repair is technically impossible without a complete or partial refinery or process unit shutdown. | Y |  |
| 60.692-6(b) | Delayed repairs shall be completed before the end of the next refinery or process unit shutdown. | Y |  |
| 60.697(a) | Each owner or operator shall comply with the recordkeeping provisions of Subpart QQQ. | Y |  |
| 60.697(b)(2) | Record the location, date, and corrective action for inspections required by 60.692-2(b) when a broken seal, gap or other problem is identified that could result in VOC emissions. | Y |  |
| 60.697(e)(1) | If an emission npoint cannot be repaired or corrected without a process unit shutdown, record the expected date of a successful repair. | Y |  |
| 60.697(e)(2) | The reason for the delay as specified in 60.692-6 shall be recorded if an emission point or equipment problem is not repaired or corrected in the specified amount of time. | Y |  |
| 60.697(e)(3) | The signature of the owner or operator whose decision it was that repair could not be effected without refinery or process shutdown shall be recorded. | Y |  |
| 60.697(e)(4) | The date of successful repair or corrective action shall be recorded. | Y |  |
| 60.697(f)(1) | A copy of the design specifications for all equipment used to comply with the provisions of this subpart shall be kept for the life of the source in a readily accessible location. | Y |  |
| 60.697(f)(2) | Detailed information pertaining to the design specifications shall be kept. | Y |  |
| 60.698(b)(1) | Submit semiannually to the Administrator a certification that all of the required inspections have been carried out in accordance with Subpart QQQ standards. | Y |  |
| 60.698(c) | Submit semiannually to the Administrator a report that summarizes all inspections when cracks, gaps, or other problems that could result in VOC emissions are identified, including information about the repairs or corrective actions taken | Y |  |

| Table IV – I Source-specific Applicable Requirements Wastewater Process Sewers/Sewer Lines – S-324 Oil/Water Separator only |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| NSPS 40 CFR 60 Subpart QQQ | Standards of Performance for VOC Emissions from Petroleum Refinery Wastewater Systems |  |  |
| 60.690(a)(1) | Applicability: Subpart QQQ applies to affected facilities constructed, modified, or reconstructed after May 4, 1987 | Y |  |
| 60.690(a)(2) | Wastewater process sewer lines are considered part of an individual drain system which is a separate affected facility | Y |  |
| 60.692-1(a) | The provisions of Subpart QQQ apply except during periods of startup, shutdown, or malfunction | Y |  |
| 60.692-1(b) | Determine compliance through review of records and reports, performance test results, and inspections | Y |  |
| 60.692-2 (c)(1) | Sewer lines shall not be open to the atmosphere and shall be covered or enclosed in a manner with no visible gaps or cracks in joints, seals. | Y |  |
| 60.692-2 (c)(2) | The portion of each unburied sewer line shall be visually inspected semiannually for indication of cracks, gaps, or other problems that could result in VOC emissions | Y |  |
| 60.692-2 (c)(3) | Whenever cracks, gaps, or other problems are detected, repairs shall be made as soon as practicable, but not later than 15 calendar days after identification, except as provided in 60.692-6. | Y |  |
| 60.692-6(a) | Delay of repairs are allowed if the repair is technically impossible without a complete or partial refinery or process unit shutdown. | Y |  |
| 60.692-6(b) | Delayed repairs shall be completed before the end of the next refinery or process unit shutdown. | Y |  |
| 60.697(a) | Each owner or operator shall comply with the recordkeeping provisions of Subpart QQQ. | Y |  |
| 60.697(b)(3) | Record the location, date, and corrective action for inspections required by 60.692-2(c) when a problem is identified that could result in VOC emissions. | Y |  |
| 60.697(e)(1) | If an emission npoint cannot be repaired or corrected without a process unit shutdown, record the expected date of a successful repair. | Y |  |
| 60.697(e)(2) | The reason for the delay as specified in 60.692-6 shall be recorded if an emission point or equipment problem is not repaired or corrected in the specified amount of time. | Y |  |
| 60.697(e)(3) | The signature of the owner or operator whose decision it was that repair could not be effected without refinery or process shutdown shall be recorded. | Y |  |
| 60.697(e)(4) | The date of successful repair or corrective action shall be recorded. | Y |  |
| 60.697(f)(1) | A copy of the design specifications for all equipment used to comply with the provisions of this subpart shall be kept for the life of the source in a readily accessible location. | Y |  |
| 60.697(f)(2) | Detailed information pertaining to the design specifications shall be kept. | Y |  |
| 60.698(b)(1) | Submit semiannually to the Administrator a certification that all of the required inspections have been carried out in accordance with Subpart QQQ standards. | Y |  |
| 60.698(c) | Submit semiannually to the Administrator a report that summarizes all inspections when cracks, gaps, or other problems that could result in VOC emissions are identified, including information about the repairs or corrective actions taken | Y |  |

| Table IV - J Source-specific Applicable Requirements Wastewater Gauging and Sampling Devices |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 8 | Wastewater (Oil-Water) Separator (6/15/94) |  |  |
| 8-8-303 | Gauging and Sampling Devices: Any compartment or access hatch shall have a vapor tight cover, seal, or lid that is closed, except for inspection, maintenance, or wastewater sampling. | Y |  |
| 8-8-603 | Vapor tight inspections shall be conducted using a portable gas detector as prescribed in EPA Reference Method 21 (40 CFR 60, Appendix A). | Y |  |

| Table IV - K Source-specific Applicable Requirements S-294 – Non-Retail Gasoline Dispensing Facility |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 7 | Organic Compounds - Gasoline Dispensing Facilities (11/6/02) |  |  |
| 8-7-113 | Tank Gauging and Inspection Exemption | Y |  |
| 8-7-301 | Phase I Requirements | Y |  |
| 8-7-301.1 | Requirement for CARB Phase I System | Y |  |
| 8-7-301.2 | Installation of Phase I Equipment per CARB Requirements | Y |  |
| 8-7-301.3 | Submerged Fill Pipes | Y |  |
| 8-7-301.5 | Maintenance of Phase I Equipment per Manufacturers Guidelines or CARB Executive Order | Y |  |
| 8-7-301.6 | Leak-Free, Vapor-Tight | Y |  |
| 8-7-301.7 | Poppetted Drybreaks | Y |  |
| 8-7-301.8 | No Coaxial Phase 1 Systems on New and Modified Tanks | Y |  |
| 8-7-301.9 | CARB-Certified Anti-Rotational Coupler or Swivel Adapter | Y |  |
| 8-7-301.10 | System Vapor Recovery Rate | Y |  |
| 8-7-301.11 | CARB-Certified Spill Box | Y |  |
| 8-7-301.12 | Drain Valve Permanently Plugged | Y |  |
| 8-7-301.13 | Annual Phase I testing | Y |  |
| 8-7-302 | Phase II Requirements | Y |  |
| 8-7-302.1 | Requirement for CARB Certified Phase II System | Y |  |
| 8-7-302.2 | Maintenance of Phase II System per CARB Requirements | Y |  |
| 8-7-302.3 | Maintenance of All Equipment as Specified by Manufacturer | Y |  |
| 8-7-302.4 | Repair of Defective Parts Within 7 Days | Y |  |
| 8-7-302.5 | Leak-Free, Vapor-Tight | Y |  |
| 8-7-302.6 | Insertion Interlocks | Y |  |
| 8-7-302.7 | Built-In Vapor Check Valve | Y |  |
| 8-7-302.8 | Minimum Liquid Removal Rate | Y |  |
| 8-7-302.9 | Coaxial Hose | Y |  |
| 8-7-302.10 | Galvanized Piping or Flexible Tubing | Y |  |
| 8-7-302.12 | Liquid Retainment Limit | Y |  |
| 8-7-302.13 | Spitting Limit | YN |  |
| 8-7-302.14 | Annual balance Phase II backpressure test | Y |  |
| 8-7-302.15 | Annual vacuum assist Phase II test | N |  |
| 8-7-303 | Topping Off | Y |  |
| 8-7-304 | Certification Requirements | Y |  |
| 8-7-306 | Prohibition of Use | Y |  |
| 8-7-307 | Posting of Operating Instructions | Y |  |
| 8-7-308 | Operating Practices | Y |  |
| 8-7-309 | Contingent Vapor Recovery Requirements | Y |  |
| 8-7-313 | Requirements for New or Modified Phase II Installations | Y |  |
| 8-7-315 | Pressure Vacuum Valve Requirement, Underground Storage Tank | Y |  |
| 8-7-401 | Permit Requirements, New and Modified Installations | Y |  |
| 8-7-406 | Testing Requirements, New and Modified Installations | Y |  |
| 8-7-407 | Periodic Testing | Y |  |
| 8-7-408 | Periodic Testing Notification | Y |  |
| 8-7-501 | Burden of Proof | Y |  |
| 8-7-502 | Right of Access | Y |  |
| 8-7-503 | Record Keeping Requirements | Y |  |
| 8-7-503.1 | Gasoline Dispensed Records | Y |  |
| 8-7-503.2 | Dispensing Facility Maintenance Records | Y |  |
| 8-7-503.3 | Dispensing Records Retention | Y |  |
| BAAQMD Condition 7523 | Gasoline throughput shall not exceed 400,000 gallons in any consecutive 12-month period. [Basis: Toxic Risk Policy] | N |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-294 [Basis: 2-1-234.3] | Y |  |
| BAAQMD Condition 18680 |  |  |  |
| Part 1 | Operation and maintenance standards for vapor recovery system (CARB Executive Order VR-101) | N |  |
| Part 2 | 36-month testing requirement | N |  |

| Table IV - L Source-specific Applicable Requirements S-296 – C-1 Flare S-398 – MP-30 Flare |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| District Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann Number 1 Limitation | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 12-11 | Flare Monitoring at Petroleum Refineries (06/04/03) |  |  |
| 12-11-401 | Flare Data Reporting Requirements | N |  |
| 12-11-402 | Flow Verification Report | N | 6/4/04 |
| 12-11-501 | Vent Gas Flow Monitoring | N | 12/4/04 |
| 12-11-502 | Vent Gas Composition Monitoring | N |  |
| 12-11-502.3 | Vent Gas Composition Monitoring | N | 03/4/04 |
| 12-11-503 | Pilot Monitoring | N |  |
| 12-11-504 | Pilot and Purge Gas Monitoring | N |  |
| 12-11-505 | Recordkeeping Requirements | N |  |
| 12-11-506 | General Monitoring Requirements | N |  |
| 12-11-506.1 | Periods of Inoperation of Vent Gas Monitoring | N | 09/4/04 |
| 12-11-507 | Video Monitoring | N |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) [S-398 ONLY] |  |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | Exempt from fuel gas H2S limit | Y |  |
| BAAQMD Condition 18255 |  |  |  |
| Part 1 | Flaring rate limit [Basis: Regs 8-1-110.3, 2-1-403] | Y | 6/1/04 |
| Part 2 | Hourly flare rate recordkeeping durinf flaring events [Basis: Regs 8-1-110.3, 2-6-409.2, 2-6-501] | Y | 6/1/04 |
| Part 3 | Flaring event definition [Basis: Reg 2-6-409.2] | Y | 6/1/04 |
| Part 4 | Flaring event inspection procedure [Basis: Regs 8-1-110.3, 2-6-409.2, 2-6-501] | Y | 6/1/04 |
| Part 5 | Flaring event compliance criteria [Basis: Regs 8-1-110.3, 2-6-409.2, 2-6-501] | Y | 6/1/04 |
| Part 6 | Flaring event records [Basis: Regs 8-1-110.3, 2-6-409.2, 2-6-501] | Y | 6/1/04 |
| Part 7 | Limitation on type of flare gas processed at S-398 [Basis: Regs 8-1-110.3, 2-6-409.2, 2-6-501] | Y | 6/1/04 |

| Table IV - M Source-specific Applicable Requirements S-300 – U-200 Delayed Coker |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 10 | Organic Compound – Process Vessel Depressurization (7/20/83) |  |  |
| 8-10-301 | Process Vessel Depressurizing. POC emissions shall be vented through a knock-out pot and then abated in one of the following ways, to as low a vessel pressure as possible, but at least until pressure is reduced to less than 1000 mm Hg: | Y |  |
| 8-10-301.1 | recovery to the fuel gas system | Y |  |
| 8-10-301.2 | combustion at a firebox or incinerator | Y |  |
| 8-10-301.3 | combustion at a flare | Y |  |
| 8-10-301.4 | containment such that emissions to atmosphere do not occur | Y |  |
| 8-10-401 | Turnaround Records. The following records shall be kept for each process unit turnaround, and retained for at least 2 years and made available to the District on demand during inspections: | Y |  |
| 8-10-401.1 | date of depressurization event | Y |  |
| 8-10-401.2 | approximate vessel hydrocarbon concentration when emissions to atmosphere begin | Y |  |
| 8-10-401.3 | approximate quantity of POC emissions to atmosphere | Y |  |
| BAAQMD Condition 21092 |  |  |  |
| Part 1 | Throughput limit [Basis: Cumulative Increase] | Y |  |
| Part 2 | Recordkeeping requirements [Basis: Cumulative Increase] | Y |  |
| Part 3 | Reporting requirement [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 21099 |  |  |  |
| Part 1 | Light hydrocarbon control valve requirements [Basis: BACT] | Y | completion of A/C 5814 modifications |
| Part 2 | Light hydrocarbon flange/connector requirements [Basis: BACT] | Y | completion of A/C 5814 modifications |
| Part 3 | Centrifugal compressor requirements [Basis: BACT] | Y | completion of A/C 5814 modifications |
| Part 4 | Light hydrocarbon centrifugal pump requirements [Basis: BACT] | Y | completion of A/C 5814 modifications |
| Part 5 | Monitoring and repair program requirement [Basis: BACT] | Y | completion of A/C 5814 modifications |
| Part 6 | ULSD project component count report requirement [Basis: BACT, Cumulative Increase, Toxic Management Policy] | Y | completion of A/C 5814 modifications |

| Table IV – N Source-specific Applicable Requirements – Process Vessels S-304 – U-229 Mid-Barrel Unionfining Unit (U-229 Light Naphtha Hydrotreater when modified in accordance with A/C 5814) S-305 – U-230 Prefractionator / Naphtha Hydrotreater S-306 – U-231 Platforming Unit S-307 – U-240 Unicracking Unit S-308 – U-244 Reforming Unit S-309 – U-248 Unisar Unit S-318 – U-76 Gasoline / Mid-Barrel Blending Unit S-319 – U-215 Gasoline Fractionating Unit S-322 – U-40 Raw materials Receiving S-435 – Reformate Splitter S-436 – Deisopentanizer S-437 – Hydrogen Plant S-460 – U-250 ULSD Hydrotreater |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 2 | Organic Compound – Miscellaneous Operations (6/15/94) APPLICABLE TO S-307 ONLY |  |  |
| 8-2-301 | Miscellaneous Operations: emissions shall not exceed 15 lb/day and 300 ppm carbon on a dry basis | Y |  |
| BAAQMD Regulation 8, Rule 9 | Organic Compound – Vacuum Producing Systems (7/20/83) |  |  |
| 8-9-301 | Vacuum Producing System POC emissions must be controlled by combustion or venting to fuel gas systems | Y |  |
| 8-9-601 | Determination of Emissions | Y |  |
| BAAQMD Regulation 8, Rule 10 | Organic Compound – Process Vessel Depressurization (7/20/83) |  |  |
| 8-10-301 | Process Vessel Depressurizing. POC emissions shall be vented through a knock-out pot and then abated in one of the following ways, to as low a vessel pressure as possible, but at least until pressure is reduced to less than 1000 mm Hg: | Y |  |
| 8-10-301.1 | recovery to the fuel gas system | Y |  |
| 8-10-301.2 | combustion at a firebox or incinerator | Y |  |
| 8-10-301.3 | combustion at a flare | Y |  |
| 8-10-301.4 | containment such that emissions to atmosphere do not occur | Y |  |
| 8-10-401 | Turnaround Records. The following records shall be kept for each process unit turnaround, and retained for at least 2 years and made available to the District on demand during inspections: | Y |  |
| 8-10-401.1 | date of depressurization event | Y |  |
| 8-10-401.2 | approximate vessel hydrocarbon concentration when emissions to atmosphere begin | Y |  |
| 8-10-401.3 | approximate quantity of POC emissions to atmosphere | Y |  |
| BAAQMD Condition 21095 | APPLICABLE TO S-304 ONLY |  |  |
| Part 1 | Daily throughput limit [Basis: 2-1-234] | Y | when modified in accordance with A/C 5814 |
| Part 2 | Daily throughput records [Basis: 2-1-234] | Y | when modified in accordance with A/C 5814 |
| BAAQMD Condition 6671 | APPLICABLE TO S-307 ONLY |  |  |
| Part 1 | Abatement requirement for E-421 condenser vent at A-50 scrubber [Basis: Regulation 8-2-301] | Y |  |
| Part 2 | Efficiency requirement for A-50 scrubber raw material throughput [Basis: Regulation 8-2-301] | Y |  |
| Part 3 | Requirement to treat A-50 blowdown at wastewater treatment plant [Basis: Cumulative Increase] | Y |  |
| Part 4 | Daily A-50 monitoring requirement [Basis: Cumulative Increase] | Y |  |
| Part 5 | Monitoring record requirement [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20620 | APPLICABLE TO S-307 AND S-308 ONLY |  |  |
| Part 1 | Application requirement for 40 CFR63, Subpart UUU | Y | 10/11/04 |
| Part 2 | Submittal requirement for Operation, Maintenance, and Monitoring Plan | Y | 4/11/05 |
| BAAQMD Condition 21094 | APPLICABLE TO S-460 ONLY |  |  |
| Part 1 | Daily throughput limit [Basis: Regulation 2-1-234] | Y | startup date |
| Part 2 | Throughput records [Basis: Regulation 2-1-234] | Y | startup date |
| BAAQMD Condition 21099 | APPLICABLE TO S-304, S-460 ONLY |  |  |
| Part 1 | Light hydrocarbon control valve requirements [Basis: BACT] | Y | startup/modification date |
| Part 2 | Light hydrocarbon flange/connector requirements [Basis: BACT] | Y | startup/modification date |
| Part 3 | Centrifugal compressor requirements [Basis: BACT] | Y | startup/modification date |
| Part 4 | Light hydrocarbon centrifugal pump requirements [Basis: BACT] | Y | startup/modification date |
| Part 5 | Monitoring and repair program requirement [Basis: BACT] | Y | startup/modification date |
| Part 6 | ULSD project component count report requirement [Basis: BACT, Cumulative Increase, Toxic Management Policy] | Y | startup/modification date |
| 40 CFR 63 Subpart UUU | National Emission Standards for Hazardous Pollutants for Petroleum Refineries: Catalytic Cracking Units, Catalytic Reforming Units, and Sulfur Recovery Units (4/11/02) [APPLICABLE TO S-307 AND S-308 ONLY] | Y | Notification by 8/9/02; compliance by 4/11/05 |
| BAAQMD Condition 20989, Part A | Throughput limits for S-304, S-305, S-306, S-307, S-435, S-436, S-437, 460 (S-304 only until modified in accordance with A/C 5814) [Basis: 2-1-234.3] | Y | for S-460, upon startup |
| BAAQMD Condition 20989, Part A | Throughput limits for S-308, S-309, S-318, S-319 [Basis: 2-1-234.3] | N |  |

| Table IV - O Source-specific Applicable Requirements S-350 – U-267 Crude Distillation Unit |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 9 | Organic Compound – Vacuum Producing Systems (7/20/83) |  |  |
| 8-9-301 | Vacuum Producing System POC emissions must be controlled by combustion or venting to fuel gas systems | Y |  |
| 8-9-601 | Determination of Emissions | Y |  |
| BAAQMD Regulation 8, Rule 10 | Organic Compound – Process Vessel Depressurization (7/20/83) |  |  |
| 8-10-301 | Process Vessel Depressurizing. POC emissions shall be vented through a knock-out pot and then abated in one of the following ways, to as low a vessel pressure as possible, but at least until pressure is reduced to less than 1000 mm Hg: | Y |  |
| 8-10-301.1 | recovery to the fuel gas system | Y |  |
| 8-10-301.2 | combustion at a firebox or incinerator | Y |  |
| 8-10-301.3 | combustion at a flare | Y |  |
| 8-10-301.4 | containment such that emissions to atmosphere do not occur | Y |  |
| 8-10-401 | Turnaround Records. The following records shall be kept for each process unit turnaround, and retained for at least 2 years and made available to the District on demand during inspections: | Y |  |
| 8-10-401.1 | date of depressurization event | Y |  |
| 8-10-401.2 | approximate vessel hydrocarbon concentration when emissions to atmosphere begin | Y |  |
| 8-10-401.3 | approximate quantity of POC emissions to atmosphere | Y |  |
| BAAQMD Condition 383 | (until modified in accordance with A/C 5814, then subject to condition 21092) |  |  |
| Part 1a | Sulfur content limit in crude [Basis: Cumulative Increase] | Y |  |
| Part 1b | Crude analysis requirement [Basis: Cumulative Increase] | Y | 4/1/04 |
| Part 2 | Daily, average daily crude feed limits [Basis: Cumulative Increase] | Y |  |
| Part 3a | Monthly recordkeeping requirements [Basis: Cumulative Increase] | Y |  |
| Part 3b | Records of sulfur content of crude feed [Basis: Cumulative Increase] | Y | 4/1/04 |
| BAAQMD Condition 21093 |  |  |  |
| Part 1a | Sulfur content limit in crude [Basis: Cumulative Increase] | Y | modification date |
| Part 1b | Crude analysis requirement [Basis: Cumulative Increase] | Y | modification date |
| Part 2 | Daily, average daily crude feed limits [Basis: Cumulative Increase] | Y | modification date |
| Part 3 | Monthly recordkeeping requirements [Basis: Cumulative Increase] | Y | modification date |
| BAAQMD Condition 21099 |  |  |  |
| Part 1 | Light hydrocarbon control valve requirements [Basis: BACT] | Y | modification date |
| Part 2 | Light hydrocarbon flange/connector requirements [Basis: BACT] | Y | modification date |
| Part 3 | Centrifugal compressor requirements [Basis: BACT] | Y | modification date |
| Part 4 | Light hydrocarbon centrifugal pump requirements [Basis: BACT] | Y | modification date |
| Part 5 | Monitoring and repair program requirement [Basis: BACT] | Y | modification date |
| Part 6 | ULSD project component count report requirement [Basis: BACT, Cumulative Increase, Toxic Management Policy] | Y | modification date |

| Table IV - P Source-specific Applicable Requirements S-432 – U-215 Deisobutanizer |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 10 | Organic Compound – Process Vessel Depressurization (7/20/83) |  |  |
| 8-10-301 | Process Vessel Depressurizing. POC emissions shall be vented through a knock-out pot and then abated in one of the following ways, to as low a vessel pressure as possible, but at least until pressure is reduced to less than 1000 mm Hg: | Y |  |
| 8-10-301.1 | recovery to the fuel gas system | Y |  |
| 8-10-301.2 | combustion at a firebox or incinerator | Y |  |
| 8-10-301.3 | combustion at a flare | Y |  |
| 8-10-301.4 | containment such that emissions to atmosphere do not occur | Y |  |
| 8-10-401 | Turnaround Records. The following records shall be kept for each process unit turnaround, and retained for at least 2 years and made available to the District on demand during inspections: | Y |  |
| 8-10-401.1 | date of depressurization event | Y |  |
| 8-10-401.2 | approximate vessel hydrocarbon concentration when emissions to atmosphere begin | Y |  |
| 8-10-401.3 | approximate quantity of POC emissions to atmosphere | Y |  |
| BAAQMD Condition 6725 |  |  |  |
| Part 1 | Flange, valve design requirements [Basis: Cumulative Increase] | Y |  |
| Part 2 | Vent collection requirement for relief valves [Basis: Cumulative Increase] | Y |  |
| Part 3 | Pump, compressor design requirements [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-432 [Basis: 2-1-234.3] | Y |  |

| Table IV – Q.1 Source-specific Applicable Requirements S-352 - Combustion Turbine S-353 - Combustion Turbine S-354 - Combustion Turbine |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-520 | Continuous Emission Monitoring | Y |  |
| 1-520.8 | Monitors pursuant to Regulation 2-1-403 | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 2, Rule 1 | Regulation 2, Rule 1 - Permits, General Requirements (8/1/01) |  |  |
| 2-1-403 | Permit conditions-measurement of emissions | N |  |
| 2-1-501 | Monitors | Y |  |
| SIP Regulation 2, Rule 1 | PROVISIONS NO LONGER IN CURRENT RULE Permits, General Requirements (1/26/99 {adopted 11/01/89}) |  |  |
| 2-1-403 | Permit conditions-measurement of emissions | Y-note 1 |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 9 | Inorganic Gaseous Pollutants - Nitrogen Oxides from Stationary Gas Turbines (9/21/94) |  |  |
| 9-9-113 | Exemption - Inspection/Maintenance | Y |  |
| 9-9-114 | Exemption - Startup/Shutdown | Y |  |
| 9-9-301 | Emission Limits – General | Y |  |
| 9-9-301.3 | Emission Limits | Y |  |
| 9-9-401 | Efficiency Certification | Y |  |
| 9-9-501 | Continuous Emission Monitoring (CEM) | Y |  |
| 9-9-600 | Manual of Procedures | Y |  |
| 9-9-601 | NOx emissions: Manual of Procedures, Vol. IV, ST-13A or B | Y |  |
| 9-9-602 | Oxygen emissions: Manual of Procedures, Vol. IV, ST-14 | Y |  |
| 9-9-603 | CEM: Manual of Procedures, Volume V | Y |  |
| 9-9-604 | Determination of HHV and LHV | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (10/2/90) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Subpart GG | Standards of Performance for Stationary Gas Turbines (1/27/82) |  |  |
| 60.330 | Applicability | Y |  |
| 60.332(a)(2) | Alternate Standard, NOx (except when ice fog deemed a traffic hazard per 60.332(f) | Y |  |
| 60.332(d) | Compliance with 60.332(a)(2) required | Y |  |
| 60.332(f) | Exemption from 60.332(a)(2) when steam injection would result in ice fog which is deemed a traffic hazard | Y |  |
| 60.332(k) | Exemption: Natural gas turbines >10 MMBTU/hr when firing emergency fuel | Y |  |
| 60.333 | Performance Standards, SO2 | Y |  |
| 60.333(b) | Fuel Sulfur Limit (in lieu of SO2 concentration emission limit – 150 ppmv @ 15% O2 - in 60.333(a)) | Y |  |
| 60.334 | Monitoring Requirements | Y |  |
| 60.334(b) | Fuel Sulfur Content | Y |  |
| 60.334(c)(2) | Excess Emissions – SO2 | Y |  |
| 60.335 | Test Methods and Procedures | Y |  |
| BAAQMD Condition 12122 |  |  |  |
| Part 1 | Restriction to natural gas and refinery fuel gas [Basis: Cumulative Increase] | Y |  |
| Part 2 | Restriction on duct burner operation to times when associated turbine is also operated [Basis: BACT, Cumulative Increase] | Y |  |
| Part 3 | Abatement requirement for S-352 and S-355 at A-13 [Basis: BACT, Cumulative Increase] | Y |  |
| Part 4 | Abatement requirement for S-353 and S-356 at A-14 [Basis: BACT, Cumulative Increase] | Y |  |
| Part 5 | Abatement requirement for S-354 and S-357 at A-15 [Basis: BACT, Cumulative Increase] | Y |  |
| Part 7 | CO exhaust concentration limit [Basis: BACT, Cumulative Increase] | Y |  |
| Part 8 | POC exhaust concentration limit [Basis: BACT, Cumulative Increase] | Y |  |
| Part 9a | NOx hourly, daily and annual emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part 9b | NOx CEM requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part 10a | CO annual emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part 10b | CO CEM requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part 11 | POC hourly and annual emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part 12 | Refinery fuel gas testing requirement for total reduced sulfur [Basis: Cumulative Increase] | Y |  |
| Part 13 | Reporting requirement for refinery fuel gas total reduced sulfur measurements [Basis: Cumulative Increase] | Y |  |
| Part 14 | Annual POC source test [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |
| Part 15 | Recordkeeping requirement [Basis: BACT, Cumulative Increase] | Y |  |
| BAAQMD Condition 18629 | PSD Approval to Construct / Modify issued 3/3/86, modified 5/26/89. The basis for each section is PSD. |  |  |
| Part III | Facilities Operation | Y |  |
| Part IV | Malfunction | Y |  |
| Part V | Right to Entry | Y |  |
| Part V.A | entry to premises | Y |  |
| Part V.B | access to records | Y |  |
| Part V.C | right to inspection of equipment and operations | Y |  |
| Part V.D | right to sample emissions | Y |  |
| Part VI | Transfer of Ownership | Y |  |
| Part VII | Severability | Y |  |
| Part VIII | Other Applicable Regulations | Y |  |
| Part IX | Special Conditions | Y |  |
| Part IX.B | Air Pollution Control Equipment | Y |  |
| Part IX.B.1 | Requirement for steam injection | Y |  |
| Part IX.B.2 | Requirement for SCR | Y |  |
| Part IX.D.1 | restriction to refinery fuel gas and natural gas | Y |  |
| Part IX.D.2 | 466 MM BTU/hr firing rate limit for each of 3 turbine/duct burner sets | Y |  |
| Part IX.D.3 | 1048 MM BTU/hr total firing rate limit | Y |  |
| Part IX.D.4 | fuel usage and related records | Y |  |
| Part IX.E | Emission Limits for NOx | Y |  |
| Part IX.F | Emission Limits for SO2 | Y |  |
| Part IX.G | Continuous Emission Monitoring | Y |  |
| Part IX.G.1.a | Requirement for NOx CEM and fuel gas H2S sampling | Y |  |
| Part IX.G.1.b | parametric monitoring of stack flowrates | Y |  |
| Part IX.G.2 | Requirement to maintain records (2 years) | Y |  |
| Part IX.G.3 | quarterly report of SO2 emissions and excess emissions | Y |  |
| Part IX.G.3.a.(1) | total sulfur concentration in each fuel gas sample | Y |  |
| Part IX.G.3.a.(2) | daily average sulfur content in fuel gas, daily average SO2 mass emission rate, total ton/yr of SO2 | Y |  |
| Part IX.G.3.b | excess SO2 emissions | Y |  |
| Part IX.G.3.c | excess SO2 emissions during startups, shutdowns and malfunctions | Y |  |
| Part IX.G.3.d | time and date of CEM failures | Y |  |
| Part IX.G.3.e | affirmative statement of CEM operation when no failures occur | Y |  |
| Part IX.G.3.f | definition of excess SO2 emissions | Y |  |
| Part IX.G.3.g | excess SO2 emissions indicated by CEM is a violation | Y |  |
| Part IX.H | New Source Performance Standards (Subparts A and GG) | Y |  |
| Part X | Agency Notifications | Y |  |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – Q.2 Source-specific Applicable Requirements S-355 – Supplemental Duct Burners for S-352 S-356 – Supplemental Duct Burners for S-353 S-357 – Supplemental Duct Burners for S-354 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) |  |  |
| 1-107 | Combination of Emissions | Y |  |
| 1-520 | Continuous Emission Monitoring | Y |  |
| 1-520.8 | Monitors pursuant to Regulation 2-1-403 | Y |  |
| 1-521 | Monitoring May Be Required | Y |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | N |  |
| 1-522.4 | reporting of inoperative CEMs | Y |  |
| 1-522.5 | CEM calibration requirements | Y |  |
| 1-522.6 | CEM accuracy requirements | Y |  |
| 1-522.7 | emission limit exceedance reporting requirements | N |  |
| 1-522.8 | monitoring data submittal requirements | Y |  |
| 1-522.9 | recordkeeping requirements | Y |  |
| 1-522.10 | Regulation 1-521 monitors shall meet requirements specified by District | Y |  |
| 1-602 | Area and Continuous Monitoring Requirements | N |  |
| SIP Regulation 1 | PROVISIONS NO LONGER IN CURRENT RULE General Provisions and Definitions (6/28/99) |  |  |
| 1-522 | Continuous Emission Monitoring and Recordkeeping Procedures | Y – note 1 |  |
| 1-522.7 | emission limit exceedance reporting requirements | Y - note 1 |  |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| BAAQMD Regulation 2, Rule 1 | Regulation 2, Rule 1 - Permits, General Requirements (8/1/01) |  |  |
| 2-1-403 | Permit conditions-measurement of emissions | N |  |
| 2-1-501 | Monitors | Y |  |
| SIP Regulation 2, Rule 1 | PROVISIONS NO LONGER IN CURRENT RULE Permits, General Requirements (1/26/99 {adopted 11/01/89}) |  |  |
| 2-1-403 | Permit conditions-measurement of emissions | Y-note 1 |  |
| BAAQMD Manual of Procedures, Volume V | Continuous Emission Monitoring Policy and Procedures (1/20/82) | N |  |
| BAAQMD Regulation 9, Rule 10 | Inorganic Gaseous Pollutants - Nitrogen Oxides and Carbon Monoxide from Boilers, Steam Generators, and Process Heaters in Petroleum Refineries (7/17/02) |  |  |
| 9-10-110.3 | Exemption: Waste heat recovery boilers associated with gas turbines | Y |  |
| NSPS 40 CFR 60 Subpart Db | Standards of Performance for Industrial-Commercial-Institutional Steam Generating Units (3/13/00) |  |  |
| 60.40b(a) | Applicability | Y |  |
| 60.40b(c) | Affected facilities subject to Subpart J are subject to PM and NOx standards in Subpart Db and SO2 standards in Subpart J | Y |  |
| 60.40b(f) | Modification for the sole purpose of combusting gases containing TRS is not a modification | Y |  |
| 60.40b(j) | Units subject to Subpart Db are not subject to Subpart D | Y |  |
| 60.44b(a) | NOx Standard | Y |  |
| 60.44b(a)(4)(i) | NOx standard for duct burner used in combined cycle system for natural gas-firing only conditions | Y |  |
| 60.44b(e) | NOx standard for refinery-produced byproduct (i.e., fuel gas) with oil or natural gas combustion. | Y |  |
| 60.44b(f) | NOx standard for refinery-produced byproduct with oil or natural gas combustion may be determined on a case-by-case basis (based on 25 ppmv NOx standard for PSD Permit Condition 18629, Part IX.E). | Y |  |
| 60.44b(h) | NOx standard applicable at all times | Y |  |
| 60.44b(i) | 30-day rolling average | Y |  |
| 60.46b | Compliance/Performance test Methods for NOx | Y |  |
| 60.46b(b) | NOx standard applicable at all times |  |  |
| 60.48b | Emission Monitoring for NOx |  |  |
| 60.48b(b)(1) | Install, calibrate, and operate CEM and record output for measuring NOx discharges | Y |  |
| 60.48b(c) | Record data during all periods of operation of CEM except during breakdown and repairs | Y |  |
| 60.48b(d) | Continuous NOx monitors measure 1-hr average emission rates | Y |  |
| 60.48b(e) | Complies with 60.13 | Y |  |
| 60.48b(e)(2) | Span values for NOx | Y |  |
| 60.48b(e)(3) | Span values for NOx rounded to nearest 500 ppm | Y |  |
| 60.48b(f) | Standby monitoring system and test methods | Y |  |
| 60.48b(g) | NOx CEM requirements for units with 250 MM BTU/hr heat input capacity or less | Y |  |
| 60.48b(g)(1) | NOx CEM requirements for units with 250 MM BTU/hr heat input capacity or less | Y |  |
| 60.48b(h) | NOx CEM not required if subject to §60.44b(a)(4) for natural gas firing-only conditions | Y |  |
| 60.49b | Reporting and Recordkeeping | Y |  |
| 60.49b(d) | Record amounts of each fuel combusted/day and calculate annual capacity factors at a 12-month rolling average | Y |  |
| 60.49b(g) | Recordkeeping – NOx data | Y |  |
| 60.49b(h) | Excess emission reports | Y |  |
| 60.49b(h)(2)(i) | Combusts natural gas, distillate oil, or residual oil with nitrogen content of 0.3 weight percent or less – for natural gas firing-only conditions | Y |  |
| 60.49b(h)(2)(ii) | Heat input capacity of affected units is 250 MM BTU/hr or less and NOx CEM is required under 60.48b(g)(1) | Y |  |
| 60.49b(h)(4) | Excess emission definition | Y |  |
| 60.49b(i) | Reports of 60.49b(g) data | Y |  |
| 60.49b(o) | Records retained for 2 years | Y |  |
| 60.49b(v) | Electronic quarterly reports | Y |  |
| 60.49b(w) | Semi-annual reports | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (10/2/90) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| BAAQMD Condition 12122 |  |  |  |
| Part 1 | Restriction to natural gas and refinery fuel gas [Basis: Cumulative Increase] | Y |  |
| Part 2 | Restriction on duct burner operation to times when associated turbine is also operated [Basis: BACT, Cumulative Increase] | Y |  |
| Part 3 | Abatement requirement for S-352 and S-355 at A-13 [Basis: BACT, Cumulative Increase] | Y |  |
| Part 4 | Abatement requirement for S-353 and S-356 at A-14 [Basis: BACT, Cumulative Increase] | Y |  |
| Part 5 | Abatement requirement for S-354 and S-357 at A-15 [Basis: BACT, Cumulative Increase] | Y |  |
| Part 6 | Duct burner annual firing limit [Basis: Cumulative Increase] | Y |  |
| Part 7 | CO exhaust concentration limit [Basis: BACT, Cumulative Increase] | Y |  |
| Part 8 | POC exhaust concentration limit [Basis: BACT, Cumulative Increase] | Y |  |
| Part 9a | NOx hourly, daily and annual emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part 9b | NOx CEM requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part 10a | CO annual emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part 10b | CO CEM requirement [Basis: BACT, Cumulative Increase] | Y |  |
| Part 11 | POC hourly and annual emission limits [Basis: BACT, Cumulative Increase] | Y |  |
| Part 12 | Refinery fuel gas testing requirement for total reduced sulfur [Basis: Cumulative Increase] | Y |  |
| Part 13 | Reporting requirement for refinery fuel gas total reduced sulfur measurements [Basis: Cumulative Increase] | Y |  |
| Part 14 | Annual POC source test [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |
| Part 15 | Recordkeeping requirement [Basis: BACT, Cumulative Increase] | Y |  |
| BAAQMD Condition 18629 | PSD Approval to Construct / Modify issued 3/3/86, modified 5/26/89. The basis for each section is PSD. |  |  |
| Part III | Facilities Operation | Y |  |
| Part IV | Malfunction | Y |  |
| Part V | Right to Entry | Y |  |
| Part V.A | entry to premises | Y |  |
| Part V.B | access to records | Y |  |
| Part V.C | right to inspection of equipment and operations | Y |  |
| Part V.D | right to sample emissions | Y |  |
| Part VI | Transfer of Ownership | Y |  |
| Part VII | Severability | Y |  |
| Part VIII | Other Applicable Regulations | Y |  |
| Part IX | Special Conditions | Y |  |
| Part IX.B | Air Pollution Control Equipment | Y |  |
| Part IX.B.1 | Requirement for steam injection | Y |  |
| Part IX.B.2 | Requirement for SCR | Y |  |
| Part IX.D.1 | restriction to refinery fuel gas and natural gas | Y |  |
| Part IX.D.2 | 466 MM BTU/hr firing rate limit for each of 3 turbine/duct burner sets | Y |  |
| Part IX.D.3 | 1048 MM BTU/hr total firing rate limit | Y |  |
| Part IX.D.4 | fuel usage and related records | Y |  |
| Part IX.E | Emission Limits for NOx | Y |  |
| Part IX.F | Emission Limits for SO2 | Y |  |
| Part IX.G | Continuous Emission Monitoring | Y |  |
| Part IX.G.1.a | Requirement for NOx CEM and fuel gas H2S sampling | Y |  |
| Part IX.G.1.b | parametric monitoring of stack flowrates | Y |  |
| Part IX.G.2 | Requirement to maintain records (2 years) | Y |  |
| Part IX.G.3 | quarterly report of SO2 emissions and excess emissions | Y |  |
| Part IX.G.3.a.(1) | total sulfur concentration in each fuel gas sample | Y |  |
| Part IX.G.3.a.(2) | daily average sulfur content in fuel gas, daily average SO2 mass emission rate, total ton/yr of SO2 | Y |  |
| Part IX.G.3.b | excess SO2 emissions | Y |  |
| Part IX.G.3.c | excess SO2 emissions during startups, shutdowns and malfunctions | Y |  |
| Part IX.G.3.d | time and date of CEM failures | Y |  |
| Part IX.G.3.e | affirmative statement of CEM operation when no failures occur | Y |  |
| Part IX.G.3.f | definition of excess SO2 emissions | Y |  |
| Part IX.G.3.g | excess SO2 emissions indicated by CEM is a violation | Y |  |
| Part IX.H | New Source Performance Standards (Subparts A and GG) | Y |  |
| Part X | Agency Notifications | Y |  |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV - R Source-specific Applicable Requirements S-376 - Tool Room Cold Cleaner S-377 – Machine Shop Cold Cleaner S-378 – Auto Shop Cold Cleaner |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 16 | Organic Compounds – Solvent Cleaning Operations (10/16/02) |  |  |
| 8-16-201 | Definitions | Y |  |
| 8-16-303 | Cold Cleaner Requirements | N |  |
| 8-16-303.1 | General Operating Requirements | N |  |
| 8-16-303.3.1 | Operate and maintain in proper working order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | N |  |
| 8-16-303.1.6 | Solvent Spray Requirements | N |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements | Y |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | Solvent Agitation | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | N |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements | N |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | N |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | N |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | N |  |
| 8-16-303.5 | Cold Cleaner Requirements for Repair and Maintenance Cleaning | N |  |
| 8-16-303.5.2 | Cleaning solution shall be branched, cyclic, or linear completely methylated siloxane (VMS) | N |  |
| 8-16-501 | Solvent Records | N |  |
| 8-16-501.2 | Facility-wide Annual Solvent Usage Records | N |  |
| 8-16-501.3 | Annual Records of Type and Amount of Solvent Used for Wipe Cleaning | N |  |
| 8-16-501.5 | Records Retained for Previous 24 Month Period | N |  |
| SIP Regulation 8, Rule 16 | Organic Compounds – Solvent Cleaning Operations (6/15/94) |  |  |
| 8-16-303 | Cold Cleaner Requirements | Y – note 1 |  |
| 8-16-303.1 | General Operating Requirements | Y – note 1 |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y – note 1 |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y – note 1 |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y – note 1 |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y – note 1 |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements | Y – note 1 |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y – note 1 |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y – note 1 |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y – note 1 |  |
| 8-16-501 | Solvent Records | Y – note 1 |  |
| 8-16-501.2 | Facility-wide Quarterly Solvent Usage Records | Y – note 1 |  |
| BAAQMD Condition 16677 |  |  |  |
| Part 1 | Net usage of citrus-based solvent at S-376, S-377 and S-378 shall not exceed 150 gallons each in any consecutive 12-month period. [Basis: Cumulative Increase] | Y |  |
| Part 2 | Criteria for using solvents other than citrus-based solvents. [Basis: Cumulative Increase and Toxic Risk Screen] | Y |  |
| Part 3a, 3b, 3c | Recordkeeping requirements. [Basis: Cumulative Increase and Toxic Risk Screen] | Y |  |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV - S Source-specific Applicable Requirements S-425 – Marine Loading Berth M1 S-426 – Marine Loading Berth M2 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 44 | Organic Compounds-Marine Vessel Loading Terminals (1/4/89) | Y |  |
| 8-44-110 | Exemption: loading events | Y |  |
| 8-44-111 | Exemption: marine vessel fueling | Y |  |
| 8-44-301 | Marine Terminal Loading Limit | Y |  |
| 8-44-301.1 | Limited to 5.7 gram per cubic meter (2 lb per 1000 bbl) of organic liquid loaded, or | Y |  |
| 8-44-301.2 | POC emissions reduced 95% by weight from uncontrolled conditions | Y |  |
| 8-44-302 | Emission control equipment | Y |  |
| 8-44-303 | Operating practice | Y |  |
| 8-44-304 | Equipment Maintenance | Y |  |
| 8-44-304.1 | Certified leak free, gas tight and in good working order | Y |  |
| 8-44-304.2 | Loading ceases any time gas or liquid leaks are discovered | Y |  |
| 8-44-402 | Safety/Emergency Operations | Y |  |
| 8-44-402.1 | Rule does not require act/omission in violation of Coast Guard/other rules | Y |  |
| 8-44-402.2 | Rule does not prevent act/omission for vessel safety or saving life at sea | Y |  |
| 8-44-305 | Ozone excess day prohibition | Y |  |
| 8-44-501 | Record keeping | Y |  |
| 8-44-501.1 | Name and location | Y |  |
| 8-44-501.2 | Responsible company | Y |  |
| 8-44-501.3 | Dates and times | Y |  |
| 8-44-501.4 | Name, registry of the vessel loaded and legal owner | Y |  |
| 8-44-501.5 | Prior cargo carried | Y |  |
| 8-44-501.6 | Type, amount of liquid cargo loaded | Y |  |
| 8-44-501.7 | Condition of tanks | Y |  |
| 8-44-502 | Burden of proof | Y |  |
| NSPS 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |  |
| 60.100 | Applicability | Y |  |
| 60.104 | Standards for Sulfur Oxides: Compliance Schedule | Y |  |
| 60.104(a)(1) | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | Y |  |
| 60.105 | Monitoring of Emissions and Operations | Y |  |
| 60.105(a)(4) | monitoring requirement for H2S (dry basis) in fuel gas prior to combustion (in lieu of separate combustion device exhaust SO2 monitors as required by 60.105(a)(3)) | Y |  |
| 60.105(e)(3)(ii) | Excess H2S emission definitions for 60.7(c) | Y |  |
| 60.106(a) | Test methods and procedures | Y |  |
| 60.106(e)(1) | Method 11 shall be used to verify compliance with 60.104(a)(1) | Y |  |
| NSPS 40 CFR 60 Appendix A | Appendix A to Part 60 – Test Methods | Y |  |
| NSPS 40 CFR 60 Appendix B | Performance Specifications |  |  |
| Performance Specification 7 | H2S continuous emission monitoring systems | Y |  |
| 40 CFR 63 | National Emission Standards for Hazardous Air Pollutants for Source Categories | Y |  |
| NESHAPS Part 63 Subpart Y | National Emission Standards for Marine Tank Vessel Loading Operations |  |  |
| 63.560(a) | Maximum Achievable Control Technology (MACT) applicability | Y |  |
| 63.560(a)(2) | MACT does not apply to existing sources with emissions < 10 or 25 tons | Y |  |
| 63.560(a)(3) | Record keeping in 63.567(j)(4) and emission estimation in 63.565(l) apply to existing sources < 10 and 25 tons | Y |  |
| 63.565(l) | Emission estimation procedures | Y |  |
| 63.567(j)(4) | Retain records of emission estimates per 63.565(l), and actual throughputs, by commodity, for 5 years | Y |  |
| BAAQMD Condition 4336 |  |  |  |
| Part 1 | A-420 oxidizer temperature requirements [Basis: Cumulative Increase] | Y |  |
| Part 2 | monitoring requirements [Basis: Cumulative Increase] | Y |  |
| Part 3 | prohibition against loading without A-420 in service [Basis: Cumulative Increase] | Y |  |
| Part 4 | leak test requirement [Basis: Cumulative Increase] | Y |  |
| Part 5 | maximum loading pressure relative to relief valve setpoint [Basis: Cumulative Increase] | Y |  |
| Part 6 | throughput limit for regulated materials [Basis: Cumulative Increase] | Y |  |
| Part 7 | recordkeeping requirement [Basis: Cumulative Increase] |  |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-425, S-426 [Basis: 2-1-234.3] | Y |  |

| Table IV - T Source-specific Applicable Requirements S-450 – Groundwater Extraction Trenches |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Condition 12245 |  |  |  |
| Part 1 | Extracted water to be treated at wastewater treatment plant [Basis: Cumulative Increase] | Y |  |
| Part 2 | Covers required on all pump vaults and piping access boxes [Basis: Cumulative Increase] | Y |  |

| Table IV – U Source-specific Applicable Requirements S-1001 - Sulfur Plant Unit 234 , S-1002 - Sulfur Plant Unit 236 S-1003 - Sulfur Plant Unit 238, S-301 - Molten Sulfur Pit 234 S-302 - Molten Sulfur Pit 236 and S-303 - Molten Sulfur Pit 238 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann #1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310.3 | Particulate Weight Limitation | Y |  |
| 6-330 | Sulfur Recovery Units (SO3, H2SO4 emission limitations) | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 9, Rule 1 | Inorganic Gaseous Pollutants – Sulfur Dioxide (3/15/95) |  |  |
| 9-1-313 | Sulfur Removal Operations at Petroleum Refineries (processing more than 20,000 bbl/day of crude oil) |  |  |
| 9-1-313.2 | operation of a sulfur removal and recovery system that removes and recovers: 95% of H2S from refinery fuel gas, 95% of H2S and ammonia from process water streams (sulfur recovery is required when a facility removes 16.5 ton/day or more of elemental sulfur). | N |  |
| SIP Regulation 9, Rule 1 | Inorganic Gaseous Pollutants – Sulfur Dioxide (6/8/99) |  |  |
| 9-1-313.2 | operation of a sulfur removal and recovery system that removes and recovers: 95% of H2S from refinery fuel gas, 95% of H2S and ammonia from process water streams | Y – note 1 |  |
| 40 CFR 63 Subpart UUU | National Emission Standards for Hazardous Pollutants for Petroleum Refineries: Catalytic Cracking Units, Catalytic Reforming Units, and Sulfur Recovery Units (4/11/02) | Y | Notification by 8/9/02; compliance by 4/11/05 |
| BAAQMD Condition 19278 |  |  |  |
| Part 1 | Annual source test requirement to verify H2S and ammonia removal efficiency. [Basis: Regulation 9-1-313.2] | Y | 4/1/04 |
| Part 2 | H2S and ammonia source test reporting requirement. | Y | 4/1/04 |
| Part 3 | Annual source test to verify SO3 and H2SO4 exhaust concentrations. [Basis: Regulation 6-330] | Y | 4/1/04 |
| BAAQMD Condition 20620 |  |  |  |
| Part 1 | Application requirement for 40 CFR63, Subpart UUU | Y | 10/11/04 |
| Part 2 | Submittal requirement for Operation, Maintenance, and Monitoring Plan | Y | 4/11/05 |
| BAAQMD Condition 21099 | APPLICABLE TO S-1002, S-1003 ONLY |  |  |
| Part 1 | Light hydrocarbon control valve requirements [Basis: BACT] | Y | modification date |
| Part 2 | Light hydrocarbon flange/connector requirements [Basis: BACT] | Y | modification date |
| Part 3 | Centrifugal compressor requirements [Basis: BACT] | Y | modification date |
| Part 4 | Light hydrocarbon centrifugal pump requirements [Basis: BACT] | Y | modification date |
| Part 5 | Monitoring and repair program requirement [Basis: BACT] | Y | modification date |
| Part 6 | ULSD project component count report requirement [Basis: BACT, Cumulative Increase, Toxic Management Policy] | Y | modification date |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-1001, S-1002, S-1003, S-301, S-302, S-303 [Basis: 2-1-234.3] | N |  |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – V Source-specific Applicable Requirements S-370 – Isomerization Unit 228 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 10 | Organic Compound – Process Vessel Depressurization (7/20/83) |  |  |
| 8-10-301 | Process Vessel Depressurizing. POC emissions shall be vented through a knock-out pot and then abated in one of the following ways, to as low a vessel pressure as possible, but at least until pressure is reduced to less than 1000 mm Hg: | Y |  |
| 8-10-301.1 | recovery to the fuel gas system | Y |  |
| 8-10-301.2 | combustion at a firebox or incinerator | Y |  |
| 8-10-301.3 | combustion at a flare | Y |  |
| 8-10-301.4 | containment such that emissions to atmosphere do not occur | Y |  |
| 8-10-401 | Turnaround Records. The following records shall be kept for each process unit turnaround, and retained for at least 2 years and made available to the District on demand during inspections: | Y |  |
| 8-10-401.1 | date of depressurization event | Y |  |
| 8-10-401.2 | approximate vessel hydrocarbon concentration when emissions to atmosphere begin | Y |  |
| 8-10-401.3 | approximate quantity of POC emissions to atmosphere | Y |  |
| BAAQMD Condition 12121 |  |  |  |
| Part 1 | Daily feed rate limit [Basis: Cumulative Increase] | Y |  |
| Part 2 | Daily feed rate records [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for S-370 [Basis: 2-1-234.3] | Y |  |

| Table IV – W Source-specific Applicable Requirements S-380 – Activated Carbon Silo (P-204) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| District Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann Number 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations (process weight rate limitation) | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition 18251 |  |  |  |
| Part 1a | Abatement requirement [Basis: Regulation 2-1-234] | Y |  |
| Part 2a | Differential pressure monitor requirement [Basis: Regulation 1-441] | Y | 4/1/04 |
| Part 2b | Baghouse differential pressure monitoring requirement [Basis: Regulation 1-441] | Y | 4/1/04 |
| Part 3 | Differential pressure recordkeeping requirement [Basis: Regulation 1-441] | Y | 4/1/04 |
| BAAQMD Condition 20989, Part A | Throughput limits for S-380 [Basis: 2-1-234.3] | Y |  |

| Table IV – X Source-specific Applicable Requirements S-389 – Diatomaceous Earth Silo (F-214) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| District Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann Number 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations (process weight rate limitation) | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition 18251 |  |  |  |
| Part 1b | Abatement requirement [Basis: Regulation 2-1-234] | Y |  |
| Part 2a | Differential pressure monitor requirement [Basis: Regulation 1-441] | Y | 4/1/04 |
| Part 2c | Baghouse differential pressure monitoring requirement [Basis: Regulation 1-441] | Y | 4/1/04 |
| Part 3 | Differential pressure recordkeeping requirement [Basis: Regulation 1-441] | Y | 4/1/04 |
| BAAQMD Condition 20989, Part A | Throughput limits for S-389 [Basis: 2-1-234.3] | Y |  |

| Table IV – Y Source-specific Applicable Requirements S-462 – U-215 Fuel Gas Caustic Treatment System S-463 – U-215 Butane Caustic Treatment System |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Condition 20989, Part A | Throughput limits for S-462, S-463 [Basis: 2-1-234.3] | Y | startup date |
| BAAQMD Condition 21099 |  |  |  |
| Part 1 | Light hydrocarbon control valve requirements [Basis: BACT] | Y | startup date |
| Part 2 | Light hydrocarbon flange/connector requirements [Basis: BACT] | Y | startup date |
| Part 3 | Centrifugal compressor requirements [Basis: BACT] | Y | startup date |
| Part 4 | Light hydrocarbon centrifugal pump requirements [Basis: BACT] | Y | startup date |
| Part 5 | Monitoring and repair program requirement [Basis: BACT] | Y | startup date |
| Part 6 | ULSD project component count report requirement [Basis: BACT, Cumulative Increase, Toxic Management Policy] | Y | startup date |

| Table IV- AA Fugitive Sources: Applicable Requirements |
| --- |
| Process Unit | BAAQMD Reg. 8-18 | BAAQMD Reg. 8-28 | NSPS Part 60, Subpart GGG; BAAQMD Reg. 10-59 | NSPS Part 60, Subpart QQQ; BAAQMD Reg. 10-69 | NSPS Part 60, Subpart VV; BAAQMD Reg. 10-52 | NESHAP Part 61, Subpart J | NESHAP Part 61, Subpart FF; BAAQMD Reg. 11-12 | NESHAP Part 61, Subpart V; BAAQMD Reg. 11-7 | NESHAP Part 63, Subpart CC |
| Refinery-wide applicability | Y | Y | N | N | N | N | Report only | N | Y |
| Specific Unit applicability |  |  |  |  |  |  |  |  |  |
| Unit 267 (S-350) | Y | Y | Y | N | Y | N | N | N | Y |
| Unit 228 (S-370) | Y | Y | Y | N | Y | N | N | N | Y |
| Unit 110 (S-438) | Y | Y | Y | N | Y | N | N | N | Y |
| Unit 100 (S-324) | Y | Y | N | Y | N | N | N | N | Y |
| Unit 233 (S-338) | Y | Y | NA | NA | NA | NA | NA | NA | NA |

| Table IV – AB Applicable Requirements COMPONENTS (Facility-Wide Except as Noted) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8-18 | Organic Compounds-Equipment Leaks (11/27/02) |  |  |
| 8-18-100 | General/Applicability | Y |  |
| 8-18-200 | Definitions | Y |  |
| 8-18-301 | General Standard | Y |  |
| 8-18-302 | Valves | Y |  |
| 8-18-303 | Pumps and compressors | Y |  |
| 8-18-304 | Connections | Y |  |
| 8-18-305 | Pressure relief devices | Y |  |
| 8-18-306 | Non-repairable equipment | Y |  |
| 8-18-307 | Liquid Leaks | Y |  |
| 8-18-308 | Alternate compliance | Y |  |
| 8-18-401 | Inspection | Y |  |
| 8-18-402 | Identification | Y |  |
| 8-18-403 | Visual inspection schedule | Y |  |
| 8-18-404 | Alternate inspection schedule | Y |  |
| 8-18-405 | Alternate inspection reduction plan | N |  |
| 8-18-406 | Interim Compliance | N |  |
| 8-18-501 | Portable Hydrocarbon Detector | Y |  |
| 8-18-502 | Records | Y |  |
| SIP Regulation 8-18 | Organic Compounds-Equipment Leaks (10/10/01) |  |  |
| 8-18-405 | Alternate inspection reduction plan | Y-note 1 |  |
| 8-18-406 | Interim Compliance | Y-note 1 |  |
| BAAQMD Regulation 8-28 | Episodic Releases From Pressure Relief Devices at Petroleum Refineries and Chemical Plants (3/18/98) | N |  |
| 8-28-100 | General/Applicability | N |  |
| 8-28-200 | Definitions | N |  |
| 8-28-302 | Pressure Relief Devices at New or Modified Sources at Petroleum Refineries | N |  |
| 8-28-303 | Pressure Relief Devices at Existing Sources at Petroleum Refineries | N |  |
| 8-28-304 | Repeat Releases - Pressure Relief Devices at Petroleum Refineries | N |  |
| 8-28-401 | Reporting at Petroleum Refineries and Chemical Plants | N |  |
| 8-28-402 | Inspection | N |  |
| 8-28-403 | Records | N |  |
| 8-28-404 | Identification | N |  |
| 8-28-405 | Prevention Measures Procedures | N |  |
| SIP Regulation 8, Rule 28 | Pressure Relief Valves at Petroleum Refineries and Chemical Plants (12/9/94) |  |  |
| 8-28-301 | Pressure Relief Valve | Y-note 1 |  |
| 8-28-401 | Reporting | Y-note 1 |  |
| 8-28-402 | Inspection | Y-note 1 |  |
| 8-28-403 | Records | Y-note 1 |  |
| 8-28-404 | Identification | Y-note 1 |  |
| NSPS Part 60 Subpart GGG applies to the S-350 crude unit, S-370 isomerization unit, S-438 hydrogen plant |  |  |  |
| NSPS Part 60 Subpart GGG; BAAQMD Regulation 10-59 | Standards of Performance for Equipment Leaks (Fugitive Emission Sources) (5/30/84); BAAQMD Standards of Performance for New Stationary Sources (4/19/89) |  |  |
| 40 CFR 60.590 | Applicability | Y |  |
| 60.591 | Definitions | Y |  |
| 60.592 | Subject to provisions of Part 60, Subpart VV | Y |  |
| 60.593 | Exceptions | Y |  |
| BAAQMD Regulation 10-59 | Incorporates by reference 40 CFR 60 Subpart GGG | Y |  |
| NSPS Part 60 Subpart QQQ applies to the S-1007 dissolved air flotation unit |  |  |  |
| NSPS Part 60 Subpart QQQ; BAAQMD Regulation 10-69 | Standards of Performance for VOC Emission From Petroleum Refinery Wastewater Systems (7/18/95); BAAQMD Standards of Performance for New Stationary Sources (12/20/95) |  |  |
| 40 CFR 60.690 | Applicability | Y |  |
| 60.691 | Definitions | Y |  |
| 60.692-5 | Closed-vent systems and control devices Standards | Y |  |
| 60.692-6 | Delay of Repair Standards | Y |  |
| 60.695 | Monitoring of closed-vent systems with bypass lines | Y |  |
| 60.696 | Performance test methods and procedures and compliance provisions | Y |  |
| 60.697 | Recordkeeping | Y |  |
| 60.698 | Reporting | Y |  |
| BAAQMD Regulation 10-69 | Incorporates by reference 40 CFR 60 Subpart QQQ | Y |  |
| NSPS Part 60 Subpart VV applies to the S-350 crude unit, S-370 isomerization unit, S-438 hydrogen plant |  |  |  |
| NSPS Part 60 Subpart VV; BAAQMD Regulation 10-52 | Standards of Performance for Equipment Leaks (Fugitive Emission Sources) (8/18/95); BAAQMD Standards of Performance for New Stationary Sources (12/20/95) | Y |  |
| 60.480 | Applicability | Y |  |
| 60.481 | Definitions | Y |  |
| 60.482-1 | General Standards | Y |  |
| 60.482-2 | Pump Standards: | Y |  |
| 60.482-2(a)(1) | Monthly monitoring of each pump, except for 60.482-1(c), 60.482-2(d), (e), or (f) | Y |  |
| 60.482-2(a)(2) | Weekly visual inspection of each pump, except for (e), (f), or (g) | Y |  |
| 60.482-2(b) | Air measurement >10,000 ppm or dripping liquid indicates leak | Y |  |
| 60.482-2(d) | Requirements for Dual-Mechanical seal pump | Y |  |
| 60.482-2(e) | No detectable emission designation: <500 ppm | Y |  |
| 60.482-2(f) | Requirements for Closed Vent Systems | Y |  |
| 60.482-8 | Pumps in heavy liquid service | Y |  |
| 60.482-9(b) | Repair may be delayed for isolated equipment | Y |  |
| 60.482-9(d)(1) | Only dual-mechanical seal pumps qualify for delay of repair | Y |  |
| 60.482-9(d)(2) | Pump leaks must be repaired within 6 months | Y |  |
| 60.482-3 | Compressor Standards | Y |  |
| 60.482-4 | Requirements for Pressure Relief Devices in gas/vapor service | Y |  |
| 60.482-5 | Requirements for Sampling connecting systems | Y |  |
| 60.482-6 | Requirements for Open-ended valves or lines | Y |  |
| 60.482-7 | Valve Standards: | Y |  |
| 60.482-7(a)-(c) | Monitor monthly unless 2 successive months <10,000 ppm, then monitor first month of each quarter. If leak >10,000 ppm is detected, resume monthly monitoring | Y |  |
| 60.482-7(e) | Methods for first attempts or minimizing valve leaks | Y |  |
| 60.482-7(f) | Designated no-emissions (<500 ppm) valves with no external actuating mechanisms in contact with process fluid, may revert to annual monitoring, or that requested by the Administrator | Y |  |
| 60.482-8 | Valves in heavy liquid service | Y |  |
| 60.482-9(b) | Repair may be delayed for isolated equipment | Y |  |
| 60.482-9(c) | Delay of repair for valves is only allowed under certain circumstances | Y |  |
| 60.482-8 | Pressure Relief Devices in liquid service and Flanges and other Connectors Standards | Y |  |
| 60.482-10 | Requirements for Closed-vent systems and control devices | Y |  |
| 60.483-1, 60.483-2, and BAAQMD 8-18-404.1 | If a process unit has 5 consecutive quarters with <2% of valves leaking at >10,000 ppm, then any individual valve which measures <100 ppm for 5 consecutive quarters may be monitored annually | Y |  |
| 60.485 | Test Methods and Procedures | Y |  |
| 60.486 | Record keeping | Y |  |
| 60.487 | Reporting | Y |  |
| BAAQMD Regulation 10-52 | Incorporates by reference 40 CFR 60 Subpart VV | Y |  |
| NESHAP Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants from Petroleum Refineries | Y |  |
| 63.640(a) | Applicability | Y |  |
| 63.640(p) | Overlap of Subpart CC with other regulations for equipment leaks. | Y |  |
| 63.641 | Definitions | Y |  |
| 63.642(e) | Keep records for 5 years | Y |  |
| 63.648(a) | Equipment leak standards. Comply with 40 CFR 60, Subpart VV | Y |  |
| 63.648(b) | Use of monitoring data from prior to 8/18/95 to qualify for less stringent monitoring frequency | Y |  |
| 63.648(e) | Equipment leak standards – reciprocating pumps in heavy liquid service | Y |  |
| 63.648(f) | Equipment leak standards – reciprocating pumps in light liquid service | Y |  |
| 63.648(g) | Equipment leak standards – compressors in hydrogen service | Y |  |
| 63.648(h) | Keep records for 5 years | Y |  |
| 63.648(i) | Equipment leak standards – reciprocating compressors | Y |  |
| 63.654(d) | Record keeping and reporting | Y |  |

1	This section has been removed from BAAQMD Regulations because it has been superseded.  Nevertheless, the source must comply with this regulation until US EPA has reviewed and approved (or disapproved) the District’s revision of the regulation.

| Table IV – B1 Source-Specific Applicable Requirements NSPS Kb Low Vapor Pressure Permitted Wastewater Sludge Tanks with Vapor Recovery to Fuel Gas S-433 (F224-MOSC) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| BAAQMD · Regulation 8, Rule 8 | Organic Compounds, Wastewater (Oil-Water Separators) (6/15/1994) REQUIREMENTS FOR SLUDGE DEWATERING UNITS |  |  |
| 8-8-113 | Exemption, Secondary Wastewater Treatment Processes and Stormwater Sewer Systems (segregated) are exempt from 8-8-301, 8-8-302, 8-8-306, 8-8-308 | Y |  |
| 8-8-303 | Standards: Gauging and Sampling Devices | Y |  |
| 8-8-304 | Standards: Sludge-dewatering Unit | Y |  |
| 8-8-504 | Monitoring and Records: Portable Hydrocarbon Detector | Y |  |
| 8-8-602 | Manual of Procedures: Determination of Emissions | Y |  |
| 8-8-603 | Manual of Procedures: Inspection Procedures | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR EMISSION POINTS ROUTED TO FUEL GAS |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| NSPS Title 40 Part 60 Subpart QQQ | NSPS Subpart QQQ VOC Emissions from Petroleum Refinery Wastewater Systems REQUIREMENTS FOR FIXED ROOF TANKS ROUTED TO FUEL GAS |  |  |
| 40 CFR 60.690(a)(1) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.690(a)(3) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.691 | Definitions: Closed Vent System. If gas or vapor from regulated equipment are routed to a process (e.g., petroleum refinery fuel gas system), the process shall not be considered a closed vent system and is not subject to the closed vent system standards. | Y |  |
| 40 CFR 60.692-1 | Standards: General | Y |  |
| 40 CFR 60.692-1(a) | Standards: General | Y |  |
| 40 CFR 60.692-1(b) | Standards: General | Y |  |
| 40 CFR 60.692-3 | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(1) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(2) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(3) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(4) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(5) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(f) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-6 | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(a) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(b) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.697 | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(a) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(c) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(3) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(4) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.698(c) | Reporting Requirements | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR RECORDKEEPING ONLY |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.110b(c) | Applicability and Designation of Affected Facility; Exemptions for storage vessels > or = to 75 cu m | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(3) | Monitoring of Operations; Determine TVP-other liquids | Y |  |
| 40 CFR 60.116b(f) | Monitoring of Operations; Waste storage tanks (indeterminate or variable composition) | Y |  |
| 40 CFR 60.116b(g) | Monitoring of Operations; Exemption from 40 CFR 60.116b(c) and 40 CFR 60.116b(d) for tanks with closed vent system and control device | Y |  |
| BAAQMD Condition 7353 | APPLICABLE TO S-433 |  |  |
| Part 1 | Requirement to vent tank to fuel gas system [Basis: Cumulative Increase] | Y |  |
| Part 2 | Valve, pump design requirements [Basis: Cumulative Increase] | Y |  |
| Part 3 | Limitation on material stored [Basis: Cumulative Increase] | Y |  |
| Part 4 | Annual throughput limit [Basis: Cumulative Increase] | Y |  |
| Part 5 | Weekly throughput records [Basis: Recordkeeping] | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

| Table IV – B2 Source-Specific Applicable Requirements Low Vapor Pressure Permitted Tanks Subject to MACT Recordkeeping S-118 (Tank 163) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.119(a)(3) | Storage Vessel Provisions – Reference Control Technology – Group 2 storage vessels comply only with recordkeeping requirements in 40 CFR 63.123(a) | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions – Recordkeeping – Group 2 storage vessels only required to keep tank dimensions and capacity analysis. Retain for life of source. | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Keep records specified in 40 CFR 63.123 | Y |  |
| 40 CFR 63.654(i)(1)(iv) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Data and assumptions used to determine Group 2 classification | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements--Recordkeeping--Record retention – 5 years | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-118 [Basis: 2-1-234.3] | N |  |

| Table IV – B3 Source-Specific Applicable Requirements Low Vapor Pressure Permitted Tanks < 10,000 Gallons S-117 (Tank 162), S-193 (Tank 305), S-194 (Tank 306) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-117, S-193, S-194 [Basis: 2-1-234.3] | N |  |

| Table IV – B4 Source-Specific Applicable Requirements Low Vapor Pressure Permitted Tanks Vented to Fuel Gas S-238 (Tank 211), S-239 (Tank 212) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR EMISSION POINTS ROUTED TO FUEL GAS |  |  |
| 40 CFR 63.640(c)(3) | Wastewater streams and treatment operations associated with petroleum refining process units meeting the criteria of section 63.640(a) | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y |  |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-238, S-239 [Basis: 2-1-234.3] | N |  |

| Table IV – B5 Source-Specific Applicable Requirements NSPS Kb Low Vapor Pressure Permitted Fixed Roof Wastewater Sludge Tanks S-195 (Tank 501), S-196 (Tank 502), S-388 (Tank 276/F205) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| BAAQMD · Regulation 8, Rule 8 | Organic Compounds, Wastewater (Oil-Water Separators) (6/15/1994) REQUIREMENTS FOR SLUDGE DEWATERING UNITS |  |  |
| 8-8-113 | Exemption, Secondary Wastewater Treatment Processes and Stormwater Sewer Systems (segregated) are exempt from 8-8-301, 8-8-302, 8-8-306, 8-8-308 | Y |  |
| 8-8-303 | Standards: Gauging and Sampling Devices | Y |  |
| 8-8-304 | Standards: Sludge-dewatering Unit | Y |  |
| 8-8-504 | Monitoring and Records: Portable Hydrocarbon Detector | Y |  |
| 8-8-602 | Manual of Procedures: Determination of Emissions | Y |  |
| 8-8-603 | Manual of Procedures: Inspection Procedures | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR TANKS ALSO SUBJECT TO NSPS Kb |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(n)(1) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Existing Group 1 or Group 2 also subject to Kb only subject to Kb and 63.640(n)(8). | Y |  |
| 40 CFR 63.640(n)(8) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR RECORDKEEPING ONLY |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.110b(c) | Applicability and Designation of Affected Facility; Exemptions for storage vessels > or = to 75 cu m | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(d) | Monitoring of Operations; 30-day notification for TVP exceedances | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(3) | Monitoring of Operations; Determine TVP-other liquids | Y |  |
| 40 CFR 60.116b(f) | Monitoring of Operations; Waste storage tanks (indeterminate or variable composition) | Y |  |
| NSPS Title 40 Part 60 Subpart QQQ | NSPS Subpart QQQ VOC Emissions from Petroleum Refinery Wastewater Systems REQUIREMENTS FOR STORAGE VESSELS NOT SUBJECT TO NSPS Kb CONTROL REQUIREMENTS (60.112b) |  |  |
| 40 CFR 60.690(a)(1) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.690(a)(3) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.692-1 | Standards: General | Y |  |
| 40 CFR 60.692-1(a) | Standards: General | Y |  |
| 40 CFR 60.692-1(b) | Standards: General | Y |  |
| 40 CFR 60.692-3 | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(1) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(2) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(3) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(4) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(5) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(f) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-6 | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(a) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(b) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.697 | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(a) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(c) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(3) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(4) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.698(c) | Reporting Requirements | Y |  |
| BAAQMD Condition 1860 | APPLICABLE TO S-388 |  |  |
| Part 1 | No detectable VOC emissions [Basis: Cumulative Increase] | Y |  |
| Part 2 | Requirement to vent to fuel gas recovery system [Basis: Cumulative Increase] | Y |  |
| Part 3 | Requirement to include S-388 in fugitive inspection program to verify compliance with Part 1 [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-195 [Basis: 2-1-234.3] | N |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-196, S-388 [Basis: 2-1-234.3] | Y |  |

| Table IV – B6 Source-Specific Applicable Requirements MACT (Small) Zero Gap External Floating Roof Tank S-121 (Tank 166) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements – Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Projection below surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – | Y |  |
| 8-5-320.3.1 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.4 | Primary seal requirements; Resilient-toroid seal requirements including seal gaps | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary seal requirements; Gap for welded tanks with seal installed after September 4, 1985 | Y |  |
| 8-5-322.6 | Secondary seal requirements; extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.119(a)(3) | Storage Vessel Provisions – Reference Control Technology – Group 2 storage vessels comply only with recordkeeping requirements in 40 CFR 63.123(a) | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions – Recordkeeping – Group 2 storage vessels only required to keep tank dimensions and capacity analysis. Retain for life of source. | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Keep records specified in 40 CFR 63.123 | Y |  |
| 40 CFR 63.654(i)(1) (iv) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Data and assumptions used to determine Group 2 classification | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements--Recordkeeping--Record retention – 5 years | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-121 [Basis: 2-1-234.3] | N |  |

| Table IV – B7 Source-Specific Applicable Requirements NSPS Kb Zero gap External Floating Roof Tanks S-439 (Tank 109), S-440 (Tank 110), S-442 (Tank 112), S-444 (Tank 243), S-451 (Tank 695) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements – Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Projection below surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – | Y |  |
| 8-5-320.3.1 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary seal requirements; Metallic shoe type seal requirements | Y |  |
| 8-5-321.3.1 | Primary seal requirements; Metallic shoe type seal requirements Geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary seal requirements; Metallic shoe type seal requirements Gaps for welded tanks | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary seal requirements; Gap for welded tanks with seal installed after September 4, 1985 | Y |  |
| 8-5-322.6 | Secondary seal requirements; extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| NESHAPS 40 CFR 63 Subpart CC | National Emission Standards for Hazardous Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS ALSO SUBJECT TO NSPS Kb |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(n)(1) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Existing Group 1 or Group 2 also subject to Kb only subject to Kb and 63.640(n)(8). | Y |  |
| 40 CFR 63.640(n)(8) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(i) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(ii) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(iii) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(iv) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(v) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(vi) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.112b(a) | Standard for Volatile Organic Compounds (VOC); Requirement for tanks-- > 151 cu m with maximum TVP >=5.2 kPa and <76.6 kPa; or >= 75 cu m and < 151 cu m with maximum TVP >= 27.6 kPa and < 76.6 kPa | Y |  |
| 40 CFR 60.112b(a)(2) | Standard for Volatile Organic Compounds (VOC); External floating roof option | Y |  |
| 40 CFR 60.112b(a)(2)(i) | Standard for Volatile Organic Compounds (VOC); External floating roof seal requirements | Y |  |
| 40 CFR 60.112b(a)(2)(i)(A) | Standard for Volatile Organic Compounds (VOC); External floating roof primary seal requirements | Y |  |
| 40 CFR 60.112b(a)(2)(i)(B) | Standard for Volatile Organic Compounds (VOC); External floating roof secondary seal requirements | Y |  |
| 40 CFR 60.112b(a)(2)(ii) | Standard for Volatile Organic Compounds (VOC); External floating roof openings requirements | Y |  |
| 40 CFR 60.112b(a)(2)(iii) | Standard for Volatile Organic Compounds (VOC); External floating roof floating requirements | Y |  |
| 40 CFR 60.113b(b)(1) | Testing and Procedures; External floating roof seal gap measurement frequency | Y |  |
| 40 CFR 60.113b(b)(1)(i) | Testing and Procedures; External floating roof primary seal gaps measurement frequency | Y |  |
| 40 CFR 60.113b(b)(1)(ii) | Testing and Procedures; External floating roof secondary seal gaps measurement frequency | Y |  |
| 40 CFR 60.113b(b)(1)(iii) | Testing and Procedures; External floating roof reintroduction of VOL | Y |  |
| 40 CFR 60.113b(b)(2) | Testing and Procedures; External floating roof seal gap measurement procedures | Y |  |
| 40 CFR 60.113b(b)(2)(i) | Testing and Procedures; External floating roof measure seal gaps when roof is floating | Y |  |
| 40 CFR 60.113b(b)(2)(ii) | Testing and Procedures; External floating roof measure seal gaps around entire circumference | Y |  |
| 40 CFR 60.113b(b)(2)(iii) | Testing and Procedures; External floating roof seal method to determine surface area of seal gaps | Y |  |
| 40 CFR 60.113b(b)(3) | Testing and Procedures; External floating roof method to calculate total surface area ratio | Y |  |
| 40 CFR 60.113b(b)(4) | Testing and Procedures; External floating roof seal gap repair requirements | Y |  |
| 40 CFR 60.113b(b)(4)(i) | Testing and Procedures; External floating roof primary seal gap limitations | Y |  |
| 40 CFR 60.113b(b)(4)(i)(A) | Testing and Procedures; External floating roof mechanical shoe primary seal requirements | Y |  |
| 40 CFR 60.113b(b)(4)(i)(B) | Testing and Procedures; External floating roof primary seals no holes, tears, openings | Y |  |
| 40 CFR 60.113b(b)(4)(ii) | Testing and Procedures; External floating roof secondary seal gap limitations | Y |  |
| 40 CFR 60.113b(b)(4)(ii)(A) | Testing and Procedures; External floating roof secondary seal installation | Y |  |
| 40 CFR 60.113b(b)(4)(ii)(B) | Testing and Procedures; External floating roof secondary seal gap | Y |  |
| 40 CFR 60.113b(b)(4)(ii)(C) | Testing and Procedures; External floating roof secondary seals no holes, tears, openings | Y |  |
| 40 CFR 60.113b(b)(4)(iii) | Testing and Procedures; External floating roof 30-day extension request for seal gap repairs | Y |  |
| 40 CFR 60.113b(b)(5) | Testing and Procedures; External floating roof seal gap inspections 30 day notification | Y |  |
| 40 CFR 60.113b(b)(6) | Testing and Procedures; External floating roof visual inspection when emptied and degassed | Y |  |
| 40 CFR 60.113b(b)(6)(i) | Testing and Procedures; External floating roof--roof or seal defect repairs | Y |  |
| 40 CFR 60.113b(b)(6)(ii) | Testing and Procedures; External floating roof notification prior to filling | Y |  |
| 40 CFR 60.115b | Reporting and Recordkeeping Requirements; 60.112b(a) tanks; Record retention | Y |  |
| 40 CFR 60.115b(b) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating | Y |  |
| 40 CFR 60.115b(b)(1) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating roof control equipment description and certification | Y |  |
| 40 CFR 60.115b(b)(2) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating roof seal gap measurement report – content requirements | Y |  |
| 40 CFR 60.115b(b)(3) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating roof seal gap measurement records requirements | Y |  |
| 40 CFR 60.115b(b)(4) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating roof seal gap exceedance report | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(c) | Monitoring of Operations; VOL storage record requirements | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(2) | Monitoring of Operations; Determine TVP-crude oil and refined petroleum | Y |  |
| BAAQMD Condition 12124 | APPLICABLE TO S-439 |  |  |
| Part 1 | Annual throughput limit [Basis: Cumulative Increase] | Y |  |
| Part 2 | Requirements for tank openings [Basis: Cumulative Increase] | Y |  |
| Part 3 | Monthly throughput records [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 12125 | APPLICABLE TO S-440 |  |  |
| Part 1 | Annual throughput limit [Basis: Cumulative Increase] | Y |  |
| Part 2 | Requirements for tank openings [Basis: Cumulative Increase] | Y |  |
| Part 3 | Monthly throughput records [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 12127 | APPLICABLE TO S-442 |  |  |
| Part 1 | Annual throughput limit [Basis: Cumulative Increase] | Y |  |
| Part 2 | Requirements for tank openings [Basis: Cumulative Increase] | Y |  |
| Part 3 | Monthly throughput records [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 12129 | APPLICABLE TO S-444 |  |  |
| Part 1 | Annual throughput limit [Basis: Cumulative Increase] | Y |  |
| Part 2 | Requirements for tank openings [Basis: Cumulative Increase] | Y |  |
| Part 3 | Monthly throughput records [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 19476 | APPLICABLE TO S-451 |  |  |
| Part 1 | Annual throughput limit [Basis: Cumulative Increase] | Y |  |
| Part 2 | Tank design requirements [Basis: BACT, Cumulative Increase] | Y |  |
| Part 3 | Monthly throughput records [Basis: Cumulative Increase] | Y |  |

| Table IV – B8 Source-Specific Applicable Requirements NSPS Kb Zero gap External Floating Roof Stormwater Equilization Tanks S-101 (Tank 104), S-102 (Tank 105), S-106 (Tank 130) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves (applies only to S-106) | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure (applies only to S-106) | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation (applies only to S-106) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements – Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Projection below surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – | Y |  |
| 8-5-320.3.1 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary seal requirements; Metallic shoe type seal requirements | Y |  |
| 8-5-321.3.1 | Primary seal requirements; Metallic shoe type seal requirements Geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary seal requirements; Metallic shoe type seal requirements Gaps for welded tanks | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary seal requirements; Gap for welded tanks with seal installed after September 4, 1985 | Y |  |
| 8-5-322.6 | Secondary seal requirements; extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves (applies only to S-106) | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure Vacuum Valve Gas Tight Determination (applies only to S-106) | Y |  |
| BAAQMD · Regulation 8, Rule 8 | Organic Compounds, Wastewater (Oil-Water Separators) (6/15/1994) REQUIREMENTS FOR WASTEWATER SEPARATORS |  |  |
| 8-8-302 | Standards: Wastewater Separators Larger than or Equal to 18.9 Liters per second (300 gal per min) | Y |  |
| 8-8-302.2 | Standards: Wastewater Separators Larger than or Equal to 18.9 Liters per second (300 gal per min); Floating roof tank with double seals | Y |  |
| 8-8-302.2.1 | Standards: Wastewater Separators Larger than or Equal to 18.9 Liters per second (300 gal per min); Floating roof tank with double seals – liquid mounted primary seal gap criteria | Y |  |
| 8-8-302.2.2 | Standards: Wastewater Separators Larger than or Equal to 18.9 Liters per second (300 gal per min); Floating roof tank with double seals – secondary and wiper seals gap criteria | Y |  |
| 8-8-302.2.3 | Standards: Wastewater Separators Larger than or Equal to 18.9 Liters per second (300 gal per min); Floating roof tank with double seals – primary and secondary seal gap inspection | Y |  |
| 8-8-303 | Standards: Gauging and Sampling Devices | Y |  |
| 8-8-503 | Monitoring and Records: Inspection and Repair Records | Y |  |
| 8-8-504 | Monitoring and Records: Portable Hydrocarbon Detector | Y |  |
| 8-8-603 | Manual of Procedures: Inspection Procedures | Y |  |
| 40 CFR 63 Subpart CC | National Emission Standards for Hazardous Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR GROUP 2 WASTEWATER SOURCES |  |  |
| 40 CFR 63.640(c)(3) | Wastewater streams and treatment operations associated with petroleum refining process units meeting the criteria of section 63.640(a) | Y |  |
| 40 CFR 63.641 | Definitions: Group 1 and Group 2 Wastewater Streams | Y |  |
| 40 CFR 63.654(a) | Reporting and Recordkeeping Requirements: Wastewater – no reporting and recordkeeping requirements for wastewater except for Group 1 wastewater streams | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.112b(a) | Standard for Volatile Organic Compounds (VOC); Requirement for tanks-- > 151 cu m with maximum TVP >=5.2 kPa and <76.6 kPa; or >= 75 cu m and < 151 cu m with maximum TVP >= 27.6 kPa and < 76.6 kPa | Y |  |
| 40 CFR 60.112b(a)(2) | Standard for Volatile Organic Compounds (VOC); External floating roof option | Y |  |
| 40 CFR 60.112b(a)(2)(i) | Standard for Volatile Organic Compounds (VOC); External floating roof seal requirements | Y |  |
| 40 CFR 60.112b(a)(2)(i)(A) | Standard for Volatile Organic Compounds (VOC); External floating roof primary seal requirements | Y |  |
| 40 CFR 60.112b(a)(2)(i)(B) | Standard for Volatile Organic Compounds (VOC); External floating roof secondary seal requirements | Y |  |
| 40 CFR 60.112b(a)(2)(ii) | Standard for Volatile Organic Compounds (VOC); External floating roof openings requirements | Y |  |
| 40 CFR 60.112b(a)(2)(iii) | Standard for Volatile Organic Compounds (VOC); External floating roof floating requirements | Y |  |
| 40 CFR 60.113b(b)(1) | Testing and Procedures; External floating roof seal gap measurement frequency | Y |  |
| 40 CFR 60.113b(b)(1)(i) | Testing and Procedures; External floating roof primary seal gaps measurement frequency | Y |  |
| 40 CFR 60.113b(b)(1)(ii) | Testing and Procedures; External floating roof secondary seal gaps measurement frequency | Y |  |
| 40 CFR 60.113b(b)(1)(iii) | Testing and Procedures; External floating roof reintroduction of VOL | Y |  |
| 40 CFR 60.113b(b)(2) | Testing and Procedures; External floating roof seal gap measurement procedures | Y |  |
| 40 CFR 60.113b(b)(2)(i) | Testing and Procedures; External floating roof measure seal gaps when roof is floating | Y |  |
| 40 CFR 60.113b(b)(2)(ii) | Testing and Procedures; External floating roof measure seal gaps around entire circumference | Y |  |
| 40 CFR 60.113b(b)(2)(iii) | Testing and Procedures; External floating roof seal method to determine surface area of seal gaps | Y |  |
| 40 CFR 60.113b(b)(3) | Testing and Procedures; External floating roof method to calculate total surface area ratio | Y |  |
| 40 CFR 60.113b(b)(4) | Testing and Procedures; External floating roof seal gap repair requirements | Y |  |
| 40 CFR 60.113b(b)(4)(i) | Testing and Procedures; External floating roof primary seal gap limitations | Y |  |
| 40 CFR 60.113b(b)(4)(i)(A) | Testing and Procedures; External floating roof mechanical shoe primary seal requirements | Y |  |
| 40 CFR 60.113b(b)(4)(i)(B) | Testing and Procedures; External floating roof primary seals no holes, tears, openings | Y |  |
| 40 CFR 60.113b(b)(4)(ii) | Testing and Procedures; External floating roof secondary seal gap limitations | Y |  |
| 40 CFR 60.113b(b)(4)(ii)(A) | Testing and Procedures; External floating roof secondary seal installation | Y |  |
| 40 CFR 60.113b(b)(4)(ii)(B) | Testing and Procedures; External floating roof secondary seal gap | Y |  |
| 40 CFR 60.113b(b)(4)(ii)(C) | Testing and Procedures; External floating roof secondary seals no holes, tears, openings | Y |  |
| 40 CFR 60.113b(b)(4)(iii) | Testing and Procedures; External floating roof 30-day extension request for seal gap repairs | Y |  |
| 40 CFR 60.113b(b)(5) | Testing and Procedures; External floating roof seal gap inspections 30 day notification | Y |  |
| 40 CFR 60.113b(b)(6) | Testing and Procedures; External floating roof visual inspection when emptied and degassed | Y |  |
| 40 CFR 60.113b(b)(6)(i) | Testing and Procedures; External floating roof--roof or seal defect repairs | Y |  |
| 40 CFR 60.113b(b)(6)(ii) | Testing and Procedures; External floating roof notification prior to filling | Y |  |
| 40 CFR 60.115b | Reporting and Recordkeeping Requirements; 60.112b(a) tanks; Record retention | Y |  |
| 40 CFR 60.115b(b) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating | Y |  |
| 40 CFR 60.115b(b)(1) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating roof control equipment description and certification | Y |  |
| 40 CFR 60.115b(b)(2) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating roof seal gap measurement report – content requirements | Y |  |
| 40 CFR 60.115b(b)(3) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating roof seal gap measurement records requirements | Y |  |
| 40 CFR 60.115b(b)(4) | Reporting and Recordkeeping Requirements; 60.112b(a) external floating roof seal gap exceedance report | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(c) | Monitoring of Operations; VOL storage record requirements | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(3) | Monitoring of Operations; Determine TVP-other liquids | Y |  |
| 40 CFR 60.116b(f) | Monitoring of Operations; Waste storage tanks (indeterminate or variable composition) | Y |  |
| NSPS Title 40 Part 60 Subpart QQQ | NSPS Subpart QQQ VOC Emissions from Petroleum Refinery Wastewater Systems REQUIREMENTS FOR STORAGE VESSELS ALSO SUBJECT TO NSPS Kb |  |  |
| 40 CFR 60.690(a)(1) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.690(a)(3) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.692-1 | Standards: General | Y |  |
| 40 CFR 60.692-1(a) | Standards: General | Y |  |
| 40 CFR 60.692-1(b) | Standards: General | Y |  |
| 40 CFR 60.692-3 | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(d) | Standards: Oil-Water Separators (includes storage vessels) – Overlap with Kb | Y |  |
| 40 CFR 60.692-6 | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(a) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(b) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.697 | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(a) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(3) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(4) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(2) | Recordkeeping Requirements | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-101, S-102, S-106 [Basis: 2-1-234.3] | Y |  |

| Table IV – B9 Source-Specific Applicable Requirements NSPS Kb Zero-Gap Internal Floating Roof Tank S-448 (Tank 1007) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8 Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR INTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-305 | Requirements for Internal Floating roofs | Y |  |
| 8-5-305.2 | Requirements for Internal Floating roofs; Seals installed after 2/1/1993 | Y |  |
| 8-5-305.3 | Requirements for Internal Floating roofs; Viewports in fixed roof tank | Y |  |
| 8-5-305.4 | Requirements for Internal Floating roofs; Tank fitting requirements | Y |  |
| 8-5-305.5 | Requirements for Internal Floating roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements; Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements; Floating roof tanks; Projection below liquid surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements; Floating roof tanks; Gasketed covers, seals, lids | Y |  |
| 8-5-320.3.1 | Tank fitting requirements; Floating roof tanks; Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.3.2 | Tank fitting requirements; Floating roof tanks; Gasketed covers, seals, lids – Inaccessible openings on internal floating roof tanks | Y |  |
| 8-5-320.4 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary seal requirements; Metallic shoe type seals requirements | Y |  |
| 8-5-321.3.1 | Primary seal requirements; Metallic shoe type seals requirements; Geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary seal requirements; Metallic shoe type seals requirements; Gaps for welded tanks | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary seal requirements; Gaps for welded tanks with seals installed after 2/1/93 | Y |  |
| 8-5-322.6 | Secondary seal requirements; Extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone excess day prohibition | Y |  |
| 8-5-402 | Inspection Requirements for Internal Floating Roof Tanks | Y |  |
| 8-5-402.1 | Inspection Requirements for Internal Floating Roof Tanks; Primary and Secondary Seal Inspections – Seal gaps | Y |  |
| 8-5-402.2 | Inspection Requirements for Internal Floating Roof Tanks; Visual Inspection of Outer Most Seal | Y |  |
| 8-5-402.3 | Inspection Requirements for Internal Floating Roof Tanks; Tank Fitting Inspection | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR INTERNAL FLOATING ROOF TANKS ALSO SUBJECT TO NSPS Kb |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(n)(1) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Existing Group 1 or Group 2 also subject to Kb only subject to Kb and 63.640(n)(8). | Y |  |
| 40 CFR 63.640(n)(8) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(ii) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(iii) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(iv) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| 40 CFR 63.640(n)(8)(v) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR INTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.112b(a) | Standard for Volatile Organic Compounds (VOC); Requirement for tanks-- > 151 cu m with maximum TVP >=5.2 kPa and <76.6; or >= 75 cu m and < 151 cu m with maximum TVP >= 27.6 kPa and < 76.6 kPa | Y |  |
| 40 CFR 60.112b(a)(1) | Standard for Volatile Organic Compounds (VOC); Fixed roof with internal floating roof option | Y |  |
| 40 CFR 60.112b(a)(1)(i) | Standard for Volatile Organic Compounds (VOC); Internal floating roof requirements | Y |  |
| 40 CFR 60.112b(a)(1)(ii) | Standard for Volatile Organic Compounds (VOC); Internal floating roof seal requirements | Y |  |
| 40 CFR 60.112b(a)(1)(ii)(B) | Standard for Volatile Organic Compounds (VOC); Internal floating roof double seal option | Y |  |
| 40 CFR 60.112b(a)(1)(iii) | Standard for Volatile Organic Compounds (VOC); Internal floating roof openings-projections below roof surface | Y |  |
| 40 CFR 60.112b(a)(1)(iv) | Standard for Volatile Organic Compounds (VOC); Internal floating roof openings covers | Y |  |
| 40 CFR 60.112b(a)(1)(v) | Standard for Volatile Organic Compounds (VOC); Internal floating roof automatic bleeder vents | Y |  |
| 40 CFR 60.112b(a)(1)(vi) | Standard for Volatile Organic Compounds (VOC); Internal floating roof rim space vents | Y |  |
| 40 CFR 60.112b(a)(1)(vii) | Standard for Volatile Organic Compounds (VOC); Internal floating roof sampling penetrations | Y |  |
| 40 CFR 60.112b(a)(1)(viii) | Standard for Volatile Organic Compounds (VOC); Internal floating roof support column penetrations | Y |  |
| 40 CFR 60.112b(a)(1)(ix) | Standard for Volatile Organic Compounds (VOC); Internal floating roof ladder penetrations | Y |  |
| 40 CFR 60.113b(a)(1) | Testing and Procedures; Internal floating roof visual inspection before filling. Repair any defects found during inspection before filling. | Y |  |
| 40 CFR 60.113b(a)(2) | Testing and Procedures; Internal floating roof tanks with liquid mounted or mechanical shoe primary seal, annual visual inspection through manholes and hatches (if complying with 40 CFR 60.113b(a)(3)(ii)) | Y |  |
| 40 CFR 60.113b(a)(3) | Testing and Procedures; Internal floating roof with double seal system, inspection requirements | Y |  |
| 40 CFR 60.113b(a)(3)(ii) | Testing and Procedures; Internal floating roof with double seal system, inspection requirements - visually inspect per 40 CFR 60.113b(a)(2) annually and per 40 CFR 60.113b(a)(4) every 10 years. | Y |  |
| 40 CFR 60.113b(a)(4) | Testing and Procedures; Internal floating roof inspection requirements each time tank is emptied and degassed (10 year intervals if complying with 40 CFR 60.113b(a)(3)(ii)) | Y |  |
| 40 CFR 60.113b(a)(5) | Testing and Procedures; Internal floating roof, 30 day notification for filling after inspection | Y |  |
| 40 CFR 60.115b | Reporting and Recordkeeping Requirements; 60.112b(a) tanks; Record retention | Y |  |
| 40 CFR 60.115b(a) | Reporting and Recordkeeping Requirements; 60.112b(a) internal floating roof tanks | Y |  |
| 40 CFR 60.115b(a)(1) | Reporting and Recordkeeping Requirements; 60.112b(a) internal floating roof control equipment description and certification | Y |  |
| 40 CFR 60.115b(a)(2) | Reporting and Recordkeeping Requirements; 60.112b(a) internal floating roof inspection records | Y |  |
| 40 CFR 60.115b(a)(3) | Reporting and Recordkeeping Requirements; 60.112b(a) internal floating roof annual inspection defects report | Y |  |
| 40 CFR 60.115b(a)(4) | Reporting and Recordkeeping Requirements; 60.112b(a) internal floating roof double seal system inspection defects report | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(c) | Monitoring of Operations; VOL storage record requirements | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(2) | Monitoring of Operations; Determine TVP-crude oil and refined petroleum | Y |  |
| BAAQMD Condition 12133 |  |  |  |
| Part 1 | Annual throughput limit [Basis: Cumulative Increase] | Y |  |
| Part 2 | Requirements for tank openings [Basis: Cumulative Increase] | Y |  |
| Part 3 | Monthly throughput records [Basis: Cumulative Increase] | Y |  |

| Table IV – B10 Source-Specific Applicable Requirements Internal Floating Roof Tanks with Dome Roofs Previously External Floating Roof Tanks S-126 (Tank 172), S-257 (Tank 1004), S-258 (Tank 1005) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8 Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR INTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves (applies only to S-126 and S-258) | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure (applies only to S-126 and S-258) | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation (applies only to S-126 and S-258) | Y |  |
| 8-5-305 | Requirements for Internal Floating roofs | Y |  |
| 8-5-305.2 | Requirements for Internal Floating roofs; Seals installed after 2/1/1993 | Y |  |
| 8-5-305.3 | Requirements for Internal Floating roofs; Viewports in fixed roof tank; not required if dome roof has translucent panels | Y |  |
| 8-5-305.4 | Requirements for Internal Floating roofs; Tank fitting requirements | Y |  |
| 8-5-305.5 | Requirements for Internal Floating roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements; Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements; Floating roof tanks; Projection below liquid surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements; Floating roof tanks; Gasketed covers, seals, lids | Y |  |
| 8-5-320.3.1 | Tank fitting requirements; Floating roof tanks; Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.3.2 | Tank fitting requirements; Floating roof tanks; Gasketed covers, seals, lids – Inaccessible openings on internal floating roof tanks | Y |  |
| 8-5-320.4 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary seal requirements; Metallic shoe type seals requirements | Y |  |
| 8-5-321.3.1 | Primary seal requirements; Metallic shoe type seals requirements; Geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary seal requirements; Metallic shoe type seals requirements; Gaps for welded tanks | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary seal requirements; Gaps for welded tanks with seals installed after 2/1/93 – note 2 | Y |  |
| 8-5-322.6 | Secondary seal requirements; Extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone excess day prohibition | Y |  |
| 8-5-402 | Inspection Requirements for Internal Floating Roof Tanks | Y |  |
| 8-5-402.1 | Inspection Requirements for Internal Floating Roof Tanks; Primary and Secondary Seal Inspections – Seal gaps | Y |  |
| 8-5-402.2 | Inspection Requirements for Internal Floating Roof Tanks; Visual Inspection of Outer Most Seal | Y |  |
| 8-5-402.3 | Inspection Requirements for Internal Floating Roof Tanks; Tank Fitting Inspection | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves (applies only to S-126 and S-258) | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure Vacuum Valve Gas Tight Determination (applies only to S-126 and S-258) | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR INTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(b) | Storage Vessel Provisions -- Reference Control Technology—Internal floating roof | Y |  |
| 40 CFR 63.119(b)(1) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(b)(1)(i) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(b)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(b)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(b)(2) | Storage Vessel Provisions -- Reference Control Technology-- Internal Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.119(b)(3) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof – seals; must have at least one seal | Y |  |
| 40 CFR 63.119(b)(3)(i) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof – seal option; single liquid-mounted seal | Y |  |
| 40 CFR 63.119(b)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof - seal option; single metallic shoe seal | Y |  |
| 40 CFR 63.119(b)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof - seal option; double seal, lower can be vapor mounted | Y |  |
| 40 CFR 63.119(b)(4) | Storage Vessel Provisions -- Reference Control Technology-- Internal floating roof – automatic bleeder valve requirements | Y |  |
| 40 CFR 63.120(a) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--Internal floating roof | Y |  |
| 40 CFR 63.120(a)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance—Internal FR tank inspection schedule | Y |  |
| 40 CFR 63.120(a)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance—Internal FR tank inspections – tanks with double seals | Y |  |
| 40 CFR 63.120(a)(3)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- Internal FR tank inspections – tanks with double seals - annual visual inspection of IFR and secondary seal through manholes and roof hatches. Also must comply with 40 CFR 63.120(a)(3)(iii) every time emptied and degassed and every 10 years. | Y |  |
| 40 CFR 63.120(a)(3)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- Internal FR tank inspections – tanks with double seals - visually inspect IFR and both seals each time emptied and degassed and at least once every 10 years [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)]. Also must comply with annual visual inspection in 40 CFR 63.120(a)(3)(ii). | Y |  |
| 40 CFR 63.120(a)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance Internal FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(a)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance Internal FR and seal visual inspection each time emptied – 30 day notification required for 10 year inspection (63.120(a)(3)(iii)) | Y |  |
| 40 CFR 63.120(a)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.120(a)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--Internal FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)] | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(c) | Storage Vessel Provisions -- Recordkeeping--Group 1 Internal floating roof tank requirements - records of each tank inspection | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR INTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [IFRs exempt from 63.119(b)(5) and (b)(6)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(2) | Periodic Reporting and Recordkeeping Requirements-- internal floating roof tanks – submit results of each tank inspection where failure is detected in control equipment | Y |  |
| 40 CFR 63.654(g)(2)(i) | Periodic Reporting and Recordkeeping Requirements--internal floating roof tanks – submit results of each tank inspection where failure is detected in control equipment – annual inspection reports | Y |  |
| 40 CFR 63.654(g)(2)(i)(A) | Periodic Reporting and Recordkeeping Requirements-- internal floating roof tanks – submit results of each tank inspection where failure is detected in control equipment – annual inspection report; definition of failure | Y |  |
| 40 CFR 63.654(g)(2)(i)(B) | Periodic Reporting and Recordkeeping Requirements—internal floating roof tanks - submit results of each tank inspection where failure is detected in control equipment – annual inspection report; Periodic Report requirements | Y |  |
| 40 CFR 63.654(g)(2)(i)(C) | Periodic Reporting and Recordkeeping Requirements—internal floating roof tanks – submit results of each tank inspection where failure is detected in control equipment – annual inspection report; extension documentation | Y |  |
| 40 CFR 63.654(g)(2)(ii) | Periodic Reporting and Recordkeeping Requirements-- internal floating roof tanks – submit results of each tank inspection where failure is detected in control equipment – internal inspection report | Y |  |
| 40 CFR 63.654(g)(2)(ii)(A) | Periodic Reporting and Recordkeeping Requirements-- internal floating roof tanks – submit results of each tank inspection where failure is detected in control equipment – internal inspection report; definition of failure | Y |  |
| 40 CFR 63.654(g)(2)(ii)(B) | Periodic Reporting and Recordkeeping Requirements-- internal floating roof tanks – submit results of each tank inspection where failure is detected in control equipment – internal inspection report; Periodic report requirements | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-126, S-257, S-258 [Basis: 2-1-234.3] | N |  |

2	Seals in S-257 and S-258 were installed prior to 2/1/1993, but these tanks will be treated as zero-gap tanks because the seals have met these requirements when the tanks were considered external floating roof.

| Table IV – B11 Source-Specific Applicable Requirements NSPS Kb Fixed Roof Tanks with Vapor Recovery to Fuel Gas S-360 (Tank 223), S-445 (Tank 271), S-449 (Tank 285) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR FIXED ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.4 | Limited Exemption, Tank Removal From and Return to Service; Use of vapor recovery | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation | Y |  |
| 8-5-306 | Requirements for Approved Emission Control Systems | Y |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1 | Tank Degassing Requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone excess day prohibition | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-603 | Determination of emissions | Y |  |
| 8-5-603.1 | Determination of Emissions; Organic compounds specified in 8-5-306 | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure Vacuum Valve Gas Tight Determination | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) EXEMPTION FOR TANKS VENTED TO FUEL GAS SYSTEM |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR FIXED ROOF TANKS |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.112b(a)(3) | Standard for Volatile Organic Compounds (VOC); Closed vent system and control device | Y |  |
| 40 CFR 60.112b(a)(3)(i) | Standard for Volatile Organic Compounds (VOC); Closed vent system and control device no detectable emissions per 40 CFR 60.485(b) (Subpart VV) | Y |  |
| 40 CFR 60.112b(a)(3)(ii) | Standard for Volatile Organic Compounds (VOC); Closed vent system and control device >= 95% inlet VOC emission reduction | Y |  |
| 40 CFR 60.113b(c) | Testing and Procedures; Closed vent system and control device (not flare) | Y |  |
| 40 CFR 60.113b(c)(1) | Testing and Procedures; Closed vent system and control device (not flare) operating plan submission | Y |  |
| 40 CFR 60.113b(c)(1)(i) | Testing and Procedures; Closed vent system and control device (not flare) operating plan--efficiency demonstration | Y |  |
| 40 CFR 60.113b(c)(1)(ii) | Testing and Procedures; Closed vent system and control device (not flare) operating plan--monitoring parameters | Y |  |
| 40 CFR 60.113b(c)(2) | Testing and Procedures; Closed vent system and control device (not flare) operate in accordance with operating plan | Y |  |
| 40 CFR 60.115b | Reporting and Recordkeeping Requirements; 40 CFR 60.112b(a) tanks; Record retention | Y |  |
| 40 CFR 60.115b(c) | Reporting and Recordkeeping Requirements; Closed vent system and control device (not flare) | Y |  |
| 40 CFR 60.115b(c)(1) | Reporting and Recordkeeping Requirements; Closed vent system and control device (not flare) operating plan copy – Retain for life of control device | Y |  |
| 40 CFR 60.115b(c)(2) | Reporting and Recordkeeping Requirements; Closed vent system and control device (not flare) operating records – Retain for at least 2 years | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(2) | Monitoring of Operations; Determine TVP-crude oil or refined petroleum products | Y |  |
| 40 CFR 60.116b(g) | Monitoring of Operations; Exemption from 40 CFR 60.116b(c) and 40 CFR 60.116b(d) for tanks with closed vent system and control device | Y |  |
| BAAQMD Condition 12130 | APPLICABLE TO S-445 |  |  |
| Part 1 | Requirement to vent emissions to fuel gas system [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 11219 | APPLICABLE TO S-449 |  |  |
| Part 1 | Requirement to vent emissions to fuel gas system [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-360 [Basis: 2-1-234.3] | Y |  |

| Table IV – B12 Source-Specific Applicable Requirements NSPS Kb Fixed Roof Tanks with Vapor Pressure >= 76.6 kPa (11 psia) with Vapor Recovery to Fuel Gas S-446 (Tank 310), S-447 (Tank 311) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR FIXED ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.4 | Limited Exemption, Tank Removal From and Return to Service; Use of vapor recovery | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation | Y |  |
| 8-5-306 | Requirements for Approved Emission Control Systems | Y |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1 | Tank Degassing Requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone excess day prohibition | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-603 | Determination of emissions | Y |  |
| 8-5-603.1 | Determination of Emissions; Organic compounds specified in 8-5-306 | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure Vacuum Valve Gas Tight Determination | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) EXEMPTION FOR TANKS VENTED TO FUEL GAS SYSTEM |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR FIXED ROOF TANKS |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.112b(a)(3) | Standard for Volatile Organic Compounds (VOC); Closed vent system and control device | Y |  |
| 40 CFR 60.112b(a)(3)(i) | Standard for Volatile Organic Compounds (VOC); Closed vent system and control device no detectable emissions per 40 CFR 60.485(b) (Subpart VV) | Y |  |
| 40 CFR 60.112b(a)(3)(ii) | Standard for Volatile Organic Compounds (VOC); Closed vent system and control device >= 95% inlet VOC emission reduction | Y |  |
| 40 CFR 60.112b(b) | Standard for Volatile Organic Compounds (VOC); Requirements for tanks >= 75 cu m and maximum TVP >= 76.6 kPa (11.1 psia) | Y |  |
| 40 CFR 60.112b(b)(1) | Standard for Volatile Organic Compounds (VOC); Closed vent system and control device option per 40 CFR60.112b(a)(3) | Y |  |
| 40 CFR 60.113b(c) | Testing and Procedures; Closed vent system and control device (not flare) | Y |  |
| 40 CFR 60.113b(c)(1) | Testing and Procedures; Closed vent system and control device (not flare) operating plan submission | Y |  |
| 40 CFR 60.113b(c)(1)(i) | Testing and Procedures; Closed vent system and control device (not flare) operating plan--efficiency demonstration | Y |  |
| 40 CFR 60.113b(c)(1)(ii) | Testing and Procedures; Closed vent system and control device (not flare) operating plan--monitoring parameters | Y |  |
| 40 CFR 60.113b(c)(2) | Testing and Procedures; Closed vent system and control device (not flare) operate in accordance with operating plan | Y |  |
| 40 CFR 60.115b | Reporting and Recordkeeping Requirements; 40 CFR 60.112b(a) tanks; Record retention | Y |  |
| 40 CFR 60.115b(c) | Reporting and Recordkeeping Requirements; Closed vent system and control device (not flare) | Y |  |
| 40 CFR 60.115b(c)(1) | Reporting and Recordkeeping Requirements; Closed vent system and control device (not flare) operating plan copy – Retain for life of control device | Y |  |
| 40 CFR 60.115b(c)(2) | Reporting and Recordkeeping Requirements; Closed vent system and control device (not flare) operating records – Retain for at least 2 years | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(2) | Monitoring of Operations; Determine TVP-crude oil or refined petroleum products | Y |  |
| 40 CFR 60.116b(g) | Monitoring of Operations; Exemption from 40 CFR 60.116b(c) and 40 CFR 60.116b(d) for tanks with closed vent system and control device | Y |  |
| BAAQMD Condition 12131 | APPLICABLE TO S-446 |  |  |
| Part 1 | Requirement to vent emissions to fuel gas system [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 12132 | APPLICABLE TO S-447 |  |  |
| Part 1 | Requirement to vent emissions to fuel gas system [Basis: Cumulative Increase] | Y |  |

| Table IV – B13 Source-Specific Applicable Requirements MACT Zero-Gap External Floating Roof Tanks S-97 (Tank 100), S-100 (Tank 103), S-110 (Tank 155), S-111 (Tank 156), S-112 (Tank 157), S-114 (Tank 159), S-115 (Tank 160), S-122 (Tank 167), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), S-150 (Tank 241), S-151 (Tank 242), S-177 (Tank 287), S-178 (Tank 288), S-186 (Tank 298), S-254 (Tank 1001), S-255 (Tank 1002), S-256 (Tank 1003), S-259 (Tank 1006) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8 Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service, Notification | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service, Notification, 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service, Notification, Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service, Tank in compliance prior to notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service, Floating roof tanks | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service, Minimize emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service, Notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service, Satisfy requirements of 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation, Notification | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation, Notification, 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation, Notification, Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation, Tank in compliance prior to start of work. Certified per 8-5-404 | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation, No product movement, Minimize emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation, Not to exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves (applies only to S-110 (Tank 155), S-115 (Tank 160), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), S-178 (Tank 288)) | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure (applies only to S-110 (Tank 155), S-115 (Tank 160), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), S-178 (Tank 288)) | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation (applies only to S-110 (Tank 155), S-115 (Tank 160), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), S-178 (Tank 288)) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320.2 | Tank Fitting Requirements; Floating roof tanks, Projection below liquid surface | Y |  |
| 8-5-320.3 | Tank Fitting Requirements; Floating roof tanks, Gasketed covers, seals, lids | Y |  |
| 8-5-320.3.1 | Tank Fitting Requirements; Floating roof tanks, Gasketed covers, seals, lids - Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank Fitting Requirements; Solid sampling or gauging well requirements--projection below liquid surface | Y |  |
| 8-5-320.4.2 | Tank Fitting Requirements; Solid sampling or gauging well requirements--cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank Fitting Requirements; Solid sampling or gauging well requirements--gap between well and roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary Seal Requirements | Y |  |
| 8-5-321.1 | Primary Seal Requirements; No holes, tears, other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary Seal Requirements; Metallic-shoe-type seal requirements | Y |  |
| 8-5-321.3.1 | Primary Seal Requirements; Metallic-shoe-type seal requirements--geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary Seal Requirements; Metallic-shoe-type seal requirements--welded tanks | Y |  |
| 8-5-322 | Secondary Seal Requirements | Y |  |
| 8-5-322.1 | Secondary Seal Requirements; No holes, tears, other openings | Y |  |
| 8-5-322.2 | Secondary Seal Requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary Seal Requirements; Welded external floating roof tanks with seals installed after 9/4/1985 or welded internal floating roof tanks with seals installed after 2/1/1993 | Y |  |
| 8-5-322.6 | Secondary Seal Requirements; Extent of seal | Y |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1 | Tank Degassing Requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements; Tanks > 75 cubic meters, Approved Emission Control System | Y |  |
| 8-5-328.2 | Tank Degassing Requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves (applies only to S-110 (Tank 155), S-115 (Tank 160), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), S-178 (Tank 288)) | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information Required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid, type of blanket gas, TVP - Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks, Seal Replacement Records - Retain 10 years | Y |  |
| 8-5-503 | Portable Hydrocarbon Detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure Vacuum Valve Gas Tight Determination (applies only to S-110 (Tank 155), S-115 (Tank 160), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), S-178 (Tank 288)) | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(c) | Storage Vessel Provisions -- Reference Control Technology--External floating roof | Y |  |
| 40 CFR 63.119(c)(1) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seals | Y |  |
| 40 CFR 63.119(c)(1)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof double seals required | Y |  |
| 40 CFR 63.119(c)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof primary seal requirements – metallic shoe or liquid-mounted | Y |  |
| 40 CFR 63.119(c)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seal requirements | Y |  |
| 40 CFR 63.119(c)(3) | Storage Vessel Provisions -- Reference Control Technology--External floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(c)(3)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(c)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(c)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(c)(4) | Storage Vessel Provisions -- Reference Control Technology--External Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.120(b) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--External floating roof | Y |  |
| 40 CFR 63.120(b)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap measurement | Y |  |
| 40 CFR 63.120(b)(1)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - primary seal gap measurement – 5 year intervals | Y |  |
| 40 CFR 63.120(b)(1)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - secondary seal gap measurement – annual requirement | Y |  |
| 40 CFR 63.120(b)(1)(iv) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal inspections prior to tank refill with organic HAP after not storing organic HAP for 1 year or longer | Y |  |
| 40 CFR 63.120(b)(2) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods | Y |  |
| 40 CFR 63.120(b)(2)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – roof not resting on legs | Y |  |
| 40 CFR 63.120(b)(2)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – measure gaps around entire circumference of seal and measure width and length of gaps | Y |  |
| 40 CFR 63.120(b)(2)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – determine total surface area of each gap | Y |  |
| 40 CFR 63.120(b)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal gap calculation method – total surface area of primary seal gaps <= 212 cm2 per meter of vessel diameter. Maximum width <= 3.81 cm | Y |  |
| 40 CFR 63.120(b)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal gap calculation method – total surface area of secondary seal gaps <= 21.2 cm2 per meter of vessel diameter. Maximum width <= 1.27 cm | Y |  |
| 40 CFR 63.120(b)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements | Y |  |
| 40 CFR 63.120(b)(5)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – metallic shoe seal – shoe geometry | Y |  |
| 40 CFR 63.120(b)(5)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – no holes, tears, or openings | Y |  |
| 40 CFR 63.120(b)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements | Y |  |
| 40 CFR 63.120(b)(6)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements – location and extent | Y |  |
| 40 CFR 63.120(b)(6)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements - no holes, tears or openings | Y |  |
| 40 CFR 63.120(b)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank | Y |  |
| 40 CFR 63.120(b)(7)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – complete measurements or inspection within 30 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(ii) | Y |  |
| 40 CFR 63.120(b)(7)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – empty and remove vessel from service within 45 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(i). Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(8) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(9) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR seal gap measurement 30 day notification | Y |  |
| 40 CFR 63.120(b)(10) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seals visual inspection each time emptied | Y |  |
| 40 CFR 63.120(b)(10)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)] | Y |  |
| 40 CFR 63.120(b)(10)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied – 30 day notification | Y |  |
| 40 CFR 63.120(b)(10)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(d) | Storage Vessel Provisions -- Recordkeeping--Group 1 External floating roof tank requirements - records of seal gap measurements (date, raw data, and required calculations) | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [EFRs exempt from 63.119(c)(2)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(3) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs | Y |  |
| 40 CFR 63.654(g)(3)(i) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs-document results of each seal gap measurement | Y |  |
| 40 CFR 63.654(g)(3)(ii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – extension documentation | Y |  |
| 40 CFR 63.654(g)(3)(iii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – documentation of failures | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-97, S-100, S-110, S-111, S-112, S-114, S-115, S-122, S-123, S-128, S-177, S-186, S-254, S-255, S-256, S-259 [Basis: 2-1-234.3] | N |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-129, S-150, S-151, S-178 [Basis: 2-1-234.3] | Y |  |

| Table IV – B14 Source-Specific Applicable Requirements NSPS K and NSPS Ka Zero-Gap External Floating Roof Tanks NSPS K - S-334 (Tank 107), NSPS Ka - S-341 (Tank 208), S-342 (Tank 209), S-343 (Tank 210) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service, Notification | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service, Notification, 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service, Notification, Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service, Tank in compliance prior to notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service, Floating roof tanks | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service, Minimize emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service, Notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service, Satisfy requirements of 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation, Notification | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation, Notification, 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation, Notification, Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation, Tank in compliance prior to start of work. Certified per 8-5-404 | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation, No product movement, Minimize emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation, Not to exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank Fitting Requirements; Floating roof tanks | Y |  |
| 8-5-320.2 | Tank Fitting Requirements; Floating roof tanks, Projection below liquid surface | Y |  |
| 8-5-320.3 | Tank Fitting Requirements; Floating roof tanks, Gasketed covers, seals, lids | Y |  |
| 8-5-320.3.1 | Tank Fitting Requirements; Floating roof tanks, Gasketed covers, seals, lids - Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank Fitting Requirements; Solid sampling or gauging well requirements--projection below liquid surface | Y |  |
| 8-5-320.4.2 | Tank Fitting Requirements; Solid sampling or gauging well requirements--cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank Fitting Requirements; Solid sampling or gauging well requirements--gap between well and roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary Seal Requirements | Y |  |
| 8-5-321.1 | Primary Seal Requirements; No holes, tears, other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary Seal Requirements; Metallic-shoe-type seal requirements | Y |  |
| 8-5-321.3.1 | Primary Seal Requirements; Metallic-shoe-type seal requirements--geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary Seal Requirements; Metallic-shoe-type seal requirements--welded tanks | Y |  |
| 8-5-322 | Secondary Seal Requirements | Y |  |
| 8-5-322.1 | Secondary Seal Requirements; No holes, tears, other openings | Y |  |
| 8-5-322.2 | Secondary Seal Requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary Seal Requirements; Welded external floating roof tanks with seals installed after 9/4/1985 or welded internal floating roof tanks with seals installed after 2/1/1993 | Y |  |
| 8-5-322.6 | Secondary Seal Requirements; Extent of seal | Y |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1 | Tank Degassing Requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements; Tanks > 75 cubic meters, Approved Emission Control System | Y |  |
| 8-5-328.2 | Tank Degassing Requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information Required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid, type of blanket gas, TVP - Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks, Seal Replacement Records - Retain 10 years | Y |  |
| 8-5-503 | Portable Hydrocarbon Detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(c) | Storage Vessel Provisions -- Reference Control Technology--External floating roof | Y |  |
| 40 CFR 63.119(c)(1) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seals | Y |  |
| 40 CFR 63.119(c)(1)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof double seals required | Y |  |
| 40 CFR 63.119(c)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof primary seal requirements – metallic shoe or liquid-mounted | Y |  |
| 40 CFR 63.119(c)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seal requirements | Y |  |
| 40 CFR 63.119(c)(3) | Storage Vessel Provisions -- Reference Control Technology--External floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(c)(3)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(c)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(c)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(c)(4) | Storage Vessel Provisions -- Reference Control Technology--External Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.120(b) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--External floating roof | Y |  |
| 40 CFR 63.120(b)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap measurement | Y |  |
| 40 CFR 63.120(b)(1)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - primary seal gap measurement – 5 year intervals | Y |  |
| 40 CFR 63.120(b)(1)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - secondary seal gap measurement – annual requirement | Y |  |
| 40 CFR 63.120(b)(1)(iv) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal inspections prior to tank refill with organic HAP after not storing organic HAP for 1 year or longer | Y |  |
| 40 CFR 63.120(b)(2) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods | Y |  |
| 40 CFR 63.120(b)(2)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – roof not resting on legs | Y |  |
| 40 CFR 63.120(b)(2)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – measure gaps around entire circumference of seal and measure width and length of gaps | Y |  |
| 40 CFR 63.120(b)(2)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – determine total surface area of each gap | Y |  |
| 40 CFR 63.120(b)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal gap calculation method – total surface area of primary seal gaps <= 212 cm2 per meter of vessel diameter. Maximum width <= 3.81 cm | Y |  |
| 40 CFR 63.120(b)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal gap calculation method – total surface area of secondary seal gaps <= 21.2 cm2 per meter of vessel diameter. Maximum width <= 1.27 cm | Y |  |
| 40 CFR 63.120(b)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements | Y |  |
| 40 CFR 63.120(b)(5)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – metallic shoe seal – shoe geometry | Y |  |
| 40 CFR 63.120(b)(5)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – no holes, tears, or openings | Y |  |
| 40 CFR 63.120(b)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements | Y |  |
| 40 CFR 63.120(b)(6)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements – location and extent | Y |  |
| 40 CFR 63.120(b)(6)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements - no holes, tears or openings | Y |  |
| 40 CFR 63.120(b)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank | Y |  |
| 40 CFR 63.120(b)(7)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – complete measurements or inspection within 30 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(ii) | Y |  |
| 40 CFR 63.120(b)(7)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – empty and remove vessel from service within 45 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(i). Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(8) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(9) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR seal gap measurement 30 day notification | Y |  |
| 40 CFR 63.120(b)(10) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seals visual inspection each time emptied | Y |  |
| 40 CFR 63.120(b)(10)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e) | Y |  |
| 40 CFR 63.120(b)(10)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied – 30 day notification | Y |  |
| 40 CFR 63.120(b)(10)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(d) | Storage Vessel Provisions -- Recordkeeping--Group 1 External floating roof tank requirements - records of seal gap measurements (date, raw data, and required calculations) | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS ALSO SUBJECT TO NSPS K OR Ka |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(n)(5) | Applicability and Designation of Affected Source Overlap for Storage Vessels— Group 1 vessel also subject to NSPS K or Ka only subject to 40 CFR 63 Subpart CC | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [EFRs exempt from 63.119(c)(2)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(3) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs | Y |  |
| 40 CFR 63.654(g)(3)(i) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs-document results of each seal gap measurement | Y |  |
| 40 CFR 63.654(g)(3)(ii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – extension documentation | Y |  |
| 40 CFR 63.654(g)(3)(iii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – documentation of failures | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |
| NSPS Title 40 Part 60 Subpart K | NSPS Subpart K for Tanks (4/4/1980) APPLIES TO S-334 (Tank 107) |  |  |
| 40 CFR 60.110(a) | Applicability and Designation of Affected Facility; Affected facility | Y |  |
| 40 CFR 60.110(c)(2) | Applicability and Designation of Affected Facility-->65,000 gal after 6/11/1973 and before 5/19/1978. | Y |  |
| NSPS Title 40 Part 60 Subpart Ka | NSPS Subpart Ka for Tanks (12/14/2000) APPLIES TO S-341 (Tank 208), S-342 (Tank 209), S-343 (Tank 210) |  |  |
| 40 CFR 60.110a(a) | Applicability and Designation of Affected Facility | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-334 [Basis: 2-1-234.3] | N |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-341, S-342, S-343 [Basis: 2-1-234.3] | Y |  |

| Table IV – B15 Source-Specific Applicable Requirements MACT Fixed Roof Tanks with Vapor Recovery to Fuel Gas S-139 (Tank 204), S-140 (Tank 205), S-182 (Tank 294) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR FIXED ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.4 | Limited Exemption, Tank Removal From and Return to Service; Use of vapor recovery | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation | Y |  |
| 8-5-306 | Requirements for Approved Emission Control Systems | Y |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1 | Tank Degassing Requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassingrequirements; Ozone excess day prohibition | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-603 | Determination of emissions | Y |  |
| 8-5-603.1 | Determination of Emissions; Organic compounds specified in 8-5-306 | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure Vacuum Valve Gas Tight Determination | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) EXEMPTION FOR TANKS VENTED TO FUEL GAS SYSTEM |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| NSPS Title 40 Part 60 Subpart K | NSPS Subpart K for Tanks (4/4/1980) EXEMPTION FOR TANKS NOT CONTAINING PETROLEUM LIQUIDS (Applicable to S-139 only) |  |  |
| 40 CFR 60.111(b) | Definitions: Petroleum liquids | Y |  |
| BAAQMD Condition 13184 | APPLICABLE TO S-182 |  |  |
| Part 1 | Requirement to vent emissions to fuel gas system [Basis: Cumulative Increase] | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-139, S-140 [Basis: 2-1-234.3] | N |  |

| Table IV – B16 Source-Specific Applicable Requirements MACT Zero-Gap External Floating Roof Wastewater Slop Oil Tank S-133 (Tank 193) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8 Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service, Notification | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service, Notification, 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service, Notification, Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service, Tank in compliance prior to notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service, Floating roof tanks | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service, Minimize emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service, Notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service, Satisfy requirements of 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation, Notification | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation, Notification, 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation, Notification, Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation, Tank in compliance prior to start of work. Certified per 8-5-404 | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation, No product movement, Minimize emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation, Not to exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320.2 | Tank Fitting Requirements; Floating roof tanks, Projection below liquid surface | Y |  |
| 8-5-320.3 | Tank Fitting Requirements; Floating roof tanks, Gasketed covers, seals, lids | Y |  |
| 8-5-320.3.1 | Tank Fitting Requirements; Floating roof tanks, Gasketed covers, seals, lids - Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank Fitting Requirements; Solid sampling or gauging well requirements--projection below liquid surface | Y |  |
| 8-5-320.4.2 | Tank Fitting Requirements; Solid sampling or gauging well requirements--cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank Fitting Requirements; Solid sampling or gauging well requirements--gap between well and roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary Seal Requirements | Y |  |
| 8-5-321.1 | Primary Seal Requirements; No holes, tears, other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary Seal Requirements; Metallic-shoe-type seal requirements | Y |  |
| 8-5-321.3.1 | Primary Seal Requirements; Metallic-shoe-type seal requirements--geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary Seal Requirements; Metallic-shoe-type seal requirements--welded tanks | Y |  |
| 8-5-322 | Secondary Seal Requirements | Y |  |
| 8-5-322.1 | Secondary Seal Requirements; No holes, tears, other openings | Y |  |
| 8-5-322.2 | Secondary Seal Requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary Seal Requirements; Welded external floating roof tanks with seals installed after 9/4/1985 or welded internal floating roof tanks with seals installed after 2/1/1993 | Y |  |
| 8-5-322.6 | Secondary Seal Requirements; Extent of seal | Y |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1 | Tank Degassing Requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements; Tanks > 75 cubic meters, Approved Emission Control System | Y |  |
| 8-5-328.2 | Tank Degassing Requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information Required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid, type of blanket gas, TVP - Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks, Seal Replacement Records - Retain 10 years | Y |  |
| 8-5-503 | Portable Hydrocarbon Detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure Vacuum Valve Gas Tight Determination | Y |  |
| BAAQMD · Regulation 8, Rule 8 | Organic Compounds, Wastewater (Oil-Water Separators) (6/15/1994) REQUIREMENTS FOR SLOP OIL VESSELS |  |  |
| 8-8-113 | Exemption, Secondary Wastewater Treatment Processes and Stormwater Sewer Systems (segregated) are exempt from 8-8-301, 8-8-302, 8-8-306, 8-8-308 | Y |  |
| 8-8-303 | Standards; Gauging and Sampling Devices | Y |  |
| 8-8-305 | Standards: Oil-Water Separator and/or Air Flotation Unit Slop Oil Vessels | Y |  |
| 8-8-305.1 | Standards: Oil-Water Separator and/or Air Flotation Unit Slop Oil Vessels – fixed cover requirements | Y |  |
| 8-8-503 | Monitoring and Records; Inspection and Records | Y |  |
| 8-8-504 | Monitoring and Records; Portable Hydrocarbon Detector | Y |  |
| 8-8-603 | Manual of Procedures; Inspection procedures | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(c) | Storage Vessel Provisions -- Reference Control Technology--External floating roof | Y |  |
| 40 CFR 63.119(c)(1) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seals | Y |  |
| 40 CFR 63.119(c)(1)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof double seals required | Y |  |
| 40 CFR 63.119(c)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof primary seal requirements – metallic shoe or liquid-mounted | Y |  |
| 40 CFR 63.119(c)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seal requirements | Y |  |
| 40 CFR 63.119(c)(3) | Storage Vessel Provisions -- Reference Control Technology--External floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(c)(3)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(c)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(c)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(c)(4) | Storage Vessel Provisions -- Reference Control Technology--External Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.120(b) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--External floating roof | Y |  |
| 40 CFR 63.120(b)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap measurement | Y |  |
| 40 CFR 63.120(b)(1)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - primary seal gap measurement – 5 year intervals | Y |  |
| 40 CFR 63.120(b)(1)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - secondary seal gap measurement – annual requirement | Y |  |
| 40 CFR 63.120(b)(1)(iv) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal inspections prior to tank refill with organic HAP after not storing organic HAP for 1 year or longer | Y |  |
| 40 CFR 63.120(b)(2) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods | Y |  |
| 40 CFR 63.120(b)(2)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – roof not resting on legs | Y |  |
| 40 CFR 63.120(b)(2)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – measure gaps around entire circumference of seal and measure width and length of gaps | Y |  |
| 40 CFR 63.120(b)(2)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – determine total surface area of each gap | Y |  |
| 40 CFR 63.120(b)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal gap calculation method – total surface area of primary seal gaps <= 212 cm2 per meter of vessel diameter. Maximum width <= 3.81 cm | Y |  |
| 40 CFR 63.120(b)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal gap calculation method – total surface area of secondary seal gaps <= 21.2 cm2 per meter of vessel diameter. Maximum width <= 1.27 cm | Y |  |
| 40 CFR 63.120(b)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements | Y |  |
| 40 CFR 63.120(b)(5)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – metallic shoe seal – shoe geometry | Y |  |
| 40 CFR 63.120(b)(5)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – no holes, tears, or openings | Y |  |
| 40 CFR 63.120(b)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements | Y |  |
| 40 CFR 63.120(b)(6)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements – location and extent | Y |  |
| 40 CFR 63.120(b)(6)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements - no holes, tears or openings | Y |  |
| 40 CFR 63.120(b)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank | Y |  |
| 40 CFR 63.120(b)(7)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – complete measurements or inspection within 30 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(ii) | Y |  |
| 40 CFR 63.120(b)(7)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – empty and remove vessel from service within 45 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(i). Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(8) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(9) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR seal gap measurement 30 day notification | Y |  |
| 40 CFR 63.120(b)(10) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seals visual inspection each time emptied | Y |  |
| 40 CFR 63.120(b)(10)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)] | Y |  |
| 40 CFR 63.120(b)(10)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied – 30 day notification | Y |  |
| 40 CFR 63.120(b)(10)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(d) | Storage Vessel Provisions -- Recordkeeping--Group 1 External floating roof tank requirements - records of seal gap measurements (date, raw data, and required calculations) | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [EFRs exempt from 63.119(c)(2)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(3) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs | Y |  |
| 40 CFR 63.654(g)(3)(i) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs-document results of each seal gap measurement | Y |  |
| 40 CFR 63.654(g)(3)(ii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – extension documentation | Y |  |
| 40 CFR 63.654(g)(3)(iii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – documentation of failures | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-133 [Basis: 2-1-234.3] | Y |  |

| Table IV – B17 Source-Specific Applicable Requirements NSPS Ka External Floating Roof Tank w/o Zero-Gap Seals S-340 (Tank 108) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements – Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Projection below surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – | Y |  |
| 8-5-320.3.1 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary Seal Requirements; Metallic-shoe-type seal requirements | Y |  |
| 8-5-321.3.1 | Primary Seal Requirements; Metallic-shoe-type seal requirements--geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary Seal Requirements; Metallic-shoe-type seal requirements--welded tanks | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.3 | Secondary seal requirements; Seal gaps (applicable as long as secondary seal is not a zero-gap seal as defined in 8-5-322.5) | Y |  |
| 8-5-322.5 | Secondary seal requirements; Gap for welded tanks with seal installed after September 4, 1985 (becomes applicable when secondary seal is considered newly installed and subject to zero-gap seal gap requirements) | Y |  |
| 8-5-322.6 | Secondary seal requirements; extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(c) | Storage Vessel Provisions -- Reference Control Technology--External floating roof | Y |  |
| 40 CFR 63.119(c)(1) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seals | Y |  |
| 40 CFR 63.119(c)(1)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof double seals required | Y |  |
| 40 CFR 63.119(c)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof primary seal requirements – metallic shoe or liquid-mounted | Y |  |
| 40 CFR 63.119(c)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seal requirements | Y |  |
| 40 CFR 63.119(c)(3) | Storage Vessel Provisions -- Reference Control Technology--External floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(c)(3)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(c)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(c)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(c)(4) | Storage Vessel Provisions -- Reference Control Technology--External Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.120(b) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--External floating roof | Y |  |
| 40 CFR 63.120(b)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap measurement | Y |  |
| 40 CFR 63.120(b)(1)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - primary seal gap measurement – 5 year intervals | Y |  |
| 40 CFR 63.120(b)(1)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - secondary seal gap measurement – annual requirement | Y |  |
| 40 CFR 63.120(b)(1)(iv) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal inspections prior to tank refill with organic HAP after not storing organic HAP for 1 year or longer | Y |  |
| 40 CFR 63.120(b)(2) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods | Y |  |
| 40 CFR 63.120(b)(2)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – roof not resting on legs | Y |  |
| 40 CFR 63.120(b)(2)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – measure gaps around entire circumference of seal and measure width and length of gaps | Y |  |
| 40 CFR 63.120(b)(2)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – determine total surface area of each gap | Y |  |
| 40 CFR 63.120(b)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal gap calculation method – total surface area of primary seal gaps <= 212 cm2 per meter of vessel diameter. Maximum width <= 3.81 cm | Y |  |
| 40 CFR 63.120(b)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal gap calculation method – total surface area of secondary seal gaps <= 21.2 cm2 per meter of vessel diameter. Maximum width <= 1.27 cm | Y |  |
| 40 CFR 63.120(b)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements | Y |  |
| 40 CFR 63.120(b)(5)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – metallic shoe seal – shoe geometry | Y |  |
| 40 CFR 63.120(b)(5)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – no holes, tears, or openings | Y |  |
| 40 CFR 63.120(b)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements | Y |  |
| 40 CFR 63.120(b)(6)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements – location and extent | Y |  |
| 40 CFR 63.120(b)(6)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements - no holes, tears or openings | Y |  |
| 40 CFR 63.120(b)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank | Y |  |
| 40 CFR 63.120(b)(7)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – complete measurements or inspection within 30 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(ii) | Y |  |
| 40 CFR 63.120(b)(7)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – empty and remove vessel from service within 45 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(i). Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(8) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(9) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR seal gap measurement 30 day notification | Y |  |
| 40 CFR 63.120(b)(10) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seals visual inspection each time emptied | Y |  |
| 40 CFR 63.120(b)(10)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)] | Y |  |
| 40 CFR 63.120(b)(10)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied – 30 day notification | Y |  |
| 40 CFR 63.120(b)(10)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(d) | Storage Vessel Provisions -- Recordkeeping--Group 1 External floating roof tank requirements - records of seal gap measurements (date, raw data, and required calculations) | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS ALSO SUBJECT TO NSPS K or Ka |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(n)(5) | Applicability and Designation of Affected Source Overlap for Storage Vessels— Group 1 vessel also subject to NSPS K or Ka only subject to 40 CFR 63 Subpart CC | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [EFRs exempt from 63.119(c)(2)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(3) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs | Y |  |
| 40 CFR 63.654(g)(3)(i) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs-document results of each seal gap measurement | Y |  |
| 40 CFR 63.654(g)(3)(ii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – extension documentation | Y |  |
| 40 CFR 63.654(g)(3)(iii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – documentation of failures | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |
| NSPS Title 40 Part 60 Subpart Ka | NSPS Subpart Ka for Tanks (12/14/2000) |  |  |
| 40 CFR 60.110a(a) | Applicability and Designation of Affected Facility | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-340 [Basis: 2-1-234.3] | Y |  |

| Table IV – B18 Source-Specific Applicable Requirements MACT External Floating Roof Tanks w/o Zero-Gap Seals S-107 (Tank 150), S-113 (Tank 158), S-124 (Tank 169), S-125 (Tank 170), S-183 (Tank 295), S-184 (Tank 296), S-261 (Tank 1010) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves (applicable to S-107 (Tank 150), S-113 (Tank 158), S-125 (Tank 170)) | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure (applicable to S-107 (Tank 150), S-113 (Tank 158), S-125 (Tank 170)) | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation (applicable to S-107 (Tank 150), S-113 (Tank 158), S-125 (Tank 170)) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements – Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Projection below surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – | Y |  |
| 8-5-320.3.1 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary Seal Requirements; Metallic-shoe-type seal requirements | Y |  |
| 8-5-321.3.1 | Primary Seal Requirements; Metallic-shoe-type seal requirements--geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary Seal Requirements; Metallic-shoe-type seal requirements--welded tanks | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.3 | Secondary seal requirements; Seal gaps (applicable as long as secondary seal is not zero-gap seal as defined in 8-5-322.5) | Y |  |
| 8-5-322.5 | Secondary seal requirements; Gap for welded tanks with seal installed after September 4, 1985 (becomes applicable when secondary seal is considered newly installed and subject to zero-gap seal gap requirements) | Y |  |
| 8-5-322.6 | Secondary seal requirements; extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves (applicable to S-107 (Tank 150), S-113 (Tank 158), S-125 (Tank 170)) | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure-Vacuum Valve Gas Tight Determination (applicable to S-107 (Tank 150), S-113 (Tank 158), S-125 (Tank 170)) | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(c) | Storage Vessel Provisions -- Reference Control Technology--External floating roof | Y |  |
| 40 CFR 63.119(c)(1) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seals | Y |  |
| 40 CFR 63.119(c)(1)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof double seals required | Y |  |
| 40 CFR 63.119(c)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof primary seal requirements – metallic shoe or liquid-mounted | Y |  |
| 40 CFR 63.119(c)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seal requirements | Y |  |
| 40 CFR 63.119(c)(3) | Storage Vessel Provisions -- Reference Control Technology--External floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(c)(3)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(c)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(c)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(c)(4) | Storage Vessel Provisions -- Reference Control Technology--External Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.120(b) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--External floating roof | Y |  |
| 40 CFR 63.120(b)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap measurement | Y |  |
| 40 CFR 63.120(b)(1)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - primary seal gap measurement – 5 year intervals | Y |  |
| 40 CFR 63.120(b)(1)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - secondary seal gap measurement – annual requirement | Y |  |
| 40 CFR 63.120(b)(1)(iv) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal inspections prior to tank refill with organic HAP after not storing organic HAP for 1 year or longer | Y |  |
| 40 CFR 63.120(b)(2) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods | Y |  |
| 40 CFR 63.120(b)(2)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – roof not resting on legs | Y |  |
| 40 CFR 63.120(b)(2)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – measure gaps around entire circumference of seal and measure width and length of gaps | Y |  |
| 40 CFR 63.120(b)(2)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – determine total surface area of each gap | Y |  |
| 40 CFR 63.120(b)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal gap calculation method – total surface area of primary seal gaps <= 212 cm2 per meter of vessel diameter. Maximum width <= 3.81 cm | Y |  |
| 40 CFR 63.120(b)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal gap calculation method – total surface area of secondary seal gaps <= 21.2 cm2 per meter of vessel diameter. Maximum width <= 1.27 cm | Y |  |
| 40 CFR 63.120(b)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements | Y |  |
| 40 CFR 63.120(b)(5)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – metallic shoe seal – shoe geometry | Y |  |
| 40 CFR 63.120(b)(5)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – no holes, tears, or openings | Y |  |
| 40 CFR 63.120(b)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements | Y |  |
| 40 CFR 63.120(b)(6)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements – location and extent | Y |  |
| 40 CFR 63.120(b)(6)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements - no holes, tears or openings | Y |  |
| 40 CFR 63.120(b)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank | Y |  |
| 40 CFR 63.120(b)(7)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – complete measurements or inspection within 30 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(ii) | Y |  |
| 40 CFR 63.120(b)(7)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – empty and remove vessel from service within 45 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(i). Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(8) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(9) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR seal gap measurement 30 day notification | Y |  |
| 40 CFR 63.120(b)(10) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seals visual inspection each time emptied | Y |  |
| 40 CFR 63.120(b)(10)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)] | Y |  |
| 40 CFR 63.120(b)(10)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied – 30 day notification | Y |  |
| 40 CFR 63.120(b)(10)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(d) | Storage Vessel Provisions -- Recordkeeping--Group 1 External floating roof tank requirements - records of seal gap measurements (date, raw data, and required calculations) | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [EFRs exempt from 63.119(c)(2)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(3) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs | Y |  |
| 40 CFR 63.654(g)(3)(i) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs-document results of each seal gap measurement | Y |  |
| 40 CFR 63.654(g)(3)(ii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – extension documentation | Y |  |
| 40 CFR 63.654(g)(3)(iii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – documentation of failures | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-107, S-113, S-124, S-125, S-261 [Basis: 2-1-234.3] | N |  |
| BAAQMD Condition 20989, Part A | Throughput limits for sources S-183, S-184 [Basis: 2-1-234.3] | Y |  |

| Table IV – B19 Source-Specific Applicable Requirements Riveted MACT External Floating Roof Tank S-216 (Tank 695a) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements – Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Projection below surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – | Y |  |
| 8-5-320.3.1 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary seal requirements; Metallic shoe type seal requirements | Y |  |
| 8-5-321.3.1 | Primary seal requirements; Metallic shoe type seal requirements Geometry of shoe | Y |  |
| 8-5-321.3.3 | Primary seal requirements; Metallic shoe type seal requirements: Gaps for riveted tanks | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.3 | Secondary seal requirements; Seal gaps | Y |  |
| 8-5-322.4 | Secondary seal requirements; Riveted tanks | Y |  |
| 8-5-322.6 | Secondary seal requirements; extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(c) | Storage Vessel Provisions -- Reference Control Technology--External floating roof | Y |  |
| 40 CFR 63.119(c)(1) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seals | Y |  |
| 40 CFR 63.119(c)(1)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof double seals required | Y |  |
| 40 CFR 63.119(c)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof primary seal requirements – metallic shoe or liquid-mounted | Y |  |
| 40 CFR 63.119(c)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seal requirements | Y |  |
| 40 CFR 63.119(c)(3) | Storage Vessel Provisions -- Reference Control Technology--External floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(c)(3)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(c)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(c)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(c)(4) | Storage Vessel Provisions -- Reference Control Technology--External Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.120(b) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--External floating roof | Y |  |
| 40 CFR 63.120(b)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap measurement | Y |  |
| 40 CFR 63.120(b)(1)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - primary seal gap measurement – 5 year intervals | Y |  |
| 40 CFR 63.120(b)(1)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - secondary seal gap measurement – annual requirement | Y |  |
| 40 CFR 63.120(b)(1)(iv) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal inspections prior to tank refill with organic HAP after not storing organic HAP for 1 year or longer | Y |  |
| 40 CFR 63.120(b)(2) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods | Y |  |
| 40 CFR 63.120(b)(2)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – roof not resting on legs | Y |  |
| 40 CFR 63.120(b)(2)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – measure gaps around entire circumference of seal and measure width and length of gaps | Y |  |
| 40 CFR 63.120(b)(2)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – determine total surface area of each gap | Y |  |
| 40 CFR 63.120(b)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal gap calculation method – total surface area of primary seal gaps <= 212 cm2 per meter of vessel diameter. Maximum width <= 3.81 cm | Y |  |
| 40 CFR 63.120(b)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal gap calculation method – total surface area of secondary seal gaps <= 21.2 cm2 per meter of vessel diameter. Maximum width <= 1.27 cm | Y |  |
| 40 CFR 63.120(b)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements | Y |  |
| 40 CFR 63.120(b)(5)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – metallic shoe seal – shoe geometry | Y |  |
| 40 CFR 63.120(b)(5)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – no holes, tears, or openings | Y |  |
| 40 CFR 63.120(b)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements | Y |  |
| 40 CFR 63.120(b)(6)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements – location and extent | Y |  |
| 40 CFR 63.120(b)(6)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements - no holes, tears or openings | Y |  |
| 40 CFR 63.120(b)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank | Y |  |
| 40 CFR 63.120(b)(7)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – complete measurements or inspection within 30 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(ii) | Y |  |
| 40 CFR 63.120(b)(7)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – empty and remove vessel from service within 45 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(i). Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(8) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(9) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR seal gap measurement 30 day notification | Y |  |
| 40 CFR 63.120(b)(10) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seals visual inspection each time emptied | Y |  |
| 40 CFR 63.120(b)(10)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)] | Y |  |
| 40 CFR 63.120(b)(10)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied – 30 day notification | Y |  |
| 40 CFR 63.120(b)(10)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(d) | Storage Vessel Provisions -- Recordkeeping--Group 1 External floating roof tank requirements - records of seal gap measurements (date, raw data, and required calculations) | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [EFRs exempt from 63.119(c)(2)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(3) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs | Y |  |
| 40 CFR 63.654(g)(3)(i) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs-document results of each seal gap measurement | Y |  |
| 40 CFR 63.654(g)(3)(ii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – extension documentation | Y |  |
| 40 CFR 63.654(g)(3)(iii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – documentation of failures | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-216 [Basis: 2-1-234.3] | N |  |

| Table IV – B20 Source-Specific Applicable Requirements MACT External Floating Roof Wastewater Slop Oil Tank w/o Zero-Gap Seals S-134 (Tank 194) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service; Floating roof tanks - continuous and quick filling, emptying and refilling | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320 | Tank fitting requirements – Floating roof tanks | Y |  |
| 8-5-320.2 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Projection below surface except p/v valves and vacuum breaker vents | Y |  |
| 8-5-320.3 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – | Y |  |
| 8-5-320.3.1 | Tank fitting requirements – Floating roof tanks, Gasketed covers, seals, lids – Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Projection below the liquid surface | Y |  |
| 8-5-320.4.2 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank fitting requirements; Floating roof tanks; Solid sampling or gauging wells; Gap between the well and the roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary seal requirements | Y |  |
| 8-5-321.1 | Primary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary Seal Requirements; Metallic-shoe-type seal requirements | Y |  |
| 8-5-321.3.1 | Primary Seal Requirements; Metallic-shoe-type seal requirements--geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary Seal Requirements; Metallic-shoe-type seal requirements--welded tanks | Y |  |
| 8-5-322 | Secondary seal requirements | Y |  |
| 8-5-322.1 | Secondary seal requirements; No holes, tears, or other openings | Y |  |
| 8-5-322.2 | Secondary seal requirements; Insertion of probes | Y |  |
| 8-5-322.3 | Secondary seal requirements; Seal gaps (applicable as long as secondary seal is not zero-gap seal as defined in 8-5-322.5) | Y |  |
| 8-5-322.5 | Secondary seal requirements; Gap for welded tanks with seal installed after September 4, 1985 (becomes applicable when secondary seal is considered newly installed and subject to zero-gap seal gap requirements) | Y |  |
| 8-5-322.6 | Secondary seal requirements; extent of seal | Y |  |
| 8-5-328 | Tank degassing requirements | Y |  |
| 8-5-328.1 | Tank degassing requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank degassing requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; true vapor pressure; Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks; Seal Replacement Records – Retain 10 years | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure-Vacuum Valve Gas Tight Determination | Y |  |
| BAAQMD · Regulation 8, Rule 8 | Organic Compounds, Wastewater (Oil-Water Separators) (6/15/1994) REQUIREMENTS FOR SLOP OIL VESSELS |  |  |
| 8-8-113 | Exemption, Secondary Wastewater Treatment Processes and Stormwater Sewer Systems (segregated) are exempt from 8-8-301, 8-8-302, 8-8-306, 8-8-308 | Y |  |
| 8-8-303 | Standards; Gauging and Sampling Devices | Y |  |
| 8-8-305 | Standards: Oil-Water Separator and/or Air Flotation Unit Slop Oil Vessels | Y |  |
| 8-8-305.1 | Standards: Oil-Water Separator and/or Air Flotation Unit Slop Oil Vessels – fixed cover requirements | Y |  |
| 8-8-503 | Monitoring and Records; Inspection and Records | Y |  |
| 8-8-504 | Monitoring and Records; Portable Hydrocarbon Detector | Y |  |
| 8-8-603 | Manual of Procedures; Inspection procedures | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(c) | Storage Vessel Provisions -- Reference Control Technology--External floating roof | Y |  |
| 40 CFR 63.119(c)(1) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seals | Y |  |
| 40 CFR 63.119(c)(1)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof double seals required | Y |  |
| 40 CFR 63.119(c)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof primary seal requirements – metallic shoe or liquid-mounted | Y |  |
| 40 CFR 63.119(c)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seal requirements | Y |  |
| 40 CFR 63.119(c)(3) | Storage Vessel Provisions -- Reference Control Technology--External floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(c)(3)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(c)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(c)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(c)(4) | Storage Vessel Provisions -- Reference Control Technology--External Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.120(b) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--External floating roof | Y |  |
| 40 CFR 63.120(b)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap measurement | Y |  |
| 40 CFR 63.120(b)(1)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - primary seal gap measurement – 5 year intervals | Y |  |
| 40 CFR 63.120(b)(1)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - secondary seal gap measurement – annual requirement | Y |  |
| 40 CFR 63.120(b)(1)(iv) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal inspections prior to tank refill with organic HAP after not storing organic HAP for 1 year or longer | Y |  |
| 40 CFR 63.120(b)(2) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods | Y |  |
| 40 CFR 63.120(b)(2)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – roof not resting on legs | Y |  |
| 40 CFR 63.120(b)(2)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – measure gaps around entire circumference of seal and measure width and length of gaps | Y |  |
| 40 CFR 63.120(b)(2)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – determine total surface area of each gap | Y |  |
| 40 CFR 63.120(b)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal gap calculation method – total surface area of primary seal gaps <= 212 cm2 per meter of vessel diameter. Maximum width <= 3.81 cm | Y |  |
| 40 CFR 63.120(b)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal gap calculation method – total surface area of secondary seal gaps <= 21.2 cm2 per meter of vessel diameter. Maximum width <= 1.27 cm | Y |  |
| 40 CFR 63.120(b)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements | Y |  |
| 40 CFR 63.120(b)(5)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – metallic shoe seal – shoe geometry | Y |  |
| 40 CFR 63.120(b)(5)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – no holes, tears, or openings | Y |  |
| 40 CFR 63.120(b)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements | Y |  |
| 40 CFR 63.120(b)(6)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements – location and extent | Y |  |
| 40 CFR 63.120(b)(6)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements - no holes, tears or openings | Y |  |
| 40 CFR 63.120(b)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank | Y |  |
| 40 CFR 63.120(b)(7)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – complete measurements or inspection within 30 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(ii) | Y |  |
| 40 CFR 63.120(b)(7)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – empty and remove vessel from service within 45 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(i). Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(8) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(9) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR seal gap measurement 30 day notification | Y |  |
| 40 CFR 63.120(b)(10) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seals visual inspection each time emptied | Y |  |
| 40 CFR 63.120(b)(10)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)] | Y |  |
| 40 CFR 63.120(b)(10)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied – 30 day notification | Y |  |
| 40 CFR 63.120(b)(10)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(d) | Storage Vessel Provisions -- Recordkeeping--Group 1 External floating roof tank requirements - records of seal gap measurements (date, raw data, and required calculations) | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [EFRs exempt from 63.119(c)(2)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(3) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs | Y |  |
| 40 CFR 63.654(g)(3)(i) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs-document results of each seal gap measurement | Y |  |
| 40 CFR 63.654(g)(3)(ii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – extension documentation | Y |  |
| 40 CFR 63.654(g)(3)(iii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – documentation of failures | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |
| BAAQMD Condition 20989, Part A | Throughput limits for source S-134 [Basis: 2-1-234.3] | N |  |

| Table IV – B21 Source-Specific Applicable Requirements Exempt Tanks Subject to MACT Recordkeeping S-91 (Tank 73), S-94 (Tank 78), S-98 (Tank 101), S-99 (Tank 102), S-103 (Tank 106), S-120 (Tank 165), S-130 (Tank 188), S-131 (Tank 189), S-132 (Tank 191), S-136 (Tank 201), S-137 (Tank 202), S-138 (Tank 203), S-141 (Tank 213), S-142 (Tank 214), S-143 (Tank 215), S-144 (Tank 216), S-145 (Tank 217), S-148 (Tank 231), S-149 (Tank 232), S-157 (Tank 252), S-162 (Tank 262), S-164 (Tank 264), S-165 (Tank 265), S-166 (Tank 266), S-167 (Tank 268), S-168 (Tank 269), S-169 (Tank 270), S-171 (Tank 273), S-172 (Tank 279), S-173 (Tank 280), S-174 (Tank 281), S-179 (Tank 291), S-180 (Tank 292), S-187 (Tank 299), S-191 (Tank 303), S-192 (Tank 304), S-202 (Tank 521), S-204 (Tank 528), S-205 (Tank 529), S-206 (Tank 530), S-207 (Tank 531), S-209 (Tank 674), S-224 (Tank 746), S-225 (Tank 747), S-226 (Tank 748), S-227 (Tank 749), S-228 (Tank 750), S-229 (Tank 751), S-230 (Tank 752), S-231 (Tank 753), S-236 (Tank 770), S-237 (Tank 771), S-240 (Tank 774), S-241 (Tank 775), S-260 (Tank 1009), S-262 (Tank 1011), S-263 (Tank 1012), S-266 (Tank 1345), S-267 (Tank 1346), S-286 (F3), S-287 (F10), S-293 (F805) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.119(a)(3) | Storage Vessel Provisions – Reference Control Technology – Group 2 storage vessels comply only with recordkeeping requirements in 40 CFR 63.123(a) | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions – Recordkeeping – Group 2 storage vessels only required to keep tank dimensions and capacity analysis. Retain for life of source. | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Keep records specified in 40 CFR 63.123 | Y |  |
| 40 CFR 63.654(i)(1) (iv) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Data and assumptions used to determine Group 2 classification | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements--Recordkeeping--Record retention – 5 years | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

| Table IV – B22 Source-Specific Applicable Requirements Exempt Fixed Roof Tanks with Vapor Recovery to Fuel Gas S-158 (Tank 258), S-175 (Tank 284) |
| --- |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) EXEMPTION FOR TANKS VENTED TO FUEL GAS SYSTEM |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

| Table IV – B23A Source-Specific Applicable Requirements Exempt External Floating Roof Tanks Subject to MACT Recordkeeping (note 2) but with Group I MACT Flexibility S-108 (Tank 153), S-109 (Tank 154), S-127 (Tank 173) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.119(a)(3) | Storage Vessel Provisions – Reference Control Technology – Group 2 storage vessels comply only with recordkeeping requirements in 40 CFR 63.123(a) | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions – Recordkeeping – Group 2 storage vessels only required to keep tank dimensions and capacity analysis. Retain for life of source. | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Keep records specified in 40 CFR 63.123 | Y |  |
| 40 CFR 63.654(i)(1)(iv) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Data and assumptions used to determine Group 2 classification | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements--Recordkeeping--Record retention – 5 years | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

2.	Sources S-108, S-109, and S-127 currently contain low vapor pressure liquids, are exempt from BAAQMD permitting requirements, and fall under the MACT Group II requirements for recordkeeping. However, these tanks may be operated as MACT Group I tanks in the future. Table B23A shows the appropriate applicability for these tanks as MACT Group II tanks. Table B23B shows the appropriate applicability for these tanks as MACT Group I tanks including the BAAQMD Regulation 8 Rule 5 requirements for zero-gap secondary seals.

| Table IV – B23B Source-Specific Applicable Requirements Exempt External Floating Roof Tanks Subject to MACT Recordkeeping (note 2) but with Group I MACT Flexibility S-108 (Tank 153), S-109 (Tank 154), S-127 (Tank 173) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8 Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service, Notification | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service, Notification, 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service, Notification, Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service, Tank in compliance prior to notification | Y |  |
| 8-5-111.3 | Limited Exemption, Tank Removal From and Return to Service, Floating roof tanks | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service, Minimize emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service, Notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service, Satisfy requirements of 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation, Notification | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation, Notification, 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation, Notification, Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation, Tank in compliance prior to start of work. Certified per 8-5-404 | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation, No product movement, Minimize emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation, Not to exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-304 | Requirements for External Floating Roofs | Y |  |
| 8-5-304.1 | Requirements for External Floating Roofs; Tank fitting requirements | Y |  |
| 8-5-304.2 | Requirements for External Floating Roofs; Primary seal requirements | Y |  |
| 8-5-304.3 | Requirements for External Floating Roofs; Secondary seal requirements | Y |  |
| 8-5-304.4 | Requirements for External Floating Roofs; Floating roof requirements | Y |  |
| 8-5-320.2 | Tank Fitting Requirements; Floating roof tanks, Projection below liquid surface | Y |  |
| 8-5-320.3 | Tank Fitting Requirements; Floating roof tanks, Gasketed covers, seals, lids | Y |  |
| 8-5-320.3.1 | Tank Fitting Requirements; Floating roof tanks, Gasketed covers, seals, lids - Gap requirements | Y |  |
| 8-5-320.4 | Tank Fitting Requirements; Solid sampling or gauging well requirements in floating roof tanks | Y |  |
| 8-5-320.4.1 | Tank Fitting Requirements; Solid sampling or gauging well requirements--projection below liquid surface | Y |  |
| 8-5-320.4.2 | Tank Fitting Requirements; Solid sampling or gauging well requirements--cover, seal, or lid | Y |  |
| 8-5-320.4.3 | Tank Fitting Requirements; Solid sampling or gauging well requirements--gap between well and roof | Y |  |
| 8-5-320.6 | Tank Fitting Requirements; Emergency roof drain | Y |  |
| 8-5-321 | Primary Seal Requirements | Y |  |
| 8-5-321.1 | Primary Seal Requirements; No holes, tears, other openings | Y |  |
| 8-5-321.2 | Primary seal requirements; The seal shall be metallic shoe or liquid mounted except as provided in 8-5-305.1.3 | Y |  |
| 8-5-321.3 | Primary Seal Requirements; Metallic-shoe-type seal requirements | Y |  |
| 8-5-321.3.1 | Primary Seal Requirements; Metallic-shoe-type seal requirements--geometry of shoe | Y |  |
| 8-5-321.3.2 | Primary Seal Requirements; Metallic-shoe-type seal requirements--welded tanks | Y |  |
| 8-5-322 | Secondary Seal Requirements | Y |  |
| 8-5-322.1 | Secondary Seal Requirements; No holes, tears, other openings | Y |  |
| 8-5-322.2 | Secondary Seal Requirements; Insertion of probes | Y |  |
| 8-5-322.5 | Secondary Seal Requirements; Welded external floating roof tanks with seals installed after 9/4/1985 or welded internal floating roof tanks with seals installed after 2/1/1993 | Y |  |
| 8-5-322.6 | Secondary Seal Requirements; Extent of seal | Y |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1 | Tank Degassing Requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements; Tanks > 75 cubic meters, Approved Emission Control System | Y |  |
| 8-5-328.2 | Tank Degassing Requirements; Ozone Excess Day Prohibition | Y |  |
| 8-5-401 | Inspection Requirements for External Floating Roof Tanks | Y |  |
| 8-5-401.1 | Inspection Requirements for External Floating Roof Tanks; Primary and Secondary Seal Inspections | Y |  |
| 8-5-401.2 | Inspection Requirements for External Floating Roof Tanks; Tank Fittings Inspections | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-405 | Information Required | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid, type of blanket gas, TVP - Retain 24 months | Y |  |
| 8-5-501.2 | Records; Internal and External Floating Roof Tanks, Seal Replacement Records - Retain 10 years | Y |  |
| 8-5-503 | Portable Hydrocarbon Detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.119(a) | Storage Vessel Provisions -- Reference Control Technology | Y |  |
| 40 CFR 63.119(a)(1) | Storage Vessel Provisions -- Reference Control Technology--Group 1, TVP < 76.6 kPa | Y |  |
| 40 CFR 63.119(c) | Storage Vessel Provisions -- Reference Control Technology--External floating roof | Y |  |
| 40 CFR 63.119(c)(1) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seals | Y |  |
| 40 CFR 63.119(c)(1)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof double seals required | Y |  |
| 40 CFR 63.119(c)(1)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof primary seal requirements – metallic shoe or liquid-mounted | Y |  |
| 40 CFR 63.119(c)(1)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof seal requirements | Y |  |
| 40 CFR 63.119(c)(3) | Storage Vessel Provisions -- Reference Control Technology--External floating roof--Must float on liquid | Y |  |
| 40 CFR 63.119(c)(3)(i) | Storage Vessel Provisions -- Reference Control Technology--External floating roof --Must float on liquid except during initial fill | Y |  |
| 40 CFR 63.119(c)(3)(ii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof-- Must float on liquid except after completely emptied and degassed | Y |  |
| 40 CFR 63.119(c)(3)(iii) | Storage Vessel Provisions -- Reference Control Technology--External floating roof -- Must float on liquid except when completely emptied before refilling | Y |  |
| 40 CFR 63.119(c)(4) | Storage Vessel Provisions -- Reference Control Technology--External Floating Roof Operations, when not floating | Y |  |
| 40 CFR 63.120(b) | Storage Vessel Provisions -- Procedures to Determine Compliance--Compliance Demonstration--External floating roof | Y |  |
| 40 CFR 63.120(b)(1) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap measurement | Y |  |
| 40 CFR 63.120(b)(1)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - primary seal gap measurement – 5 year intervals | Y |  |
| 40 CFR 63.120(b)(1)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR with double seals - secondary seal gap measurement – annual requirement | Y |  |
| 40 CFR 63.120(b)(1)(iv) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal inspections prior to tank refill with organic HAP after not storing organic HAP for 1 year or longer | Y |  |
| 40 CFR 63.120(b)(2) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods | Y |  |
| 40 CFR 63.120(b)(2)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – roof not resting on legs | Y |  |
| 40 CFR 63.120(b)(2)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – measure gaps around entire circumference of seal and measure width and length of gaps | Y |  |
| 40 CFR 63.120(b)(2)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR seal gap determination methods – determine total surface area of each gap | Y |  |
| 40 CFR 63.120(b)(3) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal gap calculation method – total surface area of primary seal gaps <= 212 cm2 per meter of vessel diameter. Maximum width <= 3.81 cm | Y |  |
| 40 CFR 63.120(b)(4) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal gap calculation method – total surface area of secondary seal gaps <= 21.2 cm2 per meter of vessel diameter. Maximum width <= 1.27 cm | Y |  |
| 40 CFR 63.120(b)(5) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements | Y |  |
| 40 CFR 63.120(b)(5)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – metallic shoe seal – shoe geometry | Y |  |
| 40 CFR 63.120(b)(5)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR primary seal additional requirements – no holes, tears, or openings | Y |  |
| 40 CFR 63.120(b)(6) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements | Y |  |
| 40 CFR 63.120(b)(6)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements – location and extent | Y |  |
| 40 CFR 63.120(b)(6)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR secondary seal requirements - no holes, tears or openings | Y |  |
| 40 CFR 63.120(b)(7) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank | Y |  |
| 40 CFR 63.120(b)(7)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – complete measurements or inspection within 30 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(ii) | Y |  |
| 40 CFR 63.120(b)(7)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR unsafe to perform seal measurements or inspect the tank – empty and remove vessel from service within 45 days after determining roof is unsafe or comply with 40 CFR 63.120(b)(7)(i). Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(8) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR Repairs must be made within 45 days after identification or empty and remove tank from service. Two 30 day extensions are allowed to empty the tank. Decision to use extension must be documented. | Y |  |
| 40 CFR 63.120(b)(9) | Storage Vessel Provisions -- Procedures to Determine Compliance External FR seal gap measurement 30 day notification | Y |  |
| 40 CFR 63.120(b)(10) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seals visual inspection each time emptied | Y |  |
| 40 CFR 63.120(b)(10)(i) | Storage Vessel Provisions -- Procedures to Determine Compliance--External FR and seal visual inspection each time emptied – Repair defects before refilling [does not apply to gaskets, slotted membranes, or sleeve seals for Group 1 Refinery MACT tanks per 40 CFR 63.646(e)] | Y |  |
| 40 CFR 63.120(b)(10)(ii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied – 30 day notification | Y |  |
| 40 CFR 63.120(b)(10)(iii) | Storage Vessel Provisions -- Procedures to Determine Compliance-- External FR and seal visual inspection each time emptied –-Notification for unplanned | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions -- Recordkeeping--Group 1 and Group 2 storage vessel dimensions and capacity. Keep for life of source. | Y |  |
| 40 CFR 63.123(d) | Storage Vessel Provisions -- Recordkeeping--Group 1 External floating roof tank requirements - records of seal gap measurements (date, raw data, and required calculations) | Y |  |
| 40 CFR 63.123(g) | Storage Vessel Provisions -- Recordkeeping, Extensions for emptying storage vessel – keep documentation specified | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | NESHAPS for Petroleum Refineries (06/12/1996) REQUIREMENTS FOR EXTERNAL FLOATING ROOF TANKS |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.646(a) | Storage Vessel Provisions--Group 1 | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.646(c) | Storage Vessel Provisions—40 CFR 63 Subpart G exclusions for storage vessels [EFRs exempt from 63.119(c)(2)] | Y |  |
| 40 CFR 63.646(d) | Storage Vessel Provisions--References | Y |  |
| 40 CFR 63.646(d)(2) | Storage Vessel Provisions--References to April 22,1994 | Y |  |
| 40 CFR 63.646(d)(3) | Storage Vessel Provisions--References to December 31, 1992 | Y |  |
| 40 CFR 63.646(d)(4) | Storage Vessel Provisions--References to compliance dates in 40 CFR 63.100 of Subpart F | Y |  |
| 40 CFR 63.646(e) | Storage Vessel Provisions—Exceptions for compliance with inspection requirements of 40 CFR 63.120 of Subpart G – Not required to comply with provisions for gaskets, slotted membranes, and sleeve seals. | Y |  |
| 40 CFR 63.646(f) | Storage Vessel Provisions--Group 1 floating roof requirements | Y |  |
| 40 CFR 63.646(f)(1) | Storage Vessel Provisions—Group 1 floating roof requirements--Covers or lids closed except when in use | Y |  |
| 40 CFR 63.646(f)(2) | Storage Vessel Provisions--Group 1 floating roof requirements--Rim space vents requirements | Y |  |
| 40 CFR 63.646(f)(3) | Storage Vessel Provisions-Group 1 floating roof requirements--Automatic bleeder vents requirements | Y |  |
| 40 CFR 63.646(l) | Storage Vessel Provisions--State or local permitting agency notification requirements | Y |  |
| 40 CFR 63.654(f) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements | Y |  |
| 40 CFR 63.654(f)(1)(i) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(f)(1)(i)(A)(1) | Reporting and Recordkeeping Requirements--Notice of compliance status report requirements--Reporting--storage vessels | Y |  |
| 40 CFR 63.654(g) | Periodic Reporting and Recordkeeping Requirements | Y |  |
| 40 CFR 63.654(g)(1) | Periodic Reporting and Recordkeeping Requirements--storage vessels [Information related to gaskets, slotted membranes, and sleeve seals not required for storage vessels that are part of existing source] | Y |  |
| 40 CFR 63.654(g)(3) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs | Y |  |
| 40 CFR 63.654(g)(3)(i) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs-document results of each seal gap measurement | Y |  |
| 40 CFR 63.654(g)(3)(ii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – extension documentation | Y |  |
| 40 CFR 63.654(g)(3)(iii) | Periodic Reporting and Recordkeeping Requirements--storage vessels with external floating roofs – documentation of failures | Y |  |
| 40 CFR 63.654(h)(2) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections. | Y |  |
| 40 CFR 63.654(h)(2)(i) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections – refilling Group 1 storage vessel. | Y |  |
| 40 CFR 63.654(h)(2)(ii) | Reporting and Recordkeeping Requirements--Other reports--Storage vessel notification of inspections –Group 1 storage vessel seal gap measurements – 30 day notification [can be waived or modified by state or local]. | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – keep records specified in 40 CFR 63.123 (Subpart G) | Y |  |
| 40 CFR 63.654(i)(1)(i) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels– keep records specified in 40 CFR 63.123 (Subpart G) except records related to gaskets, slotted membranes, and sleeve seals for vessels in existing sources | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements—Recordkeeping for storage vessels--Record retention – 5 years | Y |  |

2.	Sources S-108, S-109, and S-127 currently contain low vapor pressure liquids, are exempt from BAAQMD permitting requirements, and fall under the MACT Group II requirements for recordkeeping. However, these tanks may be operated as MACT Group I tanks in the future. Table B23A shows the appropriate applicability for these tanks as MACT Group II tanks. Table B23B shows the appropriate applicability for these tanks as MACT Group I tanks including the BAAQMD Regulation 8 Rule 5 requirements for zero-gap secondary seals.

| Table IV – B24 Source-Specific Applicable Requirements NSPS K Exempt Tanks Subject to MACT Recordkeeping S-90 (Tank 67), S-105 (Tank 129) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart G | SOCMI HON G (01/27/1995) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.119(a)(3) | Storage Vessel Provisions – Reference Control Technology – Group 2 storage vessels comply only with recordkeeping requirements in 40 CFR 63.123(a) | Y |  |
| 40 CFR 63.123(a) | Storage Vessel Provisions – Recordkeeping – Group 2 storage vessels only required to keep tank dimensions and capacity analysis. Retain for life of source. | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR GROUP 2 RECORDKEEPING ONLY |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(n) | Applicability and Designation of Affected Source Overlap for Storage Vessels | Y |  |
| 40 CFR 63.640(n)(7) | Applicability and Designation of Affected Source Overlap for Storage Vessels—Group 2 storage vessel subject to NSPS K or Ka but exempt from control requirements of NSPS K or Ka is required to comply only with 40 CFR 63 Subpart CC | Y |  |
| 40 CFR 63.646(b)(1) | Storage Vessel Provisions--Determine stored liquid % OHAP for group determination | Y |  |
| 40 CFR 63.646(b)(2) | Storage Vessel Provisions--Determine stored liquid % OHAP-method 18 to resolve disputes | Y |  |
| 40 CFR 63.654(h)(6) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(h)(6)(ii) | Reporting and Recordkeeping Requirements--Other reports--Determination of Applicability | Y |  |
| 40 CFR 63.654(i)(1) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Keep records specified in 40 CFR 63.123 | Y |  |
| 40 CFR 63.654(i)(1) (iv) | Reporting and Recordkeeping Requirements--Recordkeeping for storage vessels – Data and assumptions used to determine Group 2 classification | Y |  |
| 40 CFR 63.654(i)(4) | Reporting and Recordkeeping Requirements--Recordkeeping--Record retention – 5 years | Y |  |
| NSPS Title 40 Part 60 Subpart K | NSPS Subpart K for Tanks (4/4/1980) |  |  |
| 40 CFR 60.110(a) | Applicability and Designation of Affected Facility; Affected facility | Y |  |
| 40 CFR 60.110(c)(2) | Applicability and Designation of Affected Facility-->65,000 gal after 6/11/1973 and before 5/19/1978. | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

| Table IV – B25 Source-Specific Applicable Requirements Exempt Butane Spheres S-188 (Tank 300), S-189 (Tank 301), S-190 (Tank 302), S-253 (Tank 833) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) REQUIREMENTS FOR PRESSURE TANKS |  |  |
| 8-5-111 | Limited Exemption, Tank Removal From and Return to Service | Y |  |
| 8-5-111.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO | Y |  |
| 8-5-111.1.1 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-111.1.2 | Limited Exemption, Tank Removal From and Return to Service; Notice to the APCO; Telephone notification | Y |  |
| 8-5-111.2 | Limited Exemption, Tank Removal From and Return to Service; Compliance before notification | Y |  |
| 8-5-111.4 | Limited Exemption, Tank Removal From and Return to Service; Use of vapor recovery | Y |  |
| 8-5-111.5 | Limited Exemption, Tank Removal From and Return to Service; Minimization of emissions | Y |  |
| 8-5-111.6 | Limited Exemption, Tank Removal From and Return to Service; Written notice of completion not required | Y |  |
| 8-5-111.7 | Limited Exemption, Tank Removal From and Return to Service; Compliance with Section 8-5-328 | Y |  |
| 8-5-112 | Limited Exemption, Tanks in Operation | Y |  |
| 8-5-112.1 | Limited Exemption, Tanks in Operation; Notice to the APCO | Y |  |
| 8-5-112.1.1 | Limited Exemption, Tanks in Operation; Notice to the APCO; 3 day prior notification | Y |  |
| 8-5-112.1.2 | Limited Exemption, Tanks in Operation; Notice to the APCO; Telephone notification | Y |  |
| 8-5-112.2 | Limited Exemption, Tanks in Operation; Compliance and certification before commencement of work | Y |  |
| 8-5-112.3 | Limited Exemption, Tanks in Operation; No product movement; minimization of emissions | Y |  |
| 8-5-112.4 | Limited Exemption, Tanks in Operation; Exemption does not exceed 7 days | Y |  |
| 8-5-301 | Storage Tank Control Requirements (internal floating roof, external floating roof, or approved emission control system) | Y |  |
| 8-5-303 | Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-303.1 | Requirements for Pressure Vacuum Valves; Set pressure | Y |  |
| 8-5-303.2 | Requirements for Pressure Vacuum Valves; Installation, maintenance, operation | Y |  |
| 8-5-307 | Requirements for Pressure Tanks and Blanketed Tanks | Y |  |
| 8-5-328 | Tank Degassing Requirements | Y |  |
| 8-5-328.1 | Tank Degassing Requirements; Tanks > 75 cubic meters | Y |  |
| 8-5-328.1.2 | Tank Degassing Requirements; Tanks > 75 cubic meters; Concentration of <10,000 ppm as methane after degassing | Y |  |
| 8-5-328.2 | Tank degassing requirements; Ozone excess day prohibition | Y |  |
| 8-5-403 | Inspection Requirements for Pressure Vacuum Valves | Y |  |
| 8-5-404 | Certification | Y |  |
| 8-5-501 | Records | Y |  |
| 8-5-501.1 | Records; Type and amounts of liquid; blanket gas; true vapor pressure; Retain 24 months | Y |  |
| 8-5-503 | Portable hydrocarbon detector | Y |  |
| 8-5-602 | Analysis of Samples, True Vapor Pressure | Y |  |
| 8-5-604 | Determination of Applicability | Y |  |
| 8-5-605 | Pressure Vacuum Valve Gas Tight Determination | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) EXEMPTION FOR TANKS VENTED TO FUEL GAS SYSTEM |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) EXEMPTION FOR PRESSURE TANKS (applies to S-188 only) |  |  |
| 40 CFR 60.110b(d)(2) | Exemption for pressure vessels designed to operate in excess of 204.9 kPa and without emissions to the atmosphere. | Y |  |

| Table IV – B26 Source-Specific Applicable Requirements NSPS KB Exempt Fixed Roof Tanks Vented to Fuel Gas S-135 (Tank 200) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR TANKS VENTED TO FUEL GAS SYSTEM |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR RECORDKEEPING ONLY |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.110b(c) | Applicability and Designation of Affected Facility; Exemptions for storage vessels > or = to 75 cu m | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(2) | Monitoring of Operations; Determine TVP-crude oil and refined petroleum | Y |  |
| 40 CFR 60.116b(g) | Monitoring of Operations; Exemption from 40 CFR 60.116b(c) and 40 CFR 60.116b(d) for tanks with closed vent system and control device | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

| Table IV – B27 Source-Specific Applicable Requirements NSPS Kb Exempt Fixed Roof Wastewater Tanks Vented to Fuel Gas Tank 235, Tank 236 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR EMISSION POINTS ROUTED TO FUEL GAS |  |  |
| 40 CFR 63.640(c)(3) | Wastewater streams and treatment operations associated with petroleum refining process units meeting the criteria of section 63.640(a) | Y |  |
| 40 CFR 63.640(d)(5) | Exemption for emission points routed to fuel gas system | Y |  |
| NSPS Title 40 Part 60 Subpart QQQ | NSPS Subpart QQQ VOC Emissions from Petroleum Refinery Wastewater Systems REQUIREMENTS FOR FIXED ROOF TANKS ROUTED TO FUEL GAS |  |  |
| 40 CFR 60.690(a)(1) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.690(a)(3) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.691 | Definitions: Closed Vent System. If gas or vapor from regulated equipment are routed to a process (e.g., petroleum refinery fuel gas system), the process shall not be considered a closed vent system and is not subject to the closed vent system standards. | Y |  |
| 40 CFR 60.692-1 | Standards: General | Y |  |
| 40 CFR 60.692-1(a) | Standards: General | Y |  |
| 40 CFR 60.692-1(b) | Standards: General | Y |  |
| 40 CFR 60.692-3 | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(1) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(2) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(3) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(4) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(5) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(f) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-6 | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(a) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(b) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.697 | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(a) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(c) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(3) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(4) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.698(c) | Reporting Requirements | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR RECORDKEEPING ONLY |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.110b(c) | Applicability and Designation of Affected Facility; Exemptions for storage vessels > or = to 75 cu m | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(3) | Monitoring of Operations; Determine TVP-other liquids | Y |  |
| 40 CFR 60.116b(f) | Monitoring of Operations; Waste storage tanks (indeterminate or variable composition) | Y |  |
| 40 CFR 60.116b(g) | Monitoring of Operations; Exemption from 40 CFR 60.116b(c) and 40 CFR 60.116b(d) for tanks with closed vent system and control device | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

| Table IV – B28 Source-Specific Applicable Requirements NSPS Kb Exempt Fixed Roof Wastewater Tank Tank 237 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| 40 CFR 63 Subpart CC | National Emission Standards for Hazardous Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR GROUP 2 WASTEWATER SOURCES |  |  |
| 40 CFR 63.640(c)(3) | Wastewater streams and treatment operations associated with petroleum refining process units meeting the criteria of section 63.640(a) | Y |  |
| 40 CFR 63.641 | Definitions: Group 1 and Group 2 Wastewater Streams | Y |  |
| 40 CFR 63.654(a) | Reporting and Recordkeeping Requirements: Wastewater – no reporting and recordkeeping requirements for wastewater except for Group 1 wastewater streams | Y |  |
| NSPS Title 40 Part 60 Subpart QQQ | NSPS Subpart QQQ VOC Emissions from Petroleum Refinery Wastewater Systems REQUIREMENTS FOR FIXED ROOF TANKS NOT ROUTED TO FUEL GAS |  |  |
| 40 CFR 60.690(a)(1) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.690(a)(3) | Applicability and Designation of Affected Facility | Y |  |
| 40 CFR 60.692-1 | Standards: General | Y |  |
| 40 CFR 60.692-1(a) | Standards: General | Y |  |
| 40 CFR 60.692-1(b) | Standards: General | Y |  |
| 40 CFR 60.692-3 | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(1) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(2) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(3) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(4) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(a)(5) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-3(f) | Standards: Oil-Water Separators (includes storage vessels) | Y |  |
| 40 CFR 60.692-6 | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(a) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.692-6(b) | Standards: Delay of Repair | Y |  |
| 40 CFR 60.697 | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(a) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(c) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(3) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(e)(4) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(1) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.697(f)(2) | Recordkeeping Requirements | Y |  |
| 40 CFR 60.698(c) | Reporting Requirements | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR RECORDKEEPING ONLY |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.110b(c) | Applicability and Designation of Affected Facility; Exemptions for storage vessels > or = to 75 cu m | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(d) | Monitoring of Operations; 30-day notification for TVP exceedances | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(3) | Monitoring of Operations; Determine TVP-other liquids | Y |  |
| 40 CFR 60.116b(f) | Monitoring of Operations; Waste storage tanks (indeterminate or variable composition) | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

| Table IV – B29 Source-Specific Applicable Requirements NSPS Kb Exempt Fixed Roof Tank Tank 224 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| NESHAPS Title 40 Part 63 Subpart CC | National Emission Standards for Hazardous Air Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR TANKKS ALSO SUBJECT TO NSPS Kb |  |  |
| 40 CFR 63.640(c)(2) | Applicability and Designation of Storage Vessels | Y |  |
| 40 CFR 63.640(n)(1) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Existing Group 1 or Group 2 also subject to Kb only subject to Kb and 63.640(n)(8). | Y |  |
| 40 CFR 63.640(n)(8) | Applicability and Designation of Affected Source Overlap for Storage Vessels--Additional requirements for Kb storage vessels | Y |  |
| NSPS Title 40 Part 60 Subpart Kb | NSPS Subpart Kb for Tanks (12/14/2000) REQUIREMENTS FOR RECORDKEEPING ONLY |  |  |
| 40 CFR 60.110b(a) | Applicability and Designation of Affected Facility; Volatile organic liquid storage vessels > or = to 40 cu m, after 7/23/1984 | Y |  |
| 40 CFR 60.110b(c) | Applicability and Designation of Affected Facility; Exemptions for storage vessels > or = to 75 cu m | Y |  |
| 40 CFR 60.116b(a) | Monitoring of Operations; Record retention | Y |  |
| 40 CFR 60.116b(b) | Monitoring of Operations; Permanent record requirements | Y |  |
| 40 CFR 60.116b(d) | Monitoring of Operations; 30-day notification for TVP exceedances | Y |  |
| 40 CFR 60.116b(e) | Monitoring of Operations; Determine TVP | Y |  |
| 40 CFR 60.116b(e)(2) | Monitoring of Operations; Determine TVP-crude oil and refined petroleum | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

| Table IV – B30 Source-Specific Applicable Requirements Exempt External Floating Roof Wastewater Tanks Tank 206, Tank 207 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD · Regulation 8, Rule 5 | Organic Compounds, Storage of Organic Liquids (11/27/02) EXEMPT |  |  |
| 8-5-117 | Exemption, Low Vapor Pressure | Y |  |
| 40 CFR 63 Subpart CC | National Emission Standards for Hazardous Pollutants for Petroleum Refining (8/18/95) REQUIREMENTS FOR GROUP 2 WASTEWATER SOURCES |  |  |
| 40 CFR 63.640(c)(3) | Wastewater streams and treatment operations associated with petroleum refining process units meeting the criteria of section 63.640(a) | Y |  |
| 40 CFR 63.641 | Definitions: Group 1 and Group 2 Wastewater Streams | Y |  |
| 40 CFR 63.654(a) | Reporting and Recordkeeping Requirements: Wastewater – no reporting and recordkeeping requirements for wastewater except for Group 1 wastewater streams | Y |  |
| NSPS Title 40 Part 60 Subpart K | NSPS Subpart K for Tanks (4/4/1980) EXEMPTION FOR TANKS NOT CONTAINING PETROLEUM LIQUIDS |  |  |
| 40 CFR 60.111(b) | Definitions: Petroleum liquids | Y |  |
| BAAQMD Condition 20773 |  |  |  |
| Part 1 | Requirement to verify exempt status of tank based on true vapor pressure of contents [Basis: Regulation 8-5-117, 2-6-409.2] | Y | 4/1/04 |
| Part 2 | Record retention requirement [Basis: Regulation 2-6-409.2] | Y | 4/1/04 |

# SCHEDULE OF COMPLIANCE

The permit holder shall comply with all applicable requirements cited in this permit.  The permit holder shall also comply with applicable requirements that become effective during the term of this permit on a timely basis.

# PERMIT CONDITIONS

CONDITION 383  [Revisions are in accordance with A/C 5814.]

Conditions For S-350

1a.  The owner/operator of S-350 (Crude Unit 267) shall not process crude oil at S-350 with a sulfur content in excess of 1.5 wt %.                                                             [Cumulative Increase]

1b.  The owner/operator shall sample and analyze the crude feed to S-350 to determine the sulfur content each time a new tanker shipment or pipeline delivery of crude is introduced into the S-350 feed tanks.                                                                                 [Cumulative Increase]

2.  The owner/operator of S-350 shall not exceed an S-350 feed rate of 30,000 bbl per day on a 12 month rolling average basis.  The S-350 feed rate shall never exceed 33,000 bbl on any calendar day.  The 33,000 bbl/day limit and 30,000 bbl/day 12 month rolling average limit are absolute limits and may not be corrected for instrument error.           [Cumulative Increase]

3.  The owner/operator of S-350 shall maintain monthly records of "calendar day" throughput and "12 month rolling average" throughput at S-350 in a District-approved log.  The owner/operator shall also maintain records of all sulfur content analyses required by Part 1b.  These records shall be kept for at least five years and shall be made available to the District upon request.                                                                                        [Cumulative Increase]

CONDITION 1440

Conditions for S-324, S-381, S-382, S-383, S-384, S-385, S-386, S-387, S-390, S-392, S-400, S-401 S-1007, S-1008, S-1009

1.	S-324 API Separator shall be operated such that the liquid in the main separator basin is in full contact with fixed concrete roof.  This condition shall not apply during separator shutdown for maintenance.			[Cumulative Increase]

2.	Diversions of refinery wastewater around the Water Effluent Treating Facility to the open Storm Water Basins (S-1008, S-1009) shall be minimized.  These diversions shall not cause a nuisance as defined in District Regulation 7 or Regulation 1-301.	[Cumulative Increase]

3.	Records shall be maintained of each incident in which refinery wastewater is diverted to the open storm water basins.  These records shall include the reason for the diversion, the total quantity of wastewater diverted to the basins, and the approximate hydrocarbon content of the water.			[Cumulative Increase]

4.	The following sources shall have no detectable VOC emissions ("no detectable VOC emissions" is defined according to EPA Test Method 21 as less than 500 ppm above background levels):

a.	Doors, hatches, covers, and other openings on the S-324 API Separator, forebay, outlet basin, and channel to the S-1007 DAF Unit.

b.	Doors, hatches, covers, and other openings on the S-1007 DAF Unit and the S-400 Wet and S-401 Dry Weather Sumps, except for the vent opening on these units.

c.	Any open process vessel, distribution box, tank, or other equipment downstream of the S-1007 DAF Unit (S-381, S-382, S-383, S-384, S-385, S-386, S-387, S-390, S-392).

[Cumulative Increase]

5.	Compliance with the VOC emission criteria of Part 4 shall be determined every 6 months and records kept of each inspection.  These records shall be made available to District personnel upon request.				[Cumulative Increase]

6.	The maximum wastewater throughput at the S-324 API Separator and S-1007 DAF Unit shall not exceed 7,500 gpm during media filter backwash and 7,000 gpm during all other times for each unit.  Any modifications to equipment at this facility which increase the annual average waste water throughput at S-324 and S-1007 shall first be submitted to the BAAQMD in the form of a permit application.			[Cumulative Increase]

CONDITION 1694  [Revisions to Part 4 are in accordance with A/C 5814.]

Conditions For Combustion sources and So2 Cap, Except For Gas Turbines And Duct Burners

A.  Heater Firing Rate Limits and General Requirements

1.	Each heater listed below shall not exceed the indicated daily firing rate limit (based on higher heating value of fuel) which are considered maximum sustainable firing rates.  The indicated hourly firing rate is the daily limit divided by 24 hours and is the basis for permit fees and is the rate listed in the District database.

District	Refinery	Daily Firing	Hourly Firing

Source	ID 	Limit	Rate

Number	Number	(MM BTU/day)	(MM BTU/hr)

S-2	U229/B301	528	22

S-3	U230/B201	1,488	62

S-4	U231/B101	2,304	96

S-5	U231/B102	2,496	104

S-7	U231/B103	1,536	64

S-8	U240/B1	6,144	256

S-9	U240/B2	1,464	61

S-10	U240/B101	5,352	223

S-11	U240/B201	2,592	108

S-12	U240/B202	1,008	42

S-13	U240/B301	4,656	194

S-14	U240/B401	13,344	556

S-15 thru S19	U244/B501 thru B505	5,754	239.75

S-20	U244/B506	552	23

S-21	U244/B507	194.4	8.1

S-22	U248/B606	744	31

S-29	U200/B5	2,472	103

S-30	U200/B101	1,200	50

S-31	U200/B501	480	20

S-43	U200/B202	5,520	230

S-44	U200/B201	1,104	46

S-336	U231/B104	2,664	111

S-337	U231/B105	816	34

S-351	U267	2,424	101

S-371/372	U228/B520 and B521	1,392	58

S-438	U110	5,040	210

[Regulation 2-1-234.3]

2a.	All sources shall use only refinery fuel gas and natural gas as fuel, EXCEPT for S-438 which may also use pressure swing adsorption (PSA) off gas as fuel, and EXCEPT for S-3 and S-7 which may also use naphtha fuel.

[Regulation 9-1-304 (sulfur content), Regulation 2, Rule 1]

2b.	Sources S-3 and S-7 are permitted to use liquid fuel.  These sources shall be monitored for visible emissions during tube cleaning during daylight hours.  If any visible emissions are detected when the operation commences, corrective action shall be taken within one day, and monitoring shall be performed after the corrective action is taken.  If no visible emissions are detected, monitoring shall be performed on an hourly basis.		[Regulation 2-6-409.2]

2c.	Sources S-3 and S-7 are permitted to use liquid fuel.  These sources shall be monitored for visible emissions before each 1 million gallons of liquid fuel is combusted at each source.  If an inspection documents visible emissions, a Method 9 evaluation shall be completed within 3 working days, or during the next scheduled operating period if the specific unit ceases firing on liquid fuel within the 3 working day time frame.	[Regulation 2-6-409.2].

3a.	The refinery fuel gas shall be tested for total reduced sulfur (TRS) concentration by GC analysis at least once per 8 hour shift (3 times per calendar day).  At least 90% of these samples shall be taken each calendar month.  No readable samples or sample results shall be omitted. TRS shall include hydrogen sulfide, methyl mercaptan, methyl sulfide, dimethyl disulfide.  As an alternative to GC TRS analysis, the fuel gas total sulfur content may be measured with a dedicated total sulfur analyzer (Houston Atlas or equivalent), and TRS concentration estimated based on the total sulfur/TRS ratio, with the TRS estimate increased by a 5% margin for conservatism.  The total sulfur/TRS ratio shall be determined at least on a monthly basis through GC analyses of total sulfur and TRS values, and the most recent ratio shall be used to estimate TRS concentration.		[SO2 Bubble]

3b.	The average of the 3 daily refinery fuel gas TRS sample results shall be reported to the District in a table format each calendar month, with a separate entry for each daily average.  Sample reports shall be submitted to the District within 30 days of the end of each calendar month.  Any omitted sample results shall be explained in this report.	[SO2 Bubble]

4.	Emissions of SO2 shall not exceed 1,611 lb/day on a monthly average basis from non-cogeneration sources burning fuel gas or liquid fuel.                           [SO2 Bubble]

5.	The following records shall be maintained in a District-approved log for at least 5 years and shall be made available to the District upon request:

a.  Daily and monthly records of the type and amount of fuel combusted at each source listed in Part A.1.					[Regulation 2, Rule 1]

b.  TRS sample results as required by Part A.3		[SO2 Bubble]

c.  SO2 emissions as required by Part A.4		[SO2 Bubble]

d.  The operator shall keep records of all visible emission monitoring required by Part 2b, shall identify the person performing the monitoring and shall describe all corrective actions taken.

[Regulation 2-6-409.2]

e.  The operator shall keep records of all visible emission monitoring required by Part 2c, of the results of required visual monitoring and Method 9 evaluations on these sources, shall identify the person performing the monitoring and shall describe all corrective actions taken.

[Regulation 2-6-409.2]

B.  S-351 Preheater

1.	The S-351 heater shall be abated by the A-6 SCR unit at all times.

[BACT, Cumulative Increase]

2.	The concentration of NOx from S-351 shall not exceed 20 ppmv @ 3% oxygen, dry, averaged over any consecutive 3 hour period.  This limit shall not apply during a startup period which shall not exceed 12 hours.  The startup exemption period may last up to 24 hours to allow the proper ammonia injection temperature to be reached provided that the temperature is monitored at least once per hour and that ammonia injection begins within 2 hours of reaching the proper temperature.  This limit shall also not apply during a shutdown period which shall not exceed 9 hours.	[BACT, Cumulative Increase]

3.	The following instruments shall be installed and maintained to demonstrate compliance with Part 2:

a.  continuous NOx analyzer/recorder

b.  continuous O2 or CO analyzer/recorder	[BACT, Cumulative Increase]

C.  S-371 and S-372 Furnaces

1.	The S-371 furnace shall be abated by the A-16 SCR unit at all times.  The S-372 furnace shall be abated by the A-17 SCR unit at all times.	[BACT, Cumulative Increase]

2.	The concentration of NOx from S-371 and S-372 shall not exceed 20 ppmv, dry, corrected to 3% oxygen, averaged over any consecutive 3 hour period.  This limit shall not apply during a startup period, which shall not exceed 12 hours.  The startup exemption period may last up to 24 hours to allow the proper ammonia injection temperature to be reached provided that the temperature is monitored at least once per hour and that ammonia injection begins within 2 hours of reaching the proper temperature.  This limit shall also not apply during a shutdown period which shall not exceed 9 hours.	[BACT, Cumulative Increase]

3.	The concentration of CO emissions from S-371 and S-372 shall not exceed 50 ppmv, dry, corrected to 3% oxygen, averaged over any consecutive 3 hour period.  This limit shall not apply during a startup period, which shall not exceed 12 hours.  The startup exemption period may last up to 24 hours to allow the proper ammonia injection temperature to be reached provided that the temperature is monitored at least once per hour and that ammonia injection begins within 2 hours of reaching the proper temperature.  This limit shall also not apply during a shutdown period, which shall not exceed 9 hours.

[BACT, Cumulative Increase]

D.	S-43 Coking Furnace (Unit 200 B-202) and S-44 (Unit 200 B-201 PCT Reboil Furnace)

1.	Nitrogen oxide emissions from the S-43 Coking Furnace (Unit 200 B-202) shall be abated by Selective Catalytic Reduction Unit A-4.	[BACT, Cumulative Increase]

2.	The nitrogen oxides in the flue gases for S-43, Unit 200 B-202 Coking Furnace and S-44, Unit 200 B-201 PCT Reboil Furnace shall not exceed 40 ppmdv corrected to 3% oxygen, dry, over any consecutive 8 hour period.  This limit shall not apply during a startup period which shall not exceed 12 hours.  The startup exemption period may last up to 24 hours to allow the proper ammonia injection temperature to be reached provided that the temperature is monitored at least once per hour and that ammonia injection begins within 2 hours of reaching the proper temperature. This limit shall also not apply during a shutdown period which shall not exceed 9 hours.

[BACT, Cumulative Increase]

3.	The carbon monoxide in the flue gas for S-43, Unit 200 B-202 Coking Furnace and S-44, Unit 200 B-201 PCT Reboil Furnace shall not exceed 50 ppmdv corrected to 3% oxygen averaged over any calendar month.  This condition shall not apply during start-up and shutdown.			[BACT, Cumulative Increase]

4.	Instruments shall be installed and operated to continuously monitor the percentage of oxygen and the concentration of nitrogen oxides from the following sources:  S-43, Unit 200 B-202 Coking Furnace and S-44, Unit 200 B-201 PCT Reboil Furnace.

[BACT, Cumulative Increase]

E.	S-438 Furnace

1.	The S-438 furnace shall be abated by the A-46 SCR unit at all times.

[BACT, Cumulative Increase]

2.	Total fuel fired in S-438 shall not exceed 2.04 E 12 BTU in any rolling consecutive 365 day period.				[Cumulative Increase]

3.	Pressure swing adsorption (PSA) off gas used as fuel at S-438 shall not exceed 1.0 ppm (by weight) total reduced sulfur (TRS).  TRS shall include hydrogen sulfide, methyl mercaptan, methyl sulfide, dimethyl disulfide.		[BACT, Cumulative Increase]

4.	The following emission concentration limits from S-438 shall not be exceeded.  These limits shall not apply during startup periods not exceeding 24 hours (72 hours when drying refractory or during the first startup following catalyst replacement) and shutdown periods not exceeding 24 hours.  The District may approve other startup and shutdown durations.

NOx:  10 ppmv @ 3% oxygen, averaged over any 3 hour period

CO:  32 ppmv @ 3% oxygen, averaged over any calendar day

[BACT, Cumulative Increase]

5.	The concentration of TRS in the blended fuel gas shall not exceed 50 ppmv averaged over any calendar month.			[BACT, Cumulative Increase]

6.	Daily records of the type and amount of fuel combusted at S-438 and of the TRS and hydrogen sulfide concentration in the blended fuel gas, and monthly records of average blended fuel gas TRS concentration, shall be maintained for at least five years and shall be made available to the District upon request.	[Recordkeeping]

F.	S-2, S-3, S-4, S-5, S-7, S-8, S-9, S-10, S-11, S-12, S-13, S-14 Heaters

1.	Total fuel firing at Unit 240 (S-8, S-9, S-10, S-11, S-12, S-13, S-14) shall not exceed 993.7 MM BTU/hr averaged over any consecutive 12 month period.	[Cumulative Increase]

2.	Total fuel fired at the MP-30 Complex, including Unit 229 (S-2), Unit 230 (S-3) and Unit 231 (S-4, S-5, S-7) shall not exceed 346.5 MM BTU/hr averaged over any consecutive 12 month period.					[Cumulative Increase]

3.	Monthly records of the fuel fired at sources in Parts 1 and 2 shall be kept in a District-approved log for at least 5 years and shall be made available the District upon request.

[Recordkeeping]

CONDITION 1860

Conditions For S-388,

1.	Tank T-276 and mixer F-205 (S-388) shall be gas-tight, with no detectable emissions.  "Detectable Emissions" shall be defined as organic concentration exceeding 300 ppm as methane above background.			[Cumulative Increase]

2.	S-388 shall be vented to the Refinery Vapor Recovery System at all times that S-388 is operating.					[Cumulative Increase]

3.	S-388 shall be included in the facility fugitive emission monitoring program required by Regulation 8, Rule 18.				[Regulation 8, Rule 18]

CONDITION 4336

Conditions For S-425, S-426

1.	For each loading event of "regulated organic liquid", the A-420 shall be operated with a temperature of at least 1300 degrees F during the first 15 minutes of the loading operation.  After the initial 15 minutes of loading, the A-420 temperature shall be at least 1400 degrees F.				[Cumulative Increase]

2.	Instruments shall be installed and maintained to monitor and record the following:

a.	Static pressure developed in the marine tank vessel

b.	A-420 temperature.

c.	Hydrocarbons and flow to determine mass emissions or a concentration measurement alone if it is demonstrated to the satisfaction of the APCO that concentration alone allows verification of compliance, or

d.	Any other device that verifies compliance, with prior approval from the APCO.

[Cumulative Increase]

3.	A "regulated organic liquid" shall not be loaded from this facility into a marine tank vessel within the District whenever A-420 is not fully operational.  A-420 must be maintained to be leak free, gas tight, and in good working order.  For the purposes of this condition, "operational" shall mean the system is achieving the reductions required by Regulation 8, Rule 44; "regulated organic liquids" include gasoline, gasoline blendstocks, aviation gasoline and JP-4 aviation fuel and crude oil.			[Cumulative Increase]

4.	A leak test shall be conducted on all vessels loading under positive pressure prior to loading more than 20% of the cargo.  The leak test shall include all vessel relief valves, hatch cover, butterworth plates, gauging connections, and any other potential leak points.

[Cumulative Increase]

5.	Loading pressure shall not exceed 80% of the lowest relief valve set pressure of the vessel being loaded.				[Cumulative Increase]

The following conditions are transferred from Condition 476.

6.	No more than 25,000 barrels per day of gasoline, naphtha and C5/C6 shall be shipped across the wharf on an annual average basis.			[Cumulative Increase]

a.	When barges are used to ship gasoline, naphtha or C5/C6, the volume of these materials shipped during any reporting period is to be multiplied by a factor of 1.66 and included in the shipping totals to determine compliance with the throughput limits.

b.	When barges are used to lighter crude oil, the volume of oil lightered during any reporting period shall be multiplied by a factor of 0.42 and included in the shipping totals to determine compliance with the throughput limits.  The vessel Exxon Galveston is considered a ship for the purposes of this condition.

7.	All throughput records required to verify compliance with Part 6 and maintenance records required for A-420, which are subject to Regulation 8, Rule 44, shall be kept on site for at least 5 years and made available to the District upon request.

[Cumulative Increase]

CONDITION 6671

Conditions For S-307

1.	The vapor vent on the E-421 condenser (overhead condenser on D-406 condensate stripper in U-240 Unicracker Complex hydrogen plant) shall be vented to the A-50 condenser whenever the vent operates.				[Regulation 8-2-301]

2.	A-50 shall reduce total organic carbon emissions from the E-421 vent as necessary to a level which complies with Regulation 8-2-301.		[Regulation 8-2-301]

3.	All blowdown and other liquid effluent from A-50 shall be piped to the plant wastewater treatment system.				[Cumulative Increase]

4.	Whenever the U-240 hydrogen plant operates, normal flow of scrubbing liquid through the E-421 scrubber pumparound pump and normal flow of cooling water through the pumparound cooler shall be verified on a daily basis.		[Cumulative Increase]

5.	Daily records (on days when the U-240 hydrogen plant operates) of normal scrubbing liquid flow and normal cooling water flow shall be kept in a District-approved log for at least five years and shall be made available to the District upon request.	[Cumulative Increase]

CONDITION 6725

Conditions for S-432

1)	All new flanges in hydrocarbon service associated with the S-432 Deisobutanizer project shall utilize graphitic gaskets.  All new valves in hydrocarbon service associated with the project shall be either live-loaded valves, bellows-sealed valves, diaphragm valves, or other District approved equivalent valve designs.	[BACT, Cumulative Increase]

2)	All new pressure relief valves in hydrocarbon service associated with the S-432 project shall be vented to the refinery flare gas recovery system.

[BACT, Cumulative Increase]

3)	All new pumps and compressors in hydrocarbon service associated with the S-432 project shall utilize either a double mechanical shaft seal design with barrier fluid, a magnetically coupled shaft, or other District approved equivalent design.  If a barrier fluid is used, either the fluid reservoir shall be vented to a 95% efficient control device, or the barrier fluid shall be operated at a pressure higher than the process stream pressure.

[BACT, Cumulative Increase]

CONDITION 7353

1.	The emissions from the S-433 MOSC storage tank shall be collected and vented to the fuel gas system.					[Cumulative Increase]

2.	Valves shall be equipped with live-loaded packing.  Pumps shall be equipped with double mechanical seals separated by a barrier fluid.		[Cumulative Increase]

3.	The S-433 Fixed Roof Storage Tank shall only store sludge.	[Cumulative Increase]

4.	The total throughput of sludge at this MOSC facility shall not exceed 138,700 barrels in any rolling 52 consecutive week period.			[Cumulative Increase]

5.	The total weekly throughput of sludge withdrawn from the S-433 Storage Tank shall be recorded in a District approved log.  This record shall be retained for a period of at least five years from date of entry.  It shall be kept on site and made available to the District staff upon request.					[Cumulative Increase]

CONDITION 7523

Conditions for S-294 (GDF 7609)

Pursuant to BAAQMD Toxic Section Policy, this facility's annual gasoline throughput shall not exceed 400,000 gallons in any consecutive 12 month period.	[Basis: Toxic Risk Policy]

CONDITION 11219

CONDITIONS FOR S-449 (T-285)

1.	Working emissions from S-449 shall be collected and vented to the refinery fuel  gas supply.  Other abatement devices, which provide at least 95% abatement of VOC emissions by weight,  may be  used with the prior approval of the District.		[Cumulative Increase]

CONDITION 12121

CONDITIONS FOR S-370

1.	The feed rate at the S-370 isomerization unit (U-228) shall not exceed 11,040 barrels on any calendar day, defined as the sum of the isomerization fresh reactor charge and the adsorber fresh feed.					[Cumulative Increase]

2.	Daily records of the S-370 feed rate shall be maintained for at least five years and shall be made available to the District upon request.		[Recordkeeping]

CONDITION 12122

Conditions For S-352, 353, 354, 355, 356, 357

1.	The gas turbines (S-352, S-353 and S-354) and the heat recovery steam generator (HRG) duct burners (S-355,S-356 and S-357) shall be fired on refinery fuel gas or natural gas.

[Cumulative Increase]

2.	A HRG duct burner shall be operated only when the associated gas turbine is operated.

[Cumulative Increase]

3.	The exhaust from S-352 and S-355 shall be abated at all times by SCR unit A-13.				[BACT, Cumulative Increase]

4.	The exhaust from S-353 and S-356 shall be abated at all times by SCR unit A-14.				[BACT, Cumulative Increase]

5.	The exhaust from S-354 and S-357 shall be abated at all times by SCR unit A-15.				[BACT, Cumulative Increase]

6.	Total fuel fired in S-355, S-356, and S-357 shall not exceed 2.42 E 12 BTU in any consecutive 365 day period.		[Cumulative Increase]

7.	CO emissions from each turbine/duct burner set shall not exceed 39 ppmv at 15% oxygen, averaged over any consecutive 30 day period.  Emissions during startup periods, which shall not exceed four hours, and shutdown periods, which shall not exceed two hours, may be excluded when averaging emissions.		[BACT, Cumulative Increase]

8.	POC emissions from each turbine/duct burner set shall not exceed 6 ppmv at 15% oxygen, averaged over any consecutive 30 day period.  Emissions during startup periods, which shall not exceed four hours, and shutdown periods, which shall not exceed two hours, may be excluded when averaging emissions.		[BACT, Cumulative Increase]

9a.	The combined NOx emissions from S- 352, S-353, S-354, S-355, S-356 and S-357 shall not exceed 66 lb/hr (averaged over any 3 hour period), nor 167 tons in any consecutive 365 day period.  NOx emissions from each turbine/duct burner set shall not exceed 528 lb/day.					[BACT, Cumulative Increase]

9b.	NOx emissions from S- 352, S-353, S-354, S-355, S-356 and S-357 shall be monitored with a District-approved continuous emission monitor.	[BACT, Cumulative Increase]

10a.	The combined CO emissions from S-352, S-353, S-354, S- 355, S-356 and S-357 shall not exceed 200 tons in any consecutive 365 day period.

[BACT, Cumulative Increase]

10b.	CO emissions from S- 352, S-353, S-354, S-355, S-356 and S-357 shall be monitored with a District-approved continuous emission monitor.	[BACT, Cumulative Increase]

11.	The combined POC emissions S-352, S-353, S-354, S-355, S-356 and S-357 shall not exceed 8.3 lb/hr nor 30.5 tons in any consecutive 365 day period.

[BACT, Cumulative Increase]

12.	The refinery fuel gas shall be tested for total reduced sulfur (TRS) concentration at least once per 8 hour shift (3 times per calendar day).  At least 90% of these samples shall be taken each calendar month. No readable samples or sample results shall be omitted.  TRS shall include hydrogen sulfide, methyl mercaptan, methyl sulfide, dimethyl disulfide.						[Cumulative Increase]

13.	The average of the 3 daily refinery fuel gas TRS sample results shall be reported to the District in a table format each calendar month, with a separate entry for each daily average.  Sample reports shall be submitted to the District within 30 days of the end of each calendar month.  Any omitted sample results shall be explained in this report.

[Cumulative Increase]

14.	A source test to verify compliance with Parts 8 and 11 shall be performed each calendar year in accordance with District source test methods or other methods approved in advance by the District.  A copy of the test report shall be provided to the District Director of Compliance and Enforcement within 45 days of completion of the test.	[Regulation 2-6-409.2]

15.	Records shall be maintained to allow verification of compliance with all permit conditions.  Records shall be retained for at least five years and shall be made available to the District upon request.			[BACT, Cumulative Increase]

CONDITION 12124

CONDITIONS FOR S-439 (T-109)

1.	The following total throughput shall not be exceeded in any rolling continuous 12 month period:

3,650 thousand barrels				[Cumulative Increase]

2.	S-439 shall operate with closed, gasketed covers on all tank openings except pressure relief valves and vacuum breaker valves.			[BACT]

3.	Monthly records of the throughput of each material processed at this tank shall be kept in a District-approved log for at least 5 years and shall be made available to the District upon request.					[Cumulative Increase]

CONDITION 12125

CONDITIONS FOR S-440 (T-110)

1.	The following total throughput shall not be exceeded in any rolling continuous 12 month period:

3,600 thousand barrels				[Cumulative Increase]

2.	S-440 shall operate with closed, gasketed covers on all tank openings except pressure relief valves and vacuum breaker valves.			[BACT]

3.	Monthly records of the throughput of each material processed at this tank shall be kept in a District-approved log for at least 5 years and shall be made available to the District upon request.					[Cumulative Increase]

CONDITION 12127

CONDITIONS FOR S-442 (T-112)

1.	The following total throughput shall not be exceeded in any rolling continuous 12 month period:

2,740 thousand barrels				[Cumulative Increase]

2.	S-442 shall operate with closed, gasketed covers on all tank openings except pressure relief valves and vacuum breaker valves.			[BACT]

3.	Monthly records of the throughput of each material processed at this tank shall be kept in a District-approved log for at least 5 years and shall be made available to the District upon request.					[Cumulative Increase]

CONDITION 12129

CONDITIONS FOR S-444 (T-243)

1.	The following total throughput shall not be exceeded in any rolling continuous 12 month period:

4,380 thousand barrels				[Cumulative Increase]

2.	S-444 shall operate with closed, gasketed covers on all tank openings except pressure relief valves and vacuum breaker valves.			[BACT]

3.	Monthly records of the throughput of each material processed at this tank shall be kept in a District-approved log for at least 5 years and shall be made available to the District upon request.					[Cumulative Increase]

CONDITION 12130

CONDITIONS FOR S-445 (T-271)

1.	Working emissions from S-445 shall be collected and vented to the refinery fuel gas supply.  Other abatement devices, which provide at least 95% abatement of VOC emissions by weight, may be used with the prior approval of the District.		[Cumulative Increase]

CONDITION 12131

CONDITIONS FOR S-446 (T-310)

1.	Working emissions from S-446 shall be collected and vented to the refinery fuel gas supply.  Other abatement devices, which provide at least 95% abatement of VOC emissions by weight, may be used with the prior approval of the District.		[Cumulative Increase]

CONDITION 12132

CONDITIONS FOR S-447 (T-311)

1.	Working emissions from S-447 shall be collected and vented to the refinery fuel gas supply.  Other abatement devices, which provide at least 95% abatement of VOC emissions by weight, may be used with the prior approval of the District.		[Cumulative Increase]

CONDITION 12133

CONDITIONS FOR S-448 (T-1007)

1.	The following total throughput shall not be exceeded in any rolling continuous 12 month period:

2,190 thousand barrels				[Cumulative Increase]

2.	S-448 shall operate with closed, gasketed covers on all tank openings except pressure relief valves and vacuum breaker valves.			[BACT]

3.	Monthly records of the  throughput of each material processed at this tank shall be kept in a District-approved log for at least 5 years and shall be made available to the District upon request.					[Cumulative Increase]

CONDITION 12245

Conditions For S-450

1.	Groundwater extracted from the S-450 trench system shall be pumped to the wastewater treatment plant for treatment and shall not be exposed to the atmosphere except as required at the treatment plant.				[Cumulative Increase]

2.	All extraction pump vaults and piping access boxes shall be equipped with solid covers.

[Cumulative Increase]

CONDITION 13184

1.	The POC emissions from the S-182 fixed roof storage tank shall be collected and vented at all times to the fuel gas collection system.			[Cumulative Increase]

CONDITION 16677

Conditions For S-376, 377, 378

1.	Net usage of citrus-based solvent at S-376, S-377 and S-378 shall not exceed 150 gallons each in any consecutive 12-month period.		[Cumulative Increase]

- Cleanup solvent other than the material(s) specified in Part 1, and/or usage in excess of that specified in Part 1, may be used, provided that the Permit Holder can demonstrate that all of the following are satisfied:

a.	Total POC emissions from S-376, S-377 and S-378 do not exceed 1,095 pounds each in any consecutive 12-month period; and

b.	The use of these materials does not increase toxic emissions above any risk screening trigger level.		[Cumulative Increase and Toxic Risk Screen]

3.	To determine compliance with the above requirements, the Permit Holder shall maintain the following records and provide all of the data necessary to evaluate compliance, including:

a.	Type and monthly usage of all solvents used;

b.	If a material other than those specified in Part 1 is used, POC and toxic component contents of each material used; and mass emission calculations to demonstrate compliance with Part 2, on a monthly basis;

c.	Monthly usage and emission calculations (if calculations are required by Part 3b) shall be totaled for each consecutive 12-month period.

All records shall be retained for at least 5 years and shall be made available to the District upon request.  These requirements shall not replace the recordkeeping requirements contained in any applicable District Regulations.

[Cumulative Increase and Toxic Risk Screen]

CONDITION 18251

Conditions for S-380, S-389

1a.	Activated Carbon Silo S-380 shall be vented through the A-20 baghouse whenever it is in service.

1b.	Diatomaceous Earth Silo S-389 shall be vented through the A-21 baghouse whenever it is in service.					[Regulation 2-1-234]

2a.	Baghouses A-20 and A-21 shall be equipped with differential pressure gauges to allow monitoring of baghouse operating condition.		[Regulation 1-441]

CONDITION 18251

Conditions for S-380, S-389

2b.	Differential pressure on baghouse A-20 shall be checked at least once per calendar quarter to verify normal operating condition.			[Regulation 1-441]

2c.	Differential pressure on baghouse A-21 shall be checked each time that the baghouse is operated to verify normal operating condition.		[Regulation 1-441]

3.	A record of alldifferential pressure readings for baghouses A-20 and A-21 shall be maintained in a District-approved log for at least 5 years and shall be made available to the District upon request.				[Regulation 1-441]

Condi tion 18255

- The owner/operator shall not flare more than 1.69 E 6 pounds per hour of vent gas (total) as defined in Regulation 12-11-210 at flares S-296 and S-398.  [Regulation 8-1-110.3; 2-1-403]

- In order to demonstrate compliance with Part 1, the owner/operator shall record on an hourly basis during flaring events the pounds of vent gas flared at S-296 and S-398.  The owner/operator shall maintain these records for a period of five years from the date of entry and make these records available for the APCO upon request.  [Regulation 8-1-110.3; 2-6-409.2; 2-6-501]

  - For the purposes of these conditions, a flaring event is defined as a flow rate of vent gas flared in any consecutive 15 minutes period that continuously exceeds 330 standard cubic feet per minute (scfm).  If during a flaring event, the vent gas flow rate drops below 330 scfm and then increases above 330 scfm within 30 minutes, that shall still be considered a single flaring event, rather than two separate events.  For each flaring event during daylight hours (between sunrise and sunset), the owner/operator shall inspect the flare within 15 minutes of determining the flaring event, and within 30 minutes of the last inspection thereafter, using video monitoring or visible inspection following the procedure described in Part 2.  [Regulation 2-6-409.2]

  - The owner/operator shall use the following procedure for the initial inspection and each 30-minute inspection of a flaring event.

a.  If the owner/operator can determine that there are no visible emissions using video monitoring, then no further monitoring is necessary for that particular inspection.

b.  If the owner/operator cannot determine that there are no visible emissions using video monitoring, the owner/operator shall conduct a visual inspection outdoors using either:

i.  EPA Reference Method 9; or

ii. Survey the flare by selecting a position that enables a clear view of the flare at least 15 feet, but not more than 0.25 miles, from the emission source, where the sun is not directly in the observer’s eyes.

c.  If a visible emission is observed, the owner/operator shall continue to monitor the flare for at least 3 minutes, or until there are no visible emissions, whichever is shorter.

d.  The owner/operator shall repeat the inspection procedure for the duration of the flaring event, or until a violation is documented in accordance with Part 5.  After a violation is documented, no further inspections are required until the beginning of a new calendar day.

[Regulation 6-301, 2-1-403]

  - The owner/operator shall comply with one of the following requirements if visual inspection is used:

a.  If EPA Method 9 is used, the owner/operator shall comply with Regulation 6-301 when operating the flare.

b.  If the procedure of Part 4.b.ii is used, the owner/operator shall not operate a flare that has visible emissions for three consecutive minutes.

[Regulation 2-6-403]

  - The owner/operator shall keep records of all flaring events, as defined in Part 3.  The owner/operator shall include in the records the name of the person performing the visible emissions check, whether video monitoring or visual inspection (EPA Method 9 or visual inspection procedure of Part 4) was used, the results of each inspection, and whether any violation of this condition (using visual inspection procedure in Part 4) or Regulation 6-301 occurred (using EPA Method 9).                                                  [Regulation 2-6-501; 2-6-409.2]

  - The owner/operator shall operate S-398 to burn only process upset gases as defined by 60.101(e) or fuel gas as defined by 60.101(d) that is released to it as a result of relief valve leakage or other emergency malfunctions.                 [40 CFR 60.104(a)(1); Regulation 2-1-403]

CONDITION 18629

Conditions for S-352, S-353, S-354, S-355, S-356, S-357

May 30, 1989 PSD Permit Amendments (first issued March 3, 1986)

Permit NSR 4-4-3 SFB 85-03

[Obsolete – Approval to Construct executed in a timely manner]

[Obsolete – Approval to Construct executed in a timely manner]

III.	Facilities Operation

All equipment, facilities and systems installed or used to achieve compliance with the terms and conditions of this Approval to Construct/Modify shall at all times be maintained in good working order and be operated as efficiently as possible so as to minimize air pollutant emissions.

IV.	Malfunction

The Regional Administrator shall be notified by telephone within two working days following any failure of air pollution control equipment, process equipment, or of any process to operate in a normal manner which results in an increase in emissions above any allowable emissions limit stated in Section IX of these conditions.  In addition, the Regional Administrator shall be notified in writing within 15 days of any such failure.  This notification shall include a description of the malfunctioning equipment or abnormal operation, the date of the initial failure, the period of time over which emissions were increased due to the failure, the cause of the failure, the estimated resultant emissions in excess of those allowed under Section IX of these conditions, and the methods utilized to restore normal operations.  Compliance with this malfunction notification provision shall not excuse or otherwise constitute a defense to any violations of this permit or of any law or regulations which such malfunction may cause.

V.	Right to Entry

The Regional Administrator, the head of the State Air Pollution Control Agency, the head of the responsible local air pollution control agency, and/or their authorized representatives, upon presentation of credentials, shall be permitted:

A.  to enter upon the premises where the source is located or in which any records are required to be kept under the terms and conditions of this Approval to Construct/Modify; and

B.  at reasonable times to have access to and copy any records required to be kept under the terms and conditions of this Approval to Construct/Modify; and

CONDITION 18629

Conditions for S-352, S-353, S-354, S-355, S-356, S-357

C.  to inspect any equipment, operation, or method required in this Approval to Construct/Modify; and

D.  to sample emissions from this source.

VI.	Transfer of Ownership

In the event of any changes in control or ownership of facilities to be constructed or modified, this Approval to Construct/Modify shall be binding on all subsequent owners and operators.  The applicant shall notify the succeeding owner and operator of the existence of this Approval to Construct/Modify and its conditions by letter, a copy of which shall be forwarded to the Regional Administrator and the State and local Air Pollution Control Agency.

VII.	Severability

The provisions of this Approval to Construct/Modify are severable, and, if any provisions of this Approval to Construct/Modify is held invalid, the remainder of this Approval to Construct/Modify shall not be affected thereby.

VIII.	Other Applicable Regulations

The owner and operator of the proposed project shall construct and operate the proposed stationary source in compliance with all other applicable provisions of 40 CFR Parts 52, 60 and 61 and all other applicable Federal, State and local air quality regulations.

IX.	Special Conditions

[Obsolete – Approval to Construct executed in a timely manner]

B.  Air Pollution Control Equipment

permit holder shall install, continuously operate, and maintain the following air pollution controls to minimize emissions.  Controls listed shall be fully operational upon startup of the proposed equipment.

1.  Each gas turbine shall be equipped with steam injection for the control of NOx emissions.

2.  Each gas turbine shall be equipped with a Selective Catalytic Reduction (SCR) system for the control of NOx emissions.

CONDITION 18629

Conditions for S-352, S-353, S-354, S-355, S-356, S-357

D.  Operating Limitations

1.  The gas turbines and Heat Recovery Steam Generator (HRG) burners shall be fired only on on refinery fuel gas and natural gas

2.  The firing rate of each gas turbine/HRG burner set shall not exceed 466 MMBTU/hr.

3.  The total fuel firing rate of the Steam/Power Plant shall not exceed 1048 MMBTU/hr.

4.  The permit holder shall maintain records of the amount of fuel used in the gas turbines and the HRG Burners, hours of operation, sulfur content of the fuel, and the ratio of steam injected to fuel fired in each gas turbine, in a permanent form suitable for inspection.  The record shall be retained for at least two years following the date of record and shall be made available to EPA upon request.

E.  Emission Limits for NOx

On or after the date of startup, the permit holder shall not discharge from the gas turbine/HRG Burner sets NOx in excess of the more stringent of 83 lb/hr total or 25 ppmv at 15% O2 (3-hour average), or 664 lb/day per set.  The concentration limit shall not apply for 4 hours during startup or 2 hours during shutdown.

F.  Emission Limits for SO2

On or after the date of startup, the permit holder shall not discharge from the gas turbine/HRG Burner sets SO2 in excess of 15.6 lb/hr per set or 44 lb/hr total (3-hour average).  Additionally, total SO2 emissions shall not exceed 34 lb/hr (3 hour average) for more than 36 days per year, nor a total of 153 tons per year (365 days)

G.  Continuous Emission Monitoring

1.  Prior to the date of startup and thereafter, the permit holder shall install, maintain and operate the following continuous monitoring systems downstream of each of the gas turbine/HRG Burner units:

a.  Continuous monitoring systems to measure stack gas NOx and SO2 concentrations.  The systems shall meet EPA monitoring performance specifications (40 CFR 60.13 and 40 CFR 60, Appendix B, Performance Specifications).  Alternatively, the SO2 continuous monitor may be substituted for by a continuous monitoring system measuring H2S in the refinery fuel gas system and daily sampling for total sulfur in the fuel gas.

CONDITION 18629

Conditions for S-352, S-353, S-354, S-355, S-356, S-357

b.  A system to calculate the stack gas volumetric flow rates continuously from actual process variables.

2.  The permit holder shall maintain a file of all measurements, including continuous monitoring system performance evaluations, all continuous monitoring system monitoring device calibration checks, adjustments and maintenance performed on these systems or devices, and all other information required by 40 CFR 60 recorded in a permanent form suitable for inspection.  The file shall be retained for at least two years following the date of such measurements, maintenance, reports and records.

3.  The permit holder shall submit a written report of SO2 emission status and all excess emissions to EPA (Attn:  A-3-3) for every calendar quarter.  The report shall include the following:

a.  If fuel gas samples are used to determine SO2 emissions:

(1)  The total measured sulfur concentration in each fuel gas sample for the calendar quarter.

(2)  The daily average sulfur content in the fuel gas, daily average SO2 mass emission rate (lb/hr), and total tons per year of SO2 emitted for the last 365 consecutive days.  Total SO2 emissions exceeding 34 lb/hr must be identified.

b.  The magnitude of excess emissions computed in accordance with 40 CFR 60.13(h), any conversion factors used, and the date and time of commencement and completion of each time period of excess emissions.

c.  Specific identification of each period of excess emissions that occurs during startups, shutdowns and malfunctions of the cogeneration gas turbine system.  The nature and cause of any malfunction (if known) and the corrective action taken or preventative measures adopted shall also be reported.

d.  The date and time identifying each period during which the continuous monitoring system was inoperative except for zero and span checks, and the nature of the system repairs or adjustments.

e.  When no excess emissions have occurred or the continuous monitoring system has not been inoperative, repaired, or adjusted, such information shall be stated in the report.

f.  Excess emissions shall be defined as any three-hour period during which the average emissions of NOx and/or SO2 as measured by the continuous monitoring system and/or calculated from the daily average of the total sulfur in the fuel gas, exceeds the NOx and/or SO2 maximum emission limits set for each of the pollutants in Conditions IX.E and IX.F. above

CONDITION 18629

Conditions for S-352, S-353, S-354, S-355, S-356, S-357

g.  Excess emissions indicated by the CEM system shall be considered violations of the applicable emission limits for the purpose of this permit.

H.  New Source Performance Standards

The proposed cogeneration facility is subject to the Federal regulations entitled Standards of Performance for New Stationary Sources (40 CFR 60).  The permit holder shall meet all applicable requirements of Subparts A and GG of this regulation.

X.	Agency Notifications

All correspondence as required by this Approval to Construct/Modify shall be forwarded to:

A.	Director, Air Management Division (Attn:  A-3-3)

EPA Region 9

215 Fremont Street

San Francisco, CA 94105 (415/974-8034)

B.	Chief, Stationary Source Division

California Air Resources Board

P O Box 2815

Sacramento, CA 95812

C.	Air Pollution Control Officer

Bay Area Air Quality Management District

939 Ellis Street

San Francisco, CA 94109

CONDITION 18680

Conditions for S-294

1.	The Phil Tite EVR Phase I Vapor Recovery System, including all associated plumbing and components, shall be operated and maintained in accordance with the most recent version of California Air Resources Board (CARB) Executive Order VR-101. Section 41954(f) of the California Health and Safety Code prohibits the sale, offering for sale, or installation of any vapor control system unless the system has been certified by the state board.

2.	The owner or operator shall conduct and pass a Rotatable Adaptor Torque Test (CARB Test Procedure TP201.1B) and either a Drop Tube/Drain Valve Assembly Leak Test (TP201.1C) or, if operating drop tube overfill prevention devices ("flapper valves"), a Drop Tube Overfill Prevention Device and Spill Container Drain Valve Leak Test (TP201.1D) at least once in each 36-month period.  Measured leak rates of each component shall not exceed the levels specified in VR-101.  Results shall be submitted to BAAQMD within 15 days of the test date in a District-approved format.

CONDITION 19278

Conditions for S-1001, S-1002, S-1003

1.	Effective April 1, 2004, the owner/operator shall conduct the following District-approved analyses at least once per calendar year:

a.  H2S concentration in the fuel gas at the inlet and outlet of each refinery fuel gas treatment system,

b.  H2S concentration in the sour water at the inlet and outlet of each sour water stripper system.,

c.  H2S concentration in the inlet and outlet (upstream of any tailgas thermal oxidizer) of each sulfur plant,

d.  ammonia concentration in the sour water stream at the inlet and outlet of each sour water stripper system				[Regulation 9-1-313.2]

2.	The owner/operator shall summarize the results of these analyses in a written report to the District within 30 days of the analyses.  The report shall include a determination of compliance or noncompliance with the 95% removal and retention requirements of Regulation 9-1-313.2.  Each analysis and report shall be retained onsite for at least 5 years.

[Regulation 9-1-313.2]

3.	An annual District-approved source test shall be performed to verify compliance with the requirements of Regulation 6-330.  A copy of the source test results shall be provided to the District Director of Compliance and Enforcement within 45 days of the test.

[Regulation 6-330]

CONDITION 19476

Conditions for S-451

1.	The total throughput at tank S-451 shall not exceed 11,000,000 barrels in any consecutive 12-month period.				[Cumulative Increase]

2.	S-451 shall comply with the following design requirements, in addition to any others required by Regulation 8, Rule 5, NSPS Subpart Kb or NESHAP Subpart CC:

a.  adjustable roof legs, if used, must be equipped with vapor boot seals, or with an equivalent vapor loss control device approved by the District		[BACT, Cumulative Increase]

3.	Monthly records of the type and net amount of materials stored at S-451 shall be kept in a District-approved log for at least 5 years and shall be made available to the District upon request.					[Cumulative Increase]

CONDITION 19488

CONDITIONS FOR S-50, 51, 52

1.  The owner/operator of turbine startup engines S-50, S-51 and S-52 shall operate each of these engines no more than 100 hours per calendar year.                                   [Cumulative Increase]

2.  The owner/operator of S-50, S-51 and S-52 shall keep monthly records of the operating time of each engine.  These records shall be kept for at least 5 years and shall be made available to the District upon request.                                                                          [Regulation 9-8-502, 1-441]

CONDITIONS FOR S-53, 54, 55, 56, 57, 58, 59

3.  The owner/operator of emergency standby engines S-53, S-54, S-55, S-56, S-57, S-58, and S-59 shall operate these engines only for emergency use or for reliability-related activities.  Operations for reliability-related activities shall not exceed 100 hours per calendar year for each engine.  Operation for emergency use is unlimited.                                  [Regulation 9-8-330]

4.  Emergency use is defined as the use of an emergency standby engine during any of the following:

a. In the event of loss of regular natural gas supply;

b. In the event of failure of regular electric power supply;

c. Flood mitigation;

d. Sewage overflow mitigation;

e. Fire;

f. Failure of a primary motor, but only for such time as needed to repair or replace the primary

motor.                                                                                                             [Regulation 9-8-231]

5.  Reliability-related activities is defined as the use of an emergency standby engine during any of the following:                                                                                                  [Regulation 9-8-232]

a. Operation of an emergency standby engine to test its ability to perform for an emergency use;

b. Operation of an emergency standby engine during maintenance of a primary motor.

6.  Each emergency standby engine shall be equipped with either:                     [Regulation 9-8-530]

a. A non-resettable totalizing meter that measures and records hours of operation.

b. A non-resettable fuel usage meter

7.  All records shall be kept for at least five years, and shall be available for inspection by District

staff upon request. The owner/operator shall keep a monthly log of usage that shall indicate the

following:                                                                                            [Regulations 9-8-530, 1-441]

a. Hours of operation (total)

b. Hours of operation (emergency)

c. the nature of the emergency condition.

CONDITION 20620

1.     By October 11, 2004, the owner/operator shall submit a complete application for a significant revision to the Major Facility Review permit to incorporate the limits, compliance options, and monitoring requirements in 40 CFR 63, Subpart UUU, National Emission Standards for Hazardous Air Pollutants for Petroleum Refineries:  Catalytic Cracking Units, Catalytic Reforming Units, and Sulfur Recovery Units.

[Basis:  40 CFR 63, Subpart UUU]

2.     By April 11, 2005, the owner/operator shall submit an Operation, Maintenance and Monitoring Plan for District review in accordance with 40 CFR 63.1574(f).  The plan shall be submitted to the Director of Enforcement.		[Basis:  40 CFR 63.1574(f)]

CONDITION 20773

This condition applies to tanks that are exempt from Regulation 8, Rule 5, Storage of Organic Liquids, due to the exemption in Regulation 8-5-117 for storage of organic liquids with a true vapor pressure of less than or equal to 25.8 mm Hg (0.5 psia).

1.     Whenever the type of organic liquid in the tank is changed, the owner/operator shall verify that the true vapor pressure at the storage temperature is less than or equal to 25.8 mm Hg (0.5 psia).  The owner/operator shall use Lab Method 28 from Volume III of the District's Manual of Procedures, Determination of the Vapor Pressure of Organic Liquids from Storage Tanks.  For materials listed in Table 1 of Regulation 8 Rule 5, the owner/operator may use Table 1 to determine vapor pressure, rather than Lab Method 28.  If the results are above 25.8 mm Hg (0.5 psia), the owner/operator shall report non-compliance in accordance with Standard Condition I.F and shall submit an application to the District for a new permit to operate for the tank as quickly as possible.		[Basis:  8-5-117 and 2-6-409.2]

2.     The results of the testing shall be maintained in a District-approved log for at least five years from the date of the record, and shall be made available to District staff upon request.

[Basis:  2-6-409.2]

CONDITION 21092

CONDITIONS FOR S-300

1.	The owner/operator of S-300 shall not exceed a total charging rate to S-300 (Coking Unit 200) of 81,000 barrels on any day.			[Cumulative Increase]

2.	The owner/operator shall maintain a file which contains (1) all measurements, records, charts and other data which must be collected pursuant to the provisions of this conditional permit and (2) such other data and calculations necessary to determine actual emissions from emission points covered by this permit.  This file (which may contain confidential or proprietary data) shall include, but not be limited to: records of quantities of crude oil and other hydrocarbons processed on an actual daily basis.  This material shall be kept available for District inspection for a period of at least 5 years following the date on which such measurements, records or other data are made or recorded.		[BACT, Cumulative Increase]

3.	Each month, within 30 days of the end of the month, the owner/operator shall make an operational report to the APCO.  Each monthly report shall include the following information for the month being reported:

a.  S-300 daily charging rate for all feed streams	[BACT, Cumulative Increase]

CONDITION 21093

CONDITIONS FOR S-350

1a.	The owner/operator of S-350 (Crude Unit 267) shall not process crude oil at S-350 with a sulfur content in excess of 1.5 wt %.			[Cumulative Increase]

1b.	The owner/operator shall sample and analyze the crude feed to S-350 to determine the sulfur content each time a new tanker shipment or pipeline delivery of crude is introduced into the S-350 feed tanks.				[Cumulative Increase]

2.	The owner/operator of S-350 shall not exceed an S-350 feed rate of 30,000 bbl per day on a 12 month rolling average basis.  The S-350 feed rate shall never exceed 33,000 bbl on any calendar day.  The 33,000 bbl/day limit and 30,000 bbl/day 12 month rolling average limit are absolute limits and may not be corrected for instrument error.	[Cumulative Increase]

3.	The owner/operator of S-350 shall maintain monthly records of "calendar day" throughput and "12 month rolling average" throughput at S-350 in a District-approved log.  The owner/operator shall also maintain records of all sulfur content analyses required by Part 1b.  These records shall be kept for at least five years and shall be made available to the District upon request.				[Cumulative Increase]

CONDITION 21094

CONDITIONS FOR S-460 HYDROTREATER

1.	The owner/operator of S-460 shall not exceed a feed rate of 35,000 bbl/day on a monthly average basis at this unit.				[Regulation 2-1-234]

2.	The owner/operator of S-460 shall maintain the following records in a District-approved log.  These records shall be kept for at least 5 years and shall be made available to the District upon request.

a.  Daily records of feed throughput

b.  Average daily feed rate for each calendar month		[Regulation 2-1-234]

CONDITION 21095

CONDITIONS FOR S-304 HYDROTREATER

1.	The owner/operator of S-304 shall not exceed a feed rate of 12,198 bbl/day on a monthly average basis.				[Regulation 2-1-234]

2.	The owner/operator of S-304 shall maintain the following records in a District-approved log.  These records shall be kept for at least 5 years and shall be made available to the District upon request.

a.  Daily records of feed throughput

b.  Average daily feed rate for each calendar month		[Regulation 2-1-234]

CONDITION 21096

CONDITIONS FOR S-461 HEATER

1.	The owner/operator of the S-461 heater shall fire only refinery fuel gas or natural gas at this unit.				[BACT, Cumulative Increase]

2.	Based on refinery gas HHV, the owner/operator of S-461 shall not exceed the following firing rates:

a.  50.2 million BTU/hr

b.  439,800 million BTU in any consecutive 12-month period.	[Cumulative Increase]

3a.	The owner/operator of S-461 shall abate emissions from S-461 at the A-461 SCR system whenever S-461 is operated.		[BACT, Cumulative Increase]

3b.	The owner/operator of A-461 shall not exceed the following emission rates from S-461/A-461 except during startups and shutdowns.  Startups and shutdowns shall not exceed 24 consecutive hours.   The 24 consecutive-hour startup period is in addition to heater dryout/warmup periods, which shall not exceed 72 consecutive hours.

NOx	10 ppmv @ 3% oxygen (3 hr average)	[BACT, Cumulative Increase]

CO	28 ppmv @ 3% oxygen (8 hr average) at 25.1 MM BTU/hr and higher firing rates, 50 ppmv @ 3% oxygen (8 hr average) at firing rates below 25.1 MM BTU/hr			[BACT, Cumulative Increase]

POC	5.5 lb/MM ft3		[Cumulative Increase]

PM10	7.6 lb/MM ft3		[Cumulative Increase]

ammonia	10 ppmv @ 3% oxygen (8 hr average)	[Toxic Management]

Note:  Part 3b shall not apply until after the conclusion of the initial startup of S-461.

4.	The owner/operator shall equip S-461 with a District-approved continuous fuel flow monitor and recorder in order to determine fuel consumption.  A parametric monitor as defined in Regulation 1-238 is not acceptable.  The owner/operator shall keep continuous fuel flow records for at least five years and shall make these records available to the District upon request.				[Cumulative Increase]

5a.	The owner/operator shall install, calibrate, maintain, and operate a District-approved continuous emission monitor and recorder for NOx and O2.  The owner/operator shall keep NOx and O2 data for at least five years and shall make these records available to the District upon request.			[BACT, Cumulative Increase]

5b.	Following the initial source test required in Part 8, the owner/operator shall monitor compliance with the CO emission rate limit in Part 3b with a District-approved semi-annual source test, with at least one source test per year deemed by the District to be representative of normal operation.  The owner/operator shall submit the source test results to the District staff no later than 60 days after the source test.  The time interval between source tests shall not exceed 8 months.  CO source tests performed by the District may be substituted for semi-annual CO source tests.  If two or more CO source tests, over any consecutive five year period, indicate a CO emission rate of 200 ppmv @ 3% O2 or higher, the owner/operator shall install and operate a District-approved continuous CO monitor/recorder within the time period specified in the District Manual of Procedures.[BACT, Cumulative Increase]

6.	The owner/operator shall use only refinery fuel gas at S-461 which does not exceed the following limits:

a.  100 ppmv totaled reduced sulfur (TRS), averaged over a calendar day

b.  45 ppmv TRS, averaged over any rolling consecutive 365-day period.

[BACT, Cumulative Increase]

7a.	The owner/operator shall test refinery fuel gas prior to combustion at S-461 to determine total reduced sulfur (TRS) concentration by GC analysis at least once per 8 hour shift (3 times per calendar day).  At least 90% of these samples shall be taken each calendar month.  No readable samples or sample results shall be omitted.  TRS shall include hydrogen sulfide, methyl mercaptan, methyl sulfide, dimethyl disulfide.  If the TRS value, averaged over any rolling consecutive 365-day period, exceeds 35 ppmv, the owner/operator shall install and operate a District-approved continuous monitor/recorder to determine the total reduced sulfur content of the refinery fuel gas prior to combustion in S-461 within the time period specified in the District Manual of Procedures.		[BACT, Cumulative Increase]

7b.	To demonstrate compliance with Part 6, the owner/operator shall measure and record the 24-hour average TRS content and the 365-day average TRS content of the refinery fuel gas fired in S-461, unless required to operate a District-approved continuous monitor/recorder by Part 7a.  The owner/operator shall keep TRS records, whether they are the results of GC analysis or continuous analyzer data, for at least five years and shall make these records available to the District upon request.			[BACT, Cumulative Increase]

8.	No later than 90 days from the startup of the S-461, the owner/operator shall conduct District-approved source tests to determine initial compliance with the limits in Part 3b for NOx, CO, POC, PM10 and ammonia.  The owner/operator shall conduct the source tests in accordance with Part 9.  The owner/operator shall submit the source test results to the District staff no later than 60 days after the source test.         [BACT, Cumulative Increase, Toxic Management]

9.	The owner/operator shall obtain approval for all source test procedures from the District's Source Test Section prior to conducting any tests.  The owner/operator shall comply with all applicable testing requirements for continuous emissions monitors as specified in Volume V of the District's Manual of Procedures. The owner/operator shall notify the District's Source Test Section, in writing, of the source test protocols and projected test dates at least 7 days prior to testing.		[BACT, Cumulative Increase, Toxic Management]

CONDITION 21097

CONDITIONS FOR S-36 HEATER

1.	The owner/operator of the S-36 heater shall fire only refinery fuel gas or natural gas at this unit.				[BACT, Cumulative Increase]

2.	Based on refinery gas HHV, the owner/operator of S-36 shall not exceed the following firing rates:

a.  82.1 million BTU/hr

b.  719,200 million BTU in any consecutive 12-month period.	[Cumulative Increase]

3a.	The owner/operator of S-36 shall abate emissions from S-36 at the A-36 SCR system whenever S-36 is operated.		[BACT, Cumulative Increase]

3b.	The owner/operator of S-36 shall not exceed the following emission rates from S-36/A-36 except during startups and shutdowns.  Startups and shutdowns shall not exceed 24 consecutive hours.   The 24 consecutive-hour startup period is in addition to heater dryout/warmup periods, which shall not exceed 72 consecutive hours.

NOx	10 ppmv @ 3% oxygen (3 hr average)	[BACT, Cumulative Increase]

CO	28 ppmv @ 3% oxygen (8 hr average)	[BACT, Cumulative Increase]

POC	5.5 lb/MM ft3		[Cumulative Increase]

PM10	7.6 lb/MM ft3		[Cumulative Increase]

ammonia	10 ppmv @ 3% oxygen (8 hr average)	[Toxic Management]

Note:  Part 3b shall not apply until after the conclusion of the initial startup of S-36.

4.	The owner/operator shall equip S-36 with a District-approved continuous fuel flow monitor and recorder in order to determine fuel consumption.  A parametric monitor as defined in Regulation 1-238 is not acceptable.  The owner/operator shall keep continuous fuel flow records for at least five years and shall make these records available to the District upon request.				[Cumulative Increase]

5a.	The owner/operator shall install, calibrate, maintain, and operate a District-approved continuous emission monitor and recorder for NOx and O2.  The owner/operator shall keep NOx and O2 data for at least five years and shall make these records available to the District upon request.			[BACT, Cumulative Increase]

5b.	Following the initial source test required in Part 8, the owner/operator shall monitor compliance with the CO emission rate limit in Part 3b with a District-approved semi-annual source test, with at least one source test per year deemed by the District to be representative of normal operation.  The owner/operator shall submit the source test results to the District staff no later than 60 days after the source test.  The time interval between source tests shall not exceed 8 months.  CO source tests performed by the District may be substituted for semi-annual CO source tests.  If two or more CO source tests, over any consecutive five year period, indicate a CO emission rate of 200 ppmv @ 3% O2 or higher, the owner/operator shall install and operate a District-approved continuous CO monitor/recorder within the time period specified in the District Manual of Procedures.	[BACT, Cumulative Increase]

6.	The owner/operator shall use only refinery fuel gas at S-36 which does not exceed the following limits:

a.  100 ppmv totaled reduced sulfur (TRS), averaged over a calendar day

b.  45 ppmv TRS, averaged over any rolling consecutive 365-day period.

[BACT, Cumulative Increase]

7a.	The owner/operator shall test refinery fuel gas prior to combustion at S-36 to determine total reduced sulfur (TRS) concentration by GC analysis at least once per 8 hour shift (3 times per calendar day).  At least 90% of these samples shall be taken each calendar month.  No readable samples or sample results shall be omitted.  TRS shall include hydrogen sulfide, methyl mercaptan, methyl sulfide, dimethyl disulfide.  If the TRS value, averaged over any rolling consecutive 365-day period, exceeds 35 ppmv, the owner/operator shall install and operate a District-approved continuous monitor/recorder to determine the total reduced sulfur content of the refinery fuel gas prior to combustion in S-36 within the time period specified in the District Manual of Procedures.		[BACT, Cumulative Increase]

7b.	To demonstrate compliance with Part 6, the owner/operator shall measure and record the 24-hour average TRS content and the 365-day average TRS content of the refinery fuel gas fired in S-36, unless required to operate a District-approved continuous monitor/recorder by Part 7a.  The owner/operator shall keep TRS records, whether they are the results of GC analysis or continuous analyzer data, for at least five years and shall make these records available to the District upon request.			[BACT, Cumulative Increase]

8.	No later than 90 days from the startup of the S-36, the owner/operator shall conduct District-approved source tests to determine initial compliance with the limits in Part 3b for NOx, CO, POC, PM10 and ammonia.  The owner/operator shall conduct the source tests in accordance with Part 9.  The owner/operator shall submit the source test results to the District staff no later than 60 days after the source test.         [BACT, Cumulative Increase, Toxic Management]

9.	The owner/operator shall obtain approval for all source test procedures from the District's Source Test Section prior to conducting any tests.  The owner/operator shall comply with all applicable testing requirements for continuous emissions monitors as specified in Volume V of the District's Manual of Procedures. The owner/operator shall notify the District's Source Test Section, in writing, of the source test protocols and projected test dates at least 7 days prior to testing.		[BACT, Cumulative Increase, Toxic Management]

CONDITION 21099

CONDITIONS FOR ULSD PROJECT FUGITIVE COMPONENTS

1.	The owner/operator shall equip all light hydrocarbon control valves installed as part of the USLD Project with live loaded packing systems and polished stems, or equivalent.

[BACT]

2.	The owner/operator shall equip all flanges/connectors installed in the light hydrocarbon piping systems as part of the USLD Project with graphitic-based gaskets unless the service requirements prevent this material.				[BACT]

3.	The owner/operator shall equip all new hydrocarbon centrifugal compressors installed as part of the USLD Project with "wet" dual mechanical seals with a heavy liquid barrier fluid, or dual dry gas mechanical seals buffered with inert gas.		[BACT]

4.	The owner/operator shall equip all new light hydrocarbon centrifugal pumps installed as part of the USLD Project with a seal-less design or with dual mechanical seals with a heavy liquid barrier fluid, or equivalent.				[BACT]

5.	The owner/operator shall integrate all new fugitive equipment installed as part of the USLD Project, in organic service, into the facility fugitive equipment monitoring and repair program.

[BACT]

6.	The Owner/Operator shall submit a count of installed pumps, compressors, valves, and flanges/connectors every 180 days until completion of the project. For flanges/connectors, the owner/operator shall also provide a count of the number of graphitic-based and non-graphitic gaskets used.  The owner/operator has been permitted to install fugitive components (5,410 valves, 2,376 flanges, 3,564 connectors, 26 pumps, 14 compressors) with a total POC emission rate of 8.62 ton/yr.  If there is an increase in the total fugitive component emissions, the plant's cumulative emissions for the project shall be adjusted to reflect the difference between emissions based on predicted versus actual component counts.  The owner/operator shall provide to the District all additional required offsets at an offset ratio of 1.15:1 no later than 14 days after the submittal of the final POC fugitive equipment count.  If the actual component count is less than the predicted, at the completion of the project, the total will be adjusted accordingly and all emission offsets applied by the owner/operator in excess of the actual total fugitive emissions will be credited back to owner/operator prior to issuance of the permits.

[BACT, Cumulative Increase, Toxic Management]

CONDITION 21235

Regulation 9-10 Compliance

CONDITIONS FOR SOURCES S-2, S-3, S-4, S-5, S-7, S-8, S-9, S-10, S-11, S-12, S-13, S-14, S-15, S-16, S-17, S-18, S-19, S-20, S-22, S-29, S-30, S-31, S-43, S-44, S-336, S-337, S-351, S-371, S-372

1.	The following sources are subject to the refinery-wide NOx emission rate and CO concentration limits in Regulation 9-10:	[Regulation 9-10-301 and 305]

S#           Description		             NOx CEM

2      U229, B-301 Heater			No

3      U230, B-201 Heater			No

4      U231, B-101 Heater			No

5      U231, B-102 Heater			No

7      U231, B-103 Heater			No

8      U240, B-1 Boiler			Yes

9      U240, B-2 Boiler			No

10    U240, B-101 Heater			Yes

11    U240, B-201 Heater			No

12    U240, B-202 Heater			No

13    U240, B-301 Heater			Yes

14    U240, B-401 Heater			Yes

15    U244, B-501 Heater			Yes

16    U244, B-502 Heater			Yes

17    U244, B-503 Heater			Yes

18    U244, B-504 Heater			Yes

19    U244, B-505 Heater			Yes

20    U244, B-506 Heater			No

22    U248, B-606 Heater			No

29    U200, B-5 Heater			No

30    U200, B-101 Heater			No

31    U200, B-501 Heater			No

43    U200, B-202 Heater			Yes

44    U200, B-201 PCT Reboil Furnace	Yes

336  U231 B-104 Heater			No

337  U231 B-105 Heater			No

351  U267 B-601/602 Tower Pre-Heaters	Yes

371  U228 B-520 (Adsorber Feed) Furnace	Yes

372  U228 B-521 (Hydrogen Plant) Furnace	Yes

2.	The owner/operator of each source listed in Part 1 shall properly install, properly maintain, and properly operate an O2 monitor and recorder. This Part shall be effective September 1, 2004.					[Regulation 9-10-502]

3.	The owner/operator shall operate each source listed in Part 1, which does not have a NOx CEM within specified ranges of operating conditions (firing rate and oxygen content) as detailed in Part 5.  The ranges shall be established by utilizing data from district-approved source tests.

a.  The NOx Box for units with a maximum firing rate of 25 MM BTU/hr or more shall be established using the procedures in Part 4.

b.  The NOx Box for units with a maximum firing rate less than 25 MM BTU/hr shall be established as follows:  High-fire shall be the maximum rated capacity. Low-fire shall be 20% of the maximum rated capacity. There shall be no maximum or minimum O2.

[Regulation 9-10-502)]

4.	The owner/operator shall establish the initial NOx box for each source subject to Part 3 by June 1, 2004.  The NOx Box may consist of two operating ranges in order to allow for operating flexibility and to encourage emission minimization during standard operation.  The procedure for establishing the NOx box is as follows:

a.  Conduct District-approved source tests for NOx and CO, while varying the oxygen concentration and firing rate over the desired operating ranges for the furnace;

b.  Determine the minimum and maximum oxygen concentrations and firing rates for the desired operating ranges (Note that the minimum O2 at low-fire may be different than the minimum O2 at high-fire.  The same is true for the maximum O2). The owner/operator shall also verify the accuracy of the O2 monitor on an annual basis.

c.  Determine the highest NOx emission factor (lb/MM BTU) over the preferred operating ranges while maintaining CO concentration below 200 ppm; the owner/operator may choose to use a higher NOx emission factor than tested.

d.  Plot the points representing the desired operating ranges on a graph.  The resulting polygon(s) are the NOx Box, which represents the allowable operating range(s) for the furnace under which the NOx emission factor from part 5a is deemed to be valid.

i.  The NOx Box can represent/utilize either one or two emission factors.

ii.  The NOx Box for each emission factor can be represented either as a 4 or 5-sided polygon The NOx box is the area within the 4 or 5-sided polygon formed by connecting the source test parameters that lie about the perimeter of successful approved source tests.  The source test parameters forming the corners of the NOx box are listed in Part 5.

e.  Upon establishment of each NOx Box, the owner/operator shall prepare a graphical representation of the box. The representation shall be made available on-site for APCO review upon request.  The box shall also be submitted to the BAAQMD with permit amendments.

[Regulation 9-10-502]

5.	Except as provided in Part 5b and 5c, the owner/operator shall operate each source within the NOx Box ranges listed below at all times of operation. This part shall not apply to any source that has a properly operated and properly installed NOx CEM.

a.  NOx Box ranges

| Source No. | Emission Factor (lb/MMBtu) | Min O2 at Low Firing (O2% , MMBtu/hr) | Max O2 at Low Firing (O2% , MMBtu/hr) | Min O2 at High Firing (O2% , MMBtu/hr) | Mid O2 at Mid/High Firing (polygon) (O2% , MMBtu/hr) | Max O2 at High Firing (O2% , MMBtu/hr) |
| --- | --- | --- | --- | --- | --- | --- |
| 2 | tbd | tbd | tbd | tbd | tbd | tbd |
| 3 | tbd | tbd | tbd | tbd | tbd | tbd |
| 4 | tbd | tbd | tbd | tbd | tbd | tbd |
| 5 | tbd | tbd | tbd | tbd | tbd | tbd |
| 7 | tbd | tbd | tbd | tbd | tbd | tbd |
| 9 | tbd | tbd | tbd | tbd | tbd | tbd |
| 11 | tbd | tbd | tbd | tbd | tbd | tbd |
| 12 | tbd | tbd | tbd | tbd | tbd | tbd |
| 20 | tbd | tbd | tbd | tbd | tbd | tbd |
| 22 | tbd | tbd | tbd | tbd | tbd | tbd |
| 29 | tbd | tbd | tbd | tbd | tbd | tbd |
| 30 | tbd | tbd | tbd | tbd | tbd | tbd |
| 31 | tbd | tbd | tbd | tbd | tbd | tbd |
| 336 | tbd | tbd | tbd | tbd | tbd | tbd |
| 337 | tbd | tbd | tbd | tbd | tbd | tbd |

The limits listed above are based on a calendar day averaging period for both firing rate and O2%.

b.  Part 5a does not apply to low firing rate conditions (i.e., firing rate less than or equal to 20% of the unit’s rated capacity) during startup or shutdown periods or periods of curtailed operation (ex. during heater idling, refractory dryout, etc.) lasting 5 days or less.  During these conditions the means for determining compliance with the refinery-wide limit shall be accomplished using the method described in 9-10-301.2 (i.e. units out of service and 30-day averaging data).

c.  Part 5a does not apply during any source test required or permitted by this condition.  See Part 7 for the consequences of source test results that exceed the emission factors in Part 5.				[Regulation 9-10-502]

##### 6a.  The owner/operator may deviate from the NOx Box (either the firing rate or oxygen limit) provided that the owner/operator conducts a District-approved source test which replicates the past operation outside of the established ranges.  The source test representing the new conditions shall be conducted no later than the next regularly scheduled source test period, or within eight months, whichever is sooner.  The source test results will establish whether the source was operating outside of the emission factor utilized for the source.  The source test results shall be submitted to the District Source Test manager within 45 days of the test.  As necessary, a permit amendment shall be submitted.

i.  Source Test <= Emission Factor

If the results of this source test do not exceed the higher NOx emission factor in Part 5, or the CO limit in Part 9, the unit will not be considered to be in violation during this period for operating out of the "box."  The facility may submit an accelerated permit program permit application to request an administrative change of the permit condition to adjust the NOx Box operating range(s), based on the new test data.

ii.  Source Test > Emission Factor

If the results of this source test exceed the permitted emission concentrations or emission rates then, utilizing measured emission concentration or rate, the owner/operator shall perform an assessment, retroactive to the date of the previous source test, of compliance with Section 9-10-301.  The unit will be considered to have been in violation of 9-10-301 for each day the facility was operated in excess of the refinery wide limit.  The facility may submit a permit application to request an alteration of the permit condition to change the NOx emission factor and/or adjust the operating range, based on the new test data.	[Regulation 9-10-502]

##### 6b.  The owner/operator must report conditions outside of box within 96 hours of occurrence.

[Regulation 9-10-502]

7.	For each source subject to Part 3, the owner/operator shall conduct source tests at the schedule listed below.  The source tests are performed in order to measure NOx, CO, and O2 at the as-found firing rate, or at conditions reasonably specified by the APCO.  The source test results shall be submitted to the District Source Test manager within 45 days of the test.

##### a.  Source Testing Schedule

i.  Heater  < 25 MMBtu/hr:  One source test per consecutive 12 month period.  The time interval between source tests shall not exceed 16 months.

ii.  Heaters ≥ 25 MMBtu/hr:  Two source tests per consecutive 12 month period.  The time interval between source tests shall not exceed 8 months and not be less than 5 months apart. The source test results shall be submitted to the district source test manager within 45 days of the test.

b.  If the results of any source test under this part exceed the permitted concentrations or emission rates the owner/operator shall follow the requirements of Part 6a(ii).   If the owner/operator chooses not to submit an application to revise the emission factor, the owner/operator shall conduct another Part 7 source test, at the same conditions, within 90 days of the initial test.				[Regulation 9-10-502]

8.	For each source listed in Part 1 with a NOx CEM installed, the owner/operator shall conduct semi-annual District-approved CO source tests at as-found conditions.  The time interval between source tests shall not exceed 8 months.  District conducted CO emission tests associated with District-conducted NOx CEM field accuracy tests may be substituted for the CO semi-annual source tests.			[Regulation 9-10-502]

9.	For any source listed in Part 1 for which any two source test results over any consecutive five year period are greater than or equal to 200 ppmv CO at 3% O2, the owner/operator shall properly install, properly maintain, and properly operate a CEM to continuously measure CO and O2.  The owner/operator shall install the CEM within the time period allowed in the District's Manual of Procedures.		[Regulation 9-10-502, 1-522]

10.	In addition to records required by 9-10-504, the facility must maintain records of all source tests conducted to demonstrate compliance with Parts 1 and 5.   These records shall be kept on site for at least five years from the date of entry in a District approved log and be made available to District staff upon request.		[Recordkeeping, Regulation 9-10-504]

FACILITY-WIDE REQUIREMENTS

Condition 20989

A.  THROUGHPUT LIMITS

The following limits are imposed through this permit in accordance with Regulation 2-1-234.3.  Sources require BOTH hourly/daily and annual throughput limits (except for tanks and similar liquid storage sources, and small manually operated sources such as cold cleaners which require only annual limits).  Sources with previously imposed hourly/daily AND annual throughput limits are not listed below; the applicable limits are given in the specific permit conditions listed above in this section of the permit.  Also, where hourly/daily capacities are listed in Table II-A, these are considered enforceable limits for sources that have a New Source Review permit.  Throughput limits imposed in this section and hourly/daily capacities listed in Table  II-A are not federally enforceable for grandfathered sources.  Grandfathered sources are indicated with an asterisk in the source number column in the following table.  Refer to Title V Standard Condition J for clarification of these limits.

In the absence of specific recordkeeping requirements imposed as permit conditions, monthly throughput records shall be maintained for each source.

| source number | hourly / daily throughput limit | annual throughput limit (any consecutive 12-month period unless otherwise specified) |
| --- | --- | --- |
| 15 | Table II-A | 19.9 E 6 therm total at S-15 through S-19 |
| 16 | Table II-A | 19.9 E 6 therm total at S-15 through S-19 |
| 17 | Table II-A | 19.9 E 6 therm total at S-15 through S-19 |
| 18 | Table II-A | 19.9 E 6 therm total at S-15 through S-19 |
| 19 | Table II-A | 19.9 E 6 therm total at S-15 through S-19 |
| 20 | Table II-A | 1.9 E 6 therm |
| 21 | Table II-A | 0.7 E 6 therm |
| 22 | Table II-A | 2.6 E 6 therm |
| 29 | Table II-A | 8.6 E 6 therm |
| 30 | Table II-A | 4.2 E 6 therm |
| 31 | Table II-A | 1.7 E 6 therm |
| 43 | Table II-A | 19.1 E 6 therm |
| 44 | Table II-A | 3.8 E 6 therm |
| *97 | NA for tank | 1.1 E 7 bbl |
| *100 | NA for tank | 4.38 E 6 bbl |
| 101 | NA for tank | 3.68 E 9 gal |
| 102 | NA for tank | 3.68 E 9 gal |
| 106 | NA for tank | 3.68 E 9 gal |
| *107 | NA for tank | 8.76 E 6 bbl |
| *110 | NA for tank | 1.40 E 7 bbl |
| *111 | NA for tank | 1.31 E 7 bbl |
| *112 | NA for tank | 1.49 E 7 bbl |
| *113 | NA for tank | 1.49 E 7 bbl |
| *114 | NA for tank | 1.31 E 7 bbl |
| *115 | NA for tank | 4.38 E 6 bbl |
| *117 | NA for tank | 8.76 E 5 bbl |
| *118 | NA for tank | 15,000 bbl |
| *121 | NA for tank | 3.52 E 4 bbl |
| *122 | NA for tank | 4.38 E 6 bbl |
| *123 | NA for tank | 5.1 E 6 bbl |
| *124 | NA for tank | 4.38 E 6 bbl |
| *125 | NA for tank | 1.05 E 7 bbl |
| *126 | NA for tank | 1.05 E 7 bbl |
| *128 | NA for tank | 5.1 E 6 bbl |
| 129 | NA for tank | 4.6 E 6 bbl |
| 133 | NA for tank | 8.76 E 5 bbl |
| *134 | NA for tank | 1.31 E 7 bbl |
| *139 | NA for tank | 2.74 E 6 bbl |
| *140 | NA for tank | 2.74 E 6 bbl |
| 150 | NA for tank | 4.38 E 7 bbl |
| 151 | NA for tank | 4.38 E 7 bbl |
| *177 | NA for tank | 2.63 E 7 bbl |
| 178 | NA for tank | 3.50 E 7 bbl |
| 183 | NA for tank | 4.38 E 5 bbl |
| 184 | NA for tank | 4.38 E 6 bbl |
| *186 | NA for tank | 4.38 E 6 bbl |
| *193 | NA for tank | 100 bbl |
| *194 | NA for tank | 100 bbl |
| *195 | NA for tank | 5.0 E 4 bbl |
| 196 | NA for tank | 5.0 E 4 bbl |
| *216 | NA for tank | 4.6 E 6 bbl |
| *238 | NA for tank | 1.00 E 6 bbl |
| *239 | NA for tank | 8.76 E 6 bbl |
| *254 | NA for tank | 7.01 E 7 bbl |
| *255 | NA for tank | 7.01 E 7 bbl |
| *256 | NA for tank | 7.01 E 7 bbl |
| *257 | NA for tank | 7.01 E 7 bbl |
| *258 | NA for tank | 7.01 E 7 bbl |
| *259 | NA for tank | 7.01 E 7 bbl |
| *261 | NA for tank | 7.01 E 7 bbl |
| 294 | 20 gpm | 400,000 gallons |
| *301 | Table II-A | 89,425 long ton for S-301, 302, 303 |
| *302 | Table II-A | 89,425 long ton for S-301, 302, 303 |
| *303 | Table II-A | 89,425 long ton for S-301, 302, 303 |
| 304 (until modified in accordance with A/C 5814, then deleted from this table) | Table II-A | 3.47 E 6 bbl |
| 305 | Table II-A | 9.23 E 6 bbl |
| 306 | Table II-A | 7.67 E 6 bbl |
| 307 | Table II-A | 1.39 E 7 bbl |
| *308 | Table II-A | 5.11 E 6 bbl |
| *309 | Table II-A | 6.11 E 6 bbl |
| *318 | Table II-A | 3.3 E 7 bbl |
| *319 | Table II-A | 3.51 E 6 bbl |
| 324 | Table II-A | 3.68 E 9 gallons |
| *334 | NA for tank | 6.51 E 6 bbl |
| 336 | Table II-A | 9.2 E 6 therm |
| 337 | Table II-A | 2.8 E 6 therm |
| *338 | Table II-A | 6.6 E 10 ft3 |
| *339 | Table II-A | 5.26 E 7 bbl |
| 340 | NA for tank | 7.67 E 6 bbl |
| 341 | NA for tank | 4.38 E 7 bbl |
| 342 | NA for tank | 4.38 E 7 bbl |
| 343 | NA for tank | 4.38 E 7 bbl |
| 351 | Table II-A | 8.4 E 6 therm |
| 360 | NA for tank | 2.78 E 6 bbl |
| 370 | Condition 12121 | 4.03 E6 bbl |
| 371 | Table II-A | 4.8 E6 therm for S-371/372 |
| 372 | Table II-A | 4.8 E6 therm for S-371/372 |
| 380 | 0.3 ton/hr | 2,628 ton |
| 381 | 420,000 gal/hr | 3.68 E 9 gal |
| 382 | 420,000 gal/hr | 3.68 E 9 gal |
| 383 | 420,000 gal/hr | 3.68 E 9 gal |
| 384 | 420,000 gal/hr | 3.68 E 9 gal |
| 385 | Table II-A | 3.68 E 9 gal |
| 386 | 1800 gal/hr | 1.6 E 7 gal |
| 387 | Table II-A | 7.884 E 6 gal |
| 388 | Table II-A | 153,300 ton |
| 389 | 0.21 ton/hr | 1840 ton |
| 390 | N/A for tank | 7.884 E 6 gal |
| 392 | N/A for tank | 7.884 E 6 gal |
| 400 | N/A for sump | 3.68 E 9 gal |
| 401 | N/A for sump | 3.68 E 9 gal |
| 425 | Table II-A | 25,000 bbl/day at S-425 and S-426 (annual average) |
| 426 | Table II-A | 25,000 bbl/day at S-425 and S-426 (annual average) |
| 432 | Table II-A | 2.8 E6 bbl |
| 435 | Table II-A | 6.6 E 6 bbl |
| 436 | Table II-A | 4.7 E 6 bbl |
| 437 | Table II-A | 9.1 E 9 ft3 |
| 460 | Table II-A | 11.68 E 6 bbl |
| 462 | Table II-A | 1.533 E 9 ft3 |
| 463 | Table II-A | 73.365 E 6 lb |
| *1001 | Table II-A | 89,425 long ton for S-1001, 1002, 1003 (98,915 long ton after S-1002, 1003 modified in accordance with A/C 5814 |
| *1002 | Table II-A | 89,425 long ton for S-1001, 1002, 1003 (98,915 long ton after S-1002, 1003 modified in accordance with A/C 5814 |
| *1003 | Table II-A | 89,425 long ton for S-1001, 1002, 1003 (98,915 long ton after S-1002, 1003 modified in accordance with A/C 5814 |
| 1007 | Table II-A | 3.68 E 9 gal |
| 1008 | Table II-A | 3.68 E 9 gal |
| 1009 | Table II-A | 3.68 E 9 gal |

B.  OTHER REQUIREMENTS

1.	The owner/operator shall notify the District in writing by fax or email no less than three calendar days in advance of any scheduled startup or shutdown of any process unit, and, for any unscheduled startup or shutdown of a process unit, within 48 hours or within the next normal business day. The notification shall be sent in writing by fax or email to the Director of Enforcement and Compliance.  This requirement is not federally enforceable.                                 [Regulation 2-1-403]

# APPLICABLE LIMITS & COMPLIANCE MONITORING REQUIREMENTS

This section has been included only to summarize the applicable emission limits contained in Section IV, Source-Specific Applicable Requirements, of this permit.  The following tables show the relationship between each emission limit and the associated compliance monitoring provisions, if any.  The monitoring frequency column indicates whether periodic (P) or continuous (C) monitoring is required.  For periodic monitoring, the frequency of the monitoring has also been shown, using the following codes: annual (A), semi-annual (SA), hourly (H), quarterly (Q), monthly (M), weekly (W), daily (D), or on an event basis (E).  No monitoring (N) has been required if the current applicable rule or regulation does not require monitoring, and the operation is unlikely to deviate from the applicable emission limit based upon the nature of the operation.

| Table VII – All Sources Facility-Specific Generally Applicable Requirements |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | 40 CFR 61, Subpart FF, 61.342 (a) | Y |  | Exemption for facilities with less than 10 Mg/yr of benzene in waste | 40 CFR 61, Subpart FF, 61.357 (c) | P/A | report |
| HAP | 40 CFR 63, Subpart CC, 63.647(a) | Y |  | wastewater standards of 40 CFR 61, Subpart FF, 61.340 to 61.355 are applicable | 40 CFR 63, Subpart CC, 63.654(a) | P/A | report |
| VOC | BAAQMD Regulation 8-2-301 | Y |  | emission streams with 15 lb/day AND 300 ppm total carbon on a dry basis prohibited | None | N | None |
| VOC | BAAQMD Regulation 8-4-302.1 and SIP 8-4-302 | N Y |  | 5 ton/yr per solvent, surface coating source | None | N | None |
| VOC | BAAQMD Regulation 8-5-328.2 | Y |  | Tank cleaning control device standard includes 90% abatement efficiency requirement | BAAQMD 8-5-502 | P/A | source test |
| VOC | NSPS Subpart Kb 60.112b(a)(2) and NESHAP Subpart CC 63.647(a) | Y |  | VOC concentrations shall not exceed 500 ppmv above background | NESHAP Subpart CC 63.642(e), 63.642(f) and 63.654(i)(4) | P/Q-visual and A-measurements and reports | Visual inspections, portable HC detector (EPA Method 21) and records of detectable emissions, inspections and repairs |
| Opacity | BAAQMD Regulation 6-301 | Y |  | Ringelmann No. 1 for no more than 3 minutes/hour | None | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous fired sources | N | None |
| FP | BAAQMD Regulation 6-311 | Y |  | No emissions from source > rate specified in rule | None for gaseous fired sources | N | None |
| SO2 | BAAQMD Regulation 9-1-301 | Y |  | ground level SO2 concentrations (0.5 ppm for 3 min; 0.25 ppm for 60 min; 0.05 ppm for 24 hr) | at the request of the District, 9-1-501 requires compliance with BAAQMD 1-510 | C | SO2 GLM |
| SO2 | BAAQMD Regulation 9-1-302 | Y |  | 300 ppm SO2 (dry) | None | N | None |
| SO2 | BAAQMD Regulation 9-1-313.2 | N |  | operation of a sulfur removal and recovery system that removes and recovers: 95% of H2S from refinery fuel gas, 95% of H2S and ammonia from process water streams; operation of a sulfur recovery plant | BAAQMD Condition 19278, Part 1 | P/A | source test |
| SO2 | SIP Regulation 9-1-313.2 | Y |  | operation of a sulfur removal and recovery system that removes and recovers: 95% of H2S from refinery fuel gas, 95% of H2S and ammonia from process water streams | BAAQMD Condition 19278, Part 1 | P/A | source test |
| H2S | BAAQMD Regulation 9-2-301 | N |  | Ground level concentrations < 0.06 ppm averaged over 3 consecutive minutes or < 0.03 ppm averaged over any 60 consecutive minutes | BAAQMD 9-2-501, 1-510, 1-530 1-540, 1-542, 1-543 and 1-544 | C | Area Monitoring |

| Table VII – A.1 Applicable Limits and Compliance Monitoring Requirements S-2 – Unit 229, B-301 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/A | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.2 | Y |  | 346.5 MM BTU/hr averaged over any year at S-2, S-3, S-4, S-5, S-7 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/A | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous fired sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.2 Applicable Limits and Compliance Monitoring Requirements S-3 – Unit 230, B-201 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.2 | Y |  | 346.5 MM BTU/hr averaged over any year at S-2, S-3, S-4, S-5, S-7 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour (gaseous fuel firing) | None | N | None |
| Opacity | BAAQMD 6-301 | Y | 4/1/04 | Ringelmann 1 for no more than 3 minutes in any hour (liquid fuel firing) | BAAQMD Condition 1694, Part A.2c | P/E (before 1 million gallons of liquid fuel combusted) | visual inspection |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 (gaseous fuel firing) | None | N | None |
| FP | BAAQMD 6-310.3 | Y | 4/1/04 | 0.15 grain/dscf @ 6% O2 (liquid fuel firing) | BAAQMD Condition 1694, Part A.2c | P/E (before 1 million gallons of liquid fuel combusted) | visual inspection |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.3 Applicable Limits and Compliance Monitoring Requirements S-4 – Unit 231, B-101 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.2 | Y |  | 346.5 MM BTU/hr averaged over any year at S-2, S-3, S-4, S-5, S-7 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.4 Applicable Limits and Compliance Monitoring Requirements S-5 – Unit 231, B-102 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.2 | Y |  | 346.5 MM BTU/hr averaged over any year at S-2, S-3, S-4, S-5, S-7 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.5 Applicable Limits and Compliance Monitoring Requirements S-7 – Unit 231, B-103 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.2 | Y |  | 346.5 MM BTU/hr averaged over any year at S-2, S-3, S-4, S-5, S-7 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour (gaseous fuel firing) | None | N | None |
| Opacity | BAAQMD 6-301 | Y | 4/1/04 | Ringelmann 1 for no more than 3 minutes in any hour (liquid fuel firing) | BAAQMD Condition 1694, Part A.2c | P/E (before 1 million gallons of liquid fuel combusted) | visual inspection |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 (gaseous fuel firing) | None | N | None |
| FP | BAAQMD 6-310.3 | Y | 4/1/04 | 0.15 grain/dscf @ 6% O2 (liquid fuel firing) | BAAQMD Condition 1694, Part A.2c | P/E (before 1 million gallons of liquid fuel combusted) | visual inspection |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.6 Applicable Limits and Compliance Monitoring Requirements S-8 – Unit 240, B-1 Boiler |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx |  | Y |  | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.1 | C | CEM |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.1 | Y |  | 993.7 MM BTU/hr averaged over any year at S-8, S-9, S-10, S-11, S-12, S-13, S-14 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | Y |  | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.1 | C | CEM |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-304 | Y |  | During tube cleaning, Ringelmann No. 2 for 3 min/hr and 6 min/billion BTU in 24 hours; applies to sources rated over 140 MM BTU/hr (with tubes) | None for gaseous-fueled sources | N | None |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.7 Applicable Limits and Compliance Monitoring Requirements S-9 – Unit 240, B-2 Boiler |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.1 | Y |  | 993.7 MM BTU/hr averaged over any year at S-8, S-9, S-10, S-11, S-12, S-13, S-14 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.8 Applicable Limits and Compliance Monitoring Requirements S-10 – Unit 240, B-101 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.1 | Y |  | 993.7 MM BTU/hr averaged over any year at S-8, S-9, S-10, S-11, S-12, S-13, S-14 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-304 | Y |  | During tube cleaning, Ringelmann No. 2 for 3 min/hr and 6 min/billion BTU in 24 hours; applies to sources rated over 140 MM BTU/hr (with tubes) | None for gaseous-fueled sources | N | None |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.9 Applicable Limits and Compliance Monitoring Requirements S-11 – Unit 240, B-201 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.1 | Y |  | 993.7 MM BTU/hr averaged over any year at S-8, S-9, S-10, S-11, S-12, S-13, S-14 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.10 Applicable Limits and Compliance Monitoring Requirements S-12 – Unit 240, B-202 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.1 | Y |  | 993.7 MM BTU/hr averaged over any year at S-8, S-9, S-10, S-11, S-12, S-13, S-14 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.11 Applicable Limits and Compliance Monitoring Requirements S-13 – Unit 240, B-301 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.1 | Y |  | 993.7 MM BTU/hr averaged over any year at S-8, S-9, S-10, S-11, S-12, S-13, S-14 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-304 | Y |  | During tube cleaning, Ringelmann No. 2 for 3 min/hr and 6 min/billion BTU in 24 hours; applies to sources rated over 140 MM BTU/hr (with tubes) | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.12 Applicable Limits and Compliance Monitoring Requirements S-14 – Unit 240, B-401 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part F.1 | Y |  | 993.7 MM BTU/hr averaged over any year at S-8, S-9, S-10, S-11, S-12, S-13, S-14 | BAAQMD Condition 1694, Part F.3 | P/M | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-304 | Y |  | During tube cleaning, Ringelmann No. 2 for 3 min/hr and 6 min/billion BTU in 24 hours; applies to sources rated over 140 MM BTU/hr (with tubes) | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |

| Table VII – A.13 Applicable Limits and Compliance Monitoring Requirements S-15 – Unit 244, B-501 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 19.9 E 6 therm/yr (total) at S-15, S-16, S-17, S-18, S-19 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.14 Applicable Limits and Compliance Monitoring Requirements S-16 – Unit 244, B-502 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 19.9 E 6 therm/yr (total) at S-15, S-16, S-17, S-18, S-19 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.15 Applicable Limits and Compliance Monitoring Requirements S-17 – Unit 244, B-503 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 19.9 E 6 therm/yr (total) at S-15, S-16, S-17, S-18, S-19 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.16 Applicable Limits and Compliance Monitoring Requirements S-18 – Unit 244, B-504 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 19.9 E 6 therm/yr (total) at S-15, S-16, S-17, S-18, S-19 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.17 Applicable Limits and Compliance Monitoring Requirements S-19 – Unit 244, B-505 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 19.9 E 6 therm/yr (total) at S-15, S-16, S-17, S-18, S-19 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.18 Applicable Limits and Compliance Monitoring Requirements S-20 – Unit 244, B-506 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/A | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/A | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/A | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 1.9 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.19 Applicable Limits and Compliance Monitoring Requirements S-21 – Unit 244, B-507 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of Nuisance | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 0.7 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.20 Applicable Limits and Compliance Monitoring Requirements S-22 – Unit 248, B-606 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 2.6 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.21 Applicable Limits and Compliance Monitoring Requirements S-29 – Unit 200, B-5 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 8.6 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.22 Applicable Limits and Compliance Monitoring Requirements S-30 – Unit 200, B-101 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 4.2 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.23 Applicable Limits and Compliance Monitoring Requirements S-31 – Unit 200, B-501 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/A | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/A | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/A | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 1.7 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.24 Applicable Limits and Compliance Monitoring Requirements S-36 – Unit 200, B-N001 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx |  | Y | startup | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| NOx | BAAQMD Condition 21097, Part 3b | Y | startup | 10 ppmv NOx at 3% O2 (3 hour average), except startups and shutdowns | BAAQMD Condition 21097, Part 5a | C | CEM |
| All combustion emissions | BAAQMD Condition 21097, Part 2 | Y | startup | heat ratings, firing limits | BAAQMD Condition 21097, Part 4 | C | continuous fuel flow monitor |
| O2 |  | Y | startup | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| O2 |  | Y | startup | No limit | BAAQMD Condition 21097, Part 5a | C | CEM |
| CO | BAAQMD Condition 21097, Part 3b | Y | startup | 28 ppmv CO at 3% O2 (8 hour average), except startups and shutdowns | BAAQMD Condition 21097, Part 5b | P/SA | source test |
| POC | BAAQMD Condition 21097, Part 3b | Y | startup | 5.5 lb POC per MM ft3 of fuel | BAAQMD Condition 21097, Part 8 | E/startup | source test |
| PM10 | BAAQMD Condition 21097, Part 3b | Y | startup | 7.6 lb PM10 per MM ft3 of fuel | BAAQMD Condition 21097, Part 8 | E/startup | source test |
| ammonia | BAAQMD Condition 21097, Part 3b | N | startup | 10 ppmv amonia at 3% O2 (8 hour average), except startups and shutdowns | BAAQMD Condition 21097, Part 8 | E/startup | source test |
| Opacity | BAAQMD 6-301 | Y | startup | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y | startup | Prohibition of nuisance | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-310.3 | Y | startup | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup | 1,611 lb/day SO2 over any month | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| TRS | BAAQMD Condition 21097, Part 6 | Y | startup | 100 ppmv TRS (1 day average), 45 ppmv TRS (annual average) | BAAQMD Condition 21097, Part 7a, 7b | C | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y | startup | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J 60.105(a)(4) | C | H2S analyzer |

| Table VII – A.25 Applicable Limits and Compliance Monitoring Requirements S-43 – Unit 200, B-202 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx |  | Y | 6/1/04 for monitor-ing only | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| NOx | BAAQMD Condition 1694, Part D.2 | Y |  | 40 ppmv NOx at 3% O2 over any 8 hours, except startups and shutdowns, at S-43, S-44 | BAAQMD Condition 1694, Part D.4 | C | NOx, O2 CEM |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | Y |  | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| O2 |  | Y |  | No limit | BAAQMD Condition 1694, Part D.4 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| CO | BAAQMD Condition 1694, Part D.3 | N | 6/1/04 for monitor-ing only | 50 ppmv CO at 3% O2 over any month, except startups and shutdowns, at S-43, S-44 | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-304 | Y |  | During tube cleaning, Ringelmann No. 2 for 3 min/hr and 6 min/billion BTU in 24 hours; applies to sources rated over 140 MM BTU/hr (with tubes) | None for gaseous-fueled sources | N | None |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J,60.105(a)(4) | C | H2S analyzer |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 19.1 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.26 Applicable Limits and Compliance Monitoring Requirements S-44 – Unit 200, B-201 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx |  | Y | 6/1/04 for monitor-ing only | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| NOx | BAAQMD Condition 1694, Part D.2 | Y |  | 40 ppmv NOx at 3% O2 over any 8 hours, except startups and shutdowns, at S-43, S-44 | BAAQMD Condition 1694, Part D.4 | C | CEM |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | Y |  | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| O2 |  | Y |  | No limit | BAAQMD Condition 1694, Part D.4 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| CO | BAAQMD Condition 1694, Part D.3 | Y | 6/1/04 for monitor-ing only | 50 ppmv CO at 3% O2 over any month, except startups and shutdowns, at S-43, S-44 | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J 60.105(a)(4) | C | H2S analyzer |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 3.8 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.27 Applicable Limits and Compliance Monitoring Requirements S-50, S-51, S-52 – Turbine Startup Engines |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-303.1 | Y |  | Ringelmann No. 2 for no more than 3 minutes in any hour | None | N | N/A |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | None | N | N/A |
| Hours of operation | 9-8-111.1 | Y |  | Exemptions: Engines rated at or below 1000 brake horsepower which operate less than 200 hours in any 12-consecutive month period | BAAQMD 9-8-502 | P/M | records |
| Hours of operation | BAAQMD Condition 19488, Part 1 | N |  | up to 100 hour/yr | BAAQMD Condition 19488, Part 2 | P/M | records |
| SO2 | BAAQMD 9-1-304 | Y |  | Fuel Sulfur Limit 0.5% by weight | None | P/E | fuel certification |

| Table VII – A.28 Applicable Limits and Compliance Monitoring Requirements S-53, S-54, S-55, S-56, S-57, S-58, S-59 – Emergency Diesel Engines |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-303.1 | Y |  | Ringelmann No. 2 for no more than 3 minutes in any hour | None | N | N/A |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | None | N | N/A |
| Hours of operation | BAAQMD Condition 19488, Part 3 | N |  | up to 100 hour/yr (non-emergency) | BAAQMD Condition 19488, Part 6 | C | totalizing meter |
| Hours of operation | BAAQMD 9-8-330 | N |  | up to 100 hours for reliability testing | BAAQMD 9-8-530 | C | totalizing meter |
| SO2 | BAAQMD 9-1-304 | Y |  | Fuel Sulfur Limit 0.5% by weight | None | P/E | fuel certification |

| Table VII – A.29 Applicable Limits and Compliance Monitoring Requirements S-336 – Unit 231, B-104 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J 60.105(a)(4) | C | H2S analyzer |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 9.2 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.30 Applicable Limits and Compliance Monitoring Requirements S-337 – Unit 231, B-105 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | P/SA | source test |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 7 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J 60.105(a)(4) | C | H2S analyzer |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 2.8 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.31 Applicable Limits and Compliance Monitoring Requirements S-351 – Unit 267, B-601/602 Heaters |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx |  | Y | 6/1/04 for monitor-ing only | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| NOx | BAAQMD Condition 1694, Part B.2 | Y |  | 20 ppmv NOx at 3% O2 over any 3 hours, except startups and shutdowns, at S-351 | BAAQMD Condition 1694, Part B.3 | C | NOx, O2 CEM |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | Y |  | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| O2 |  | Y |  | No limit | BAAQMD Condition 1694, Part B.3 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J, 60.105(a)(4) | C | H2S analyzer |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 8.4 E 6 therm/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.32 Applicable Limits and Compliance Monitoring Requirements S-371 – Unit 228, B-520 Furnace |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| NOx | BAAQMD Condition 1694, Part C.2 | Y |  | 20 ppmv NOx at 3% O2 over any 3 hours, except startups and shutdowns | None | C | CEM |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| CO | BAAQMD Condition 1694, Part C.3 | Y | 6/1/04 for monitor-ing only | 50 ppmv CO at 3% O2 over any 3 hours, except startups and shutdowns | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J, 60.105(a)(4) | C | H2S analyzer |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 4.8 E 6 therm/yr for S-371 and S-372 combined | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.33 Applicable Limits and Compliance Monitoring Requirements S-372 – Unit 228, B-521 Furnace |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-10-301 | N | 6/1/04 for monitor-ing only | Refinery-wide emissions: 0.033 lb NOx/ MMBTU | BAAQMD 9-10-502.1 | C | CEM |
| NOx | BAAQMD 9-10-303 | Y |  | Federal emissions: Refinery-wide emissions: 0.20 lb NOx/MMBTU | None | N | None |
| NOx | BAAQMD Condition 1694, Part C.2 | Y |  | 20 ppmv NOx at 3% O2 over any 3 hours, except startups and shutdowns | None | C | NOx, O2 CEM |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| O2 |  | N | 9/1/04 for monitor-ing only | No limit | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 2 | C | CEM |
| CO | BAAQMD 9-10-305 | N | 6/1/04 for monitor-ing only | 400 ppmv (dry, 3% O2) | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| CO | BAAQMD Condition 1694, Part C.3 | Y | 6/1/04 for monitor-ing only | 50 ppmv CO at 3% O2 over any 3 hours, except startups and shutdowns | BAAQMD 9-10-502.1 BAAQMD Condition 21235, Part 8 | P/SA | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J 60.105(a)(4) | C | H2S analyzer |
| Fuel Flow |  | Y |  | No limit | BAAQMD 9-10-502.2 | C | Fuel Flowmeter |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 4.8 E 6 therm/yr for S-371 and S-372 combined | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – A.34 Applicable Limits and Compliance Monitoring Requirements S-438 – Unit 110, H-1 Furnace |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD Condition 1694, Part E.4 | Y |  | 10 ppmv NOx at 3% O2 over any 3 hours, except startups and shutdowns, at S-438 | None | C | CEM |
| All combustion emissions | BAAQMD Condition 1694, Part A.1 | N |  | heat ratings, firing limits (see condition) | BAAQMD Condition 1694, Part A.5 | P/D | records |
| all combustion emissions | BAAQMD Condition 1694, Part E.2 | Y |  | 2.04 E 12 BTU/yr fuel combustion at S-438 | BAAQMD Condition 1694, Part E.6 | P/D | records |
| O2 |  | Y |  | CEM for NOx and O2 (or CO2) | None | C | CEM |
| CO | BAAQMD Condition 1694, Part E.4 | Y |  | 32 ppmv CO at 3% O2 over any 24 hr, except startups and shutdowns, at S-438 | None | N | None |
| TRS | BAAQMD Condition 1694, Part E.3 | Y |  | 1 ppmw TRS in PSA offgas used as fuel, at S-438 | Overall fuel TRS monitored by BAAQMD Condition 1694, Part E.5 | P/D | records |
| TRS | BAAQMD Condition 1694, Part E.5 | Y |  | 50 ppmv TRS over any month, in fuel gas, at S-438 | BAAQMD Condition 1694, Part E.5 | P/3 times per day | TRS analysis |
| Opacity | BAAQMD 6-304 | Y |  | During tube cleaning, Ringelmann No. 2 for 3 min/hr and 6 min/billion BTU in 24 hours; applies to sources rated over 140 MM BTU/hr (with tubes) | None for gaseous-fueled sources | N | None |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None | N | None |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup of S-36, S-461 for modified limit | 1,558 lb/day SO2 over any month (1,611 lb/day after startup of S-36 and S-461) | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 40 CFR 60.105(a)(4) | C | H2S analyzer |

| Table VII – A.35 Applicable Limits and Compliance Monitoring Requirements S-461 – Unit 250, B-1 Heater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx |  | Y | startup | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| NOx | BAAQMD Condition 21096, Part 3b | Y | startup | 10 ppmv NOx at 3% O2 (3 hour average), except startups and shutdowns | BAAQMD Condition 21096, Part 5a | C | CEM |
| All combustion emissions | BAAQMD Condition 21096, Part 2 | Y | startup | heat ratings, firing limits (see condition) | BAAQMD Condition 21096, Part 4 | C | continuous fuel flow monitor |
| O2 |  | Y | startup | CEM for NOx and O2 (or CO2) | BAAQMD 1-520.8 | C | CEM |
| O2 |  | Y | startup | No limit | BAAQMD Condition 21096, Part 5a | C | CEM |
| CO | BAAQMD Condition 21096, Part 3b | Y | startup | 28 ppmv CO at 3% O2 (8 hour average) when fired 50% capacity or more and 50 ppmv CO at 3% O2 (8 hour average) when fired less than 50% capacity, except startups and shutdowns | BAAQMD Condition 21096, Part 5b | P/SA | source test |
| POC | BAAQMD Condition 21096, Part 3b | Y | startup | 5.5 lb POC per MM ft3 of fuel | BAAQMD Condition 21096, Part 8 | E/startup | source test |
| PM10 | BAAQMD Condition 21096, Part 3b | Y | startup | 7.6 lb PM10 per MM ft3 of fuel | BAAQMD Condition 21096, Part 8 | E/startup | source test |
| ammonia | BAAQMD Condition 21096, Part 3b | N | startup | 10 ppmv amonia at 3% O2 (8 hour average), except startups and shutdowns | BAAQMD Condition 21096, Part 8 | E/startup | source test |
| Opacity | BAAQMD 6-301 | Y | startup | Ringelmann 1 for no more than 3 minutes in any hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y | startup | Prohibition of nuisance | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-310.3 | Y | startup | 0.15 grain/dscf @ 6% O2 | None for gaseous-fueled sources | N | None |
| SO2 | BAAQMD Condition 1694, Part A.4 | Y | startup | 1,611 lb/day SO2 over any month | BAAQMD Condition 1694, Part A.3a | P/3 times per day | TRS analysis |
| TRS | BAAQMD Condition 21096, Part 6 | Y | startup | 100 ppmv TRS (1 day average), 45 ppmv TRS (annual average) | BAAQMD Condition 21096, Part 7a, 7b | C | TRS analysis |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y | startup | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J 60.105(a)(4) | C | H2S analyzer |

| Table VII – B Applicable Limits and Compliance Monitoring Requirements S-400 Wet Weather Wastewater Sump S-401 Dry Weather Wastewater Sump |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | BAAQMD Condition 1440, Part 4.b | Y |  | no detectable VOC emissions | BAAQMD Condition 1440, Part 5 | P/SA | VOC analyzer |
| VOC | NSPS Subpart QQQ, 40 CFR 60.692-2(c)(1) | Y |  | No visible gaps or cracks in joints or seals, or other problems that could result in VOC emissions | NSPS Subpart QQQ, 40 CFR 60.692-2(c)(2) | P/SA | Visual inspections |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 3.68 E 9 gal/yr each for S-400, S-401 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII - C Applicable Limits and Compliance Monitoring Requirements S-324 API Oil/Wastewater Separator |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | BAAQMD Condition 1440, Part 4.a | Y |  | no detectable VOC emissions | BAAQMD Condition 1440, Part 5 | P/SA | VOC analyzer |
| VOC | BAAQMD 8-8-306.1 | Y |  | No cracks or gaps in roof seals, acess doors, and other openings in the effluent channel greater than 0.32 cm (0.125 inch) between the roof and wall | BAAQMD 8-8-306.1 | P/SA | Visual inspections |
| VOC | NSPS Subpart QQQ, 40 CFR 60.692-3(a) | Y |  | Fixed roof access doors or openings shall be gasketed, latched, and kept closed | NSPS Subpart QQQ, 40 CFR 60.692-3(a)(4) | P/SA | Visual inspections |
| through-put | BAAQMD Condition 1440, Part 6 | Y |  | maximum design throughput - 7,500 gpm during media filter backwash and 7,000 gpm during all other times | None | N | None |
| Through-put | BAAQMD Condition 20989, Part A | Y |  | 3.68 E 9 gal/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – D Applicable Limits and Compliance Monitoring Requirements S-1007 Dissolved Air Flotation Unit |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | BAAQMD 8-8-307.1 | Y |  | Roof seals, access doors, and other openings shall be checked by visual inspection initially and semiannually thereafter to ensure that no cracks or gaps greater than 0.32 cm (0.125 inch) occur in the roof or between the roof and wall; and that the access doors and other openings are closed and gasketed properly | BAAQMD 8-8-307.1 | P/SA | visual |
| VOC | BAAQMD Condition 1440, Part 4.b | Y |  | no detectable VOC emissions | BAAQMD Condition 1440, Part 5 | P/SA | VOC analyzer |
| through-put | BAAQMD Condition 1440, Part 6 | Y |  | maximum design throughput - 7,500 gpm during media filter backwash and 7,000 gpm during all other times | None | N | None |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 3.68 E 9 gal/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII - E Applicable Limits and Compliance Monitoring Requirements S-381 Aeration Tank F-201 S-382 Aeration Tank F-202 S-383 Clarifier F-203 S-384 Clarifier F-204 |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | BAAQMD Condition 1440, Part 4.c | Y |  | no detectable VOC emissions | BAAQMD Condition 1440, Part 5 | P/SA | VOC analyzer |
| Through-put | BAAQMD Condition 20989, Part A | Y |  | 3.68 E 9 gal/yr each for S-381, S-382, S-383, S-384 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII - F Applicable Limits and Compliance Monitoring Requirements S-1008 Primary Stormwater Basin S-1009 Main Stormwater Basin |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Through-put | BAAQMD Condition 20989, Part A | Y |  | 3.68 E 9 gal/yr each for S-1008, S-1009 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – G Applicable Limits and Compliance Monitoring Requirements S-385 – Wastewater Effluent Media Filter F-207 S-386 – PAC Regeneration Sludge Thickener F-211 S-387 – Wet Air Regeneration System P-202 S-390 – Thickened Sludge Storage F-106 S-392 – Regenerated PAC Slurry Storage F-266 |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | BAAQMD Condition 1440, Part 4.c | Y |  | no detectable VOC emissions | BAAQMD Condition 1440, Part 5 | P/SA | VOC analyzer |
| Through-put | BAAQMD Condition 20989, Part A | Y |  | S-385: 3.68 E 9 gal/yr S-386: 1.6 E 7 gal/yr, S-387: 7.884 E 6 gal/yr S-390: 7.884 E 6 gal/yr S-392: 7.884 E 6 gal/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – H Applicable Limits and Compliance Monitoring Requirements Wastewater Junction Boxes |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| None |  |  |  |  |  |  |  |
| VOC | NSPS Subpart QQQ, 40 CFR 60.692-2(b)(2) | Y |  | Junction box covers shall have a tight seal around the edge and kept in place at all times | NSPS Subpart QQQ, 40 CFR 60.692-2(b)(3) | P/SA | Visual inspections |

| Table VII – I Applicable Limits and Compliance Monitoring Requirements Wastewater Process Sewers/Sewer Lines |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | NSPS Subpart QQQ, 40 CFR 60.692-2(c)(1) | Y |  | No visible gaps or cracks in joints or seals, or other problems that could result in VOC emissions | NSPS Subpart QQQ, 40 CFR 60.692-2(c)(2) | P/SA | Visual inspections |

| Table VII – J Applicable Limits and Compliance Monitoring Requirements Wastewater Gauging and Sampling Devices |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | BAAQMD 8-8-303 | Y |  | Vapor tight gauging and sampling devices | BAAQMD 8-8-504 8-8-603 | N | Portable hydrocarbon detector |

| Table VII – K Applicable Limits and Compliance Monitoring Requirements S294 – Non-Retail Gasoline Dispensing Facility |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | BAAQMD Regulation 8-7-301.6 and 8-7-302.5 | Y |  | Vapor recovery equipment shall be leak-free and vapor tight | BAAQMD Regulation 8-7-301.13 | A | Vapor tightness test |
| VOC | BAAQMD Regulation 8-7-301.10 | N |  | 98% or highest vapor recovery rate specified by CARB | None | N | None |
| VOC | None |  |  | None | BAAQMD Regulation 8-7-302.14 | A | Backpressure test |
| VOC | BAAQMD Regulation 8-7-313.1 | N |  | Fugitives < 0.42 lb/1000 gallon | None | N | None |
| VOC | BAAQMD Regulation 8-7-313.2 | N |  | Spillage < 0.42 lb/1000 gallon | None | N | None |
| VOC | BAAQMD Regulation 8-7-313.3 | N |  | Liquid Retain + Spitting < 0.42 lb/1000 gallon | None | N | None |
| VOC | SIP Regulation 8-7-301.2 | Y |  | 95% recovery of gasoline vapors | None | N | None |
| VOC | California Air Resources Board Executive Order VR-101 | N |  | leakage levels as specified in Executive Order VR-101 | BAAQMD Condition 18680, Part 2 | leak test | P/36 months |
| throughput | BAAQMD Condition 7523 | N |  | 400,000 gal/yr | BAAQMD Regulation 8-7-503 BAAQMD Condition 20989, Part A | P/A P/M | Records Records |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 20 gpm | None | N | None |

| Table VII - L Applicable Limits and Compliance Monitoring Requirements S-296 – C-1 Flare S-398 – MP-30 Flare [Flares which are visually inspected upon release, with no remote viewing system] |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD Regulation 6-301 | Y | 6/1/04 | Ringelmann No. 1 for no more than 3 minutes/hr | BAAQMD Condition 18255, Part 4 | P/E | Visual Inspection |
| FP | BAAQMD Regulation 6-310 | Y | 6/1/04 | No emissions from source > 0.15 grains per dscf of gas volume | BAAQMD Condition 18255, Part 4 | P/E | Visual Inspection |
| SO2 | 60.104(a)(1) | Y |  | S-398 is exempt per restriction in Condition 18255, Part 7; does not apply to S-296 | None | N | None |
| All |  | N |  |  | BAAQMD Regulation 12-11-501 & 12-11-505 | P/C | Flow Rate |
| All |  | N |  |  | BAAQMD Regulation 12-11-502.1 & 12-11-505 | P/E | Composition |
| All |  | N | 3/4/04 |  | BAAQMD Regulation 12-11-502.3 & 12-11-505 | P/E | Composition |
| All |  | N |  |  | BAAQMD Regulation 12-11-503 & 12-11-505 | P/C | Flame Detector |
| All |  | N |  |  | BAAQMD Regulation 12-11-504 & 12-11-505 | P/C | Purge Gas Flow Rate |
| All |  | N |  |  | BAAQMD Regulation 12-11-507 | P/C | 1 frame per minute image video recording |
| All |  | N |  |  | BAAQMD Regulation 12-11-507 | P/C | 1 frame per minute image video recording |
| throughput | BAAQMD Condition 18255, Part 1 | Y | 6/1/04 | 1.69 E 6 lb/hr of vent gas at each flare | BAAQMD Condition 21092, Part 2 | P/E | records |

| Table VII – M Applicable Limits and Compliance Monitoring Requirements S-300 – U-200 Delayed Coker |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | BAAQMD 8-10-301 | Y |  | abatement of emissions from process vessel depressurization is required until pressure is reduced to less than 1000 mm Hg | 8-10-401.2 | P/E | Records |
| throughput | BAAQMD Condition 21092, Part 1 | Y |  | 81,000 bbl/day | BAAQMD Condition 21092, Part 2 | P/D | records |

| Table VII – N Applicable Limits and Compliance Monitoring Requirements S-304 – U-229 Mid-Barrel Unionfining Unit (U-229 Light Naphtha Hydrotreater when modified in accordance with A/C 5814) S-305 – U-230 Prefractionator / Naphtha Hydrotreater S-306 – U-231 Platforming Unit S-307 – U-240 Unicracking Unit S-308 – U-244 Reforming Unit S-309 – U-248 Unisar Unit S-318 – U-76 Gasoline / Mid-Barrel Blending Unit S-319 – U-215 Gasoline Fractionating Unit S-322 – U-40 Raw materials Receiving S-435 – Reformate Splitter S-436 – Deisopentanizer S-437 – Hydrogen Plant S-460 – U-250 ULSD Hydrotreater |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | BAAQMD 8-10-301 | Y |  | abatement of emissions from process vessel depressurization is required until pressure is reduced to less than 1000 mm Hg | 8-10-401.2 | P/E | Records |
| VOC (S-307 only) | BAAQMD Condition 6671, Part 2 and 8-2-301 | Y |  | emission streams with 15 lb/day AND 300 ppm total carbon on a dry basis prohibited | BAAQMD Condition 6671, Part 4 | P/D | visual inspection |
| throughput (S-304 only) | BAAQMD Condition 21095, Part 1 | Y | when modified in accordance with A/C 5814 | 12,198 bbl/day (monthly average) | BAAQMD Condition 21095, Part 2 | P/D | records |
| throughput (S-460 only) | BAAQMD Condition 21094, Part 1 | Y | startup | 35,000 bbl/day (monthly average) | BAAQMD Condition 21094, Part 2 | P/D | records |
| throughput | BAAQMD Condition 20989, Part A | Y |  | S-304: 3.47 E 6 bbl/yr (only until modified in accordance with A/C 5814) S-305: 9.21 E 6 bbl/yr S-306: 5.66 E 6 bbl/yr S-307: 1.26 E 7 bbl/yr S-435: 6.6 E 6 bbl/yr S-436: 4.7 E 6 bbl/yr S-437: 9.1 E 9 ft3/yr | BAAQMD Condition 20989, Part A | P/M | records |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-308: 5.11 E 6 bbl/yr S-309: 6.6 E 8 bbl/yr S-318: 3.3 E 7 bbl/yr S-319: 3.51 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – O Applicable Limits and Compliance Monitoring Requirements S-350 – U-267 Crude Distillation Unit |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | BAAQMD 8-10-301 | Y |  | abatement of emissions from process vessel depressurization is required until pressure is reduced to less than 1000 mm Hg | 8-10-401.2 | P/E | Records |
| SO2 | BAAQMD Condition 383, Part 1a | Y | 4/1/04 | crude oil sulfur content limit (1.5 weight%) (only until modified in accordance with A/C 5814) | BAAQMD Condition 383, Part 1b | P/E | analysis |
| throughput | BAAQMD Condition 383, Part 2 | Y |  | 33,000 bbl/day, 30,000 bbl/day annual average (only until modified in accordance with A/C 5814) | BAAQMD Condition 383, Part 3a | P/M | records |
| SO2 | BAAQMD Condition 21093, Part 1a | Y | 4/1/04 | crude oil sulfur content limit (1.5 weight%) (when modified in accordance with A/C 5814) | BAAQMD Condition 21093, Part 1b | P/E | analysis |
| throughput | BAAQMD Condition 21093, Part 2 | Y |  | 33,000 bbl/day, 30,000 bbl/day annual average (when modified in accordance with A/C 5814) | BAAQMD Condition 21093, Part 3 | P/M | records |

| Table VII – P Applicable Limits and Compliance Monitoring Requirements S-432 – U-215 Deisobutanizer |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | BAAQMD 8-10-301 | Y |  | abatement of emissions from process vessel depressurization is required until pressure is reduced to less than 1000 mm Hg | 8-10-401.2 | P/E | Records |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 2.8 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – Q.1 Applicable Limits and Compliance Monitoring Requirements S-352 - Combustion Turbine S-353 - Combustion Turbine S-354 - Combustion Turbine |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD 9-9-301.3 | Y |  | 9 ppmv (note 1) @15% O2 (dry) | BAAQMD 9-9-501, Condition 12122, Part 9b | C | CEM |
| NOx | NSPS 40 CFR 60 Subpart GG, 60.332 (a)(2) | Y |  | 110 ppmv @15% O2 (dry) | BAAQMD 9-9-501, Condition 12122, Part 9b | C | CEM |
| NOx | BAAQMD Condition 12122, Part 9a | Y |  | 66 lb/hr and 167 ton/yr for all sources; 528 lb/day for each turbine/duct burner set | BAAQMD Condition 12122, Part 9b | C | CEM |
| NOx | BAAQMD Condition 18629, Part IX.E | Y |  | 664 lb/day per turbine/duct burner set AND 83 lb/hr total or 25 ppmv at 15% O2 (3 hr average) | BAAQMD Condition 18629, Part IX.G.1.a | C | CEM |
| CO | BAAQMD Condition 12122, Part 7 | Y |  | 39 ppmv @ 15% O2 | BAAQMD Condition 12122, Part 10b | C | CEM |
| CO | BAAQMD Condition 12122, Part 10a | Y |  | 200 ton/yr | BAAQMD Condition 12122, Part 10b | C | CEM |
| POC | BAAQMD Condition 12122, Part 8 | Y | 4/1/04 | 6 ppmv @ 15% O2 | BAAQMD Condition 12122, Part 14 | P/A | source test |
| POC | BAAQMD Condition 12122, Part 11 | Y | 4/1/04 | 8.3 lb/hr, 30.5 ton/yr | BAAQMD Condition 12122, Part 14 | P/A | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann No. 1 for no more than 3 minutes/hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-310 | Y |  | 0.15 grain/dscf | None for gaseous-fueled sources | N | None |
| throughput | BAAQMD Condition 18629, Part IX.D.2 | Y |  | 466 MM BTU/hr at each turbine/duct burner set | BAAQMD Condition 18629, Part IX.D.4 | P/M | records |
| throughput | BAAQMD Condition 18629, Part IX.D.3 | Y |  | 1048 MM BTU/hr total | BAAQMD Condition 18629, Part IX.D.4 | P/M | records |
| SO2 | 40 CFR 60 Subpart GG, 60.333(b) | Y |  | 0.8 % sulfur in fuel by weight | Condition 12122, Part 12 | P/3 times per day | TRS analysis |
| SO2 | BAAQMD Condition 18629, Part IX.F | Y |  | 15.6 lb/hr at each turbine/duct burner set AND 44 lb/hr total (3-hr average); 34 lb/hr total (3-hr average) for more than 36 days per year AND 153 ton/yr total | BAAQMD Condition 18629, Part IX.G.1.a | C/P | H2S CEM for fuel gas AND daily total sulfur sampling of fuel gas |
| H2S | 40 CFR 60, Subpart J, 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | 40 CFR 60, Subpart J 60.105(a)(4) | C | H2S analyzer |

1	BAAQMD Regulation 9-9-301.2, 9-9-301.3, 9-9-303, and 9-9-305 emission limits may be adjusted pursuant to BAAQMD Regulation 9-9-401.

| Table VII – Q.2 Applicable Limits and Compliance Monitoring Requirements S-355 – Supplemental Duct Burners for S-352 S-356 – Supplemental Duct Burners for S-353 S-357 – Supplemental Duct Burners for S-354 |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| NOx | BAAQMD Condition 12122, Part 9a | Y |  | 66 lb/hr and 167 ton/yr for all sources; 528 lb/day for each turbine/duct burner set | BAAQMD Condition 12122, Part 9b | C | CEM |
| NOx | 40 CFR 60, Subpart Db, 60.44b(a)(4)(i) | Y |  | 0.20 lb/MM BTU for natural gas-firing only conditions | 40 CFR 60, Subpart Db, 60.48b(h) – Exempt from NOx CEM during natural gas-firing only conditions | N | None |
| NOx | 40 CFR 60, Subpart Db, 60.44b(f) | Y |  | 25 ppmv @ 15% O2 (3-hr average) (based on PSD Permit Condition 18629, Part IX.E) | 40 CFR 60, Subpart Db, 60.48b(b)(l) and BAAQMD Condition 18629, Part IX.G.1.a | C | CEM |
| NOx | BAAQMD Condition 18629, Part IX.E | Y |  | 664 lb/day per turbine/duct burner set AND 83 lb/hr total or 25 ppmv at 15% O2 (3 hr average) | BAAQMD Condition 18629, Part IX.G.1.a | C | CEM |
| CO | BAAQMD Condition 12122, Part 7 | Y |  | 39 ppmv @ 15% O2 | BAAQMD Condition 12122, Part 10b | C | CEM |
| CO | BAAQMD Condition 12122, Part 10a | Y |  | 200 ton/yr | BAAQMD Condition 12122, Part 10b | C | CEM |
| POC | BAAQMD Condition 12122, Part 8 | Y | 4/1/04 | 6 ppmv @ 15% O2 | BAAQMD Condition 12122, Part 14 | P/A | source test |
| POC | BAAQMD Condition 12122, Part 11 | Y | 4/1/04 | 8.3 lb/hr, 30.5 ton/yr | BAAQMD Condition 12122, Part 14 | P/A | source test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann No. 1 for no more than 3 minutes/hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-310 | Y |  | 0.15 grain/dscf | None for gaseous-fueled sources | N | None |
| throughput | BAAQMD Condition 12122, Part 6 | Y |  | 2.42 E 12 BTU/yr at S-355, S-356, S-357 (combined) | BAAQMD Condition 12122, Part 15 | P/D | records |
| throughput | BAAQMD Condition 18629, Part IX.D.2 | Y |  | 466 MM BTU/hr at each turbine/duct burner set | BAAQMD Condition 18629, Part IX.D.4 | P/M | records |
| throughput | BAAQMD Condition 18629, Part IX.D.3 | Y |  | 1048 MM BTU/hr total | BAAQMD Condition 18629, Part IX.D.4 | P/M | records |
| SO2 | BAAQMD Condition 18629, Part IX.F | Y |  | 15.6 lb/hr at each turbine/duct burner set AND 44 lb/hr total (3-hr average); 34 lb/hr total (3-hr average) for more than 36 days per year AND 153 ton/yr total | BAAQMD Condition 18629, Part IX.G.1.a | C/P | H2S CEM for fuel gas AND daily total sulfur sampling of fuel gas |
| H2S | 40 CFR 60, Subpart J, 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions | 40 CFR 60, Subpart J 60.105(a)(4) | C | H2S analyzer |

| Table VII - R Applicable Limits and Compliance Monitoring Requirements S376 - Tool Room Cold Cleaner S377 – Machine Shop Cold Cleaner S378 – Auto Shop Cold Cleaner |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | BAAQMD Condition 16677, Part 1 | Y |  | 150 gal/yr of citrus-based solvents, or equivalent amount as allowed in Part 2 | BAAQMD Condition 16677, Part 3a | P/M | usage records |

| Table VII - S Applicable Limits and Compliance Monitoring Requirements S-425 – Marine Loading Berth M1 S-426 – Marine Loading Berth M2 |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | BAAQMD 8-44-301.1 | Y |  | POC Emission < 5.7 grams per cubic meter (2 lb/1000 barrel) loaded, or | BAAQMD Condition 4336, Part 1 | C | A-420 temperature |
| POC | BAAQMD 8-44.301.2 | Y |  | Controlled > 95% weight | BAAQMD Condition 4336, Part 1 | C | A-420 temperature |
| POC | BAAQMD 8-44-303 | Y |  | Leak free and gas tight | Equipment leak inspections as specified in BAAQMD Regulation 8, Rule 18 | P/Q | inspection with portable VOC monitor |
| POC | BAAQMD Condition 4336, Part 1 | Y |  | 1300 degrees F minimum temperature during startup, 1400 degrees F minimum temperature after startup | BAAQMD Condition 4336, Part 2b | C | A-420 temperature |
| POC | BAAQMD Condition 4336, Part 5 | Y |  | maximum loading pressure relative to lowest relief valve setting (80%) | BAAQMD Condition 4336, Part 2a | C | loading pressure |
| POC | BAAQMD Condition 4336, Part 6 | Y |  | 25,000 bbl/day of gasoline, naphtha and C5/C6 compounds | BAAQMD Condition 4336, Part 7 | P/D | loading records |
| H2S | 40 CFR 60 Subpart J 60.104(a) (1) | Y |  | fuel gas H2S concentration limited to 230 mg/dscm (0.10 gr/dscf) except for gas burned as a result of process upset or gas burned at flares from relief valve leaks or other emergency malfunctions; this requirement applies to sources installed/modified after 6/11/73 and burning refinery gas | 40 CFR 60 Subpart J 60.105(a)(4) | C | H2S analyzer |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 2.8 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – T Applicable Limits and Compliance Monitoring Requirements S-450 – Groundwater Extraction Trenches |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| None |  |  |  |  |  |  |  |

| Table VII – U Applicable Limits and Compliance Monitoring Requirements S1001 - Sulfur Plant Unit 234 S1002 - Sulfur Plant Unit 236 S1003 - Sulfur Plant Unit 238 S-301 - Molten Sulfur Pit 234 S-302 - Molten Sulfur Pit 236 S-303 - Molten Sulfur Pit 238 |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| (H2S, ammonia) | BAAQMD 9-1-313.2 and SIP 9-1-313.2 | N Y | 4/1/04 | 95% of H2S in refinery fuel gas is removed and recovered on a refinery-wide basis AND 95% of H2S in process water streams is removed and recovered on a refinery-wide basis AND 95% of ammonia in process water streams is removed; refineries which remove the equivalent of 16.5 ton/day or more of elemental sulfur shall install a sulfur recovery plant or sulfuric acid plant | BAAQMD Condition 19278 Part 1 | P/A | Source Test |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann No. 1 for no more than 3 minutes/hour | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-305 | Y |  | Prohibition of nuisance | None for gaseous-fueled sources | N | None |
| FP | BAAQMD 6-310 | Y |  | 0.15 grain/dscf | None for gaseous-fueled sources | N | None |
| SO3, H2SO4 | BAAQMD 6-330 | Y | 4/1/04 | 0.08 grain/dscf exhaust concentration of SO3 and H2SO4, expressed as 100% H2SO4 | BAAQMD Condition 19278 Part 2 | P/A | Source Test |
| throughput | BAAQMD Condition 20989, Part A | N |  | 89,425 long ton/yr for S-1001, 1002, 1003, 301, 302, 303 | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – V Applicable Limits and Compliance Monitoring Requirements S-370 – Isomerization Unit 228 |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | BAAQMD 8-10-301 | Y |  | abatement of emissions from process vessel depressurization is required until pressure is reduced to less than 1000 mm Hg | 8-10-401.2 | P/E | Records |
| VOC | BAAQMD Condition 12121, Part 1 | Y |  | daily feed rate limit (11,040 bbl/day) | BAAQMD Condition 12121, Part 2 | P/D | records |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 4.03 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – W Applicable Limits and Compliance Monitoring Requirements S-380 – Activated Carbon Silo (P-204) |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD Regulation 6-301 | Y | 4/1/04 | Ringelmann No. less than 1 for more than 3 minutes/hr | BAAQMD Condition 18251, Part 2b | P/Q | Pressure Drop |
| FP | BAAQMD 6-305 | Y | 4/1/04 | Prohibition of nuisance | BAAQMD Condition 18251, Part 2b | P/Q | Pressure Drop |
| FP | BAAQMD Regulation 6-310 | Y | 4/1/04 | No emissions from source > 0.15 grains per dscf of gas volume | BAAQMD Condition 18251, Part 2b | P/Q | Pressure Drop |
| FP | BAAQMD Regulation 6-311 | Y | 4/1/04 | No emissions from source > rate specified in rule | BAAQMD Condition 18251, Part 2b | P/Q | Pressure Drop |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 2,628 ton/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII - X Applicable Limits and Compliance Monitoring Requirements S-389 – Diatomaceous Earth Silo (F-214) |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD Regulation 6-301 | Y | 4/1/04 | Ringelmann No. less than 1 for more than 3 minutes/hr | BAAQMD Condition 18251, Part 2c | P/E (baghouse operation) | Pressure Drop |
| FP | BAAQMD 6-305 | Y | 4/1/04 | Prohibition of nuisance | BAAQMD Condition 18251, Part 2c | P/E (baghouse operation) | Pressure Drop |
| FP | BAAQMD Regulation 6-310 | Y | 4/1/04 | No emissions from source > 0.15 grains per dscf of gas volume | BAAQMD Condition 18251, Part 2c | P/E (baghouse operation) | Pressure Drop |
| FP | BAAQMD Regulation 6-311 | Y | 4/1/04 | No emissions from source > rate specified in rule | BAAQMD Condition 18251, Part 2c | P/E (baghouse operation) | Pressure Drop |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 1,840 ton/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – Y Applicable Limits and Compliance Monitoring Requirements S-462 – U-215 Fuel Gas Caustic Treatment System S-463 – U-215 Butane Caustic Treatment System |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| throughput | BAAQMD Condition 20989, Part A | Y | startup | S-462: 1.533 E 9 ft3/yr S-463: 73.365 E 6 lb/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – AB Applicable Limits and Compliance Monitoring Requirements Components |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| POC | BAAQMD Reg. 8-18-301 | Y |  | General equipment leak < 100 ppm | BAAQMD Reg. 8-18-401.2 | P/Q | Inspection |
| POC | BAAQMD Reg. 8-18-302 | Y |  | Valve leak < 100 ppm | BAAQMD Reg. 8-18-401.2 | P/Q | Inspection |
| POC | BAAQMD Reg. 8-18-303 | Y |  | Pump and compressor leak < 500 ppm | BAAQMD Reg. 8-18-401.2 | P/Q | Inspection |
| POC | BAAQMD Reg. 8-18-304 | Y |  | Connection leak < 100 ppm | BAAQMD Reg. 8-18-401.2e | P/Q | Inspection |
| POC | BAAQMD Reg. 8-18-305 | Y |  | Pressure relief valve leak < 500 ppm | BAAQMD Reg. 8-18-401.2 | P/Q | Inspection |
| POC | BAAQMD Reg. 8-18-306.1 | Y |  | Valve, pressure relief, pump or compressor must be repaired within 5 years or at the next scheduled turnaround | BAAQMD Reg. 8-18-502.4 | P/quarterly | report |
| POC | BAAQMD Reg. 8-18-306.2 | Y |  | Awaiting repair Valves < 0.5% Pressure Relief < 1% Pump and Connector < 1% | BAAQMD Reg. 8-18-401.5 | P/within 24 hours | Inspection |
| POC | BAAQMD Reg. 8-18-306.3.2 | Y |  | Mass emissions & non-repairable equipment allowed Valve < 0.1 lb/day & <1.0% Pressure Relief < 0.2 lb/day & < 5% Pump and Connector < 0.2 lb/day & < 5% | BAAQMD Reg. 8-18-401.3 | P/D | Inspection |
| POC | BAAQMD Reg. 8-18-306.3.3 | Y |  | Total valve, pressure relief, pump or compressor leaks > 15 lb/day, they must be repaired within 7 days | BAAQMD 8-18-502.4 | P/Q | sampling or equivalent |
| POC | SIP Reg. 8-28-301 | Y |  | 10,000 ppm | BAAQMD 8-28-402 | P/Q | inspection |
| POC | BAAQMD Reg.8-28-303 | N |  | Vent Pressure Relief Devices to an Abatement Device with at least 95% by weight control efficiency or Meet Prevention Measures Procedures | BAAQMD 8-28-405 | P/turn-around | None |
| POC | BAAQMD Reg.8-28-304 | N |  | PHA within 90 days and meet Prevention Measures Procedures. After 2nd release Vent Pressure Relief Devices to an Abatement Device with at least 95% by weight control efficiency. | BAAQMD 8-28-405 | P/release per 5 calendar year | None |
| 40 CFR 60; Subpart QQQ |
| POC | 40 CFR 60.692-5 (e)(1) | Y |  | Closed-vent systems <500 ppm above background | 40 CFR 60.692-5 (e)(1) | P/SA | Measure for leaks |
| POC | 40 CFR 60.692-5 (a) | Y |  | Closed-vent systems using combustion devices shall have 0.75 seconds residence and minimum temp of 816C | 40 CFR 60.692-5 (e)(5) | P/E | Repair after emissions are detected within 30 days |
| POC | 40 CFR 60.692-5 (b) | Y |  | Vapor recovery greater than or equal to 95% | None | N | None |
| 40 CFR 60; Subpart VV |
| POC | 40 CFR 60.482-2 (b)(1) | Y |  | Pump leak  10,000 ppm | 40 CFR 60.482-2 (a)(1) | P/M | Measure for leaks |
| POC | 40 CFR 60.482-2 (b)(2) | Y |  | Pump leak Indicated by dripping liquid | 40 CFR 60.482-2 (a)(2) | P/W | Visual Inspection |
| POC | 40 CFR 60.482-2(e) | Y |  | Designated “No detectable emissions”  500 ppm | 40 CFR 60.482-2(e)(3) | P/A | Measure for leaks |
| POC | 40 CFR 60.482-8 (b) | Y |  | Pump leak  10,000 ppm | 40 CFR 60.482-8 (a) | P/5 days | Visual, audible, olfactory Inspection; Measure for leaks |
| POC | 40 CFR 60.482-4(b) | Y |  | Pressure relief valve (gas/vapor) leak  500 ppm within 5 days after a pressure release event | 40 CFR 60.482-4(b) | P/E | Measure for leaks within 5 days after release |
| POC | 40 CFR 60.482-7(b) | Y |  | Valve leak  10,000 ppm | 40 CFR 60.482-7(a) | P/M | Measure for leaks |
| POC | 40 CFR 60.482-7(b) | Y |  | Valve leak  10,000 ppm; 2 successive months w/o leaking | 40 CFR 60.482-7(c) | P/Q | Measure for leaks |
| POC | 40 CFR 60.482-7(f) | Y |  | Designated “No detectable emissions”  500 ppm | 40 CFR 60.482-7 (f)(3) | P/A | Measure for leaks |
| POC | 40 CFR 60.482-8(a) | Y |  | Pumps and valves in heavy liquid service, Pressure Relief devices (light or heavy liquid), Flanges, Connectors leak shall be measured for leak in 5 days if detected by inspection | 40 CFR 60.482-8(a) | P/E | Visible, Audible, or olfactory Inspection |
| POC | 40 CFR 60.482-8(b) | Y |  | Pressure Relief devices (liquid), Flanges, Connectors leak  10,000 ppm | 40 CFR 60.482-8(a) | P/E | Measure for leaks |
| POC | 40 CFR 60.482-10 (b) | Y |  | Closed-vent systems and control devices: Vapor recovery systems 95% | None | N | None |
| POC | 40 CFR 60.482-10 (c) | Y |  | Combustion devices  95% destruction efficiency or  0.75 seconds and  816°C | None | N | None |
| POC | 40 CFR 60.482-10 (g) | Y |  | Closed-vent systems leak  500 ppm and visible leak indication | 40 CFR 60.482-10 (f) | P/A | Measure for leaks; Visual Inspection |
| POC | 40 CFR 60.483 and BAAQMD 8-18-404.1 | Y |  | Individual valve that measures <100 ppm for 5 consecutive quarters may be monitored annually, if in a process unit with 5 consecutive quarters <2% valves leaking 10,000 ppm. | same as limit | P/Q P/A | Measure for leaks |
| 40 CFR 61; Subpart FF |
| POC | 40 CFR 61.342 (a) | Y |  | Exemption for facilities with less than 10 Mg/yr of benzene in waste | 40 CFR 61.357 (c) | P/A | report |

| Table VII – B1 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Low Vapor Pressure Permitted Wastewater Sludge Tanks with Vapor Recovery to Fuel Gas S-433 (F224 - MOSC) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| BAAQMD 8-8 | BAAQMD 8-8 – Organic Compounds – Wastewater (Oil Water Separators) |
| VOC | BAAQMD 8-8-303 | Y |  | Vapor tight gauging and sampling devices | BAAQMD 8-8-504 8-8-603 | N | Portable hydrocarbon detector |
| VOC | BAAQMD 8-8-304 | Y |  | Combined collection/destruction efficiency of 95% by weight. | BAAQMD 8-8-602 | N | Source test or EPA Method 25 or 25A |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system. |
| NSPS QQQ | 40 CFR 60 Subpart QQQ – VOC Emissions from Petroleum Refinery Wastewater Systems |
| VOC | 40 CFR 60.692-3(a) | Y |  | Fixed roof closure standards | 40 CFR 60.692-3(a)(4) | periodic initially and semi-annually | Visual inspection |
| VOC |  | Y |  | Problems identified during 40 CFR 60.692-3(a) inspections that could result in VOC emissions | 40 CFR 60.697(c) | periodic when problem is identified | Records |
| VOC |  | Y |  | Problems identified during 40 CFR 60.692-3(a) inspections that could result in VOC emissions | 40 CFR 60.698(c) | periodic initially and semi-annually | Report |
| NSPS Kb | 40 CFR 60 Subpart Kb – NSPS for VOL Storage Vessels MONITORING FOR RECORDKEEPING ONLY |
| VOC | 40 CFR 60.110b(c) | Y |  | True vapor pressure less than 3.5 kPa. | 40 CFR 60.116b (b) | periodic initially and upon change of service | Record |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 7353, Part 4 | Y |  | 138,700 bbl/yr | BAAQMD Condition 7353, Part 5 | P/W | records |

| Table VII – B2 Applicable Limits and Compliance Monitoring Requirements Low Vapor Pressure Permitted Tanks Subject to MACT Recordkeeping S-118 (Tank 163 ) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAP for Petroleum Refineries MONITORING FOR RECORDKEEPING ONLY |
| HAP | 40 CFR 63.641 | Y |  | Retain weight percent total organic HAP in stored liquid for Group 2 determination. | 40 CFR 63.654(i)(1) (iv) | periodic initially and upon change in service | Records |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | 15,000 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |

| Table VII – B3 Applicable Limits and Compliance Monitoring Requirements Low Vapor Pressure Permitted Tanks < 10,000 gallons S-117 (Tank 162), S-193 (Tank 305), S-194 (Tank 306) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.641 storage vessel definition. Size less than or equal to 10,000 gallons. |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-117: 8.76 E 5 bbl/yr S-193: 100 bbl/yr S-194: 100 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |

| Table VII – B4 Applicable Limits and Compliance Monitoring Requirements Low Vapor Pressure Permitted Tanks Vented to Fuel Gas S-238 (Tank 211), S-239 (Tank 212) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system. |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-238: 1.0 E 6 bbl/yr S-239: 8.76 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |

| Table VII – B5 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Low Vapor Pressure Permitted Wastewater Sludge Tanks S-195 (Tank 501), S-196 (Tank 502), S-388 (Tank 276/F205) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| BAAQMD 8-8 | BAAQMD 8-8 – Organic Compounds – Wastewater (Oil Water Separators) |
| VOC | BAAQMD 8-8-303 | Y |  | Vapor tight gauging and sampling devices | BAAQMD 8-8-504 8-8-603 | N | Portable hydrocarbon detector |
| VOC | BAAQMD 8-8-304 | Y |  | Combined collection/destruction efficiency of 95% by weight. | BAAQMD 8-8-602 | N | Source test or EPA Method 25 or 25A |
| NESHAPS CC and NSPS Kb | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 60 Subpart Kb - NSPS for VOL Storage Vessels at Petroleum Refineries RECORDKEEPING ONLY |
| Vapor pressure | 40 CFR 63.640(n)(1) 60.110b(c) | Y |  | True vapor pressure less than 3.5 kPa. | 40 CFR 63.640(n)(8) 60.116b(b) | P/E | Record |
| Vapor pressure |  | Y |  | TVP exceedances (> 5.2 kPa). | 40 CFR 63.640(n)(8) 60.116b(d) | periodic within 30 days of exceedance | Notification |
| NSPS QQQ | 40 CFR 60 Subpart QQQ – VOC Emissions from Petroleum Refinery Wastewater Systems |
| VOC | 40 CFR 60.692-3(a) | Y |  | Fixed roof closure standards | 40 CFR 60.692-3(a)(4) | periodic initially and semi-annually | Visual inspection |
| VOC |  | Y |  | Problems identified during 40 CFR 60.692-3(a) inspections that could result in VOC emissions | 40 CFR 60.697(c) | periodic when problem is identified | Records |
| VOC |  | Y |  | Problems identified during 40 CFR 60.692-3(a) inspections that could result in VOC emissions | 40 CFR 60.698(c) | periodic initially and semi-annually | Report |
| BAAQMD Permit | PERMIT CONDITIONS |
| Condition 1860 applies to S-388 only |
| VOC | BAAQMD Condition 1860, Part 1 | Y |  | fugitive emissions (300 ppm as methane above background) | BAAQMD Condition 1860, Part 3 | periodic as required by BAAQMD Regulation 8, Rule 18 | VOC monitor |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-195: 5.0 E 4 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |
| throughput | BAAQMD Condition 20989, Part A | Y |  | S-196: 5.0 E 4 bbl/yr S-388: 153,300 ton/yr | BAAQMD Condition 20989, Part A | P/M | Records |

| Table VII – B6 Applicable Limits and Compliance Monitoring Requirements MACT (Small) Zero Gap External Floating Roof Tank S-121 (Tank 166) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | Certification Report |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | Records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries MONITORING FOR RECORDKEEPING ONLY |
| HAP | 40 CFR 63.641 | Y |  | Retain weight percent total organic HAP in stored liquid for Group 2 determination. | 40 CFR 63.654(i)(1) (iv) | periodic initially and upon change in service | Records |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | 3.52 E 4 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – B7 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Zero gap External Floating Roof Tanks S-439 (Tank 109), S-440 (Tank 110), S-442 (Tank 112), S-444 (Tank 243), S-451 (Tank 695) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | Certification report |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacment | records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NESHAPS CC and NSPS Kb | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 60 Subpart Kb – NSPS for VOL Storage Vessels LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| VOC | 40 CFR 63.640 (n)(1), 60.112b (a)(2)(ii) | Y |  | Deck fitting closure standards; includes gasketed covers | 40 CFR 63.640(n)(8), 60.113b (b)(6) | periodic initially & each time emptied & degassed | visual inspection |
| VOC | 40 CFR 63.640 (n)(1), 60.113b (b)(4)(i) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.640(n)(8), 60.113b (b)(1)-(b)(3) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| VOC | 40 CFR 63.640 (n)(1), 60.113b (b)(4)(ii) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.640(n)(8), 60.113b (b)(1)-(b)(3) | periodic initially & annually | measurement and visual inspection |
| VOC | 40 CFR 63.640 (n)(1), 60.116b (c) | Y |  | Record of liquid stored and rue vapor pressure | 40 CFR 63.640(n)(8), 60.116b (c) & (e) | periodic upon change of service | Records |
| VOC |  | Y |  | Seal inspection records for report in 40 CFR 60.115b(b)(2) | 40 CFR 63.640(n)(8), 60.115b(b)(3) | periodic For each gap measurement | Records |
| VOC |  | Y |  | Inspection report for seal gap measurements | 40 CFR 63.640(n)(8), 60.115b(b)(2) | periodic Within 60 days of seal gap measurement | Report |
| VOC |  | Y |  | Inspection report for non-compliant seals | 40 CFR 63.640(n)(8), 60.115b(b)(4) | periodic Within 30 days of seal inspection | Report |
| BAAQMD Permit | PERMIT CONDITIONS |
| The following applies to S-439 only |
| throughput | BAAQMD Condition 12124, Part 1 | Y |  | 3,650,000 bbl/yr | BAAQMD Condition 12124, Part 3 | P/M | records |
| The following applies to S-440 only |
| throughput | BAAQMD Condition 12125, Part 1 | Y |  | 3,600,000 bbl/yr | BAAQMD Condition 12125, Part 3 | P/M | records |
| The following applies to S-442 only |
| throughput | BAAQMD Condition 12127, Part 1 | Y |  | 2,740,000 bbl/yr | BAAQMD Condition 12127, Part 3 | P/M | records |
| The following applies to S-444 only |
| throughput | BAAQMD Condition 12129, Part 1 | Y |  | 4,380,000 bbl/yr | BAAQMD Condition 12129, Part 3 | P/M | records |
| The following applies to S-451 only |
| throughput | BAAQMD Condition 19476, Part 1 | Y |  | 11,000,000 bbl/yr | BAAQMD Condition 19476, Part 3 | P/M | Records |

| Table VII – B8 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Zero gap External Floating Roof Stormwater Equilization Tanks S-101 (Tank 104), S-102 (Tank 105), S-106 (Tank 130) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | Certification report |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| The following apply to S-106 only |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| The following apply to S-106 only |
| BAAQMD 8-8 | BAAQMD 8-8 – Organic Compounds – Wastewater (Oil Water Separators) |
| VOC | BAAQMD 8-8-302.2 8-8-302.2.1 | Y |  | Primary seal gap criteria | BAAQMD 8-8-302.2.3 | periodic initially and every 5 years | measurement and inspection |
| VOC | BAAQMD 8-8-302.2 8-8-302.2.2 | Y |  | Secondary and wiper seal gap criteria | BAAQMD 8-8-302.2.3 | periodic initially and every 5 years | measurement and inspection |
| VOC | BAAQMD 8-8-303 | Y |  | Vapor tight gauging and sampling devices | BAAQMD 8-8-504 8-8-603 | N | Portable hydrocarbon detector |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries NO MONITORING REQUIREMENTS FOR GROUP 2 WASTEWATER SOURCES |
| NSPS Kb and NSPS QQQ | 40 CFR 60 Subpart Kb – NSPS for VOL Storage Vessels 40 CFR 60 Subpart QQQ – VOC Emissions from Petroleum Refinery Wastewater Systems LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| VOC | 40 CFR 60.692-3(d) 60.112b (a)(2)(ii) | Y |  | Deck fitting closure standards; includes gasketed covers | 40 CFR 60.692-3(d) 60.113b (b)(6) | periodic initially & each time emptied & degassed | visual inspection |
| VOC | 40 CFR 60.692-3(d) 60.113b (b)(4)(i) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 60.692-3(d) 60.113b (b)(1)-(b)(3) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| VOC | 40 CFR 60.692-3(d) 60.113b (b)(4)(ii) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 60.692-3(d) 60.113b (b)(1)-(b)(3) | periodic initially & annually | measurement and visual inspection |
| VOC | 40 CFR 60.692-3(d) 60.116b (c) | Y |  | Record of liquid stored and true vapor pressure | 40 CFR 60.692-3(d) 60.116b (c) & (e) | periodic upon change of service | Records |
| VOC |  | Y |  | Seal inspection records for report in 40 CFR 60.115b(b)(2) | 40 CFR 60.692-3(d) 60.115b(b)(3) | periodic For each gap measurement | Records |
| VOC |  | Y |  | Inspection report for seal gap measurements | 40 CFR 60.692-3(d) 60.115b(b)(2) | periodic Within 60 days of seal gap measurement | Report |
| VOC |  | Y |  | Inspection report for non-compliant seals | 40 CFR 60.692-3(d) 60.115b(b)(4) | periodic Within 30 days of seal inspection | Report |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | Y |  | S-101: 3.68 E 9 gal/yr S-102: 3.68 E 9 gall/yr S-106: 3.68 E 9 gal/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – B9 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Zero Gap Internal Floating Roof Tank S-448 (Tank 1007) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR INTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-402.3 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-402.1 | periodic 10 year intervals and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-402.1 | periodic 10 year intervals and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-305, 8-5-321.1, 8-5-322.1 | Y |  | Visual inspection of outer most seal | BAAQMD 8-5-402.2 | P/SA | Visual inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | Certification report |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | Records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NESHAPS CC and NSPS Kb | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 60 Subpart Kb – NSPS for VOL Storage Vessels LIMITS AND MONITORING FOR INTERNAL FLOATING ROOF TANKS |
| VOC | 40 CFR 63.640 (n)(1), 60.112b (a)(1) | Y |  | Deck fitting closure standards; includes gasketed covers | 40 CFR 63.640(n)(8), 60.113b (a)(3) & (4) | periodic initially & each time emptied & degassed, at least every 10 yr | visual inspection |
| VOC | 40 CFR 63.640 (n)(1), 60.113b (a)(1) & (4) | Y |  | Primary rim-seal standards; no holes or tears | 40 CFR 63.640(n)(8), 60.113b (a)(3) & (4) | periodic initially & each time emptied & degassed, at least every 10 yr | visual inspection |
| VOC | 40 CFR 63.640 (n)(1), 60.113b (a)(1) & (4) | Y |  | Secondary rim-seal standards; no holes or tears | 40 CFR 63.640(n)(8), 60.113b (a)(3) & (4) | periodic initially & each time emptied & degassed, at least every 10 yr | visual inspection |
| VOC | 40 CFR 63.640 (n)(1), 60.113b (a)(2) | Y |  | Internal visual inspection from viewports of fixed roof | 40 CFR 63.640(n)(8), 60.113b (a)(2) & (3) | periodic initially & annually | visual inspection |
| VOC | 40 CFR 63.640 (n)(1), 60.116b (c) | Y |  | Record of liquid stored and true vapor pressure | 40 CFR 63.640(n)(8), 60.116b (c) & (e) | periodic upon change of service | records |
| VOC |  | Y |  | Record of each initial, annual, and 10-year tank inspection | 40 CFR 63.640(n)(8), 60.115b(a)(2) | periodic for each tank inspection | records |
| VOC |  | Y |  | Report of non-compliant annual inspection for tanks with secondary seals | 40 CFR 63.640(n)(8), 60.115b(a)(4) | periodic within 30 days of tank inspection | report |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 12133, Part 1 | Y |  | 2,190,000 bbl/yr | BAAQMD Condition 12133, Part 3 | P/M | records |

| Table VII – B10 Applicable Limits and Compliance Monitoring Requirements Internal Floating Roof Tanks with Dome Roofs Previously External Floating Roof Tanks S-126 (Tank 172), S-257 (Tank 1004), S-258 (Tank 1005) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR INTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-402.3 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-402.1 | periodic 10 year intervals and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-402.1 | periodic 10 year intervals and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-305, 8-5-321.1, 8-5-322.1 | Y |  | Visual inspection of outer most seal | BAAQMD 8-5-402.2 | P/SA | Visual inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | Certification report |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | Records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| The following apply only to S-126 and S-258 |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| The following apply only to S-126 and S-258 |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON LIMITS AND MONITORING FOR INTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.646 (a) & (e) 63.120(a)(3) | periodic each time emptied & degassed, at least every 10 years | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120(a)(7) | Y |  | Primary rim-seal standards; no holes or tears | 40 CFR 63.646(a) 63.120(a)(3) | periodic each time emptied & degassed, at least every 10 years | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120(a)(4) | Y |  | No gaps visible from the tank top | 40 CFR 63.646(a) 63.120(a)(3) | P/A | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120(a)(4) | Y |  | No liquid on the floating roof or other obvious defects visible from the tank top | 40 CFR 63.646(a) 63.120(a)(3) | P/A | visual inspection |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-126: 1.05 E 7 bbl/yr S-257: 7.01 E 7 bbl/yr S-258: 7.01 E 7 bbl/yr | BAAQMD Condition , Part A | P/M | records |

| Table VII – B11 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Fixed Roof Tanks with Vapor Recovery to Fuel Gas S-360 (Tank 223), S-445 (Tank 271)S-449 (Tank 285) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR CVS & CONTROL DEVICES |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | records |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| VOC | BAAQMD 8-5-306 | Y |  | Control device standards; includes 95% efficiency requirement | BAAQMD 8-5-603.1 | not specified | MOP Volume IV ST-4 |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Organic concentration in tank <10,000 ppm as methane after cleaning | BAAQMD 8-5-503 | periodic each time emptied & degassed | portable hydrocarbon detector |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system. |
| NSPS Kb | 40 CFR 60 Subpart Kb – NSPS for VOL Storage Vessels LIMITS AND MONITORING FOR CVS & CONTROL DEVICES (NOT A FLARE) |
| VOC | 40 CFR 60.112b (a)(3)(i) | Y |  | Closed vent system leak tightness standards (< 500 ppmw) | 40 CFR 60.112b (a)(3)(i) | as required in 40 CFR 60.485(b) [Subpart VV] | Method 21 |
| VOC | 40 CFR 60.112b (a)(3)(ii) | Y |  | Control device standards; includes 95% efficiency requirement | 40 CFR 60.113b (c)(2) | as approved | specified parameter |
| BAAQMD Permit | PERMIT CONDITIONS |
| The following applies to S-445 only |
| VOC | BAAQMD Condition 12130, Part 1 | Y |  | Requirement to vent working emissions to fuel gas system | None | N | None |
| The following applies to S-449 only |
| VOC | BAAQMD Condition 11219, Part 1 | Y |  | Requirement to vent working emissions to fuel gas system | None | N | None |
| The following applies to S-360 only |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 2.78 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – B12 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Fixed Roof Tanks with Vapor Pressure >= 76.6 kPa (11 psia) with Vapor Recovery to Fuel Gas S-446 (Tank 310), S-447 (Tank 311) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR CVS & CONTROL DEVICES |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | records |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| VOC | BAAQMD 8-5-306 | Y |  | Control device standards; includes 95% efficiency requirement | BAAQMD 8-5-603.1 | not specified | MOP Volume IV ST-4 |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Organic concentration in tank <10,000 ppm as methane after cleaning | BAAQMD 8-5-503 | periodic each time emptied & degassed | portable hydrocarbon detector |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system. |
| NSPS Kb | 40 CFR 60 Subpart Kb – NSPS for VOL Storage Vessels LIMITS AND MONITORING FOR CVS & CONTROL DEVICES (NOT A FLARE) |
| VOC | 40 CFR 60.112b (a)(3)(i) | Y |  | Closed vent system leak tightness standards (< 500 ppmw) | 40 CFR 60.112b (a)(3)(i) | as required in 40 CFR 60.485(b) [Subpart VV] | Method 21 |
| VOC | 40 CFR 60.112b (a)(3)(ii) | Y |  | Control device standards; includes 95% efficiency requirement | 40 CFR 60.113b(c)(2) | as approved | specified parameter |
| BAAQMD Permit | PERMIT CONDITIONS |
| The following applies only to S-446 |
| VOC | BAAQMD Condition 12131, Part 1 | Y |  | Requirement to vent working emissions to fuel gas system | None | N | None |
| The following applies only to S-447 |
| VOC | BAAQMD Condition 12132, Part 1 | Y |  | Requirement to vent working emissions to fuel gas system | None | N | None |

| Table VII – B13 Applicable Limits and Compliance Monitoring Requirements MACT Zero-Gap External Floating-Roof Tanks S-97 (Tank 100), S-100 (Tank 103), S-110 (Tank 155), S-111 (Tank 156), S-112 (Tank 157), S-114 (Tank 159), S-115 (Tank 160), S-122 (Tank 167), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), S-150 (Tank 241), S-151 (Tank 242), S-177 (Tank 287), S-178 (Tank 288), S-186 (Tank 298), S-254 (Tank 1001), S-255 (Tank 1002), S-256 (Tank 1003), S-259 (Tank 1006) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | Reports |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | Records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| The following apply only to S-110 (Tank 155), S-115 (Tank 160), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), and S-178 (Tank 288) |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| The following apply only to S-110 (Tank 155), S-115 (Tank 160), S-123 (Tank 168), S-128 (Tank 174), S-129 (Tank 180), and S-178 (Tank 288) |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.646 (a) & (e) 63.120 (b)(10) | periodic initially & each time emptied & degassed | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(3)&(5) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(4)&(6) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & annually | measurement and visual inspection |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-97: 1.1 E 7 bbl/yr S-100: 4.38 E 6 bbl/yr S-110: 1.40 E 7 bbl/yr S-111: 1.31 E 7 bbl/yr S-112: 1.49 E 7 bbl/yr S-114: 1.31 E 7 bbl/yr S-115: 4.38 E 6 bbl/yr S-122: 4.38 E 6 bbl/yr S-123: 5.1 E 6 bbl/yr S-128: 5.1 E 6 bbl/yr S-177: 2.63 E 7 bbl/yr S-186: 4.38 E 6 bbl/yr S-254: 7.01 E 7 bbl/yr S-255: 7.01 E 7 bbl/yr S-256: 7.01 E 7 bbl/yr S-259: 7.01 E 7 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |
| throughput | BAAQMD Condition 20989, Part A | Y |  | S-129: 4.6 E 6 bbl/yr S-150: 4.38 E 7 bbl/yr S-151: 4.38 E 7 bbl/yr S-178: 3.50 E 7 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – B14 Applicable Limits and Compliance Monitoring Requirements NSPS K and NSPS Ka Zero-Gap External Floating Roof Tanks NSPS K - S-334 (Tank 107), NSPS Ka - S-341 (Tank 208), S-342 (Tank 209), S-343 (Tank 210) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | Reports |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | Records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NESHAPS CC, NSPS K (note 2), and NSPS Ka (note 3) | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON 40 CFR 60 Subpart K – NSPS for Petroleum Storage Vessels 40 CFR 60 Subpart Ka – NSPS for Petroleum Storage Vessels LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.640(n)(5) 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.640(n)(5) 63.646 (a) & (e) 63.120 (b)(10) | periodic initially & each time emptied & degassed | visual inspection |
| HAP | 40 CFR 63.640(n)(5)63.646(a) 63.120 (b)(3)&(5) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.640(n)(5) 63.646(a) 63.120 (b)(1) & (2) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| HAP | 40 CFR 63.640(n)(5)63.646(a) 63.120 (b)(4)&(6) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.640(n)(5) 63.646(a) 63.120 (b)(1) & (2) | periodic initially & annually | measurement and visual inspection |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | Y |  | S-341: 4.38 E 7 bbl/yr S-342: 4.38 E 7 bbl/yr S-343: 4.38 E 7 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-334: 6.51 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

2.	Tanks subject to 40 CFR 63 Subpart CC (MACT) and NSPS K are subject only to MACT per 63.640(n)(5). Source S-334 (Tank 107) is subject to NSPS K and MACT.

3.	Tanks subject to 40 CFR 63 Subpart CC (MACT) and NSPS Ka are subject only to MACT per 63.640(n)(5). Sources S-341 (Tank 208), S-342 (Tank 209), and S-343 (Tank 210) are subject to NSPS Ka and MACT.

| Table VII – B15 Applicable Limits and Compliance Monitoring Requirements MACT Fixed Roof Tanks with Vapor Recovery to Fuel Gas S-139 (Tank 204), S-140 (Tank 205), S-182 (Tank 294) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR CVS & CONTROL DEVICES |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | records |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| VOC | BAAQMD 8-5-306 | Y |  | Control device standards; includes 95% efficiency requirement | BAAQMD 8-5-603.1 | not specified | MOP Volume IV ST-4 |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Organic concentration in tank <10,000 ppm as methane after cleaning | BAAQMD 8-5-503 | periodic each time emptied & degassed | portable hydrocarbon detector |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system. |
| BAAQMD Permit | PERMIT CONDITIONS |
| The following applies to S-182 only |
| VOC | BAAQMD Condition 13184, Part 1 | Y |  | Requirement to vent working emissions to fuel gas system |  | N |  |
| The following applies to S-139 and S-140 only |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-139: 2.74 E 6 bbl/yr S-140: 2.74 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – B16 Applicable Limits and Compliance Monitoring Requirements MACT Zero Gap External Floating Roof Wastewater Slop Oil Tank S-133 (Tank 193) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | reports |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| BAAQMD 8-8 | BAAQMD 8-8 – Organic Compounds – Wastewater (Oil Water Separators) |
| VOC | BAAQMD 8-8-303 | Y |  | Vapor tight gauging and sampling devices | BAAQMD 8-8-504 8-8-603 | N | Portable hydrocarbon detector |
| VOC | BAAQMD 8-8-305.1 | Y |  | Slop oil tank vessel roof criteria; includes gap criteria | BAAQMD 8-8-305.1 | periodic initially & semi-annually | visual inspection |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.646 (a) & (e) 63.120 (b)(10) | periodic initially & each time emptied & degassed | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(3)&(5) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(4)&(6) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & annually | measurement and visual inspection |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 8.76 E 5 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |

| Table VII – B17 Applicable Limits and Compliance Monitoring Requirements NSPS Ka External Floating Roof Tank w/o Zero-Gap Seals S-340 (Tank 108) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | reports |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NESHAPS CC and NSPS Ka (note 2) | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON 40 CFR 60 Subpart Ka – NSPS for Petroleum Storage Vessels LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.640(n)(5) 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.640(n)(5) 63.646 (a) & (e) 63.120 (b)(10) | periodic initially & each time emptied & degassed | visual inspection |
| HAP | 40 CFR 63.640(n)(5) 63.646(a) 63.120 (b)(3)&(5) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.640(n)(5) 63.646(a) 63.120 (b)(1) & (2) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| HAP | 40 CFR 63.640(n)(5) 63.646(a) 63.120 (b)(4)&(6) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.640(n)(5) 63.646(a) 63.120 (b)(1) & (2) | periodic initially & annually | measurement and visual inspection |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | Y |  | 7.67 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |

2.	Tanks subject to 40 CFR 63 Subpart CC (MACT) and NSPS Ka are subject only to MACT per 63.640(n)(5). Source S-340 (Tank 108) is subject to NSPS Ka and MACT.

| Table VII – B18 Applicable Limits and Compliance Monitoring Requirements MACT External Floating-Roof Tanks w/o Zero-Gap Seals S-107 (Tank 150), S-113 (Tank 158), S-124 (Tank 169), S-125 (Tank 170), S-183 (Tank 295), S-184 (Tank 296), S-261 (Tank 1010) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | reports |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| The following apply only to S-107 (Tank 150), S-113 (Tank 158), S-125 (Tank 170) |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| The following apply only to S-107 (Tank 150), S-113 (Tank 158), S-125 (Tank 170) |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.646 (a) & (e) 63.120 (b)(10) | periodic initially & each time emptied & degassed | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(3)&(5) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(4)&(6) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & annually | measurement and visual inspection |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | S-107: 8.76 E 6 bbl/yr S-113: 1.49 E 7 bbl/yr S-124: 4.38 E 6 bbl/yr S-125: 1.05 E 7 bbl/yr S-261: 7.01 E 7 bbl/yr | BAAQMD Condition , Part A | P/M | Records |
| throughput | BAAQMD Condition 20989, Part A | Y |  | S-183: 4.38 E 5 bbl/yr S-184: 4.38 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – B19 Applicable Limits and Compliance Monitoring Requirements Riveted MACT External Floating Roof Tank S-216 (Tank 695) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | reports |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.646 (a) & (e) 63.120 (b)(10) | periodic initially & each time emptied & degassed | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(3)&(5) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(4)&(6) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & annually | measurement and visual inspection |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | 4.6 E 6 bbl/yr | BAAQMD Condition 20989, Part A | P/M | Records |

| Table VII – B20 Applicable Limits and Compliance Monitoring Requirements MACT External Floating-Roof Wastewater Slop Oil Tank w/o Zero-Gap Seals S-134 (Tank 194) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | reports |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| BAAQMD 8-8 | BAAQMD 8-8 – Organic Compounds – Wastewater (Oil Water Separators) |
| VOC | BAAQMD 8-8-303 | Y |  | Vapor tight gauging and sampling devices | BAAQMD 8-8-504 8-8-603 | N | Portable hydrocarbon detector |
| VOC | BAAQMD 8-8-305.1 | Y |  | Slop oil tank vessel roof criteria; includes gap criteria | BAAQMD 8-8-305.1 | periodic initially & semi-annually | visual inspection |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.646 (a) & (e) 63.120 (b)(10) | periodic initially & each time emptied & degassed | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(3)&(5) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(4)&(6) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & annually | measurement and visual inspection |
| BAAQMD Permit | PERMIT CONDITIONS |
| throughput | BAAQMD Condition 20989, Part A | N |  | 1.31 E 7 bbl/yr | BAAQMD Condition 20989, Part A | P/M | records |

| Table VII – B21 Applicable Limits and Compliance Monitoring Requirements Exempt Tanks Subject to MACT Recordkeeping S-91 (Tank 73), S-94 (Tank 78), S-98 (Tank 101), S-99 (Tank 102), S-103 (Tank 106), S-120 (Tank 165), S-130 (Tank 188), S-131 (Tank 189), S-132 (Tank 191), S-136 (Tank 201), S-137 (Tank 202), S-138 (Tank 203), S-141 (Tank 213), S-142 (Tank 214), S-143 (Tank 215), S-144 (Tank 216), S-145 (Tank 217), S-148 (Tank 231), S-149 (Tank 232), S-157 (Tank 252), S-162 (Tank 262), S-164 (Tank 264), S-165 (Tank 265), S-166 (Tank 266), S-167 (Tank 268), S-168 (Tank 269), S-169 (Tank 270), S-171 (Tank 273), S-172 (Tank 279), S-173 (Tank 280), S-174 (Tank 281), S-179 (Tank 291), S-180 (Tank 292), S-187 (Tank 299), S-191 (Tank 303), S-192 (Tank 304), S-202 (Tank 521), S-204 (Tank 528), S-205 (Tank 529), S-206 (Tank 530), S-207 (Tank 531), S-209 (Tank 674), S-224 (Tank 746), S-225 (Tank 747), S-226 (Tank 748), S-227 (Tank 749), S-228 (Tank 750), S-229 (Tank 751), S-230 (Tank 752), S-231 (Tank 753), S-236 (Tank 770), S-237 (Tank 771), S-240 (Tank 774), S-241 (Tank 775), S-260 (Tank 1009), S-262 (Tank 1011), S-263 (Tank 1012), S-266 (Tank 1345), S-267 (Tank 1346), S-286 (F3), S-287 (F10), S-293 (F805) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAP for Petroleum Refineries MONITORING FOR RECORDKEEPING ONLY |
| HAP | 40 CFR 63.641 | Y |  | Retain weight percent total organic HAP in stored liquid for Group 2 determination. | 40 CFR 63.654(i)(1) (iv) | periodic initially and upon change in service | Records |

| Table VII – B22 Applicable Limits and Compliance Monitoring Requirements Exempt Fixed Roof Tanks with Vapor Recovery to Fuel Gas S-158 (Tank 258), S-175 (Tank 284) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system. |

| Table VII – B23A Applicable Limits and Compliance Monitoring Requirements Exempt External Floating Roof Tanks Subject to MACT Recordkeeping ( but with Group I MACT Flexibility S-108 (Tank 153), S-109 (Tank 154), S-127 (Tank 173) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAP for Petroleum Refineries MONITORING FOR RECORDKEEPING ONLY |
| HAP | 40 CFR 63.641 | Y |  | Retain weight percent total organic HAP in stored liquid for Group 2 determination. | 40 CFR 63.654(i)(1) (iv) | periodic initially and upon change in service | Records |

| Table VII – B23B Applicable Limits and Compliance Monitoring Requirements Exempt External Floating Roof Tanks Subject to MACT Recordkeeping ( but with Group I MACT Flexibility S-108 (Tank 153), S-109 (Tank 154), S-127 (Tank 173) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR EXTERNAL FLOATING-ROOF TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | Records |
| VOC | BAAQMD 8-5-320 | Y |  | Floating roof fitting closure standards; includes gasketed covers | BAAQMD 8-5-401.2 | P/SA | Measurement and visual inspection |
| VOC | BAAQMD 8-5-321 | Y |  | Primary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-322 | Y |  | Secondary rim-seal standards; includes gap criteria | BAAQMD 8-5-401.1 | P/SA and every time a seal is replaced | Seal inspection |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Concentration of < 10,000 ppm as methane after degassing | BAAQMD 8-5-503 | periodic each time emptied & degassed | Portable hydrocarbon detector |
| VOC |  | Y |  | Certification reports on tank inspections and source tests | BAAQMD 8-5-404 8-5-405 | periodic after each tank inspection and source test | Reports |
| VOC |  | Y |  | Records of tank seal replacement | BAAQMD 8-5-501.2 | periodic after each tank seal replacement | Records |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NESHAPS CC | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 63 Subpart G – SOCMI HON LIMITS AND MONITORING FOR EXTERNAL FLOATING ROOF TANKS |
| HAP | 40 CFR 63.646(f) | Y |  | Deck fitting closure standards | 40 CFR 63.646 (a) & (e) 63.120 (b)(10) | periodic initially & each time emptied & degassed | visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(3)&(5) | Y |  | Primary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & at 5 yr intervals | measurement and visual inspection |
| HAP | 40 CFR 63.646(a) 63.120 (b)(4)&(6) | Y |  | Secondary rim-seal standards; includes gap criteria | 40 CFR 63.646(a) 63.120 (b)(1) & (2) | periodic initially & annually | measurement and visual inspection |

| Table VII – B24 Applicable Limits and Compliance Monitoring Requirements NSPS K Exempt Tanks Subject to MACT Recordkeeping S-90 (Tank 67), S-105 (Tank 129) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NESHAPS CC | 40 CFR 60 Subpart K – NSPS for Petroleum Storage Vessels 40 CFR 63 Subpart CC – NESHAP for Petroleum Refineries MONITORING FOR RECORDKEEPING ONLY |
| HAP | 40 CFR 63.640(n)(7) 63.641 | Y |  | Retain weight percent total organic HAP in stored liquid for Group 2 determination. | 40 CFR 63.654(i)(1) (iv) | periodic initially and upon change in service | Records |

| Table VII – B25 Applicable Limits and Compliance Monitoring Requirements Exempt Butane Spheres S-188 (Tank 300), S-189 (Tank 301), S-190 (Tank 302), S-253 (Tank 833) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| BAAQMD 8-5 | Organic Compounds - STORAGE OF ORGANIC LIQUIDS LIMITS AND MONITORING FOR PRESSURE TANKS |
| VOC | BAAQMD 8-5-301 | Y |  | Record of liquids stored and true vapor pressure | BAAQMD 8-5-501.1 | periodic initially and upon change of service | records |
| VOC | BAAQMD 8-5-303.1 | Y |  | Pressure vacuum valve set pressure within 10% of maximum allowable working pressure of the tank, or at least 0.5 psig | BAAQMD 8-5-403 | P/SA | visual inspection |
| VOC | BAAQMD 8-5-303.2 | Y |  | Pressure vacuum valve must be gas-tight: < 500 ppm (as methane) above background | BAAQMD 8-5-403 8-5-503 8-5-605 | P/SA | Method 21 portable hydrocarbon detector |
| VOC | BAAQMD 8-5-307 | Y |  | Pressure tank must be gas tight: < 100 ppm (as methane) above background | BAAQMD 8-5-503 8-5-605 | not specified | Method 21 portable hydrocarbon detector |
| VOC | BAAQMD 8-5-328.1.2 | Y |  | Organic concentration in tank <10,000 ppm as methane after cleaning | BAAQMD 8-5-503 | periodic each time emptied & degassed | portable hydrocarbon detector |
| VOC |  | Y |  | Determination of applicability | BAAQMD 8-5-604 | P/E | look-up table or sample analysis |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system |
| The following applies to S-188 only |
| NONE | 40 CFR 60 Subpart Kb – NESHAPS for Petroleum Refineries Exempt per 60.110b(d)(2). Pressure vessel designed to operate in excess of 204.9 kPa and without emissions to the atmosphere. |

| Table VII – B26 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Exempt Fixed Roof Tank Vented to Fuel Gas S-135 (Tank 200) |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system. |
| NSPS Kb | 40 CFR 60 Subpart Kb - NSPS for VOL Storage Vessels at Petroleum Refineries RECORDKEEPING ONLY |
| Vapor pressure | 40 CFR 60.110b(c) | Y |  | True vapor pressure less than 3.5 kPa. | 40 CFR 60.116b(b) | P/E | Record |

| Table VII – B27 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Exempt Fixed Roof Wastewater Tanks Vented to Fuel Gas Tank 235, Tank 236 |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries Exempt per 63.640(d)(5). Emission point routed to fuel gas system. |
| NSPS Kb | 40 CFR 60 Subpart Kb - NSPS for VOL Storage Vessels at Petroleum Refineries RECORDKEEPING ONLY |
| Vapor pressure | 40 CFR 60.110b(c) | Y |  | True vapor pressure less than 3.5 kPa. | 40 CFR 60.116b(b) | P/E | Record |
| NSPS QQQ | 40 CFR 60 Subpart QQQ – VOC Emissions from Petroleum Refinery Wastewater Systems |
| VOC | 40 CFR 60.692-3(a) | Y |  | Fixed roof closure standards | 40 CFR 60.692-3(a)(4) | periodic initially and semi-annually | Visual inspection |
| VOC |  | Y |  | Problems identified during 40 CFR 60.692-3(a) inspections that could result in VOC emissions | 40 CFR 60.697(c) | periodic when problem is identified | Records |
| VOC |  | Y |  | Problems identified during 40 CFR 60.692-3(a) inspections that could result in VOC emissions | 40 CFR 60.698(c) | periodic initially and semi-annually | Report |

| Table VII – B28 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Exempt Fixed Roof Wastewater Tank Tank 237 |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries NO MONITORING REQUIREMENTS FOR GROUP 2 WASTEWATER SOURCES |
| NSPS Kb | 40 CFR 60 Subpart Kb - NSPS for VOL Storage Vessels at Petroleum Refineries RECORDKEEPING ONLY |
| Vapor pressure | 40 CFR 60.110b(c) | Y |  | True vapor pressure less than 3.5 kPa. | 40 CFR 60.116b(b) | P/E | Record |
| Vapor pressure |  | Y |  | TVP exceedances (> 5.2 kPa). | 40 CFR 60.116b(d) | periodic within 30 days of exceedance | Notification |
| NSPS QQQ | 40 CFR 60 Subpart QQQ – VOC Emissions from Petroleum Refinery Wastewater Systems |
| VOC | 40 CFR 60.692-3(a) | Y |  | Fixed roof closure standards | 40 CFR 60.692-3(a)(4) | periodic initially and semi-annually | Visual inspection |
| VOC |  | Y |  | Problems identified during 40 CFR 60.692-3(a) inspections that could result in VOC emissions | 40 CFR 60.697(c) | periodic when problem is identified | Records |
| VOC |  | Y |  | Problems identified during 40 CFR 60.692-3(a) inspections that could result in VOC emissions | 40 CFR 60.698(c) | periodic initially and semi-annually | Report |

| Table VII – B29 Applicable Limits and Compliance Monitoring Requirements NSPS Kb Exempt Fixed Roof Tank Tank 224 |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NESHAPS CC and NSPS Kb | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries 40 CFR 60 Subpart Kb - NSPS for VOL Storage Vessels at Petroleum Refineries RECORDKEEPING ONLY |
| Vapor pressure | 40 CFR 63.640(n)(1) 60.110b(c) | Y |  | True vapor pressure less than 3.5 kPa. | 40 CFR 63.640(n)(8) 60.116b(b) | P/E | Record |
| Vapor pressure |  | Y |  | TVP exceedances (> 5.2 kPa). | 40 CFR 60.116b(d) | periodic within 30 days of exceedance | Notification |

| Table VII – B30 Applicable Limits and Compliance Monitoring Requirements Exempt External Floating Roof Wastewater Tanks Tank 206, Tank 207 |
| --- |
| Type of Limit | Emission Limit Citation | FE Y/N | Future Effective Date | Emission Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
|  | BAAQMD 8-5 - Organic Compounds - STORAGE OF ORGANIC LIQUIDS Exempt per 8-5-117. Low vapor pressure |
| POC | 8-5-117 & Condition 20773, Part 1 | Y | 4/1/04 | Exemption from Regulation 8-5 when true vapor pressure is less than 25.8 mm Hg (0.5 psia). | 2-6-409.2 & Condition 20773, Part 2 | P/E | Vapor pressure determination upon material change |
| NONE | 40 CFR 63 Subpart CC – NESHAPS for Petroleum Refineries NO MONITORING REQUIREMENTS FOR GROUP 2 WASTEWATER SOURCES |

# TEST METHODS

The test methods associated with the emission limit of a District regulation are generally referenced in Section 600 et seq. of the regulation.  The following table indicates only the test methods associated with the emission limits referenced in Section VII, Applicable Emission Limits & Compliance Monitoring Requirements, of this permit.

| Table VIII Test Methods |
| --- |
| Applicable Requirement | Description of Requirement | Acceptable Test Methods |
| BAAQMD Regulations |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Manual of Procedures, Volume I, Evaluation of Visible Emissions; EPA Method 9 |
| 6-304 | Tube Cleaning | Manual of Procedures, Volume I, Evaluation of Visible Emissions |
| 6-310 | Particulate Weight Limitation | Manual of Procedures, Volume IV, ST-15, Particulates Sampling U.S. EPA Method 5 |
| 6-311 | General Operations | Manual of Procedures, Volume IV, ST-15, Particulates Sampling U.S. EPA Method 5 |
| 8-2-301 | VOC Emission Limit for Miscellaneous Operations | Manual of Procedures, Volume IV, ST-7 or EPA Method 25 or 25A |
| 8-5-301 | Tank Emission Control System Requirements, 95% Abatement Efficiency | Manual of Procedures, Volume IV, ST-4 |
| 8-5-303.2 8-5-306, and 8-5-307 | Gas Tight Requirements for Organic Liquid Storage Tanks | Organic compounds shall be measured using a portable gas detector as prescribed in EPA Reference Method 21 (40 CFR 60, Appendix A) |
| 8-5-320 | Floating Roof Tank (internal and external) tank fitting gap measurement | Physical measurements as described in BAAQMD 8-5-320 when required in BAAQMD 8-5-401 or BAAQMD 8-5-402. |
| 8-5-321 | Floating Roof Tank (internal and external) primary rim seal gap gap measurement | Physical measurements as described in BAAQMD 8-5-321 when required in BAAQMD 8-5-401 or BAAQMD 8-5-402. |
| 8-5-322 | Floating Roof Tank (internal and external) secondary rim seal gap gap measurement | Physical measurements as described in BAAQMD 8-5-322 when required in BAAQMD 8-5-401 or BAAQMD 8-5-402. |
| 8-5-328.1.2 | Tank Degassing Emission Control System Requirements | Manual of Procedures, Volume IV, ST-7 |
| 8-7-301 | Phase I Vapor Recovery Requirements | Manual of Procedures, Volume IV, ST-30, Gasoline Vapor Recovery Leak Test Procedure; and ST-36, Gasoline Dispensing Facility Phase I Volumetric Efficiency |
| 8-7-302 | Phase II Vapor Recovery Requirements | Manual of Procedures, Volume IV, ST-30, Vapor Tightness; ST-37, Liquid Removal; and ST-41, Liquid Retain and Spitting from Nozzles |
| 8-8-302.3 | Oil-Water Separator Vapor Recovery System Requirements | Manual of Procedures, Volume IV, ST-7 or EPA Method 25 or 25A |
| 8-8-307.2 | Air Flotation Unit Vapor Recovery System Requirements | Manual of Procedures, Volume IV, ST-7 or EPA Method 25 or 25A |
| 8-8-504 | Portable Hydrocarbon Detector | A gas detector that meets the specifications and performance criteria of and has been calibrated in accordance with EPA Reference Method 21 (40 CFR 60, Appendix A) |
| 8-8-601 | Wastewater Analysis for Critical OCs | Samples of wastewater shall be taken at the influent stream for each unit and analyzed for the concentration of dissolved critical organic compounds as prescribed in the District's Manual of Procedures, Volume III, Lab Method 33. |
| 8-8-602, 8-8-301.3, 8-8-302.3, 8-8-304, 8-8-305.2, 8-8-306.2, and 8-8-307.2 | Determination of Emissions | Emissions of POCs, as specified in Sections 8-8-301.3, 8-8-302.3, 8-8-304, 8-8-305.2, 8-8-306.2, and 8-8-307.2 shall be measured by as prescribed by any of the following methods: 1). BAAQMD MOP, Volume IV, ST-7 or; 2). EPA Method 25 or 25(A). |
| 8-8-603, 8-8-301, 8-8-302, 8-8-303, and 8-8-304 | Inspection Procedures | For the purposes of 8-8-301, 302, 303, and 304, leaks shall be measured using a portable gas detector as prescribed in EPA Reference Method 21 (40 CFR 60, Appendix A) |
| 8-18 | Fugitive Emission Monitoring Requirements | EPA Method 21 |
| 8-44-301.1 8-44-301.2 | POC emission rate limitation during marine tank vessel loading | Manual of Procedures, ST-34, Bulk Marine Loading Terminals, Vapor Recovery Units |
| 8-44-303 | Tank vessel is leak free and gas tight | EPA Method 21 |
| 8-44-603 | Leak Tests and Gas Tight Determinations | EPA Method 21 |
| 9-1-301, 9-2-301, 9-1-604 | Ground Level Monitoring | Manual of Procedures, Volume VI, Section 1, Area Monitoring |
| 9-1-302 | Sampling and Analysis, SO2 | Manual of Procedures, Volume IV, ST-19 A or B |
| 9-1-501, 9-1-502, 9-2-501 | Continuous Monitoring | Manual of Procedures, Volume 5, Continuous Monitoring |
| 9-1-313 | NH3 and H2S abatement efficiency | Manual of Procedures, Volume III, Lab 32, Determination of H2S in Process Water Streams Manual of Procedures, Volume III, Lab 1, Determination of NH3 in Effluents |
| 9-9-301.3 | Emission Limits- Turbines Rated > 10 MW with SCR | Manual of Procedures, Volume IV, ST-13A, Oxides of Nitrogen, Continuous Sampling and ST-14, Oxygen, Continuous Sampling |
| 9-10-301 | Refinery-Wide NOx Emission Limit | Manual of Procedures, Volume V and Manual of Procedures, Volume IV, ST-13A or B (nitrogen oxides) and ST-14 (oxygen) |
| 9-10-303.1 | NOx Emission Limit | Manual of Procedures, Volume V and Manual of Procedures, Volume IV, ST-13A or B (nitrogen oxides) and ST-14 (oxygen) |
| 9-10-305 | CO Emission Limit | Manual of Procedures, Volume V and Manual of Procedures, Volume IV, ST-6 (carbon monoxide) for CEM verification by source test |
| 40 CFR 60 Subpart A | New Source Performance Standards – General Provisions (12/23/71) |  |
| 40 CFR Subpart A 60.18(c)(1) | Visible emission monitoring | EPA Method 22: Visible Emissions |
| 40 CFR 60 Subpart Db | Standards of Performance for Industrial-Commercial-Institutional Steam Generating Units (3/13/00) |  |
| 40 CFR 60 Subpart Db 60.44b(a) 60.44b(e) | NOx Emission Limit | 40 CFR 60 Appendix B, Performance Specification 2 |
| 40 CFR 60 Subpart J | Standards of Performance for Petroleum Refineries (7/1/00) |  |
| 40 CFR 60 Subpart J, 60.104(a)(1) | Fuel Gas H2S Concentration Limit | 40 CFR 60 Appendix B, Performance Specification 7 and Method 11 for Relative Accuracy |
| 40 CFR 60, Subpart J, 60.106(f)(3) | H2S concentration monitoring | EPA Method 3: O2 |
| 40 CFR 60,Subpart J, 60.106(f)(1) | SO2 concentration monitoring | EPA Method 6: SO2 |
| 40 CFR 60, Subpart J, 60.106(e) | H2S concentration monitoring | EPA Method 11: H2S |
| 40 CFR 60,Subpart J, 60.106(f)(2) | TRS concentration monitoring | EPA Method 15: Total Reduced Sulfur |
| 40 CFR 60 Subpart Kb | Standards of Performance for Volatile Organic Liquid Storage Vessels |  |
| 40 CFR 60 Subpart Kb 60.112b (a)(3)(i) | NSPS Subpart Kb Closed Vent System – leak detection | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(b) |
| 40 CFR 60 Subpart Kb 60.112b (a)(3)(ii) | NSPS Subpart Kb Closed Vent System Performance (95% efficiency) | 40 CFR 60 Subpart Kb 60.113b(c) Testing and Procedures |
| 40 CFR 60 Subpart Kb 60.113b (b)(4)(i) | NSPS Subpart Kb External Floating Roof Tank primary rim seal gap measurement | 40 CFR 61 Subpart Kb 60.113b(b)(1) through 60.113b(b)(3) Testing and Procedures |
| 40 CFR 60 Subpart Kb 60.113b (b)(4)(ii) | NSPS Subpart Kb External Floating Roof Tank secondary rim seal gap measurement | 40 CFR 61 Subpart Kb 60.113b(b)(1) through 60.113b(b)(3) Testing and Procedures |
| 40 CFR 60 Subpart GG | Standards of Performance for Stationary Gas Turbines (1/27/82) |  |
| 60.332 (a)(1) | Performance Standard, NOx | EPA Method 20, Determination of Nitrogen Oxides, Sulfur Dioxide, and Diluent Emissions from Stationary Gas Turbines |
| 60.332 (a)(2) | Performance Standard, NOx | EPA Method 20, Determination of Nitrogen Oxides, Sulfur Dioxide, and Diluent Emissions from Stationary Gas Turbines |
| 60.333 (a) | SO2 Volumetric Emission Limit | EPA Method 20, Determination of Nitrogen Oxides, Sulfur Dioxide, and Diluent Emissions from Stationary Gas Turbines |
| 60.333 (b) | Fuel Sulfur Limit (gaseous fuel) | ASTM D 1072-80, Standard Method for Total Sulfur in Fuel Gases ASTM D 3031-81, Standard Test Method for Total Sulfur in Natural Gas by Hydrogenation ASTM D 4084-82, Standard Method for Analysis of Hydrogen Sulfide in Gaseous Fuels (Lead Acetate Reaction Rate Method), ASTM D 3246-81, Standard Method for Sulfur in Petroleum Gas by Oxidative Microcoulometry |
| 60.333 (b) | Fuel Sulfur Limit (liquid fuel) | ASTM D 2880-71, Standard Specification for Gas Turbine Fuel Oils |
| 40 CFR 60, Appendix A | Inspection Procedures | EPA Reference Method 21 |
| 40 CFR 60 Subpart VV | Standards of Performance for Equipment Leaks of VOC in SOCMI |  |
| 40 CFR 60 Subpart VV 60.482-2(b)(1) | Pumps in light liquid service – leak detection | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(b) |
| 40 CFR 60 Subpart VV 60.482-2(e) | Pumps in light liquid service and designated for “no detectable emission” – leak detection | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(c) |
| 40 CFR 60 Subpart VV 60.482-3 | Compressors designated for “no detectable emission” – leak detection | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(c) |
| 40 CFR 60 Subpart VV 60.482-4(b) | Pressure relief valve (gas/vapor) no detectable emissions after a pressure release event. | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(c) |
| 40 CFR 60 Subpart VV 60.482-7(b) | Valves in gas/vapor service and in light liquid service – leak detection. | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(b) |
| 40 CFR 60 Subpart VV 60.482-7(f) | Valves in gas/vapor service and in light liquid service and designated for “no detectable emission” – leak detection | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(c) |
| 40 CFR 60 Subpart VV 60.482-7(h) | Valves in gas/vapor service and in light liquid service and designated as difficult-to-monitor. | 40 CFR 60 Appendix A, Method 21 once per year in accordance with written plan (60.482-7(h)(3) |
| 40 CFR 60 Subpart VV 60.482-8(b) | Pumps and valves in heavy liquid service, pressure relief devices (liquid), and flanges and other connectors – leak detection | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(b) |
| 40 CFR 60 Subpart VV 60.483-2 | Individual valves meeting criteria for skip period leak detection – leak detection | 40 CFR 60 Appendix A, Method 21 as specified in 40 CFR 60 Subpart VV 60.485(b) |
| 40 CFR 60 Subpart QQQ | Standards of Performance For Petroleum Refinery Wastewater Systems |  |
| 40 CFR 60, Subpart QQQ, 60.696 | Performance test methods and procedures and compliance provisions | Sources equipped with a closed-vent system and control device shall use EPA Method 21 to measure the emission concentrations, using 500 ppm as the no detectable emission limit. Acceptable seal gap criteria also included. |
| 40 CFR 60, Subpart QQQ | Leak inspection procedures | 40 CFR 60 Subpart QQQ, 60.696: EPA reference method 21 (40 CFR 60, Appendix A), Determination of Volatile Organic Compound Leaks |
| 40 CFR 61 Subpart FF | National Emission Standard for Benzene Waste Operations |  |
| 40 CFR 61, Subpart FF 61.349 (a)(1)(i) | Leak inspection procedures | 40 CFR 61 Subpart FF, 61.355(h): EPA reference method 21 (40 CFR 60, Appendix A), Determination of Volatile Organic Compound Leaks |
| 40 CFR 61, Subpart FF 61.354 (f) | Visual Inspection | 40 CFR 61 Subpart FF, 61.354(f) |
| 40 CFR 63 Subpart CC | National Emissions Standards for Hazardous Air Pollutants from Petroleum Refineries – General Standards |  |
| 40 CFR 63 Subpart CC 63.646(a) 40 CFR 63 Subpart G 63.120(b)(3) 63.120(b)(5) | Refinery MACT (40 CFR 63 Subpart CC) Group 1 external floating roof tanks primary rim-seal gap measurement | 40 CFR 63 Subpart G 60.120(b)(1) and 60.120(b)(2) Procedures to Determine Compliance |
| 40 CFR 63 Subpart CC 63.646(a) 40 CFR 63 Subpart G 63.120(b)(4) 63.120(b)(6) | Refinery MACT (40 CFR 63 Subpart CC) Group 1 external floating roof tanks secondary rim-seal gap measurement | 40 CFR 63 Subpart G 60.120(b)(1) and 60.120(b)(2) Procedures to Determine Compliance |
| California Air Resources Board (CARB) |  |  |
| BAAQMD Condition 18680, Part 2 | Gasoline dispensing facility leak test | CARB Test Procedure TP201.1B: “Rotatable Adaptor Torgue Test” |
| BAAQMD Condition 18680, Part 2 | Gasoline dispensing facility leak test | CARB Test Procedure TP201.1C: “Drop Tube/Drain Valve Assembly” |
| BAAQMD Condition 18680, Part 2 | Gasoline dispensing facility leak test | CARB Test Procedure TP201.1D: “Drop Tube Overfill Prevention Device and Spill Container Drain Valve Leak Test” |

# PERMIT SHIELD

## Non-applicable Requirements

Pursuant to District Regulations 2-6-233 and 2-6-409.12, the federally enforceable regulations and/or standards cited in the following table[s] are not applicable to the source or group of sources identified at the top of the table[s].  Enforcement actions and litigation may not be initiated against the source or group of sources covered by this shield based on the regulatory and/or statutory provisions cited, as long as the reasons listed below remain valid for the source or group of sources covered by this shield.

| Table IX A - 1 Permit Shield for Non-applicable Requirements All Sources |
| --- |
| Citation | Title or Description (Reason not applicable) |
| BAAQMD Regulation 8, Rule 51 | "Organic Compounds – Adhesive and Sealant Products" (7/17/02) The applicant has certified that none of the regulated activities specified in this rule are currently taking place at this facility. |
| BAAQMD Regulation 11, Rule 1 | "Hazardous Pollutants – Lead" (3/17/82) The applicant has certified that there are no sources at this facility with the potential to emit in excess of 15 pounds per day (11-1-301) each, or with the potential to result in ground level lead concentrations in excess of 1.0 microgram/m3 averaged over 24 hours (11-1-302). |

| Table IX B - 1 Permit Shield for Subsumed Requirements S-324 API Oil/Wastewater Separator |
| --- |
| Subsumed Requirement Citation | Title or Description | Streamlined Requirements | Title or Description |
| NSPS Subpart QQQ, 40 CFR 60.693-2(a)(1) | Floating roofs installed as alternative standard for oil-water separators shall be equipped with a closure device. | BAAQMD 8-8-302.1 and Permit Condition 1440, Part 1 | The API separator shall be equipped and operated such that the fixed roof is in full contact with the liquid at all times. As described in the NSPS Subpart QQQ Request for Alternative Standards pursuant to 40 CFR 60.693-2(b) and 60.694 submitted to USEPA by Unocal on December 28, 1987, in lieu of a floating roof equipped with a closure device, the separator would be equipped with the full contact fixed roof as an equivalent closure device. |
| NSPS Subpart QQQ, 40 CFR 60.693-2(a)(3) | Floating roofs installed as alternative standard for oil-water separators shall be floating on the liquid (i.e., off the roof supports) at all times, except for low flow conditions. | BAAQMD 8-8-302.1 and Permit Condition 1440, Part 1 | The API separator shall be equipped and operated such that the fixed roof is in full contact with the liquid at all times. As described in the NSPS Subpart QQQ Request for Alternative Standards pursuant to 40 CFR 60.693-2(b) and 60.694 submitted to USEPA by Unocal on December 28, 1987, in lieu of a floating roof equipped with a closure device, the separator would be equipped with the full contact fixed roof as an equivalent closure device. |
| NSPS Subpart QQQ, 40 CFR 60.697(k) | For oil-water separators subject to 60.693-2, record information from inspections conducted pursuant to the 60.693-2(a)(1)(iii)(A) and (B) requirements for floating roofs equipped with a closure device. | BAAQMD 8-8-302.1 and Permit Condition 1440, Part 1 | The API separator shall be equipped and operated such that the fixed roof is in full contact with the liquid at all times. As described in the NSPS Subpart QQQ Request for Alternative Standards pursuant to 40 CFR 60.693-2(b) and 60.694 submitted to USEPA by Unocal on December 28, 1987, in lieu of a floating roof equipped with a closure device, the separator would be equipped with the full contact fixed roof as an equivalent closure device. |

| Table IX B - 2 Permit Shield for Subsumed Requirements S-352 – Combustion Turbine S-353 – Combustion Turbine S-354 – Combustion Turbine |
| --- |
| Subsumed Requirement Citation | Title or Description | Streamlined Requirements | Title or Description |
| NSPS Subpart GG, 40 CFR 60.334(a) | Install and operate a continuous monitoring system to monitor and record the ratio of water to fuel being fired in the turbine. | BAAQMD 9-9-501, Permit Condition 12122, Part 9b, Permit Condition 18629, Part IX.G.1.a., and proposed Subpart GG Amendments: 40 CFR 60.334(b). | Per BAAQMD regulations and permit conditions, ConocoPhillips has equipped the turbines with NOx CEMs in lieu of monitoring the water-to-fuel-ratio being fired in the turbines. Further, proposed amendments to Subpart GG (FR 17990), allow facilities to install and operate a NOx CEM in lieu of water to fuel ratio monitoring. |
| NSPS Subpart GG, 40 CFR 60.334(b) | Monitor nitrogen content of the fuel being fired in the turbine. | Proposed Subpart GG Amendments: 40 CFR 60.334(h)(2). | Per proposed amendments to Subpart GG (FR 17990), facilities that elect to take no allowance for fuel bound nitrogen in determining the applicable NOx standard are not required to monitor nitrogen fuel content. ConocoPhillips will elect to take this approach when the proposed amendments become effective (May 29, 2003), resulting in a revised NOx standard per 60.332(a)(2) of 150 ppmv at 15% O2 with no fuel bound nitrogen monitoring. |
| NSPS Subpart GG, 40 CFR 60.334(c)(1) | Definition of excess nitrogen oxide emissions for purposes of reports under 40 CFR 60.7(c) is based on any one-hour period during which the average water-to-fuel ratio falls below the water-to-fuel ratio determined to demonstrate compliance by the performance test required in 60.8.. | BAAQMD 9-9-501, Permit Condition 12122, Part 9b, Permit Condition 18629, Part IX.G.1.a., and proposed Subpart GG Amendments: 40 CFR 60.334(j)(1)(iii). | Per proposed amendments to Subpart GG (FR 17990), the definition of excess emissions is revised for facilities that install and operate a NOx CEMS in lieu of water to fuel ratio monitoring. The revised definition is based on an operating hour in which the 4-hour rolling average NOx concentration as measured by the CEM exceeds the 60.332(a)(2) limit. |

# GLOSSARY

# ACT

# Federal Clean Air Act

# APCO

# Air Pollution Control Officer

# ARB

# Air Resources Board

# BAAQMD

# Bay Area Air Quality Management District

# BACT

# Best Available Control Technology

# BARCT

# Best Available Retrofit Control Technology

Basis

The underlying authority which allows the District to impose requirements.

# CAA

# The federal Clean Air Act

# CAAQS

# California Ambient Air Quality Standards

# CAPCOA

# California Air Pollution Control Officers Association

# CEC

# California Energy Commission

# CEQA

# California Environmental Quality Act

CEM

A "continuous emission monitor" is a monitoring device which provides a continuous record of some parameter (e.g. NOx concentration) in an exhaust steam.

# CFR

The Code of Federal Regulations.  40 CFR contains the implementing regulations for federal environmental statutes such as the Clean Air Act.  Parts 50-99 of  40 CFR contain the requirements for air pollution programs.

# CO

# Carbon Monoxide

CO2

Carbon Dioxide

Cumulative Increase

The sum of permitted emissions from each new or modified source since a specified date pursuant to BAAQMD Rule 2-1-403, Permit Conditions (as amended by the District Board on 7/17/91) and SIP Rule 2-1-403, Permit Conditions (as approved by EPA on 6/23/95).  Used to determine whether threshold-based requirements are triggered.

# DAF

# A "dissolved air flotation" unit is a process vessel where air bubbles injected at the bottom of the vessel are used to carry solids in the liquid into a froth on the liquid surface, where it is removed.

# DWT

# Dead Weight Tons

# District

# The Bay Area Air Quality Management District

dscf

Dry Standard Cubic Feet

E 6, E 9, E 12

Very large or very small number values are commonly expressed in a form called scientific notation, which consists of a decimal part multiplied by 10 raised to some power.  For example, 4.53 E 6 equals (4.53)x(106) = (4.53)x(10x10x10x10x10x10) = 4,530,000.  Scientific notation is used to express large or small numbers without writing out long strings of zeros.

EFRT

An "external floating roof tank" minimizes VOC emissions with a roof with floats on the surface of the liquid, thus preventing the formation of a VOC-rich vapor space above the liquid surface as the level in the tank drops.  If such a vapor space were allowed to form, it would be expelled when the tank was re-filled.  On an EFRT, the floating roof is not enclosed by a second, fixed tank roof, and is thus described as an "external" roof.

EMP

Environmental Management Plan

ESP

Electrostatic Precipitator

# EPA

# The federal Environmental Protection Agency.

# Excluded

# Not subject to any District Regulations.

FCC

Fluid Catalytic Cracker

# Federally Enforceable, FE

All limitations and conditions which are enforceable by the Administrator of the EPA including those requirements developed pursuant to 40 CFR Part 51, Subpart I (NSR), Part 52.21 (PSD), Part 60 (NSPS), Part 61 (NESHAPs), Part 63 (HAP), and Part 72 (Permits Regulation, Acid Rain), and also including limitations and conditions contained in operating permits issued under an EPA-approved program that has been incorporated into the SIP.

FP

Filterable Particulate as measured by BAAQMD Method ST-15, Particulate.

GRU

Gas Recovery Unit

H2S

Hydrogen sulfide

H2SO4

Sulfuric Acid

# HAP

Hazardous Air Pollutant.  Any pollutant listed pursuant to Section 112(b) of the Act.  Also refers to the program mandated by Title I, Section 112, of the Act and implemented by 40 CFR Part 63.

HC

Hydrocarbon

Hg

Mercury

HNC

Heavy Neutral Hydrocracker

HNHF

Heavy Neutral Hydrofinisher

# HHV

High Heating Value.  The quantity of heat evolved as determined by a calorimeter where the combustion products are cooled to 60F and all water vapor is condensed to liquid.

IFRT

An "internal floating roof tank" minimizes VOC emissions with a roof with floats on the surface of the liquid, thus preventing the formation of a VOC-rich vapor space above the liquid surface as the level in the tank drops.  If such a vapor space were allowed to form, it would be expelled when the tank was re-filled.  On an IFRT, the floating roof is enclosed by a second, fixed tank roof, and thus is described as an "internal" roof.

LFSO

Low sulfur fuel oil

# Lighter

# "Lightering" is a transfer operation during which liquid is pumped from an ocean-going tanker vessel to a smaller vessel such as a barge.  Like any liquid transfer operation, lightering of organic liquids produces organic vapor emissions.

LNC

Light Neutral Hydrocracker

LNHF

Light Neutral Hydrofinisher

LPG

Liquid Petroleum Gas

# Major Facility

A facility with potential emissions of: (1) at least 100 tons per year of regulated air pollutants, (2) at least 10 tons per year of any single hazardous air pollutant, and/or (3) at least 25 tons per year of any combination of hazardous air pollutants, or such lesser quantity of hazardous air pollutants as determined by the EPA administrator.

# MFR

Major Facility Review.  The District's term for the federal operating permit program mandated by Title V of the Act and implemented by District Regulation 2, Rule 6.

MM

Million

# Mo Gas

# Motor gasoline

# MOP

# The District's Manual of Procedures

MTBE

Methyl Tertiary Butyl Ether

NA

Not applicable

# NAAQS

# National Ambient Air Quality Standards

# NESHAPs

# National Emission Standards for Hazardous Air Pollutants.  See in 40 CFR Parts 61 and 63.

# NMHC

# Non-methane Hydrocarbons

# NMOC

Non-methane Organic Compounds (Same as NMHC)

# NOx

# Oxides of nitrogen.

# NSPS

Standards of Performance for New Stationary Sources.  Federal standards for emissions from new stationary sources.  Mandated by Title I, Section 111 of the Act, and implemented by 40 CFR Part 60 and District Regulation 10.

# NSR

New Source Review.  A federal program for pre-construction review and permitting of new and modified sources of air pollutants for which the District is classified "non-attainment".  Mandated by Title I of the Clean Air Act and implemented by 40 CFR Parts 51 and 52 as well as District Regulation 2, Rule 2.  (Note:  There are additional NSR requirements mandated by the California Clean Air Act.)

# O2

# The chemical name for naturally-occurring oxygen gas.

# Offset Requirement

A New Source Review requirement to provide federally enforceable emission offsets at a specified ratio for the emissions from a new or modified source and any pre-existing cumulative increase minus any onsite contemporaneous emission reduction credits.  Applies to emissions of POC, NOx, PM10, and SO2.

# Phase II Acid Rain Facility

A facility that generates electricity for sale through fossil-fuel combustion and is not exempted by 40 CFR 72 from Titles IV and V of the Clean Air Act.

# POC

# Precursor Organic Compounds

# PM

# Total Particulate Matter

# PM10

# Particulate matter with aerodynamic equivalent diameter of less than or equal to 10 microns

# Process Unit

# For the purpose of startup and shutdown reporting, a process unit is defined as found in 40 CFR Part 60 Subpart GGG:

# Process Unit means components assembled to produce intermediates or final products from petroleum, unfinished petroleum derivatives, or other intermediates; a process unit can operate independently if supplied with sufficient feed or raw materials and sufficient storage facilities for the product.

# PSD

Prevention of Significant Deterioration.  A federal program for permitting new and modified sources of air pollutants for which the District is classified "attainment" of the National Air Ambient Quality Standards.  Mandated by Title I of the Act and implemented by both 40 CFR Part 52 and  District Regulation 2, Rule 2.

RACT

Reasonably Available Control Technology

Regulated Organic Liquid

"Regulated organic liquids" are those liquids which require permits, or which are subject to some regulation, when processed at a liquid-handling operation.  For example, for refinery marine terminals, regulated organic liquids are defined as "organic liquids" in Regulation 8, Rule 44.

# SCR

# A "selective catalytic reduction" unit is an abatement device which reduces NOx concentrations in the exhaust stream of a combustion device.  SCRs utilize a catalyst, which operates at a specific temperature range, and injected ammonia to promote the conversion of NOx compounds to nitrogen gas.

SDA

Solvent deasphalting

# Shutdown

# For reporting purposes only, a shutdown shall be defined as any of the following:  there is no process feed to a unit, no furnace fires, or the boundary blinds are installed.

# SIP

State Implementation Plan.  State and District programs and regulations approved by EPA and developed in order to attain the National Air Ambient Quality Standards.  Mandated by Title I of the Act.

# SO2

# Sulfur dioxide

# SO2 Bubble

# An SO2 bubble is an overall cap on the SO2 emissions from a defined group of sources, or from an entire facility.  SO2 bubbles are sometimes used at refineries because combustion sources are typically fired entirely or in part by "refinery fuel gas" (RFG), a waste gas product from refining operations.  Thus, total SO2 emissions may be conveniently quantified by monitoring the total amount of RFG that is consumed, and the concentration of H2S and other sulfur compounds in the RFG.

SO3

Sulfur trioxide

SRU

Sulfur Recovery Unit

ST-7

Source Test Method #7:  Non-Methane Organic Carbon Sampling

# Startup

# For reporting purposes only, a startup shall be defined as any of the following:  the removal of boundary blinds, first fire to a furnace, or the introduction of process feed to a unit.  A startup only occurs following a shutdown unless it involves a newly constructed process unit.

THC

Total Hydrocarbons (NMHC + Methane)

# Title V

Title V of the federal Clean Air Act.  Requires a federally enforceable operating permit program for major and certain other facilities.

TKC

Taylor Kinetic Cracking

TOC

Total Organic Compounds (NMOC + Methane, Same as THC)

TPH

Total Petroleum Hydrocarbons

TRMP

Toxic Risk Management Plan

# TRS

# "Total reduced sulfur" is a measure of the amount of sulfur-containing compounds in a gas stream, typically a fuel gas stream, including, but not limited to, hydrogen sulfide.  The TRS content of a fuel gas determines the concentration of SO2 that will be present in the combusted fuel gas, since sulfur compounds are converted to SO2 by the combustion process.

# TSP

# Total Suspended Particulate

VGO

Vacuum Gas Oil

# VOC

# Volatile Organic Compounds

VR

Vapor Recovery

WWT

Wastewater Treatment

# Units of Measure:

bbl	=	barrels

bhp	=	brake-horsepower

btu	=	British Thermal Unit

g	  =	grams

gal	=	gallon

gpm	=	gallons per minute

hp	=	horsepower

hr	=	hour

lb	=	pound

in	=	inches

max	=	maximum

m2	=	square meter

min	=	minute

mm	=	million, millimeter

ppmv	=	parts per million, by volume

ppmw	=	parts per million, by weight

psia	=	pounds per square inch, absolute

psig	=	pounds per square inch, gauge

scfm	=	standard cubic feet per minute

yr	=	year

# APPLICABLE STATE IMPLEMENTATION PLAN

The Bay Area Air Quality Management District’s portion of the State Implementation Plan can be found at EPA Region 9’s website.  The address is:

http://yosemite1.epa.gov/r9/r9sips.nsf/California?ReadForm&Start=1&Count=30&Expand=3.1

# Footnotes

( Sources S-108, S-109, and S-127 currently contain low vapor pressure liquids, are exempt from BAAQMD permitting requirements, and fall under the MACT Group II requirements for recordkeeping. However, these tanks may be operated as MACT Group I tanks in the future. Table B23A shows the appropriate applicability for these tanks as MACT Group II tanks. Table B23B shows the appropriate applicability for these tanks as MACT Group I tanks including the BAAQMD Regulation 8 Rule 5 requirements for zero-gap secondary seals.

( Sources S-108, S-109, and S-127 currently contain low vapor pressure liquids, are exempt from BAAQMD permitting requirements, and fall under the MACT Group II requirements for recordkeeping. However, these tanks may be operated as MACT Group I tanks in the future. Table B23A shows the appropriate applicability for these tanks as MACT Group II tanks. Table B23B shows the appropriate applicability for these tanks as MACT Group I tanks including the BAAQMD Regulation 8 Rule 5 requirements for zero-gap secondary seals.

Group 2 storage vessels as defined in 40 CFR 63 Subpart CC (MACT) that are subject to NSPS K but are exempt from control requirements in NSPS K are subject only to MACT per 63.640(n)(7).